## Slide 1
1
.
DRD4 Collaboration Meeting,
WG-2 session: CERN, April 11 2025
V, P, Matprops
“Green radiators”: Update on (thoughts on) gas radiator development
(based on previous presentations: see next slide)
* See also the talk of Fulvio Tessarotto, Tuesday morning WP3 meeting
(https://indico.cern.ch/event/1536396/contributions/6465189/attachments/3047336/5384716/
tessarotto_radiator_gas_system_DRD4_WP3_2025_04_08.pdf)
G. Hallewell
Aix Marseille Université,
CNRS/IN2P3, CPPM, Marseille, France
Notes: 1

## Slide 2
2
.
This is a follow-on from previous presentations in this vein:
(too much for here): for more information see:
“Green radiators”: Controlling refractive index & reducing Cherenkov gas radiator GWP: a challenge in an era of diminishing fluorocarbon availability
Related paper: https://link.springer.com/article/10.1140/epjp/s13360-023-04703-w
Also DRD4 meeting, May 2023 https://indico.cern.ch/event/1263731/contributions/5398511
ATLAS sustainability forum CERN, Jan 26 2024
https://indico.cern.ch/event/1371158/contributions/5773321/attachments/2788215/4861759/G_Hallewell_ATLAS_sustainability_forum_Jan_26_2024_v2.pptx
Sustainable HEP 2024 https://indico.global/event/4744/contributions/39611/
ICHEP2024 (July 2024): https://indico.cern.ch/event/1291157/contributions/5900402
DRD4 meeting Oct. 2024: https://indico.cern.ch/event/1456663/sessions/566400/#20241024
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Notes: 2

## Slide 3
COMPASS, LHCb use C4F10 & CF4 Cherenkov gas radiators.
These Saturated Fluorocarbons (CnF(2n+2)) have high GWPs (5000-9000*CO2)
 impetus at CERN to reduce their use;
Sound velocity measurement was used in real-time C5F12 /N2 & C4F10 /N2 blending. Valuable in future to meet optical & low GWP constraints of blended Cherenkov gas radiators
also in continuously sensitive real-time leak detection (ATLAS Si tracker).
Fluoro-olefins (or fluoro-ketones: CnF2nO) can offer similar optical performance, with GWPs equivalent to CO2 (or zero);
But GWPs are geometry-specific: closed molecular rings with O atom link have GWPs as high as SFCs. Reactivity & toxicity likely to be geometry dependent;
Legislation may limit SFC & F-K PFAS (*Per- and polyfluoroalkyl substances) availability, leaving “holes” in the CnFx “spectrum”, unfilled by CnF2nO equivalents;
Blending low molar concentrations of heritage-stock higher-order SFCs
or C5F10O (GWPzero) with light gases, N2, Ar, CO2… would reduce overall
radiator volume GWP “load” and mean less FC liquid mass stockage;
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 4: The CERN Green Scene: Fairly recently: (Cherenkov gas radiators a small part of overall thematic...)
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Watch this (CEPS) space
- and GET SB MEMBERSHIP
- to represent the
Cherenkov detector
community and its needs!

## Slide 5
But no mention at all of the ATLAS ultrasonic fluorocarbon leak monitor system !
https://doi.org/10.25325/CERN-Environment-2023-003
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 6
This latest CERN environmental report https://doi.org/10.25325/CERN-Environment-2023-003
R449: (CFH blend) GWP=1397
R1234 (HFO): GWP = 7
NOVEC 649 (C6F12O): GWP=0
Collective loss of SFCs only around 10 tonnes (whole of LHC + expts)
(compare that to mass-loss at a ‘grande surface’ supermarket!)
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 7: CERN F-gas policy document on EDMS (July 2024)
https://edms.cern.ch/ui/file/3120169/1/
CERN_F-gas_policy_docx_cpdf.pdf
Page 1 of 4
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 8
EU strategy to reduce Fluronated (PFAS) compound production and use
(includes also fluorinated plastics not shown here: see back-up material)
From: ICHEP2024
Projected Usage
Dynamic price hiking :
like Trimposing demand-dependent tariffs…?
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 9
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 10
(from Guida talk)
Watch this (CEPS) space
- and GET SB MEMBERSHIP
- to represent the
Cherenkov detector
community and its needs!
CERN and the Environment (what?)Town Hall meeting 8 November 2024
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 11: And coming up soon…
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 12
Is the Chemical industry dragging its feet
(3M plans to stop PFAS production in 2025: …other companies filling the gap?)
Is a ban even realistic (semiconductor industry…?)
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 13: Molecular shapes, GWP & toxicity
Cherenkov
Radiator
(hist.) + Cooling (Liq.)
Si cooling
(Evap.)
COOLING (Liq.)
Ih.T H331,
reactive
Ih.T H330, reactive
Ih.T H331,
reactive
Ih.T. H335
Ih.T. H335
Ih.T. H335
Cherenkov
Radiator
Cherenkov
Radiator
Cherenkov
Radiator
(hist.)
Cherenkov
Radiator
(hist.)
Upper: molecular shapes of SFCs, including common gaseous Cherenkov radiators.
Lower: shapes of some non-cyclic CnF2nO analogues (20-year GWPs & GHS inhalation toxicities (source www.synquest.com
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
C2F4O
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335

## Slide 14: GHS Classification Criteria for Inhalation & skin Toxicity
H330 | Fatal if inhaled
H331 | Toxic if inhaled
H332 | Harmful if inhaled
H333 | May be harmful if inhaled
H334 | May cause allergy or asthma symptoms or breathing difficulties if inhaled
H335 | May cause respiratory irritation
H336 | May cause drowsiness or dizziness
H310 | Fatal in contact with skin
H311 | Toxic in contact with skin
H312 | Harmful in contact with skin
H313 | May be harmful in contact with skin
H314 | Causes severe skin burns and eye damage
H315 | Causes skin irritation
Global Harmonized System of Classification and Labelling of Chemicals (GHS). 10th revision, United Nations (2023}
About the GHS | UNECE https://unece.org/about-ghs
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 15
C4F8O Linear with Oxygen atom as
internal link and double carbon
bonded link
C4F8O
Cyclic
Perfluorotetrahydrofuran,
Octofluorotetrahydrofuran
(GWP20 = 8975) [ref EPJP]
[H335]
C4F8O Linear & iso, with
Oxygen atom on external spur
Octafloro-1-methoxyprop-1-ene
(GWP20 = ?) [H332, 335, 336]
Octafluoro-2-butanone
(GWP20 = ?) [H335]
Heptafluorobutyryl fluoride
(GWP20 = ?) [H331]
Heptafluoroisobutyryl fluoride
(GWP20 = ?) [H335]
Pentafyoroethyltrifluorovinyl ether
(GWP20 = ?) [H332, 335]
Molecular shape is important for GWP and toxicity
Cyclic, non-cyclic & non-cyclic double c-bonded C4F8O isomers
Optical performance similar
to C4F10: (BTeV & ALICE VHMPID)
High GWP!!
GWP ?

GWP ?
GWP ?
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 16: Q: What gives NOVEC 649/1230 its low GWP?
Scission by UV photons of l around 300 nm
In the atmosphere (low pressure, high UV): the fragments do not reassociate* into saturated fluorocarbons of the type CnF(2n+2) (which would have high GWP)
*The Environmental Impact of CFC Replacements HFCs and HCFCs
T. WALLINGTON et al Environ.Sci.Technol.1994(28)7 320A https://doi.org/10.1021/es00056a714
https://www.nist.gov/system/files/documents/el/fire_research/R0301570.pdf
16
[15]
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Problematic UV absorbance
band for Cherenkov
light detection?

## Slide 17: - Use Fluoro-ketone substitites for SFCs where possible (evaluation of C5F10O/CO2 planned: Antonello di Mauro) ; - Better ‘husbandry’ of SFCs if we must continue with them (better leaktightnes, blend & leak monitoring, reduced losses in circulation & purification)  lower FC stocks; - GWP Load lightening: blending a low concentration of a heavy SFC or F-K with N2 to replicate refractive index of a lighter SFC at high concentration; - No to flammable substitutes (you’ll see why…); - Avoidance of pressures > 105 hPa (PV stored energy)
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Cherenkovgreenicity

## Slide 18: Surrounding a Fluorocarbon RICH radiator with a thin (for example: N2) -purged leak sniffing jacket equipped with ultrasonic monitoring of FC molar mass
Continuous real-time monitoring
Alarm raising
Cumulative loss calculation (compliments tankage mass loss measurements)

Can also condense the FC leaking into the sampling volume to reduce losses!
Internal placement of ultrasonic transducers?
Aspiration to analyser: membrane pumps & tubes?
Aspiration from the bottom best: hydrostatics of heavier FC
Care with volume calculation if jacket walls are flexible:
(Hydrostatic bowing with heavy FCs)
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
SensComp
(ex-Polaroid) 50 kHz
Ultrasonic transducer
https://senscomp.com

## Slide 19: Buffer volume changes: an issue to consider & mitigate…
Calculations & measurements made by Paul Flower (RAL-CLRC) in 1980s for wall deflections of the 122m3 OMEGA RICH gas radiator vessel (originally ran with N2)
for conversion to C2F6, using a new gas circulation system by Michel Bosteels
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 20: Example of Ultrasonic gas analysis in a process environment with multiple background gases
https://www.mdpi.com/2410-390X/5/1/6
Gas aspirated through
150m tubes from
silicon tracker
N2 environmental
volumes to
‘sonar’ devices
to look for C3F8
leak rates
(C3F8 in N2 )
Chart: CO2 concentration (ppm)
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 21
Refractive index & GWP ’load’ in a Cherenkov Gas Radiator
3 large RICH detectors currently in operation at CERN:
using saturated fluorocarbon gas volumes:
C4F10 (COMPASS: 100m3, LHCb RICH 1: 4m3): GWP20 = 4880,
CF4 (LHCb RICH 2: 100m3): GWP20 = 6870
A Cherenkov radiator vessel of volume V(m3) filled with
a blend of gases of densities ri (kgm-3),
fractional concentrations wi and individual GWPi (tonnes CO2 eq.)
has a GWP environmental “load” (& release potential) L given by:
) (tonnes CO2 eq.) [Eq. (1)]
The corresponding radiator gas mixture refractivity is given by :
) [Eq. (2)]
For just two gases we can blend small conc. wx of (heavier) SFC or Fluoro-Ketone
vapour of high refractivity (n-1)x with wy of light transparent gas, refractivity (n-1)y
to replicate refractivity (n-1)z of a lighter SFC at high conc. – for a lower GWP load.
wx = [Eq. (3)]
V,r
With j contaminant gases of known molar concentrations wj present we can still
add a small concentration wx of (heavier) SFC or Lin-FK vapour of high refractivity
(n-1)x with wy of light transparent gas to substitute the refractivity (n-1)z(target)
of a lighter SFC at high concentration – to achieve a lower overall GWP load.
+
[Eq. (2) Eq. (2b)]
wx = [Eq. (3)  Eq. (3b)]
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 22: Targeting the refractivity of CF4 & C4F10 (100 m3: examples) at 1 barabs with gases of differing molecular weight in varying fractional concentrations with N2 (conc. > 100% indicate need for overpressure): includes hypothetical fluoro-ketones
CF4
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
C4F10

## Slide 23
Chart: 
| 361.57150866452997 | 256.66370132773199 | 207.76041110631601 | 177.74100163378299 | 156.771959339836 | 140.96541864529999 | 128.432486611158 | 118.12923971441801 | 109.42497216462201 | 101.912772216321 | 95.316482075286103
e thresh | 0.20021 | 0.16566 | 0.14445 | 0.12974 | 0.11878 | 0.11019 | 0.10324 | 0.09746 | 0.092555 | 0.088324 | 0.084626
mu thresh | 4.2043 | 3.4788 | 3.0335 | 2.7246 | 2.4943 | 2.3141 | 2.1681 | 2.0467 | 1.9436 | 1.8548 | 1.7772
pi thresh | 5.4857 | 4.5391 | 3.9579 | 3.555 | 3.2545 | 3.0193 | 2.8288 | 2.6704 | 2.536 | 2.4201 | 2.3188
kthresh | 19.9006 | 16.4666 | 14.3584 | 12.8965 | 11.8065 | 10.9534 | 10.2622 | 9.6876 | 9.1999 | 8.7794 | 8.4119
pthresh | 37.4788 | 31.0115 | 27.0412 | 24.288 | 22.2351 | 20.6285 | 19.3269 | 18.2446 | 17.3262 | 16.5342 | 15.842
% C5F12 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
C5F12 or C5F10O concentration (%)
LHCb RICH 2 with C5F10O/N2
GWP load = (0.13 molar*1*V.r)
LHCb RICH 2: CF4 thresholds
GWP load = (0.95 molar*4880*V.r)
Cherenkov threshold: C5F10O/N2 & (heritage) C5F12/N2 blend and GWP load comparison for LHCb RICH2 (100m3 CF4)
C5F12 SFC/N2 and NOVEC5110 (C5F10O) /N2 will be very similar (MW 266 vs. 288)
~ 14% molar C5F10O
gives a GWP load reduction of 1737 tonnes:
Even substituting CF4 with ~ 13% molar heritage stock C5F12 reduces GWP load by ~800 tonnes
23
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 24
Chart: 
| 361.57150866452997 | 256.66370132773199 | 207.76041110631601 | 177.74100163378299 | 156.771959339836 | 140.96541864529999 | 128.432486611158 | 118.12923971441801 | 109.42497216462201 | 101.912772216321 | 95.316482075286103
e thresh | 0.20021 | 0.16566 | 0.14445 | 0.12974 | 0.11878 | 0.11019 | 0.10324 | 0.09746 | 0.092555 | 0.088324 | 0.084626
mu thresh | 4.2043 | 3.4788 | 3.0335 | 2.7246 | 2.4943 | 2.3141 | 2.1681 | 2.0467 | 1.9436 | 1.8548 | 1.7772
pi thresh | 5.4857 | 4.5391 | 3.9579 | 3.555 | 3.2545 | 3.0193 | 2.8288 | 2.6704 | 2.536 | 2.4201 | 2.3188
kthresh | 19.9006 | 16.4666 | 14.3584 | 12.8965 | 11.8065 | 10.9534 | 10.2622 | 9.6876 | 9.1999 | 8.7794 | 8.4119
pthresh | 37.4788 | 31.0115 | 27.0412 | 24.288 | 22.2351 | 20.6285 | 19.3269 | 18.2446 | 17.3262 | 16.5342 | 15.842
% C5F12 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
C5F10O concentration (%)
COMPASS (& LHCb RICH 1): C4F10 thresholds
COMPASS RICH GWP load = (6849 tonnes)
Cherenkov threshold in C5F10O/N2 mixtures and GWP load comparison with COMPASS RICH (100m3)
N2-NOVEC5110 (C5F10O) very similar to C5F12 (MW 266 vs. 288)
85% Novec 5110 gives a huge GWP load reduction of 6849 tonnes
24
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 25
    Legacy C4F10 replacing CF4 in the context of LHCb RICH-2
    Legacy C5F12 replacing C4F10 for COMPASS and LHCb RICH-1.
Sound velocity in C5F12 and C4F10 is based on extensive thermodynamic data:
corresponding required concentrations for C5F10O and C4F8O
will be slightly higher due to their lower densities.
Other (heritage/legacy) options (in N2)
C5F12
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 26
NA9 8m3 Cherenkov C5H12 (!!!) recirculation – the constraints of
flammable radiator gas usage – in a SURFACE building!!
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Can we now forget thinking
of using large flammable
gas radiators
in underground areas?

## Slide 27
The high pressure issue: considering a 100m3 radiator vessel with cheap
N2 or CO2 simulating the refractive index of CF4 & C4F10
(Source of pressure slopes: V. P. Zrelov book (1968))
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Chart: PV (MJoules) vs 100m3 Cherenkov radiator overpressure
| 1 | 2 | 3 | 4 | 5 | 6 | 7
PV (MJ) | 0 | 10.13 | 20.26 | 30.39 | 40.52 | 50.65 | 60.78
Chart: Overpressure stored energy for 100m3 radiator volume (MJ))
| 0 | 10.129999999999995 | 20.259999999999991 | 30.389999999999993 | 40.519999999999996 | 50.649999999999984 | 60.779999999999987
Nitrogen | 0.00029 | 0.00054 | 0.00079 | 0.00104 | 0.00129 | 0.00154 | 0.00179
CO2 | 0.00045 | 0.00085 | 0.00125 | 0.00165 | 0.00205 | 0.00245 | 0.00285
CF4 match
(n-1) = 488E-6
C4F10 match
(n-1) = 1450E-6
Cost/risk assessment for use of elevated pressures,
particularly for index-matching large C4F10 volumes
N2 matching C4F10
(n-1) = 1450E-6
CO2 matching C4F10
(n-1) = 1450E-6
N2 matching CH4
(n-1)=488E-6

## Slide 28
From 1st DRD4 Meeting: 17-20 June 2024
Real? Repeatable?
very crude device,
lacking details
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Antonello di Mauro has since started a study of C5F10O
as a Cherenkov radiator

## Slide 29
UV transparency, refractivity, cmhemical stability & compatibility studies needed
for different CnF2nO molecular shapes. RICH detector community very competent & equipped for detailed UVT & (n-1) - much ex-DELPHI RICH diagnostic equipment at CERN for example
Minuteman Model 302 VM.
Most probable PC spectral range
in new build gas RICH detectors
A
ALICE VHMPID: transparancy
measurements in c-C4F8O
Octafluorotetrahydrofuran
CAS: 773-14-8
Synquest Inc. FL, USA
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 30: CnF2nO fluid selection search criteria
Start(ed)
Non-toxic
(MSDS)
?
N
Y
Non-
Flammable
(MSDS)
?
N
Y
Non-
Oxone-
depleting
?
N
Y
Next CnF2nO fluid
(order & isomer)
to evaluate
Materials/
purifier
Compatible
?
N
Y
N
Y
Rad.
Tolerant
(more for
cooling)
?
N
Y
Dielectric
?
Acid
formation
with H2O
?
N
Y
N
Y
N
Recirc.
Thermo-
dynamics
OK
?
Y
Y
Y
UV-Vis
transparency
OK
?
(n-1) &
Chrom. Disp.
OK
?
N
N
Accept
fluid
Optotests
Materials tests
Bibliographic
Low GWP!
?
N
Y
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 31: Fulvio gave an excellent presentation on Tuesday, detailing the COMPASS RICH radiator and the issues of FC circulation, purification & monitoring, recovery & replacement with passivation gas. He also discussed a possible new CO2/C2F6 radiator
The roots of this system are in an earlier system that Michel Bosteels built for C2F6 circulation in the OMEGA RICH (Haug SOGX oil-free compressors)

## Slide 32
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
I have no report or nice photos of this system ,
just notebook entries by Paul Flower (RAL-CLRC) and Michel Bosteels.
System mostly scrapped in 1990’s:   :
compressors ended up at a carosserie for paint spraying:
M.B. MOST upset: typical CERN wastebin wastage policy
System built by Michel Bosteels for C2F6 circulation in the OMEGA RICH (Haug SOGX oil-free compressors): - mid 1980’s
Passivation
gas
C2F6
storage
Paul Flower
(RAL-CLRC)
by Michel Bosteels
Haug
compressors
C2F6
trapping
Haug
compressors
C2F6
storage
C2F6
trapping
Purifier
Purifier

## Slide 33
Also from Fulvio’s talk: A possible new CO2/C2F6 radiator…
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 34
C2F6 (mw=138)
CO2 (mw=44)
50%C2F6,50%CO2
25%C2F6, 75% CO2
75%C2F6, 25% CO2
Circulation can involve bi-component condensation/evaporation in closed system
(for reduced FC losses)
Pressure enthalpy plots by NIST RefProp DB23 (BWR EOS + Helmholtz corr.)
Fulvio has started a study of (quasi-azeotropic) C2F6, CO2
(Azeotropic behavior makes bi-component circulation easier)
Condensation
Evaporation
Radiator
vessel
Purification
Pure components: condensation & evaporation isotherms are isobaric
Azeotropic blends:
condensation & evaporation isotherms
aimed to be almost isobaric
But here Azeotropicity is reduced:
condensation & evaporation isotherms
less isobaric: thermal “glide” exhibited
P
P
P
P
P
h
h
h
h
h
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 35
Antonello di Mauro has started a study of (quasi-azeotropic) C5F10O, CO2
(These mixtures are likely to be zeotropic with noticeable thermal glide:
behavior makes bi-component circulation easier)
Note: C5F10O (mw: 266) P-h curves likely to be similar to C5F12 (mw: 288)
for which NIST-REFPROP can be used to calculate mixtures with CO2
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
C5F12
75%C5F12, 25% CO2
50%C5F12, 50% CO2
25%C5F12, 75% CO2
P
h
P
h
P
h
P
h
Zeotropicity and significant thermal “glide” exhibited over the blend range: “throwaway mode” for the
CO2 component may be best

## Slide 36: It is possible to circulate a zeotropic blend in a closed circuit, however…
25%C2F6 :75% C3F8 (ATLAS Si tracker cooling study)
https://iopscience.iop.org/article/10.1088/1748-0221/10/03/P03027/pdf
Paper also discusses procedure for massmolar
mixing of 2 liquids in refrigerated reservoir &
Ultrasonic analysis of circulating vapour mixture
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 37
https://iopscience.iop.org/article/10.1088/1748-0221/10/03/P03027/pdf
Procedure for mixing of 2 liquids in refrigerated reservoir &
Ultrasonic analysis of circulating vapour mixture
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 38
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Experience in distillation-separation of liquifable co-circulants @ CERN (DELPHI RICH)
Might be applicable to C2F2/CO2 or C5F10O/CO2 (or just mix with
N2 and let the N2 escape from -100 °C condenser tank (SLAC SLD) CRID

## Slide 39
Low temperature (-80°C)
N2 gas-induced condensation (B):
of C5F12 fromC5F12/N2 radiator gas (flow~1m3/hr, negligible C5F12 loss)
followed by (C) electric re-evaporation
(1-1.5m below condenser liq. level)
Cold N2 gas (‘conditioned’ by
counter-flow with boil-off LN2
from liquid argon calorimeter: (A))
Ultrasonic (speed of sound) – aided
“on-the fly” mixing of typical
17%N2 /83%C5F12 (molar) radiator gas mixture (D)
SLD Barrel CRID C5F12/N2 gas radiator: continuous thermodynamic recirculation
A
B
C
D
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 40
(A) C5F12 Condenser
(cooled with GN2)
LN2 conditioner
(Chills GN2 in counterflow with LN2
from liquid argon calorimeter source)
(B) C5F12 storage tank
and N2 separator
(C) C5F12 Evaporator
SLD Barrel CRID C5F12/N2 gas thermodynamic recirculator
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 41: SLD CRID C5F12 circulation
Electric evaporation of C5F12
(dh ~ 1.3m)
Condensation in tank (B) @ varying temperature 
down to “keep-cold” temp of -80°C (PC5F12 ~ mbar),
drastically reduces C5F12 loss by evaporation
(D) N2 addition (C5F12 p.p. reduction)
& flow through CRID Radiator vessel
Collapsing C5F12 partial pressure
& some condensation in precooler (A)
Pure C5F12@ -80C from
bottom of tank
(C) Electric heating
of liquid C5F12
SLD CRID C5F12 Thermodynamic circulation: Pressure-Enthalpy
1barabs condenser
Headspace (& CRID
radiator vessel)
pressure maintained
by N2 in return radiator gas & condenser N2
vent to atmosphere
rgh of 1.5m C5F12 !
Vapour
Liquid
Changing Phase
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 42: -
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Conclusion:
(Quoting W. Churchill & Peter Sharp)
Cherenkov-greeni-city
is a ‘House of Many Mansions’
(too many to include in this talk*:
so please see ongoing back-up material & links)
*But we need a thermodynamic circulation
working group…

## Slide 43: Back up stuff
“Green radiators”: Controlling refractive index & reducing Cherenkov gas radiator GWP: a challenge in an era of diminishing fluorocarbon availability
Related paper: https://link.springer.com/article/10.1140/epjp/s13360-023-04703-w
Also DRD4 meeting, May 2023 https://indico.cern.ch/event/1263731/contributions/5398511
ATLAS sustainability forum CERN, Jan 26 2024
https://indico.cern.ch/event/1371158/contributions/5773321/attachments/2788215/4861759/G_Hallewell_ATLAS_sustainability_forum_Jan_26_2024_v2.pptx
Sustainable HEP 2024 https://indico.global/event/4744/contributions/39611/
ICHEP2024 (July 2024): https://indico.cern.ch/event/1291157/contributions/5900402
DRD4 meeting Oct. 2024: https://indico.cern.ch/event/1456663/sessions/566400/#20241024
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 44: Back up stuff
(ALICE, BTeV) experiences
with C4F8O as a substitute for C4F10
Cherenkov radiator gas
44

## Slide 45
octafluorotetrahydrofuran
MW = 216: GWP=12000
a.k.a.
c-octafluoro-oxolane
C – F
C – F
l
F
F – C
F – C
l
F
F O F
45

## Slide 46: Shapes of CnF2nO molecules and GWP:
c-octafluorooxolane (C4F8O),
MW = 216: GWP = 12000 BTEV stuff?
3M Specialty Gas PFG-3480 is a high-performance chamber cleaning gas that has environmental advantages and can help reduce operating costs. PFG-3480 reduces emissions of global warming compounds by 90 percent when compared to the traditional plasma enhanced chemical vapor deposition(PECVD) cleaning gas, C2F6. The replacement does not require changes to existing processes
Perfluortetrahydrofuran – the probable BTeV choice
From June 2000 3M datasheet
https://repository.library.noaa.gov/
044ed5ad-93ae-40e3-9420-d78
a4729ff0f
46

## Slide 47: Shapes of CnF2nO molecules and GWP:
Octafluortetrahydrofuran – the probable ALICE VHPID config
C4F8O acquired from Synquest : reported by Antonello di Mauro:
C – F
C – F
l
F
F – C
F – C
l
F
F O F
47

## Slide 48: SynQuest Labs Inc., 13201 Rachael Boulevard Rt 2054, Alachua, FL 32615, USA
48
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 49: SynQuest Labs, Inc. Can manufacture different C4F8O configurations
The cyclic molecule seems to be cheaper for SynQuest to manufacture:
whereas 3M make NOVEC 649, which is non-cyclic
49
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 50
Historical: The SLD barrel CRID gas radiators (SLAC: 1990s)
87% C5F12/13%N2
gas radiator
Sonar transducer
6 transducer pairs
@ 3 different heights
(hydrostatics)
50
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 51
Maintaining C5F12/N2 refractive index
through sonar-based active mixture control
(In this paper submitted to IEEE TNS)
Flowmeter
analyzer in supply line
to tune the blend by
hardwired 4-20mA
links to mass flow controllers
51
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 52
Chart: C5F12-N2 40 ⁰C
| 361.57150866452997 | 256.66370132773199 | 207.76041110631601 | 177.74100163378299 | 156.771959339836 | 140.96541864529999 | 128.432486611158 | 118.12923971441801 | 109.42497216462201 | 101.912772216321 | 95.316482075286103
e thresh | 0.20021 | 0.16566 | 0.14445 | 0.12974 | 0.11878 | 0.11019 | 0.10324 | 0.09746 | 0.092555 | 0.088324 | 0.084626
mu thresh | 4.2043 | 3.4788 | 3.0335 | 2.7246 | 2.4943 | 2.3141 | 2.1681 | 2.0467 | 1.9436 | 1.8548 | 1.7772
pi thresh | 5.4857 | 4.5391 | 3.9579 | 3.555 | 3.2545 | 3.0193 | 2.8288 | 2.6704 | 2.536 | 2.4201 | 2.3188
kthresh | 19.9006 | 16.4666 | 14.3584 | 12.8965 | 11.8065 | 10.9534 | 10.2622 | 9.6876 | 9.1999 | 8.7794 | 8.4119
pthresh | 37.4788 | 31.0115 | 27.0412 | 24.288 | 22.2351 | 20.6285 | 19.3269 | 18.2446 | 17.3262 | 16.5342 | 15.842
% C5F12 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
SLD-CRID: Cherenkov threshold in C5F12/N2 mixtures vs. measured speed of sound in radiator gas mixture (1)
Typical mix 87%C5F12,13%N2
C5F12 concentration (%)
52
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 53
Chart: C5F12-N2 40 ⁰C: (N2-C5F10O should be very similar
| 361.57150866452997 | 256.66370132773199 | 207.76041110631601 | 177.74100163378299 | 156.771959339836 | 140.96541864529999 | 128.432486611158 | 118.12923971441801 | 109.42497216462201 | 101.912772216321 | 95.316482075286103
e thresh | 0.20021 | 0.16566 | 0.14445 | 0.12974 | 0.11878 | 0.11019 | 0.10324 | 0.09746 | 0.092555 | 0.088324 | 0.084626
mu thresh | 4.2043 | 3.4788 | 3.0335 | 2.7246 | 2.4943 | 2.3141 | 2.1681 | 2.0467 | 1.9436 | 1.8548 | 1.7772
pi thresh | 5.4857 | 4.5391 | 3.9579 | 3.555 | 3.2545 | 3.0193 | 2.8288 | 2.6704 | 2.536 | 2.4201 | 2.3188
kthresh | 19.9006 | 16.4666 | 14.3584 | 12.8965 | 11.8065 | 10.9534 | 10.2622 | 9.6876 | 9.1999 | 8.7794 | 8.4119
pthresh | 37.4788 | 31.0115 | 27.0412 | 24.288 | 22.2351 | 20.6285 | 19.3269 | 18.2446 | 17.3262 | 16.5342 | 15.842
Thresh/c | 0.99969 | 0.99954 | 0.9994 | 0.99926 | 0.99911 | 0.99897 | 0.99883 | 0.99868 | 0.99854 | 0.9984 | 0.99825
SLD-CRID: Cherenkov threshold in C5F12/N2 mixtures
vs. measured speed of sound in radiator gas mixture (2)
Cherenkov Threshold (GeV/c)
b = 1/n
Measured Sound Velocity (m/s)
So.. from (“acoustic”) c to b…
53
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024