## Slide 1: ARIADNE+ Results, Optical FLArE TPC Option & Cylindrical Cryostat Study
Kostas Mavrokoridis
k.mavrokoridis@liv.ac.uk
+
http://hep.ph.liv.ac.uk/ariadne
FPF Collaboration meeting Jan 20 2025

## Slide 2: Talk Outline
Background to the ARIADNE program
  TPX3Cam results taken with the ARIADNE 1-ton dual phase LAr detector
ARIADNE+: Larger scale demonstration using the CERN “Cold Box” at the Neutrino Platform
  Results and informing next generation designs
Conceptual FLArE TPC design based on TPXCam optical readout
Cylindrical Cryostat option for Optical TPC

## Slide 3: ARIADNE Detection Principle
ARIADNE has demonstrated light readout as a viable alternative to charge in dual-phase TPC neutrino experiments
Incoming particles ionise LAr and create prompt scintillation light (S1)
Electrons drift towards the extraction grid situated below the liquid level
A THGEM (THick-Gaseous Electron Multiplier) amplifies drift charge (capable of >30 kV/cm in LAr) generating secondary scintillation light (S2)
WLS (Wavelength Shifting) before imaging with ultrafast Timepix3 camera
ARIADNE (ARgon ImAging DetectioN chambEr)
Cameras
Benefits over previous charge readout techniques:
High resolution
Sensitivity to low energies
Very low noise, decoupled from TPC
Ease of access
Cost efficient
https://www.mdpi.com/2410-390X/4/4/35
https://iopscience.iop.org/article/10.1088/1748-0221/14/06/P06001
TPX3 provides simultaneous time-over-threshold (ToT) and time-of-arrival (ToA). Complete (x,y,z,E) event reconstruction using a single device.
Full 3D optical TPC

## Slide 4: 2D-> Full 3D Optical Readout
Silicon pixel readout chip developed by the Medipix collaboration. Very well established technology at CERN.
Sensor resolution | 256x256 pixels
Pixel size | 55µm x 55µm
Max readout rate | 40Mhits•cm-2 •sec-1
Time resolution | 1.6 ns
TPX3 provides simultaneous time-over-threshold (ToT) and time-of-arrival (ToA). Complete (x,y,z,E) event reconstruction using a single device.
Time over threshold provides intensity / energy measurement ->10-bit resolution.
Time of arrival provides z (drift) axis position information -> 1.6 nanosecond resolution.
Data driven readout -> Event streaming with native zero suppression.
Efficient raw data storage. Triggerless operation.
TPX3 ASIC bonded to optical sensor

## Slide 5: TPX3Cam Optical Readout
Single photon sensitivity when combined with image intensifier.
Intensifier gain ~1E6 photons/photon.
Relay lens couples intensified image onto light sensitive
sensor which is bump bonded onto TPX3 ASIC.
Timepix3 camera installed in place of an EMMCD camera.
~ 30cm x 30cm field of view
Photonis Cricket image intensifier with Hi-QE green photocathode.
30% quantum efficiency at 430nm (TPB peak emission)
ARIADNE results
Coldbox Intensifier
TPB emission
Intensifier provides flexibility -> Many photocathode options are available to customise spectral sensitivity.
– Now also Direct VUV!

## Slide 6: ARIADNE 1-ton LAr Tracks

## Slide 7: TPX3Cam 3D Cosmics LAr
Continuous streaming, 10 msec slice (playing 1ms jump per frame)
Top View
Side View

## Slide 8
Larger Scale Demonstration at the CERN Neutrino Platform
CERN LOI: https://cds.cern.ch/record/2739360
Test optical readout on a scale relevant for DUNE using the existing cold box
Operation March/April 2022

## Slide 9: ARIADNE+: Cryostat Optical Configuration
TPX3 Camera
Assembly (1 x VUV)
Light Readout Plane (LRP)
Cathode
TPX3 Camera
Assembly (3 x visible)
Large scale test of ARIADNE optical readout principle for dual-phase LArTPCs.
Four Timepix3 based cameras, each covering 1m x 1m readout area.
Three cameras detect visible light (wavelength shifter installed above THGEMs)
One camera directly detects VUV.

## Slide 10: ARIADNE+: Cryostat Optical Configuration
20 cm electron drift
Re-entrance viewports, cameras in gas nitrogen

## Slide 11: ARIADNE+: Key components
2mx2m LRP G-THGEMs from underneath
TPX3Cam
Photochemically etched extraction grids, 15mm extraction region
1.1mm 50cm2 glass THGEM
Visible lenses (f0.95, 10.5 mm
https://arxiv.org/pdf/2301.02530v2.pdf
Cosmics 30 sec integral

## Slide 12: Commissioning at CERN
3 weeks data collection

## Slide 13: Using ARIADNE optical readout system for FLArE TPC

## Slide 14: Optical FLArE Overview Design
56 TPX3 Cams in cryostat ports. This will provide 1.8mm/pixel resolution
Two invar LRPs with 56 glass THGEMs, similar to the ARIADNE cold box test
Two CPAs (same size as LRPs)
Aluminum profile Field Cage (similar to ProtoDUNE)
Total instrumented LAr volume 20000 litres/32 tons
CAD by G.Stavrakis
Assumes ProtoDune type field cage assembly approach

## Slide 15: Side view & Bias
0.5 kV/cm
Cathode: 95kV
For 1.8m e drift
Extraction grid: 5kV
185kV
5kV
THGEMs 25-30kV/cm
1 kV/cm
(current successfully operated HV 300kV)

## Slide 16: Resolution examples - EMCCD
4x4 (1.1mm/pix)
8x8 (2.2 mm/pix)
16x16 (4.4mm/pix)
0.5 m
Changing EMCCD binning
LAr Cosmic interactions collected @0.5kV/cm electron drift

## Slide 17: TOP view
Each camera is looking a 45x45cm glass THGEM (active area 1.8m x 6.4m, 56 cameras)

## Slide 18: TOP view
In red box 1mx1mx6.4m fiducial area and 28 cameras with ~2mm/pixel

## Slide 19: LRP Design
One LRP to contain 7x4 Glass THGEMS (similar to ARIADNE LRP)
Made out of Invar
Will hang from 4/6 top cryostat ports and will be able to move up down using levelling motors
3290mm
CAD by G.Stavrakis

## Slide 20: LRP Design
3.4 m
Size of LRP designed in order to fit within the CERN cold box to allow for QA before installation to FLArE

## Slide 21: FLArE Cylindrical Cryostat with Removable Lid for Optical Readout Option
CAD Models by George Stavrakis

## Slide 22
Double vac jacketed cryostat

## Slide 23
TPC hangs from cryostat ports
Double vac jacketed cryostat

## Slide 24
Double vac jacketed cryostat

## Slide 25
Double vac jacketed cryostat

## Slide 26
Weight at this configuration:
Flange 15t
Cylindrical vessel 30t

## Slide 27: Preliminary FEA Analysis

## Slide 28
FEA inputs:
Considering 15 mm thick
Stiffening rings
2 bar pressure (1b vac, 1b positive)
FEA inner cylinder with stiffening rings

## Slide 29
FEA: Deformation inner cylinder
8 mm deflection@2bar

## Slide 30
FEA: Hydrostatic inner cylinder
0.3 bar

## Slide 31
FEA: Stress inner cylinder

## Slide 32: Access to tunnel checks
Possible to take down at 60 degrees (before install lift and stairs in the shaft)
Lower cryostat without lid keeping the weight below 25t (currently is 30t for 15mm thick skin )

## Slide 33: Access to tunnel checks
Possible to take down at 60 degrees (before install lift and stairs in the saft)
Clearance around 90 cm from each side
Shaft top view

## Slide 34: cylindrical cryostat removable lid
Many thanks to Julien Prosic for providing the cad models of the cavern

## Slide 35: cylindrical cryostat removable lid
Entire TPC assembly hangs from the top lid

## Slide 36: cylindrical cryostat removable lid

## Slide 37: cylindrical cryostat removable lid

## Slide 38: cylindrical cryostat removable lid
Cavern top view

## Slide 39: Installation procedure
Use Hydraulics, since crane has no clearance
CAD by H. Frandini
https://hyquip.co.uk/tdm-double-acting-telescopic-cylinders-/4726-double-acting-telescopic-cylinders-type-tdm-series.html

## Slide 40: cylindrical cryostat removable lid

## Slide 41: cylindrical cryostat removable lid

## Slide 42: Summary & Remarks
Study is preliminary needs more design optimizations for the cryostat and TPC
Needs further discussion with Wessington Cryogenics to understand better the cost and feasibility
Commercial construction, with know how
Cost to be determined (likely cheaper than membrane cryostat)
Avoids liquid seals
Very good vac insulation, avoids foam
Flexible, easy TPC access
Will need hydraulics to lift the lid
Cryostat
3D Optical TPC
Optical readout achieved with stable detector conditions has been demonstrated at the larger scale (CERN Neutrino Platform Cold Box). Proposal also for implementation at ProtoDUNE NP02 cryostat.
Dual phase extraction region (new design) very stable at large scale!
Can provide the required mm resolution
Cost efficient
TPX3 and Glass THGEM technology is ready for deployment now

## Slide 43: Extra Slides

## Slide 44: TPX3 -> TPX4

## Slide 45: TPX3 QUAD
You could have 4 tpx3 ASICs together creating a 512x512 pixels sensor.
Has been done, but not bonded to an optical Si sensor. Will need some R&D
https://inspirehep.net/files/0d645abf22e9e30063b70a74b69b0b6e

## Slide 46: LRP Installation Rectangular Cryostat
For a ~3mx2.5m membrane type cryostat we will need to reduce the LRP size to 2mx2.3m in order to fit from the side.
Side entrance is welded similar to protoDUNE
CAD by H. Frandini

## Slide 47: LRP Installation Rectangular Cryostat
CAD by H. Frandini

## Slide 48: Conceptual FLArE TPC dimensions

## Slide 49: Simulated TPC & requirements

## Slide 50: Novel G-THGEM Production
FR4 THGEM with Copper electrodes and holes formed by mechanical drilling.
G-THGEM with ITO electrodes and holes formed by abrasive machining.
Borofloat 33 substrate G-THGEM
Abrasive machining vs drilled holes with chemically etched rims.
G-THGEM: https://www.mdpi.com/2076-3417/11/20/9450

## Slide 51: G-THGEM Characterisation
THGEM charging behaviour
THGEM bias scan
Bi-conical holes lead to “upwards” charging over time.
Straight wall holes lead to “downwards” charging over time
The charging behaviour of fused silica THGEMs results in greater light production for the same applied field.
All circle hole glass THGEMs produced more light than the equivalent FR4 THGEM.
https://www.mdpi.com/2076-3417/11/20/9450

## Slide 52: 50cm Glass THGEMs
Sixteen 50cm x 50cm glass THGEMs
1.1mm thick,
500μm ID holes,
800μm pitch hexagonal array
Novel Glass THGEMs developed at Liverpool (Patent accepted GB2019563.2)
See for more details:
https://www.mdpi.com/2076-3417/11/20/9450

## Slide 53
THGEM S2 light production
VUV (126nm) light produced through de-excitation of Argon gas. TPB Wavelength shifter above THGEM converts to 430nm.
At low field (<2kV/cm), S2 light production is linearly proportional to THGEM field. No charge gain. Very stable operation without discharges. No ion production.
At higher fields, electron multiplication occurs (Townsend avalanche).
Exponentially increasing S2 light production -> Improved sensitivity/threshold
Simulation

## Slide 54: PEN WLS
Two grades of TEONEX PEN foil investigated Q51 and Q53.
Thinner PEN consistently found to have a better conversion efficiency than thicker sheets (surface interaction).
Q51 consistently found to have a better conversion efficiency than Q53.
50cmx50cm Q51 25μm PEN film glued on glass panel