## Slide 1: “Science DMZ” security
Tim Chown, Duncan Rand (Jisc)
GridPP 53, Manchester, 11 April 2025

## Slide 2: Science DMZ
The Science DMZ model was documented by ESnet in 2013
  https://www.es.net/assets/pubs_presos/sc13sciDMZ-final.pdf
  Appropriate “friction free” (zero loss) local network architecture
  Appropriate software tools – e.g., Globus not FTP
  Dedicated data transfer node(s) (DTNs) and (TCP) tuning
  Efficient application of security policy (NOT a “firewall bypass”)
  Persistent monitoring of network characteristics
GridPP sites have evolved similar practices over time, just not written it up or come up with a cool name
  But we could write up a short guide… hence this talk to solicit input…

## Slide 3: GridPP network architectures
Historically GridPP sites have used different Janet links for science traffic to campus “business” traffic
  University has 4x10G: 2x10G for GridPP, 10G campus and 10G backup
  GridPP traffic is then filtered by stateful ACLs rather than big, stateful campus firewalls (which then don’t need to be so big and costly)
But what are the newly 100G-connected sites doing?
  Might use a “backup” link for GridPP? Or carve out 40G of their resilient 100G?
LHCONE provides a “trust fabric” over which WLCG traffic is carried between T0/T1/T2 sites
  Specific prefixes used, may be routed differently, then split out at campus edge
  But only 2 UK sites are on LHCONE (RAL and Imperial)

## Slide 4: GridPP – other Science DMZ elements
Software tools
  Rucio, FTS, XRootD, dCache,… GridPP seems happy with these
Tuned DTNs
  Interface to back-end CEPH/other
  But is there network tuning applied – if so, what? Might it be improved?
Efficient application of security policy
  Stateless ACLs and host firewalls minimise exposed services/ports
  Would use of LHCONE give greater assurance of peer trust?
Persistent network monitoring
  perfSONAR in use (as recommended by Science DMZ)
  Other tooling emerging, e.g., Scitags

## Slide 5: Some considerations / discussion points
How is GridPP doing “Science DMZ” today?
  What is technical state-of-the-art? Any BCP examples to share?
What general security practice advice should we share to ensure appropriate controls and mitigations are still followed?
Are newer, high-performance, high-throughput firewalls changing the rationale for Science DMZ?
  Or is the price point still too high for most sites?
How do we take care to avoid ‘accidental’ exposure
  Services/data appearing in a Science DMZ that shouldn’t?
Is the GridPP compute/storage/network model changing with HL?

## Slide 6: And more things to think about…
LHCONE seems useful for “static-to-static” (T0/1/2) transfers, but what about other (T3, non-LHCONE) access to GridPP resources?
  In other disciplines, data may be downloaded for local compute
Sites presumably run periodic security posture checks
  How are GridPP resources included – if so, is bespoke knowledge used?
What about zero trust architectures? (e.g., as per [1] and [2])
  Becoming popular elsewhere – should they be explored for GridPP?
Should we require common policies across GridPP sites?
  Recent example: filtering practices for ICMP and UDP (they vary!)

## Slide 7: Discuss!
tim.chown@jisc.ac.uk
duncan.rand@jisc.ac.uk