## Slide 1: Storage Technology Outlook
Ed Childers
April 2025

## Slide 2: ~30 years of HDD technology scaling with Data Demand has ended
Insert your favorite data growth chart here

## Slide 3
What Are The Options?
Pour concrete, spend more $ on HDD
Delete Data
Hope for a storage technology breakthrough
Play the cards in your hand

## Slide 4
What Are The Options?
Pour concrete, spend more $ on HDD
Delete Data
Hope for a storage technology breakthrough
Play the cards in your hand

## Slide 5
The Bits Have No Intrinsic Value
Data is a:
Currency
representing underlying
Assets
(currencies can suffer from inflation)
2x Data ≠ 2x Asset Value

## Slide 6
What Are The Options?
Pour concrete, spend more $ on HDD
  An answer IF budgets growing with data growth
Delete Data
Hope for a storage technology breakthrough
Play the cards in your hand

## Slide 7
What Are The Options?
Pour concrete, spend more $ on HDD
  An answer IF budgets growing with data growth
Delete Data
Hope for a storage technology breakthrough
Play the cards in your hand

## Slide 8
The Bits Have No Intrinsic Value
Data can be distilled only to:
Enlighten
or
Entertain
(are they the same thing?)
2x Data ≠ 2x Enlightenment

## Slide 9
Representing an Asset
or Distilled to Enlightenment
Data Enables a
Competitive
Advantage
(how much is that worth?)
More Data = More Competitive
(it’s just not a linear relationship)

## Slide 10
What Are The Options?
Pour concrete, spend more $ on HDD
  An answer IF budgets growing with data growth
Delete Data
  Maybe, You go first.
Hope for a storage technology breakthrough
Play the cards in your hand

## Slide 11
What Are The Options?
Pour concrete, spend more $ on HDD
  An answer IF budgets growing with data growth
Delete Data
  Maybe, You go first.
Hope for a storage technology breakthrough
Play the cards in your hand

## Slide 12: How Do You Store A Bit?
Whether in Hand, Traditional IT, or Cloud,
Data lives on:
Flash
HDD
Tape
Optical
Bits
Physical Things Obey The Laws Of Physics

## Slide 13
How do you store a bit?
Magnetize something
Tape & HDD
Change optical reflection
ODA, BluRay, DVD
Phase change
Capture charge
Flash
Align electron spin
Via external magnetic field
Via electric current
“spintronics”
MRAM (non-volatile memory)
Change structure of matter
DNA – base pair molecules
Phase Change Memory
Holographic, magneto optical, ablative,
5D crystal
PCM (non-volatile memory)
High density chemical storage
to create optical change
to create base pair molecule
to create resistive change
Change other characteristic
Atom scale manipulation
by arrangement of atoms
High density atomic storage
In semiconductor structures
MLC & 3D structures
Capacity/active
Low cost, archive
Cold/Deep archive

## Slide 14
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
Storage Technology Improvement Recipe

## Slide 15
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
Storage Technology Improvement Recipe
HDD

## Slide 16: Noise and Magnetic Media Structure
~10 nm
To Increase Density You Have To Make Smaller Magnetizable Things
Information is encoded in transition edge. Large grains  media noise
~10 nm
Courtesy Mark Lantz, IBM Zurich

## Slide 17: HDD - The Superparamagnetic “Limit”
~10 nm
Magnetic Media “Trilemma”:
Small particles (V)
Thermal Stability
Writability
HDD has reached the limit of(current) materials to produce larger write fields.
Technologies to go beyond the superparamagnetic limit:
Heat Assisted Magnetic Recording (HAMR)
Microwave Assisted Magnetic Recording (MAMR)
Bit Patterned Media (BPM)
All technologies increase cost of the brick
If grains become too small, magnetic state is unstable  = superparamagnetic effect
~10 nm
Too Small of Magnetizable Things And They Don’t Stay Magnetized At Room Temperature
Courtesy Mark Lantz, IBM Zurich

## Slide 18
Storage Technology Improvement Recipe
HDD Technology
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
  Net
  Increased cost of mfg
  No new “S-curve” – just a roadblock in existing path
  HAMR coming…….

## Slide 19
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
Storage Technology Improvement Recipe
Optical Disc

## Slide 20: Optical Disc Storage Basics
Better areal density / higher capacity achieved by heating smaller spot on disc
Spots are put on embossed tracks in disc
1
Write with heat
Read with reflection
2
The “spot” is fuzzy
3
By FDominec - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=3017519
Size of spot =
Wavelength of light
Numerical Aperture
(a measure lens capability)
“Hottest” & “brightest” in center
Write here
Guard bands
A measure of how well the lens can focus the laser.
Limited by mfg – can’t get better!
Optical roadmap has traditionally made gains by decreasing wavelength of laser.
CD  DVD  BluRay
Red    Blue
Can’t get to next step = UV “light”

## Slide 21
Storage Technology Improvement Recipe
Traditional Optical Disc Technology
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
  Net – Traditional Optical Disc
  Can’t scale smaller
  Can’t scale deeper
  The light has gone out on traditional optics
  Interesting Alternatives Modifying the Recipe
  Don't push areal density, push on area (more layers) and cost = Folio
    Femtosecond lasers = Silica, Cerabyte
Spot size limited by wavelength of light
Red-DVD, Blue-BluRay – UV not commercially feasible
Track pitch limited by embossment patterns
Multi-layer limited by limitations of laser power or degradation of adjacent data

## Slide 22
Storage Technology Improvement Recipe - Modified
Folio – $/TB via low-cost multilayer media
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
  Net
  Potential for permanent Write Once archive
  Potential Challenges
    Scale up of media manufacturing ?
Unknown – whitepaper lists 360MB/sec at system level parallel
Make more “buckets” at a lower cost - not smaller “buckets”
Multilayer extruded optical media
Smaller not necessary as not pushing areal density (ie. smaller buckets)
Use of “blue” light eliminates need for new optics, lasers

## Slide 23
Storage Technology Improvement Recipe - Modified
Cerabyte – Immutable, “forever” Write Once
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
  Net
  Potential for permanent Write Once archive
  Potential Challenges
    Future scaling of density / going to shorter wavelengths
    Scale up of media manufacturing ?
    Femtosecond laser ecosystem ?
Unknown
Write - Single Femtosecond laser images ~1M domains via DMD
Read – imaging of blocks should be capable of reasonable datarates
Make permanent “buckets” at a competitive $/TB, not smaller
Ceramic coated glass ablation by a femtosecond laser
Imaging of domains within capabilities of existing optics/CCDs
Femtosecond lasers required for ablation of domains

## Slide 24
Storage Technology Improvement Recipe – Modified
5D Optical / Silica Technology
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
Unknown
Write - Demo was slow, Superman Movie demo estimated to take ~110 days to write @ 8kB/sec
Read - ? Imaging of domains should be faster than write
Imaging of domains within capabilities of existing optics
Femtosecond lasers required for ablation of domains
Make permanent “buckets” at a competitive $/TB, not smaller
3D recording in glass + 2 more Ds via nanograting polarity
  Net
  Potential for permanent Write Once archive
  Potential Challenges
    Datarate?
    Future scaling of density / going to shorter wavelengths
    Scale up of media manufacturing ?
    Femtosecond laser ecosystem ?

## Slide 25
Storage Technology Improvement Recipe
DNA Technology
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
Currently Slow
Demonstrated capability to R/W
Very, very, very small
“Open source” data encoding – kind of…
  Net
  Potential for permanent Write Once deep archive
  Incredible densities possible - EB/in^3
  Extreme long life + low power
  Challenges
    Reading (aka sequencing) destroys the copy
    Slow Read/Writer speed

## Slide 26
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
Storage Technology Improvement Recipe
Tape

## Slide 27
Make smaller buckets to store bits
Smaller Magnetic Particles
Packed Tighter and Better Arranged
MP particles are sintered and coated & magnetized linearly in media
BaFe particles are crystalline and grown & magnetized orthogonally in media
Substrate
Mag Layer
Non-Mag Under Layer
Backcoat
Tape Construction
Dual Coat
Fe2O3
CrO2
MP – MP+++
BaFe
SSputtered
SSrFe
epsilon FeO2
Perp Orient.
Cartridge
Reel-Reel
Tape Improvement Recipe

## Slide 28
Make a more sensitive thing to R/W the smaller bits
Better Readers - AMR GMR TMR
Improved Writers – Trimmed, High Moment
Reduced Spacing = Smoother media & improved tribology
Without messing up friction & wear
Better
Media
Media
Head
Head
8 Chnl / 2 bump
Wire Wound
AMR
GMR
TMR
S64 Chnl
16 Chnl / 2 bump
32 Chnl / 3 bump
Trimmed Wrt
High Moment
SSmaller
SPMR
Tape Improvement Recipe

## Slide 29: MR Sensor (aka Head) Technology
201 Gbit/in2
sputtered tape
123 Gbit/in2
BaFe tape
GMR
GMR
TMR
TMR
AMR
16 track
8 track
32 track
LTO8

## Slide 30
Make a better thing to get the sensor onto the bits
Improved Servo Patterns
Improved Track Following Servo
Improved Skew Servo
Improved Tape Tension Servo
Amp Based Servo
Fixed Head
Track Following
Coarse/Fine
Skew Servo
Timing Based Servo
H Infinity comp
3570
Improved
Timing Based Servo
Tension Servo
SBetter
SEfficent
Tape Improvement Recipe

## Slide 31
Make a more efficient means of putting data onto tape
Improved ECC
Improved data format
More efficient servo
PRML 16/17 mod
Improved Rewrite Eff.
3570
Iterative C1
PRML 32/33 mod
Improved ECC
Tape Improvement Recipe

## Slide 32
Storage Technology Improvement Recipe
Tape Technology
Make smaller buckets in which to store bits
Make a smaller, more sensitive thing to R/W the smaller bits
Make a better, faster, more accurate thing to get the sensor located on the bits
Make a more efficient means of encoding data into the bits
  Net
  No looming fundamentals of physics limitations
  Technology roadmap supported by research demonstrations well into the 2030’s
  Rate of technology advancement outpacing HDD today
LTO 10 Coming!
Mark Lantz – IBM Zurich Research

## Slide 33: Tape Areal Density Scaling
So why doesn’t tape have the same problems as HDD?
Better areal density / higher capacity achieved by shrinking the same basic technology to write smaller and smaller bits on disk
Smaller magnetic pieces to make smaller bits
Smaller write heads to magnetize smaller pieces
Better “MR” sensors to read smaller bits
1
Write with electro-magnet
Read with “MR” sensor
(“magneto-restrictive” sensor changes resistance in a magnetic field)
The smaller the magnetic piece, the less stable. When a bit gets so small it’s unstable @ room temperature = “superparamagnetic limit”
2
3
Much, much bigger magnetic pieces
& much, much larger surface to store data

## Slide 34: Storage Technologies Domain Sizes
Tape Technology Is Unique Among Storage Technologies As It Is Not Facing Fundamental Scaling Limitations
Mark Lantz – IBM Research Zurich
Scaled bit cells:
LTO8 Tape ~8.6 Gb/in2
1560 nm x 48.4 nm
NAND Flash (3 bits) 2150 Gb/in2
17.3 nm x 17.3 nm
HDD 1000 Gb/in2
47 nm x 13 nm
Sputtered Demo 201 Gb/in2
103 nm x 31 nm
BaFe Demo 123 Gb/in2
140 nm x 37 nm
Jag5A Tape ~9.6 Gb/in2
1347 nm x 50 nm

## Slide 35: Tape vs HDD Surface Area
TAPE
Disk
Tape Makes Up For Larger Domain Sizes With Much Larger Surface Area
~12 sq m
8 platters ~0.09 sq m

## Slide 36
What Are The Options?
Pour concrete, spend more $ on HDD
  An answer IF budgets growing with data growth
Delete Data
  Maybe, You go first.
Hope for a storage technology breakthrough
  Nothing new coming in big in near term
  Tape has strong technology pipeline
Play the cards in your hand

## Slide 37
What Are The Options?
Pour concrete, spend more $ on HDD
  An answer IF budgets growing with data growth
Delete Data
  Maybe, You go first.
Hope for a storage technology breakthrough
  Nothing new coming in big in near term
  Tape has a strong technology pipeline
Play the cards in your hand
  Increased Tape Use – Cost, Sustainability, Security
  New Tape models – scale out vs scale up (aka The Cube)
TAPE
FL
HD

## Slide 38
Storage Technology Outlook Take Aways
HDD is not keeping up with data growth.
  HAMR, MAMR, EAMR, etc. will not change the trend.
There is not a new technology coming to save the day tomorrow.
  There are some interesting femtosecond and low-cost optical possibilities, but you will see them coming with enough lead time to plan.
Tape Technology Outlook is Strong
  No looming fundamentals of physics limitations
  Technology roadmap supported by research demonstrations well into the 2030’s
  Rate of technology advancement outpacing HDD today

## Slide 39
And now, a word from our sponsor..

## Slide 40: Data Center Pain
Fibre Channel is the traditional connection
  Disk/SAN and Tape connectivity
  Switches with complex Zoning
Most Fibre has phased out for SAN in favor of Ethernet
Expense continues to grow
  64G switches $30-90K - plus HBAs, cabling, maintenance, expertise, etc
Tape underutilizes Fibre bandwidth per drive
Spectra customers openly vocal about wanting an alternative to Fibre Channel
SAS is also available for Tape Drive connectivity
  SAS is the highest volume tape drive ~70% of the market
  LTO-9 introduced FH-SAS , same with LTO-10 and beyond
SAS is cheaper by ~$1000 per Tape drive and direct connect so no switch needed or hassle
But… SAS is 3-4 meter max so the server has to be on top or RIGHT next to the library.
Until….

## Slide 41: OSW-2448 Specifications SAS Switch
Item | OSW-2448
SAS Host distance | 100m (AOC)
SAS ports | 12 (mini HD) 24G, 12G, 6G
SAS lanes | 48 (4 per port)
SAS Configurations | 12, 24, 36, or 48 lanes
FC ports | 0
Ethernet mgmt ports | 1 (1Gb)
Height | 1U (1.735”)
Width | 19in Rack (17.31”)
Length | Half depth (12”)
Weight | 12.9 lbs (unboxed)
Power (input) | 100-240 VAC
Power Supply | Dual Redundant 220W
Mount/Airflow | Front or Back of Rack
Throughput | OSW-2448
Max (system) | 108GB/s
Max SAS (per lane) | 2.25GB/s
Max Tape Drives (devices per system) Dual 24 | 40 connectivity
Max Tape Drive Bandwidth (full throughput per port at 24Gb) | 40 @ bandwidth
Max Tape Drive Bandwidth (full throughput per port at 12Gb) | 36 @ bandwidth
Tape Drives Supported | LTO-6 and newer, IBM TS1160 & TS1170
Tape Libraries Supported | Spectra Stack, Spectra Cube™, Spectra T950 and TFinity® Plus
Datasheet: PowerPoint Presentation

## Slide 42: LumOS Library Management Software – Next Generation
LumOS is a new platform for Spectra Enterprise tape libraries
Released 1/11/2024 for Spectra TFinity
New Spectra TFinity, T950, and Cube tape libraries ship with LumOS installed
Available to install for Spectra T950 upgrades Now!
Currently running in over 50 Enterprise TFinity libraries in production environments
New Linux based UI with extensive roadmap of new features coming out quarterly