## Slide 1
SUSTAINABILITY AT SCALE
MOST EFFICIENT
 | SSD1 | Hard drive2 | Tape3
Embodied carbon4 (CO2/TB/yr) | 32kg | <0.2kg | <0.6 kg
Online Power5 (Watt/TB) | 0.56 | <0.31 | 1.1
Offline Use-Case7 CO2e Emissions (Archive) | 33x | 1x | 2-5x
1. Swamit Tannu and Prashant J Nair, “The Dirty Secret of SSDs: Embodied Carbon,” ACM SIGENERGY Energy Informatics Review, September 2023. 2. Embodied carbon prediction for Seagate Exos Mozaic 3+ hard drives per TB for five-year life cycle.
3. “Breakdown of the CO2e and Other Positive Sustainability Impacts of IBM Physical Tape Products “ IBM LTO FH drive with 1 media. January, 2022. 4. Using total embodied carbon per TB with a 5-year lifecycle.
5. Assumes hyperscaler use case with 24x7 operation and no idle time.
6. 30.7TB NVMe SSD. 7. Seagate analysis of power consumption and carbon emissions for different archive workloads. Comparing LTO9 Tape with Hard drives and SSD
Hard drives help address data center sustainability challenges.
Notes: Data centers are responsible for a significant portion of the worlds power consumption.
Sustainability initiatives have ever-increasing importance for data center operators, as they race to achieve carbon neutrality.
As AI programs scale, the power-hungry computing capabilities required to drive them, challenge this paradigm.
When we consider both power consumption and embodied carbon, hard drives are unmistakably the most carbon-efficient storage media on the planet, and can help contribute to sustainability goals.
Embodied carbon has been recalculated to a 5-year product life cycle using CO2e data from specified sources.
Online power specified as watt per terabyte has been calculated using the specified SSD and hard drive. For tape, the capacity of LTO9 and one media was used.
The offline use-case is comparing carbon emissions for an archive task. After the write operation is completed, all hard drives, SSDs, and tape are powered off. It is factoring in the embodied carbon of products and operational power emissions to write all archival data in an acceptable period, especially for tape as write speed is limited by the numbers of LTO9 drives in use. Hard drive and SSDs perform concurrent write operations and calculating a factor how SSD and LTO9 tape compares to Mozaic 3+ 30TB hard drives.

## Slide 2: Online Seamless HDD Self-Healing Discussion
April 2025
Curtis E. Stevens
Strategist
Keeping your HDD online longer.

## Slide 3: Discussion
Online Drive Regeneration
01
Solutions available today
02
Solutions for the future
03
The purpose of this presentation is to start a discussion on how to preserve the data on a CMR device when a head fails

## Slide 4: The case for self-healing storage
Data center increase data durability and availability
The average datacenter has 5%+ drives in a failed state
Slots may go for weeks or months before replacement storage is added
Each drive has a replacement cost beyond the cost of the storage
Sustainability – disposal of failed drive also has a cost
Slot uptime may increase by removing a failed head from service
Operating systems are still catching up
Offline methods are already available, but they destroy all the existing data triggering a rebuild operation
Some datacenters are not reasonably accessible
self-healing storage increases the useful life of datacenter infrastructure
Objective: Keep the good data valid, eliminating both the data regeneration and drive replacement steps.

## Slide 5: Self-Healing Hard Disk Drives
Head failure is one of the major reasons a drive is replaced
In a 10-platter drive, a head failure affects only 5% of the available storage
Most systems maintain a margin of free space at >5%
Standardization has already occurred
Taking a head offline is called Storage Element Depopulation
Operating systems are still catching up
Offline methods are already available, but they destroy all the existing data triggering a rebuild operation
Online methods are under development
There is now a standardized method for Host Managed Shingled Magnetic Recording (SMR) devices
A method needs to be developed to support Conventional Magnetic Recording (CMR) devices
1.
2.
3.

## Slide 6: Fully standardized: Marking Zones Offline
For systems with Host Managed Shingled Magnetic Recording (SMR) only
If a head is about to fail, the initiator (Host) is notified by the target (Hard Drive)
The initiator may then backup the contents of the target
Once the backup operation is complete the initiator marks all the zones associated with the defective head as OFFLINE
Generally, 95% of the data remains valid and accessible
The 5% that has been lost is determined by the initiator using a REPORT ZONES EXT command
If a head fails, the initiator is notified by the target
The initiator may remove the offending head
Once the head removal is complete, REPORT ZONES EXT is used to determine which data was lost
This method takes a short amount of time to perform, but only works for SMR devices

## Slide 7
c
Organize the drive using report zones but have CMR instead of SMR media
We value your input on recommendations.
  Requires the drive to be organized in same sized zones (typically 256MB)
  REPORT ZONES EXT indicates the zones that go offline
  This organization affects drive wear and performance
  However, it is very clear which zones go offline when a head is removed
  Structures to do this are already in standards, but need some modification to include CMR
CMR – Head Removal Strategies
Return a list of affected LBA ranges (available today)
  The drive is organized the way it is today with variable sized zones
  Allow the host to request a list of LBA ranges that have gone offline
  The host may then avoid those LBAs and regenerate their data elsewhere
  This method potentially produces 100k+ ranges to be mapped out by the host
Do it all in the drive, transparent to the host
  No host side changes – data is reorganized prior to head failure (most of the time) no data is lost
  Requires the trim command be used – commonly used on SSDs, but not on HDDs today
  Requires 5%-10% free space on the drive
  Uses a capability similar to thin provisioning (Fault Tolerance Provisioning)
  Requires this capability to be ported from SAS to SATA in standards
  Drive performance metrics become more random over time
STRATEGY 1
STRATEGY 2
STRATEGY 3

## Slide 8: Organize the drive using report zones
Reporting zone structure would need to be enabled for standard CMR HDD’s
Need to agree on a standard zone size, for SMR it’s 256MB
Drive would still report head health as it does today
When a head becomes unhealthy, the zone report indicates the media that would go offline line when the head fails
Based on this information, the host moves the affected data elsewhere
The host then stops using those sectors.
Benefits
Challenges
Solution
All zones need to be the same size
Smaller zone sizes allow the HDD to wear-level its data better, allowing for more consistent performance
The granularity of this data is a bit large
There will be collateral damage from zones that span heads
Works better for RAID type arrangements, especially if your stripe size is a multiple of the zone size...
Average LBA loss is approx. 7% (due to collateral damage)

## Slide 9: Return a list of affected LBA ranges
There is already a standardized method to return a list of affected LBAs when a head fails. In SATA this is LBA Status log.
When the drive reports a head is unhealthy, the host looks to the LBA Status log to find a list of the affected LBAs. The host may then relocate the good data.
Consider using new command WRITE GATHERED EXT to move data without using the datacenter infrastructure
  This command takes a list of LBA ranges and copies the data to a new location
  Normal read and write commands may also be used, but these will use the datacenter infrastructure to move the data
The host may then avoid using the LBAs that are about to fail
Benefits
Challenges
The average LBA loss using this method is 5% and collateral damage is minimized
Works better for filesystems with a cluster size under 1MB
Can result in millions of entries, potentially challenging host-management capabilities.
Solution

## Slide 10: Do it all in the drive
Based on the thin provisioning concept – Currently coined Optimized Provisioning
When a head becomes unhealthy or fails
The drive automatically redirects LBA accesses targeted at the failing head to a good head
The host is informed that a head is unhealthy, but no action needs to be taken by the host
Operation continues normally
Requires the drive to have available free space
The host issues trim commands to inform the drive which LBAs are unused
Optimized provisioning reports when the free media (media the LBAs point to) has dropped to a critical level
Benefits
Challenges
The Optimized provisioning system is disabled when an offline depopulation is performed
All the data is lost
The drive becomes smaller
The data becomes spaghetti over time – Causes unpredictable performance degradation over time
Increases firmware complexity in the drive - includes a need for internal garbage collection
Requires a firmware-controlled translation layer that does not exist today
Requires Optimized provisioning to be brought into standards
Solution

## Slide 11: Connect with Curtis Stevens for questions and to share ideas... Curtis.Stevens@Seagate.com
Thank you