Six Bend Achromat for FCC_ee injector Damping Ring
Antonio De Santis

---
Ring layout
Exagonal shape: 6 Arcs + 6 Straight
Arcs based on Six Bend Achromat (6BA)
Straight sections used for specialized purpose: Injection or extraction, wigglers, RF cavity
Playing with optical functions possible to have super-periodicity of three (as for the triangle shaped DR)
Injection
Wiggler
RF
Wiggler
Wiggler
Extraction

---
Six Bend Achromat

---
Six Bend Achromat cell (6BA)
Ncell = 24
Lcell = 11.76 m
Ndipole = 6
Ldipole = 0.7 m
Nqua = 15
Lqua = 0.26 m
Nsxp = 6
Lsxp = 0.10 m
Cell is symmetrical w.r.t. the center
Kq1 = 2.676 m-2
Kq2 = 1.398 m-2
Kq3 = -4.007 m-2
Kq4 = 4.722 m-2
Kq5 = -3.431 m-2
Kq6 = 4.199 m-2
Kq7 = -1.754 m-2
Kq8 = -2.011 m-2

---
Six Bend Achromat cell (6BA)
Beam envelope (98%)
\epsilon_{inj}(h/v) = 2.38 \mbox{ mm mrad}

---
Straight sections elements

---
FODO Cell
FODO Cell
LCell: 4.52 m
Ldrift = 2.0 m
LQUA: 0.26 m
KF: 2.505m-2
KD: -2.505 m-2
90 degree phase advance
½ QF_FD
½ QF_FD
QD_FD

---
FODO Wiggler
FODO Cell
KF: 2.505m-2
KD: -2.502 m-2
WGL parameters:
Lw(cell): 5 cm
Bw: 1.5 T

---
6BA-FODO Matching cell
Four independent QUA
Lqua = 0.26 m
ms_kq1 = 0.662
ms_kq2 = -2.833
ms_kq3 = -1.307
ms_kq4 = -0.262

---
Full Ring

---
Full ring parameters
L = 395.89 m
Tper = 1.317 ms ;
ac = 0.000731
Qx = 34.069
Qy = 26.862
xx = 7.11e-9 (corr) / -72.80 (nat)
xy = 1.07e-8 (corr) / -38.33 (nat)
bx(max) = 12.05 m
by(max) = 7.80 m
U0 = 744 keV
DE = 7e-4

---
Full ring parameters (2)
e = 9.78e-10
tx = 10.15 ms
tz = 5.08 ms
Synchrotron integrals:
I1 = 0.290
I2 = 0.789
I3 = 0.0734
I4 = -6.24e-5
I5 = 6.44e-5

---
Timing considerations

---
Minimal damping time
KCK pulse
Bunch train: 75 ns
n(train) = \frac{T_{per}}{\Delta t + t_K} \simeq 10
\epsilon(t) = \epsilon_{inj}e^{-\frac{2t}{\tau}}
T_{store} = -\frac{\tau}{2} \ln{\frac{\epsilon_{ext}}{\epsilon_0}} \simeq 5\tau
\tau \le \frac{n(train) T_{pulse}}{5(\Delta t + t_K)} \simeq 20 \mbox{ ms}