## Slide 1: Overview of the work ongoing at CERN for ET vacuum
Carlo Scarcia
20.11.2024

## Slide 2
The main objectives are:
Coordinate the contributions of all parties involved in the study of ET beampipes.
Design, manufacture, assemble, and test a pilot sector of the selected ET beampipe vacuum systems.
Preparing and writing the ‘Technical Design Report’ for the vacuum systems of the ET’s arms, including cost estimations.
Contact and sharing of information with the Cosmic Explorer community.
CERN activities on ET beampipe vacuum
Since September 2022, a collaboration between CERN-INFN-NIKHEF-IFAE has been established
(management has been assigned to ETO).

## Slide 3
Vacuum layout & operations
Main areas for cost reduction and potential solutions
Materials
Design
Bakeout temperature & duration optimisation
Insulation material selection
Vacuum sectorization
Pumping modules design
…
Low H2 content/outgassing rate
Lower cost than 304L
Possibility to avoid high temperature degassing treatments
(e.g. vacuum firing or air bakeout)
Ferritic alloys
Mild steels and ferritic StS
Fast and lean beampipe production
(~8000 – 15 m modules required)
Easy to handle in an underground environment
Less expensive bakeout
(bakeout typically done via direct joule effect)
Thin-walled corrugated beampipe
Objectives
Potential
solution

## Slide 4
Completed ET beampipe studies
Design
Corrugated beampipe profile design
Supporting system and transfer function
Materials
UHV characterisation of ferritic alloys
Welding parameters optimisation
Magnetic properties of ferritic alloys
Corrosion studies (ongoing with UGhent)
Post-manufacturing treatments
Industrial facilities cleanliness assessment
Robot cleaning performance
Vacuum
Bakeout simulation and optimisation
Insulation performance studies
Preliminary vacuum system design
Examples of completed studies
(not exhaustive list)

## Slide 5
The ET pilot sector mock-up
Objectives: Test sleeve joints for welding and cutting, including cleanliness and dust assessment during welding.
Sleeve joint (CERN proposal)
All components but flanges in AISI 441
(proposed material for ET)
With filler material (AISI 317)
Autogenous weld
DN850 x 1.5 m

## Slide 6
The ET pilot sector mock-up – Workflow
Cleanroom conditions
TT4: installation site
B.107: cleaning site
Start of the activities: End of November 2024

## Slide 7
The ET Pilot Sector (ET-PS)
Q1 2024 (January)
From Q4 2024/Q1 2025
The pilot sector aims to test the design, fabrication, installation and commissioning of the proposed beampipes and support system. It also aims to compare the feasibility of a selected number of technical choices.
Project peer reviewed (international experts panel).
Material and vacuum system validated.
Start of installation of a
AISI 441 VIRGO-like pipe Ø 1.08 m x 4 mm x 36 m
Q2-Q4 2024
Manufacturing and procurement of the ancillary components/equipment.

## Slide 8
The ET Pilot Sector (ET-PS) - Status
The procurement of components is completed, and productions are launched.
All raw materials and ancillary vacuum components are at CERN.
DN1000 AISI 316L bellows
(internal convolutions)
Ancillary vacuum components acceptance test / conditioning
Raw material (AISI 441) for beampipe and extremities production

## Slide 9
The ET Pilot Sector (ET-PS) - Status
The procurement of components is completed, and productions are launched.
All raw materials and ancillary vacuum components are at CERN.
The premises have been serviced (Wi-Fi, bakeout returning cables, cleaning etc.) and will be available from Dec. 2024.
The hosting tunnel: TT4

## Slide 10
The ET Pilot Sector (ET-PS) - Master schedule
Phase 1
“Background” measurements
Phase 2
Beampipe measurements
2024 | 2025 |  |  | 
Q4 | Q1 | Q2 | Q3 | Q4
Assembly and leak detection
Test programme
Extended TDR writing

## Slide 11
The ET Pilot Sector (ET-PS) - Extended schedule
2024 | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  | 
Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Assembly and leak detection
Test programme
Extended TDR writing
Extended test programme
Final TDR writing
The extended test programme aims to test alternative solutions not included in the first amendment:
New insulation materials.
Different pumping schemes.
Leak detection tools.
Alternative beampipe manufacturing solutions (continuous welded pipe from Aachen, corrugated beampipe from NL consortium, etc..).
Test of large sector valves.
Venting and tube section dismounting impact on dust content.

## Slide 12
Preliminary Technical Design Report (TDR)
In the framework of ET-PP, a preliminary Technical Design Report (TDR) has been produced.
The prelimary TDR includes:
Overview and assumptions.
Functional specifications, scientific requirements and technical constraints.
Materials for the vacuum pipes.
Mechanical design of the vacuum pipes.
Fabrication and surface treatments.
Vacuum layout.
Installation.
Bakeout: thermal insulation, electrical configuration and procedure.
Vacuum control system.
Vacuum commissioning.
Vacuum operation and maintenance.
Quality assurance plan.
Risk management.
Logistics and sustainability.
~ 70 pages

## Slide 13
Preliminary Technical Design Report (TDR)
The prelimary TDR includes:
Overview and assumptions.
Functional specifications, scientific requirements and technical constraints.
Materials for the vacuum pipes.
Mechanical design of the vacuum pipes.
Fabrication and surface treatments.
Vacuum layout.
Installation.
Bakeout: thermal insulation, electrical configuration and procedure.
Vacuum control system.
Vacuum commissioning.
Vacuum operation and maintenance.
Quality assurance plan.
Risk management.
Logistics and sustainability.
Installation and repair procedure

## Slide 14
Preliminary Technical Design Report (TDR)
The prelimary TDR includes:
Overview and assumptions.
Functional specifications, scientific requirements and technical constraints.
Materials for the vacuum pipes.
Mechanical design of the vacuum pipes.
Fabrication and surface treatments.
Vacuum layout.
Installation.
Bakeout: thermal insulation, electrical configuration and procedure.
Vacuum control system.
Vacuum commissioning.
Vacuum operation and maintenance.
Quality assurance plan.
Risk management.
Logistics and sustainability.
Compact UHV pumping system

## Slide 15
Preliminary Technical Design Report (TDR)
The prelimary TDR includes:
Overview and assumptions.
Functional specifications, scientific requirements and technical constraints.
Materials for the vacuum pipes.
Mechanical design of the vacuum pipes.
Fabrication and surface treatments.
Vacuum layout.
Installation.
Bakeout: thermal insulation, electrical configuration and procedure.
Vacuum control system.
Vacuum commissioning.
Vacuum operation and maintenance.
Quality assurance plan.
Risk management.
Logistics and sustainability.
Temperature distribution at the end of the bakeout (150°C, 7d)
Current distribution during bakeout

## Slide 16
Preliminary Technical Design Report (TDR)
The prelimary TDR includes:
Overview and assumptions.
Functional specifications, scientific requirements and technical constraints.
Materials for the vacuum pipes.
Mechanical design of the vacuum pipes.
Fabrication and surface treatments.
Vacuum layout.
Installation.
Bakeout: thermal insulation, electrical configuration and procedure.
Vacuum control system.
Vacuum commissioning.
Vacuum operation and maintenance.
Quality assurance plan.
Risk management.
Logistics and sustainability.
Air leaks impacts and recovery

## Slide 17
Preliminary Technical Design Report (TDR)
The prelimary TDR includes:
Overview and assumptions.
Functional specifications, scientific requirements and technical constraints.
Materials for the vacuum pipes.
Mechanical design of the vacuum pipes.
Fabrication and surface treatments.
Vacuum layout.
Installation.
Bakeout: thermal insulation, electrical configuration and procedure.
Vacuum control system.
Vacuum commissioning.
Vacuum operation and maintenance.
Quality assurance plan.
Risk management.
Logistics and sustainability.
Identification of risks of different categories:
Technical
Financial
Safety
Scope
Schedule

## Slide 18
Technical Design Report (TDR)
New schedule allows the TDR to be updated for changes:
Preminary TDR (Q4 2024) [ET-PP]
Description of the system, materials, assembly, commissioning and risks identification.
Extended TDR (Q4 2025)
Detailing of all the chapters of the preliminary version (with in-depth reports). Logistics and sustainability further investigated. Preliminary cost estimation. Integration with civil engineering.
Final TDR (Q4 2027)
Final version with optimal solutions. Full detailing of chapters. Full integration with civil engineering considering all the other services (HVAC, fire safety, …).