## Slide 2
Design inputs and concept
Specifications:
  Geometry:
    Aperture of 1000 mm
    About 100 km long
  Vacuum: 10-9 mbar
    Low outgassing materials
    In-situ bake out at 150 °C
  Mechanics:
    Vacuum/atmospheric pressure
    Gravity
  Environment
    Corrosion resistant
  As cheap as possible

## Slide 3
Design inputs and concept
  Mechanical aspects of thin-walled corrugated tubes
    Withstand external pressure
    Stainless steel material
    No need of bellows
    Easier bake out
    Less raw material
    lighter forming equipment (thinner wall)

## Slide 4
Mechanical aspects
The design is driven by the buckling pressure of a corrugated tube.
For long thin tube, typical buckling mode 2 is observed.
Safety coefficient of 3 is included.
Simplified geometry with two parameters.
h
2h
p
Unfolded length of one pitch: Lr
Equivalent thickness for the material quantity: teq=t*Lr/p
t
A flat section between each corrugation accommodates baffle interfaces and simplifies tooling insertion if required

## Slide 5
Mechanical aspects
Wall thickness in the range 1.2-1.5 mm can be considered for a buckling differential pressure of 3 bars.
1.5 mm thick wall chamber could be a good starting point considering welding, convolution height.
h
2h
p
t

## Slide 6
Specific stiffness:
Axial (E.S): 1.53E6 N
Transversal (E.I): 2.4E11 N.mm2
1 mm ↔ 61.5 N
3600 mm
1 mm ↔ 425 N
Mechanical aspects
Specific weight: 48 kg/m
Bakeout induced axial force: -3.3 kN
(< 95 kN thrust force)
Euler buckling force (in case of accidental venting during bakeout), assuming simple supports distanced by 7.5 m : -42 kN
 Global column instability not expected.
1.3 mm thick, 120 mm pitch, 35 mm convolution height.

## Slide 7
Mechanical aspects
Von Mises equivalent stress during bakeout under gravity (singularity at support removed)
Transversal displacement induced by bakeout
Behaviour during bakeout (150°C) :
Stress of about 50 MPa
Diameter dilatation of about 2.3 mm
Von Mises equivalent stress field during bakeout

## Slide 8
Mechanical aspects
Von Mises equivalent stress field during bakeout under gravity with supports distanced by 7.5 m (deformed shape factor: 100)
Behaviour during bakeout with gravity:
Assumption of a 14 m long tube
  Supported at 3.25 m from the extremities
    Sag ~ 18.3 mm
    Stress in the 60 MPa (support area excluded)
  Supported at 3.25 m from the extremities with central crutch
    Sag ~ 2.5 mm
    Stress in the 50 MPa (support area excluded)
Von Mises equivalent stress field during bakeout under gravity with additional central support (deformed shape factor: 100)

## Slide 9
Aramid fibre ropes
The proposed design, based on a suspended vacuum chamber, aims at reducing vibrations on the baffles.
Basic concept is based on harmonic oscillator and aims at lowering the first eigen frequencies.
Insulated vacuum chamber
Supporting frame
Supporting beam
A support proposal

## Slide 10
Assembly side view
Support top view
1/8
~15m
Space for tube module interconnection – insulation mounted subsequently
1/4
Elementary module would be composed of a ~15m long chamber, insulated and installed on a the supporting frame.
Supporting beam would be mounted and pre-aligned before module installation.
A support proposal

## Slide 11
Passage width: 1,8 m
Depending on the tunnel floor heigh
~ 1.8 m
~ 1.7 m
~3.72m
Preliminary implementation in a tunnel cross-section

## Slide 12
Mechanical aspects
Column Stability for hanging structure
Chamber
Support/wheel
Rope
The chamber behaves as a pendulum that corresponds in lateral direction to an elastic foundation.
Specific foundation stiffness:
h
Specific mass
Pendulum height
Expected buckling force for infinitely long column on elastic foundation:
During the thermal treatment, the chamber is in compression without vacuum  subjected to column buckling.
y
y
For h = 1 m, EI = 2.4E11 N.mm2 and m= 48 kg.m-1: Fcr ~ 21.25 kN

## Slide 13
Two models:
Beams in 2D with equivalent springs to model the pendulum effect; eigen mode study
Beams in 3D with gravity and initial imperfection; non linear large displacement study
Mechanical aspects
Column Stability for hanging structure
g

## Slide 14
100 m model:
2D eigen value model: buckling force: 22.15 kN
3D non linear model:
  Instability at ~ 23 kN (930 C)
  Plateau with stable deformation related to initial imperfection
Mechanical aspects
Column Stability for hanging structure

## Slide 15
1000 m model:
2D eigen value model: buckling force: 21.3 kN
Mechanical aspects
Column Stability for hanging structure
No significant difference between the 100 and 1000 m models.
Very good agreement between the two models and the theoretical values.
The chamber remains stable during the heat treatment in the 200-300 C range (Safety coefficient: 3-4).

## Slide 16
https://www.ail.ca/product/corrugated-steel-pipe/
https://www.prdcompany.com/corrugated-metal-pipe/
Spiral corrugations
Annular vs spiral corrugations

## Slide 17
Spiral corrugations
Drawbacks
Influence of band width (helice angle) on the relative buckling pressure for different convolution parameters
Decrease of mechanical performance:
Higher longitudinal stiffness
Lower buckling strength

## Slide 18
Spiral corrugations
Drawbacks
Axial/torsional coupling:
Axial force induces rotation or torque.
Only thermal expansion
Fixed
Free
Thermal expansion & 1 bar external pressure
x
y
z
Case 1.5 mm thick, 100 mm pitch, 30 mm convolution height, 6 convolutions/band
12 m

## Slide 19
Spiral corrugations
Drawbacks
Axial/torsional coupling:
Axial force induces rotation or torque.
Case 1.5 mm thick, 100 mm pitch, 30 mm convolution height, 2 convolutions/band
Case 1.5 mm thick, 100 mm pitch, 30 mm convolution height, 6 convolutions/band