## Slide 1: Comprehensive redesign of CLIC MB Injector
Y. Zhao, S. Doebert, A. Grudiev, A. Kurtulus, A. Latina, CERN
CLIC MB Injector Meeting
21/11/2024

## Slide 2: Layout
Old (baseline?)
New (alternative?)

## Slide 3: e- Injector Linac
Layout
RF structure
  f = 2 GHz, L = 1.5 m, Δφ = 2π/3 per cell, Ncell = 30, G = 15 MV/m, φ = 0°
  a0 = (16+14)/2 = 15 mm, d0 = (4.16+4.76)/2 = 4.46 mm
Beam parameters (DBA @ 380 GeV)
  δE = 1%, σz = 1 mm, Qb = 1 nC
  Polarized e-: εn,x,y = 10 um, Unpolarized e-: εn,x,y = 50 um
FODO lattice
  FODO phase advance: 76.345°, k1 ~ 1.4715 m-1
1.5 m

## Slide 4: e- Injector Linac
60 FODO cells, 120 structures.
Twiss matching in MAD-X
Full bunch tracking in RF-Track

## Slide 5: e- Injector Linac
Jitter amplifications (original wakefield from Adnan for 3 m structure)
Sum(|Wt|) = 9.86 V/pC/m/mm
Jitter amplification factor | x | y
Coherent (average) | 1.000 | 1.000
Coherent (maximum) | 1.023 | 1.023
Incoherent (average) | 1.186 | 1.062
Incoherent (maximum) | 1.269 | 1.109
Single particle tracking in RF-Track with 1.5 m structure.

## Slide 6: e- Injector Linac
Jitter amplifications (absolute wakefield)
Sum(|Wt|) = 9.86 V/pC/m/mm
Jitter amplification factor | x | y
Coherent (average) | 1.552 | 1.550
Coherent (maximum) | 1.731 | 1.729
Incoherent (average) | 1.287 | 1.113
Incoherent (maximum) | 1.370 | 1.166
Single particle tracking in RF-Track with 1.5 m structure.

## Slide 7: e- Injector Linac
Jitter amplifications (fitted absolute wakefield)
Sum(|Wt|) = 39.87 V/pC/m/mm
Fitting function:
Jitter amplification factor | x | y
Coherent (average) | 12.041 | 11.920
Coherent (maximum) | 15.304 | 15.112
Incoherent (average) | 5.730 | 4.827
Incoherent (maximum) | 7.154 | 6.096
Single particle tracking in RF-Track with 1.5 m structure.

## Slide 8: e- Injector Linac
Imperfections and Beam-Based Alignment
Imperfections considered
  Position error (x, y): σ = 100 um
  Angular error (roll, pitch, yaw): σ = 100 urad
  BPM resolution: 1 um
  Following errors not considered for now:
    Magnatic strength error: σ = 0.1%
    RF gradient error: σ = 1%
    RF phase error: σ = 0.1°
    Beam position jitter (x, y): σ = 100 um
    Beam angular jitter (x’, y’): σ = 100 urad

## Slide 9: e- Injector Linac
Imperfections and Beam-Based Alignment
20 machines simulated for now.
Average emittance growths
Final emittances

## Slide 10: Next steps
To do:
  Finalize e- Injector Linac study
  Restudy Positron Source for new layout
  Restudy RTML for new layout
  CLIC Project Meeting presentation
  IPAC’25 poster and paper

## Slide 11: BACKUP

## Slide 12: Design of new layout
Electron source
Electron source | Particle | Final energy | Simulation
DC e- Gun | Polarized e- | ~MeV | -
Thermionic e- Gun | Unpolarized e- | ~MeV | -
Polarized e- Pre-injector Linac | Polarized e- | 200 MeV | -
Unpolarized e- Pre-injector Linac | Unpolarized e- | 200 MeV | -
e- Injector Linac | Polarized e- Unpolarized e- | 2.86 GeV | RF-Track
Positron source:
PDR, DRs: not to simulate
SR, BC1, BL: included in RTML simulation