## Slide 1
BLM Thresholds for the 2024 Ion Quench Test
Sara Morales Vigo and Belen Salvachua
Ad-hoc BLM Thresholds WG Meeting
15/11/2024

## Slide 2
BLM Family Name | Power Loss Limit Channeling B1H [kW] | Power Loss Limit Amorphous B1H [kW] | Power Loss Limit Volume Reflection B1H [kW]
THRI_COLL_7_TCLA_LO_ION | 113 | 20 | 30
THRI_COLL_7_TCSPM_LO_ION_H_CH | 66 | 329 | 217
THRI_COLL_7_TCSPM_LO_ION_V_CH | 25840 | 16644 | 7456
THRI_COLL_7_TCSG_LO_ION_H_CH | 55 | 257 | 148
THRI_COLL_7_TCSG_ME_ION_V_CH | 6491 | 1263 | 934
THRI_COLL_7_TCSG_ME_ION_V_AM | 375 | 68 | 32
THRI_COLL_7_TCSPM_LO_ION_H_AM | 118 | 22 | 17
THRI.IP7.P1_MQTL_FT_ION_COLL | 237 | 42 | 64
THRI.IP7.P2_MQTL_FT_ION_COLL | 298 | 55 | 77
THRI.IP7.P2_MB_ION_COLL | 81 | 16 | 24
THRI.IP7.P3_MB_ION_COLL | 312 | 59 | 95
THRI.ARDS_MBMB_ION_COLL | 294 | 45 | 85
THRI.ARDS.P1_MQ_ION_COLL | 177 | 31 | 82
THRI.ARDS.P3_MQ_ION_COLL | 6512 | 653 | 421
BLM Thresholds Power Loss Limits for B1H - Today
2024 Ion Quench test scheduled for the 24th of November, increasing losses in B1H with crystal in channeling
Power loss limits for the master thresholds RS09 (1.3 s) at top energy in B1H with the dedicated ion families
Overall, B1H limit of ~55kW in channeling, ~16kW in amorphous, ~17kW in VR
IR7 collimators
IR7 Q6
IR7 DS
New family created for bottleneck this year, in V plane

## Slide 3
RS | Duration | kW channeling operation | kW channeling quench test?
RS01 | 40 us | 375000 | 625000
RS02 | 80 us | 187500 | 312500
RS03 | 320 us | 46875 | 78125
RS04 | 640 us | 23438 | 39062
RS05 | 2.56 ms | 5859 | 9766
RS06 | 10.24 ms | 1465 | 2441
RS07 | 81.92 ms | 732 | 1221
RS08 | 655 ms | 91 | 153
RS09 | 1.3 s | 60 | 100
RS10 | 5.2 s | 60 | 100
RS11 | 21 s | 29 | 48
RS12 | 84 s | 24 | 40
Target power loss in each RS in channeling
Do we want to change the target power loss limit from ~60kW to ~100kW in RS09/RS10 (scaling similarly the rest of RS) for the quench test?

## Slide 4
Factors needed to reach 100kW (RS09-10) in B1H Channeling
BLM Family Name (B1 / B2) | RS01 | RS02 | RS03 | RS04 | RS05 | RS06 | RS07 | RS08 | RS09 | RS10 | RS11 | RS12
THRI_COLL_7_TCLA_LO_ION | Max | Max | Max | Max | 1.2 | 1.2 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 1.2
THRI_COLL_7_TCSPM_LO_ION_H_CH | Max | Max | Max | Max | Max | Max | 1.6 | 1.6 | 1.5 | 1.5 | 1.5 | 1.5
THRI_COLL_7_TCSPM_LO_ION_V_CH | Max | Max | Max | Max | Max | 0.004 | 0.004 | 0.004 | 0.004 | 0.004 | 0.003 | 0.001
THRI_COLL_7_TCSG_LO_ION_H_CH | Max | Max | Max | Max | Max | Max | 1.6 | 1.6 | 1.8 | 1.8 | 1.8 | 1.8
THRI_COLL_7_TCSG_ME_ION_V_CH | Max | Max | Max | Max | Max | 0.02 | 0.01 | 0.01 | 0.02 | 0.02 | 0.01 | 0.01
THRI_COLL_7_TCSG_ME_ION_V_AM | 0.17 | 0.14 | 0.1 | 0.1 | 0.1 | 0.4 | 0.3 | 0.3 | 0.3 | 0.3 | 0.2 | 0.1
THRI_COLL_7_TCSPM_LO_ION_H_AM | Max | Max | 0.9 | 0.9 | 0.9 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 1.5
THRI.IP7.P1_MQTL_FT_ION_COLL | Max | Max | 0.7 | 0.7 | 0.7 | 0.7 | 1.0 | 0.6 | 0.4 | 0.4 | 0.2 | 0.2
THRI.IP7.P2_MQTL_FT_ION_COLL | Max | Max | 0.1 | 0.1 | 0.1 | 0.1 | 0.8 | 0.5 | 0.3 | 0.3 | 0.2 | 0.1
THRI.IP7.P2_MB_ION_COLL | 9.9 | 8.9 | 4.3 | 3.6 | 0.9 | 0.9 | 1.2 | 1.2 | 1.2 | 1.2 | 1.1 | 1.1
THRI.IP7.P3_MB_ION_COLL | 6.9 | 3.9 | 1.6 | 1.3 | 0.4 | 0.4 | 0.4 | 0.4 | 0.3 | 0.3 | 0.4 | 0.6
THRI.ARDS_MBMB_ION_COLL | 1 | 0.6 | 0.6 | 0.5 | 0.4 | 0.2 | 0.2 | 1 | 0.4 | 0.3 | 0.4 | 0.6
THRI.ARDS.P1_MQ_ION_COLL | 1.4 | 1.1 | 0.6 | 0.5 | 0.2 | 0.2 | 0.8 | 0.6 | 0.6 | 0.6 | 0.6 | 0.5
THRI.ARDS.P3_MQ_ION_COLL | 0.07 | 0.04 | 0.02 | 0.02 | 0.02 | 0.01 | 0.02 | 0.02 | 0.02 | 0.02 | 0.01 | 0.004
Max: Threshold already at maximum electronics limit
In red: would need to apply factor to reach 100kW (RS09-10) or equivalent
In green: not limiting
Other bottlenecks:
BLMTI.06R7.B1E10_TCLA.C6R7.B1 and BLMTI.06L7.B2I10_TCLA.C6L7.B2 in THRI_COLL_7_TCLA_LO, factor 1.1 in RS07-08
BLMQI.06R7.B2I20_MQTL in THRI.IP7.P2_MQTL_FT, factor 1.2 in RS07, 1.1 in RS08 -> move to THRI.IP7.P2_MQTL_FT_ION_COLL?
BLMs with a filter in THRI_TCD_RC would need corrections in RS01-04, not sure about scaling