## Slide 1: WR Node (WR PTP Core)
Maciej Lipinski
WR Collaboration / CERN
Training material

## Slide 2: WR Node = WR PTP Core + hardware
Simple PCIe FMC carrier (SPEC)
Simple VME FMC carrier (SVEC)
PCI eXtensions for Instr. (PXI) module
FPGA Mezzanine Card (FMC) module
CompactRIO White Rabbit
Mini-WR to WR-enable carrier
WR PTP Core (WRPC)
Serdes
CLKREF
CLKDMTD
adjust
I2C
User Data
1-PPS
timecode
frequency
Peripheral
CPU/registers
source
sink
timing I/F
MAC I/F
Aux diags
Control/status
Pipelined WB
Slave I/F
EEPROM
External oscillators
PHY
Tx
Ethernet
Rx
WR PTP Core
Hardware with WR support
GW: https://ohwr.org/project/wr-cores
SW: https://ohwr.org/project/wrpc-sw
Wiki: https://ohwr.org/project/wr-cores/-/wikis/wrpc-core
Release: https://ohwr.org/project/wr-cores/-/wikis/Current-release

## Slide 3: WR Node = WR PTP Core + hardware
WR PTP Core (WRPC)
Serdes
CLKREF
CLKDMTD
adjust
I2C
User Data
1-PPS
timecode
frequency
Peripheral
CPU/registers
source
sink
timing I/F
MAC I/F
Aux diags
Control/status
Pipelined WB
Slave I/F
EEPROM
External oscillators
PHY
Tx
Ethernet
Rx
FPGA
WR PTP Core
Simple PCIe FMC carrier (SPEC)
Simple VME FMC carrier (SVEC)
PCI eXtensions for Instr. (PXI) module
FPGA Mezzanine Card (FMC) module
CompactRIO White Rabbit
Mini-WR to WR-enable carrier
Hardware with WR support
GW: https://ohwr.org/project/wr-cores
SW: https://ohwr.org/project/wrpc-sw
Wiki: https://ohwr.org/project/wr-cores/-/wikis/wrpc-core
Release: https://ohwr.org/project/wr-cores/-/wikis/Current-release

## Slide 4: WR Node = WR PTP Core + hardware
FPGA
WR PTP Core (WRPC)
Serdes
CLKREF
CLKDMTD
adjust
I2C
User Data
1-PPS
timecode
frequency
Peripheral
CPU/registers
source
sink
timing I/F
MAC I/F
Aux diags
Control/status
Pipelined WB
Slave I/F
EEPROM
External oscillators
PHY
Tx
Ethernet
Rx
Simple PCIe FMC carrier (SPEC)
Simple VME FMC carrier (SVEC)
PCI eXtensions for Instr. (PXI) module
FPGA Mezzanine Card (FMC) module
CompactRIO White Rabbit
Mini-WR to WR-enable carrier
Hardware with WR support
GW: https://ohwr.org/project/wr-cores
SW: https://ohwr.org/project/wrpc-sw
Wiki: https://ohwr.org/project/wr-cores/-/wikis/wrpc-core
Release: https://ohwr.org/project/wr-cores/-/wikis/Current-release

## Slide 5: Accessing WR PTP Core
Host
FPGA
Parallel BUS
WR
Network
Register access
Chip-external: PCIe, VME, PXI
Chip-internal: AXI bus in SoC
Serial Communication over USB
Ethernet Communication
UART

## Slide 6: Accessing WR PTP Core
Register access over parallel bus (access to all registers, using dedicated tools or direct memory mapping)
  Configuration and diagnostics
  Firmware loading
  Debugging (GDB, SoftPLL)
  Access to WRC shell via virtual UART
Serial communication over UART
  Access to WRC shell via physical UART
Ethernet communication over WR Network
  Access to WRC shell via netconsole
  SNMP get/set
  Syslog
Host
  Machine with OS (ideally Linux), e.g., PC, PL of SoC
  Hosts tools used to access WRPC
  Tools available in tools folder of https://ohwr.org/project/wrpc-sw

## Slide 7: WRC shell: ways of accessing
Register access over parallel bus: vuart
  Tools available in tool folder of https://ohwr.org/project/wrpc-sw
    wrpc-vuart -f <resource> –o <UART module offset> - [depricated]
    wrpc vuart –b <board> -f <resource> -o <WRPC offset> - new “Swisstool”
    Example execution for SPEC reference design over PCIe) host# sudo ./wrpc-vuart -f /sys/bus/pci/devices/0000:01:00.0/resource0 -o 0x00500 host# sudo ./wrpc vuart -b pci -f /sys/bus/pci/devices/0000:01:00.0/resource0 -o 0x00000
Serial communication over UART: use your favorite tool
  Bautrate: 115200
  Example tools: putty, picocom, minicom
  Example command: host# sudo picocom -b 115200 /dev/ttyUSB0
Ethernet communication over WR Network: nc
  netconsole must be enabled and configured on WRPC (see later slides)
  Example command: host# nc –u <IP of WRPC> 55
WRPC offset for SPEC ref design: 0x00000

## Slide 8: WRC shell: commands
WRC shell can be accessed using
  wrpc-vuart over parallel bus,
  serial communication over UART
  netconsole over WR Network
Commands available in WRC shell
  Basic commands: available by default in WRPC software binary available with release
  Advanced commands that need to be enabled before compiling new WRPC software binary - info later in this presentation

## Slide 9: WRC shell: gui
wrc# gui
The best tool to start with
Equivalent of wr_mon available on WR Switch (see detailed description in “WR Switch Basics” presentation)
Redesigned for WRPC v5
Gives many important information about WRPC status and configuration:
  Build version
  Link status
  PTP/WR configuration
  MAC of the peer
  PLL locking status
  Timing mode
  WR time
  Servo status (if in slave mode)

## Slide 10: WRC shell: initial configuration
wrc# sdb fs 0
SDB = Self-Describing Bus (link)
Creates SDB FS image in Flash memory Base address and sector size taken from HDL
SDBFS stores
  MAC address
  SFP database
  Init script
  t24p calibration
wrc# sfp add <PN> <egLat> <inLat> <relCoefH> <relCoefL>
Add SFP parameters to database:
  <PN> - SFP’s part number
  <egLat> - egress latency (deltaTx) [ps]
  <inLat> - ingress latency (deltaRx) [ps]
  <relCoefH> <relCoefL> - most & least significant 9 digits of relative delay coefficient (alpha)
Database organized differently than on Switch
wrc# sfp match
Match inserted SFP with entry in database
wrc# sfp show
Show SFP database

## Slide 11: WRC shell: initial configuration
wrc# mode <PTP Mode>
Set PTP mode
  gm – for Grandmaster
  master for Free-running master
  slave for Slave
wrc# mac get
Report MAC address of WRPC
wrc# mac <cmd> xx:xx:xx:xx:xx:xx
Set MAC address to the value indicates with xx:xx:xx:xx:xx:xx in HEX
cmd:
  set – set for runtime
  setp – set permanently
wrc# ip
Report IP address of WRPC which can be either retrieved from DHCP server using bootp, or set manually
wrc# ip set
Set manually IP v4 address of WRPC
d
d

## Slide 12: WRC shell: init script
WRPC allows to load user-defined initialization script on every startup
This mechanism allows custom configuration
Commands
wrc# init add <cmd>
Adds command to the “user-defined” part
Any configuration command can be added
wrc# init show
Shows content of the script
wrc# init boot
Restart WRPC
d

## Slide 13: WRC shell: monitoring
wrc# stat <on | off>
Reports repeatedly (until off) loggable statistics
Without parameter, toggles reporting
wrc# stat bts
Prints bitslide value for established WR Link
wrc# ps
Manual – section 5.4.5
Prints:
  Task list
  Total time spent on task
  Maximum time spent on task
Possible to reset counters
If any task is executed longer than 250-500ms might cause problems with synchronization. This tool can help detect this
d

## Slide 14: WRC shell: debugging
wrc# verbose bbbbbb
Sets level of verbosity of PTP daemon (PPSi)
Verbosity levels
d

## Slide 15: WRC shell: advanced commands
wrc# sfp info
Limited equivalent of wrs_sfp_dump
Prints basic information about SFP
Compilation options:
  CONFIG_CMD_SFP_INFO=y
wrc# netconsole
Manual – section 4.4
Enable netconsole, ready to accept connections from remote host
Compilation options
  CONFIG_CMD_NETCONSOLE=y
  NETCONSOLE_DEF_WAIT=y
host#nc –u <IP> 55
d

## Slide 16: WRC compilation configuration
WRC software: https://ohwr.org/project/wrpc-sw
Needs to be compiled with suitable configuration
  Predefined for existing boards in configs
  Using predefined configuration: host# make <configuration file name>
  Access configuration menu: host# make menuconfig
  Configuration saved to file: .config
Important parameters which must match HW/GW
  Target Platform
    Generic WR Node 8-bit PCS/PHY
    Generic WR Node 16-bit PCS/PHY
    WR Switch
    AFCZ
    eRTM14/15
  Size of RAM in FPGA (in Advanced config)
    Should match RAM in FPGA
Many advanced commands can be added, e.g.,
  netconsole
  sfp info
  freqmon
Predefined SW configs:

## Slide 17: WRC host tools
Host tools are in tools folder of https://ohwr.org/project/wrpc-sw
Old tools (to be deprecated, still available): host# wrpc-vuart -f <resource> –o <UART module offset> - access virtual UART host# wrpc-diags -f <resource> –o <UART module offset> - access diagnostics registers host# wrpc-load -f <resource> –o <UART module offset> - load software binary
New “swiss tool”: host# wrpc <cmd> -b <board> <board-specific access to resource> <cmd-specific>
  Replaces existing tools above
  Provides new functionalities:
    Reading board and wrpc info
    Recording data from SoftPLL
    Providing gdb server for Risk-V
    Displaying diagnostics from auxiliary input (user-specific)
  More info on presentation by Tristan

## Slide 18: Standard services (1)
BOOTP (Manual – section 6)
  Allows to obtain IPv4 address from BOOTP server
SNMP (Manual – section 5.1)
  Single Network Management Protocol
  Diagnostics and configuration over WR Network
  MIB: WR-WRPC-MIB.txt
  Allows:
    Reading the monitoring values
    Managing SFP database
    Setting up init script
    Generating SDBFS
    Configuring netconsole
    Running shell commands
    Useful commands: host# snmpwalk host# snmpget host# snmpset
  Syslog (Manual – section 5.2)
    Send to server: boot time, links/sync status, temp
    Command to enable/configure wrp# syslog <IP> <MAC>
BOOTP/syslog server
SNMP client
BOOTP
SNMP
syslog

## Slide 19: Standard services (2)
  LLDP
    Link Layer Discovery Protocol
    Allows to retreive information about device on the other side of a link
    WRPC: only reports its presence to a peer
    WR Switch uses LLDP to discover devices connected to it. WR Switch reports this information over SNMP to SNMP server
    Used to draw network tree:
SNMP client
SNMP
LLDP

## Slide 20: Thank you
Summary
Method of accessing WR PTP Core
WRPC Shell
  Ways of accessing
  Ways of enabling command
  Commands
Compilation configuration
Host tools
Standard services

## Slide 21: WR Node = WR PTP Core + hardware
FPGA
WR PTP Core
WR Port
SFP
Parallel BUS
UART
WR
Network
External: PCIe, VME, PXI
Internal: AXI bus in SoC
Serial Communication over USB
Ethernet Frames

## Slide 22: Accessing WR PTP Core
Host
FPGA
Parallel BUS
Register access
Chip-external: PCIe, VME, PXI
Chip-internal: AXI bus in SoC
Serial Communication over USB
Ethernet Communication
UART
WR Switch