## Slide 1
Matteo Solfaroli
Moriond QCD and high energy interactions
March 31st, 2025
LHC status

## Slide 2: Outline
2024 run highlights
2025 configuration and main challenges
Considerations on beam intensity increase
2025 schedule and projections
Oxygen run preparation

## Slide 3: LHC in 2024
First injection: 8th March (3 days early)
First Stable Beams @6.8 TeV 5th April (3 days early)
LHCb VELO closed for the 1st time
1200 bunches on 14th April (10 days early)
Reverse Polarity optics
commissioned (~ +1 week)
β* limited to 36 cm 17th April
Bunch length control/target
Limit RF module heating risk
VdM & Calibration
Runs, 16th – 20th May
BCMS beams
May
β* back to 30 cm 17th June
Beyond 110 fb-1
IONS run
(YETS started on 25th November)
pp reference run 28th Oct – 2nd Nov
90% availability
Q1
Q4
March
April
May
June
July
September
October
pp run
August
IONS run
November
ref run
Stable Lumi
Production
Summer period
1.9 nb-1 in IP1/2/5
(same as 2023 in 50% of the time)

## Slide 4: 2024 production
124 fb-1 in ATLAS/CMS
11 fb-1 in LHCb
67.5 pb-1 in ALICE
Highest production rate ever
Single most productive year in LHC history so far!
2024 AVG rate = 0.83 fb-1/24h
2024 highest rate = 1.5 fb-1/24h
(midnight to midnight)
LS1
LS2
IP1/2/5: Almost same luminosity as 2023, in about half the time, achieving the (ambitious) target of 1.9 nb-1
IP8: About double the 2023 luminosity in about half the time
~2h of levelling at 6.4x1027 cm-2 s-1
~30% higher intensity with performance beyond HL-LHC projection
IONS
M.Lamont @Moriond-QCD 2024

## Slide 5: Outline
2024 run highlights
2025 configuration and main challenges
Considerations on beam intensity increase
2025 schedule and projections
Oxygen run preparation

## Slide 6: Triplet radiation and optics
2024: RP optics in IP1
   increased background FASER / SND
2025 compromise:
  Nominal polarity in IR1
  RP in IR5
  Plane inversion
  Simulations indicate good background for FASER and SND
Radiation doses to the inner triplet magnets approach estimated damage levels (large uncertainties!)
  Dose can be spread over different azimuths by:
    Changing crossing angles (sign, plane)
    Inverting the triplet quadrupole polarities (RP optics)
RP in both IR1 and IR5 with flipped planes is the best configuration!

## Slide 7: Flat optics in 2025 machine cycle
Flat optics configurations were already tested in MDs, no issues expected
New optics corrections will have to be established for all configurations
Apertures must be checked to confirm configuration choices
  Xing/sep planes maintained as previous years at injection to maximize aperture
  Never had bad surprises in Runs 2 & 3
The IT beam screen shape is asymmetric and optimized to allow larger aperture in the “standard” crossing plane
  Beam size in IT quadrupoles is  1/
For rotated crossing planes:
  Less aperture in the rotated crossing plane: minimum b* increases 30->60 cm
  More aperture in the rotated separation plane: minimum b* decreases 30->18 cm
  To ensure equivalent performance reach use flat optics (β*x  β *y)

## Slide 8: BCMS beam
With a nx36b patterns filling scheme, standard 25 ns and Batch Compression and (bunch) Merging and (bunch) Splitting (BCMS) beams are interchangeable
Standard: ~ 2 µm
BCMS
~ 1.7 µm
+ ~2h levelling with BCMS beams
2025
BCMS will be used as baseline
Optimized BCMS beam deployed in May
  10% higher brightness
  Better equivalent cross-section
  Smaller emittance also beneficial for losses reduction, especially at injection

## Slide 9: Levelling in physics
Luminosity levelling is required by cooling limitations in the Inner Triplet magnets
Combined b* (~beam size) & offset levelling allowed for
  6-7 hours levelling with BCMS beams
  Well balanced luminosity bet CMS and ATLAS
  LHCb levelled through the entire fill
Luminosity control below 2.5% (5% is Run3 request)
Bunch intensity increase will extend levelling time
2025: adding “continuous” Xing angle levelling:
  Additional 1.5h of levelling
  +3.5% integrated luminosity (when no premature dump)
  Main motivation: explore flat optics in aggressive beam-beam configuration to prepare for HL-LHC alternative to baseline scenario

## Slide 10: Availability
Availability is THE key factor for accelerator performance
Availability factor was ~constant through Run2 and Run3 for small (<24h) faults
NOTE: the availability of the proton run is calculated on the effective time from the retrospetctively calculated schedule (long faults are not included)
Minor differences in numbers are due to slightly different choices in term of dates (including or not scrubbing run, TS recovery etc)
pp run
pp reference run

## Slide 11: Outline
2024 run highlights
2025 configuration and main challenges
Considerations on beam intensity increase
2025 schedule and projections
Oxygen run preparation

## Slide 12: Intensity limitations - vacuum modules
IMPACT in 2023
~5 days lost
Bunch intensity limited to 1.6x1011 ppb
IMPACT in 2024
Bunch intensity limited to 1.6x1011 ppb, while maximizing the bunch length throughout the cycle
  Difficult to identify intensity limitation (strong dependence on contact quality)
Problem traced to localized heating of the tension spring of diameter 212 (ID212) modules, consolidation completed:
71 most critical module replaced
2025
This operational improvement, together with the consolidation open a potential window for higher intensity tests/operation, with very low risk of impact on availability
Improved control of bunch length provides safety factor in power deposition

## Slide 13: Intensity limitations - heat load
Operation challenges coming from heat load:
IT heat load:
  Limits instantaneous lumi at ~2.1x1034 cm-2 s-1
Arc heat load:
  Limitation on train length, total number of bunches, bunch intensity
  Limited by ~170 W/half-cell in sector 7-8 (+10 W for operational margin)
2024 operation with trains of 3x36b
2025
Small margin (~10%) gained by conditioning over 2024 (not enough for an additional full train)
3x36b: 2024 scheme, compatible with 1.8e11 ppb
4x36b: compromise with more collisions than in 2024, expected limit ~1.7e11 ppb
5x36b: maximizes n. of collisions, limited to ~1.6e11 ppb

## Slide 14: Bunch intensity in 2025
In Run3 LHC has been so far operated with train of 1.6×1011 ppb:
  Run3 target of 1.8×1011 was not (yet) achieved
The injector chain achieved LIU target parameters at SPS flat top in 2024
  4x72b @2.3×1011 ppb
Different scenarios discussed for 2025 run
  No risk pp production - NOT more knowledge at end of 2025 than today!
  Early, distributed, late intensity steps towards 1.8x1011 ppb (Run 3 goal)
Chosen scenario
Stable run at 1.6x1011 ppb until september THEN increase bunch intensity until 1.8x1011 ppb, before ION run

## Slide 15: Towards HL-LHC bunch intensities
End of Run 3: last window to probe HL-LHC beam intensities
Critical investment into the success of HL-LHC!
Increasing intensity can reveal “unexpected limitations”
  BSRT mirror, (old) TDIs, vacuum modules, roman pots
Once operation at 1.8x1011 ppb (Run3 goal) demonstrated, explore intensity range up to 2.3x1011 ppb
  Beam dynamics tests: compatible with intensity limits (lower number of bunches)
    Started: RF capture, electron cloud, beam in(stability), beam-beam…
  Heating test ( 2000 bunches)
    Heating power will exceed the peak values achievable in operation with 1.8×1011 ppb
    Potential risk to components and to machine availability from “unexpected limitations”
Heating test proposed for the end of Run 3:
Advance the ion run by 2 weeks
No risk to physics program in case of failures
Collisions not needed but would be possible

## Slide 16: Outline
2024 run highlights
2025 configuration and main challenges
Considerations on beam intensity increase
2025 schedule and projections
Oxygen run preparation

## Slide 17: Schedule
First stable beams at 6.8 TeV in week of May 1st
Intensity ramp up (number of bunches) at 1.6×1011 p/b  full machine around mid-May
Oxygen run during 1st week of July
Injector complex already restarted
  Beam is in the SPS
Experimental caverns closed on April 2nd
Transfer lines check on April 4th
Beam in LHC ~April 8th
About 2-day delay wrt original schedule due to ATLAS cooling problem (water leak) in the Argon calorimeter

## Slide 18
Almost 1600 superconducting circuits
Over 10,000 tests to be executed and analysed
Sophysticated tools to ensure robustness reproducibility and traceability throughout the execution process
Enhanced automation for increased efficiency
Cross-departmental effort: two weeks campaign involving approximately 10 groups across ATS sector
Entering now Machine check-out phase
~800 quick interlock tests

## Slide 19: Performance estimate
LHCb prediction (driven by hours in stable beams and levelling target)
12 fb-1
Performance estimate depends on filling schemes and availability…
Assuming availability 2024-like and filling scheme based on 4x36b, expected perfomance (based on 2024 AVG rate):
  ATLAS/CMS: ~120 fb-1
  LHCb: ~12 fb-1
  ALICE: ~50 pb-1
Impact from delay generated by ATLAS leak negligible
ATLAS/CMS prediction
~120 fb-1
2024 AVG production rate
0.83 fb-1

## Slide 20: Outline
2024 run highlights
2025 configuration and main challenges
Considerations on beam intensity increase
2025 schedule and projections
Oxygen run preparation

## Slide 21: Oxygen run
Plan by LPC
Luminosity targets in nb-1
Injection
Ramp to 6.8 Z TeV, β*=1m/
1.5m
Squeeze β*=0.5m 1m
Physics
Injection
Physics
Ramp to 5.36 Z TeV, β*=1m/
1.5m
p-O
O-O
Preferred by experiments
Injection
Ramp to 6.8 Z TeV, β*=1m/
1.5m
Pb-Pb
Squeeze β*=0.5m 1m
Physics
8 days allocated for Oxygen - setup and physics run
Initial plan relied on a single machine configuration for PbPb, OO and pO to minimize setup overhead:
The requests from the experiments are however incompatible with this simple plan (LHCf b*  1m, OO at 5.36 TeV)
We will need 3 distinct configurations for PbPb, OO and pO

## Slide 22: Oxygen run
OO 5.36 Z TeV, β*IP1/2/5 = 0.5 m, β*IP8 = 1 m
pO 6.8 Z TeV, β*IP1/2/5 = 1m, β*IP8 = 1 .5m
R. Bruce, N. Triantafyllou, LBOC #176
First estimates indicate that some targets are difficult to reach. Time estimates range between 7days (perfect availability) and 9days
Short run is very sensitive to availability
O-O performance depends strongly on bunch intensity (and emittance) delivered by injectors
NeNe run does not fit into the time frame
  No overhead wrt OO on machine side

## Slide 23: Conclusions
LHC is ready for 2025 operation
  Stable operation with 1.6x1011 ppb until the end of summer
  Increase bunch intensity to reach 1.8x1011 ppb before the ION run
  ~120 fb-1, 12 fb-1, ~50pb-1 can be in reach in 2025, assuming 2024-like availability
The 2025 pp configuration will be adapted to limit radiation to the triplet magnets and to improve conditions for forward physics in IR1
  Polarity back to “normal” in IR1, “reversed” in IR5
Pushing bunch intensity during Run3 is key to unveil potential limitations before LS3 and prepare the road to HL-LHC
The oxygen run boundary conditions are complex: iterations needed to converge to a performance and configuration that fits into the time frame
It looks easy, but…
This is challenging stuff - that we can operate the LHC at this level is a phenomenal achievement and a testament to the remarkable commitment of everyone involved.
M.Lamont @Moriond-QCD 2024

## Slide 24: SPARE

## Slide 25: HL-LHC at a glance
HL-LHC is the main project for LS3
No accelerator upgrade project has so many challenging novelties, covering such a broad technology spectrum
Technology intensive project!
Major upgrades in P1 and P5, large fraction of LHC will remain unchanged
The above picture shows only a subset of the major technology landmarks of the project

## Slide 26: Crab cavities
Staged installation in YETS 30/31 was initially considered to cope with delay in equipment delivery
Studies show that staged RFD installation is not feasible, without having impact on Run 4 physics program
Mitigation action being implemented to ensure that the full system can be installed during LS3
NO delay expected

## Slide 27: Vertical cores
Technical constraints to execution of the Vertical Cores, combined with the limited access to LHC (2-month), created significant challenges
   first invitation to tender unsuccessful
Revision of the schedule and constraints to ensure that the works could proceed
New invitation to tender, allowing more flexibility
  issued in January, outcome assessment by May 2025
NO delay expected

## Slide 28: Magnets
Coil |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Magnet |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cold mass |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Test | MQXFB03 |  |  |  | MQXFB04 |  |  |  | MQXFB05 |  |  |  | MQXFB06 |  |  |  | MQXFB07 |  |  |  | MQXFB08 |  |  |  | MQXFB09 |  |  |  | MQXFB10 |  |  |  | MQXFB11 |  |  |  | MQXFB12 |  |  |  |  | 
NO delay expected
NbTi Magnets: well known technology, smooth production
Nb3Sn Magnets: new technology that entails some challenges
  Technology well under control
  Full production speed
  ≈ 1 year float for installation for each magnet
4 more magnets to build (B09-B12)

## Slide 29: Beam Screen Treatment (BST)
BST to cope with higher heat load due to increased intensity and (possibly) further surface degradation
Initial scope of 100 cells, new baseline 120 cells, (140 under discussion), to gain extra margin in case of degradation
Run2-Run3 Heat load comparison

## Slide 30: HL-LHC operation
Recent update: IONS operation in 2031-2041

## Slide 31: HL-LHC operation
NO pile-up increase
losses mitigation (dynamic aperture and tails control)
flat optics
Pile-up increase
Most efficient way to increase integrated luminosity
200 pile-up (7.5x1034 cm-2s-1) relies on engineering margins
Several options are being studied to prepare mitigations for potential performance limitations and/or to further push integrated luminosity

## Slide 32: HL-LHC operation
Identify parameters for HL-LHC operation (still to be further developed) to reach the 3000 fb-1 goal, even with ion runs until the end of HL-LHC
An intermediate PU value in Run 5 would allow to reach the 3000 fb-1 goal

## Slide 33: Beam screen treatment
Possible mitigations?
Treat larger number of half-cells (more margins)
Produce less e-cloud
  Filling scheme (36b/48b (2022), hybrid (2023))
  Continue the beam screen treatment in future LS
Risks:
Degradation of un-treated half-cells during future LS
  Extremely difficult to quantity and impossible to localize
Higher than expecter heat loads of treated half-cells
Low(er) number of treated half-cells in LS3
A scenario treating 100 half-cells looks realistic
OBJECTIVES
Remove CuO and/or increase surface carbon concentration on selected BS
Beam Screen (BS) surface passivation (robustness against re-oxidation)

## Slide 34: Heat-load – the problem
BASE
(2 K loops, thermal shields, DFB, SAM, RF, etc.)
Beam screen*
170 W/hc
LHC
Today
HL-LHC
(without BST)
BASE
(2 K loops, thermal shields, DFB, SAM, RF, etc.)
Beam screen*
285 W/hc
HL-LHC
(with BST)
BASE
(2 K loops, thermal shields, DFB, SAM, RF, etc.)
Beam screen*
160 W/hc
NB: The graphics are not scaled, they are only illustrative
Cryogenic operation margin
for daily operation
(handle transients during
injection and magnet ramping)
+ facing disturbances
Operational margin
Operational margin

BASE
(2 K loops, thermal shields, DFB, SAM, RF, etc.)
Operational margin
Beam screen
84 W/h
LHC
Design Report
*Beam screen values are given as example, as e-cloud varies along the machine
Inner Triplet
Inner Triplet
1 cryoplant capacity
~18 kW @4.5 K

## Slide 35: Why flat optics ?
IT beam screen
ATLAS for standard
V crossing
Beam separation in due to crossing angle bump
The IT beam screen shape is asymmetric and optimized to allow larger aperture in the “standard” crossing plane
accommodates the beam separation due to the crossing angle bump to reach the same b* in both planes
Beam size in IT quadrupoles is  1/
For rotated crossing planes:
Less aperture in the rotated crossing plane: minimum b* increases from 30 cm to 60 cm
More aperture in the rotated separation plane: minimum b* decreases from 30 cm to 18 cm
to ensure equivalent performance reach use flat optics (β*x  β *y)

## Slide 36: Beta* limitation (36 cm)
Significant losses on secondary collimator in fill 9530 (17th April)
300-400 um orbit shift is needed to induce observed hierarchy breakage
Highest losses in the
middle of insertion (instead of extremities, where primary collimators are located)
Broken hierarchy can compromise protection
 limitation on beta* (about 1-2% loss)
Studies, tests and simulations indicated that losses are generated by particles in the off-momentum halo (not core of the beam)
Various mitigations put in place to improve the behaviour
Machine re-validated after TS#1 with mitigations in place
Beta* limitation lifted

## Slide 37: Intensity limitations – vacuum modules
Problem traced to localized heating of the tension spring of diameter 212 (ID212) modules for:
non ideal contact fingers/tube
two beams
beam offsets
Consolidation campaign, completed during the present YETS 24-25
4 modules left in single beam configuration (no offset)
Pipe tube
RF fingers
Tension spring
2023 JAP talk, C.Antuono & P.Krkotic
ID212
Deformable RF fingers (DRF)
Optimized unshielded bellows
aggravating factors
Vacuum module failure in cell 4L1 (June 2023):
Repair results in ~5 days loss
Bunch intensity limited to 1.6×1011 p/b in 2023/2024