## Slide 1: Automating Linear Optics Measurements
And Update for ADT AC Dipole in Multiturn
Ujani Kar
Thanks to:
Tobias H. B. Persson, Michi Hostettler, Andrea Calia,
Delphine Jacquet, Joschua W. Dilly, Ewen H. Maclean,...
Automating Multiturn Operations
Automating Optics Measurements

## Slide 2: Outline
Part 1:
  Updates in Multiturn – ADT AC Dipole
Part 2:
  Automate Optics Measurements - Multiturn
Automating Multiturn Operations
Automating Optics Measurements

## Slide 3
I. ADT AC Dipole in Multiturn
Automating Multiturn Operations
Automating Optics Measurements

## Slide 4: Purpose
  Current measurements of ADT AC Dipole using the AccPit goes to Coupling Server, and overloads it.
  Putting the tab in the Multiturn directly writes the kick data to the OMC logbook. Easier to keep track of the data generated.
Automating Multiturn Operations
Automating Optics Measurements

## Slide 5: Adding the ADT AC Dipole Tab in Multiturn
ADT AC Dipole controls on the Multiturn, showing status and allowing controls
Required expert controls here:
(Similar to AccPit)
Excitation Amplitude
Controlled number of turns for Rising, Falling and Flat top in the ADT AC Dipole instead of default settings.
Automating Multiturn Operations
Automating Optics Measurements

## Slide 6
II. Automating Linear Optics Measurements
Automating Multiturn Operations
Automating Optics Measurements

## Slide 7
Objective:
To Automate Linear Optics Measurements in LHC
Automating Multiturn Operations
Automating Optics Measurements
Motivation:
Make Linear Optics Measurements easier for non-experts, reducing the workload of experts.

## Slide 8: How Optics Measurements are done
Machine and Beam in Correct State
Excite with AC Dipole until we have sufficient amount of high amplitude kicks
Analyse Data from kicks
Automating Multiturn Operations
Automating Optics Measurements

## Slide 9: Plan to Automate Optics Measurements – A Flow Chart
Tunes
Chroma
Landau Damping
BCM Masked
Collimators open
Beam Intensity
Bringing Machine to Correct State
Excite
Losses?
Intensity?
Increase Amplitude
Not Enough Amplitude
All Good
Store kicks
Send to Analysis
Huge Losses/
Large Drop in Intensity
Stop
Call for Help
Automating Multiturn Operations
Automating Optics Measurements
Enough Amplitude?

## Slide 10: Plan to Automate Optics Measurements
Bringing Machine to Correct State
Done
Undergoing
Automating Multiturn Operations
Automating Optics Measurements
Tunes
Chroma
Landau Damping
BCM Masked
Collimators open
Beam Intensity
Bringing Machine to Correct State
Excite
Losses?
Intensity?
Increase Amplitude
Not Enough Amplitude
All Good
Store kicks
Send to Analysis
Huge Losses/
Large Drop in Intensity
Stop
Call for Help
Enough Amplitude?

## Slide 11: Step 1: Before Kicking/Exciting :
Tunes
Chroma
Landau Damping
BCM Masking
Collimators Check
Beam Intensity
At correct values(as required)
≤3
ATLAS BCM Masked
~0
In course settings
<3x1010
Bringing Machine to Correct State
Make all the manual checks semi-automatised.
Check every time before kicking- individual steps
Work still ongoing
Status indicators for visual checks
Automating Multiturn Operations
Automating Optics Measurements

## Slide 12: Step 2 : Condition Checks after each Kick
Excite
Losses?
Intensity?
Increase Amplitude
Not Enough Amplitude
All Good
Store kicks
Send to Analysis
Huge Losses/
Large Drop in Intensity
Stop
Call for Help
Enough Amplitude?
Requests for human help when out of set limits in BLMs or Intensity
Message boxes providing immediate updates on acquisition and control parameters.
Automating Multiturn Operations
Automating Optics Measurements

## Slide 13: Step 3 : Excite based on Amplitude
Losses?
Intensity?
Increase Amplitude
Not Enough Amplitude
All Good
Store kicks
Send to Analysis
Huge Losses/
Large Drop in Intensity
Stop
Call for Help
Enough Amplitude?
Excite
Betabeat analysed for different kick to find an acceptable level of errorbars in beta amplitude to get a good kick.
Higher amplitude kicks -> Signal-to-noise ratio gets better
Fill nos: 9403, 8521
Analysis of Error in Beta Beat for Every Kick
[Only works if there are no major changes in the optics/beam set up, such as in 60 degrees]
Automating Multiturn Operations
Automating Optics Measurements
[%]

## Slide 14: 2. Conditional Kicking Based on Peak-to-Peak Amplitude
If the BPMs peak-to-peak is above ~2mm --> acceptable for the errorbars of betabeat --> Programmed exit.
Peak-to-peak amplitude is computed for individual BPM in Non-ATS arc and checked.
[Non-ATS arcs as they stay constant]
Turn-by-turn Plot of BPMs
Automating Multiturn Operations
Automating Optics Measurements

## Slide 15
Step 4 : Store kicks, Send for Analysis
Every good kick has to be stored and sent for analysis automatically.
Analysis can be done in a very similar way as in a coupling server--> reusable.
Next step in the direction of automating the Optics Measurements.
Automating Multiturn Operations
Automating Optics Measurements
Losses?
Intensity?
Increase Amplitude
Not Enough Amplitude
All Good
Store kicks
Send to Analysis
Huge Losses/
Large Drop in Intensity
Stop
Call for Help
Enough Amplitude?
Excite

## Slide 16: Conclusions
Done: The precondition checks and ongoing checks during kicks
Undergoing: The Analysis for the excitation amplitude and programming a higher kick or exit based on this analysis.
Future Prospect : Integrating with Optics Measurement tools for a complete automated Optics Measurement in LHC.
Automating Multiturn Operations
Automating Optics Measurements

## Slide 17: Thank You
Automating Multiturn Operations
Automating Optics Measurements
Automating Multiturn Operations
Automating Optics Measurements

## Slide 18: Extra Slides
Automating Multiturn Operations
Automating Optics Measurements

## Slide 19: Action Vs Amplitude(kick)
With Amplitude --> Model invariant (except for 60degs) --> Else we have to normalise and make a model of AC Dipole
Automating Multiturn Operations
Automating Optics Measurements