## Slide 1: Coronagraph at the LHC
Jan Pucek
Presentation made for the Students and R&D meeting
22.11.2024

## Slide 2: Introduction – what is a coronagraph?
Source
Image
Simple imaging system
Aperture
Point source imaged as a distribution
+ potential diffraction on the aperture (dependent on 𝜃)
Position at detector
Measured intensity
Figures from D. Butti

## Slide 3: Introduction – what is a coronagraph?
photosphere
corona
diff. tails
Figures from D. Butti
The PSF is small compared to the Sun’s radius,
only the diffraction tails visible

## Slide 4: Introduction – what is a coronagraph?
Figures from D. Butti
Occulter – blocks ”core” component
occulter
photosphere
corona
diff. tails

## Slide 5: Introduction – what is a coronagraph?
Figures from D. Butti
Lyot’s stop
photosphere
corona
occulter
Field lens
Field lens images the entrance aperture onto the Lyot’s stop that stops the diffracted portion of the light.
A telescope using a field lens + Lyot’s stop = Coronagraph

## Slide 6: Introduction – the source
Distance between D3 and BSRTM (extraction mirror) ≈ 21m
Synchrotron radiation emitted in a narrow cone (due to Lorenz transformation) ≈ 140 µrad
D3
D3
D3
D3
Beam 1
Beam 2
RF cavities
D4
D4
SR radiation
Extraction mirror
*not to scale

## Slide 7: Introduction – the source
Sharp edge of the extraction mirror within the light spot -> source of diffraction in horizontal plane
Simulation and figure produced by D. Butti
When imaged
Diffraction tail

## Slide 8: Introduction – the functional specifications
In the era of the HL-LHC the “beam halo” might contain 35MJ – danger to the collimation system
  online monitoring needed
The BSRH should provide reliable measurement of the beam halo population (beam halo = particles outside of 4.7𝜎ref from closed orbit)

## Slide 9: Instrument calibration
From image to p+ population
Physical units on the axis
(alias magnification)
Charge scaling = camera counts to p+ population

## Slide 10: Instrument calibration
Two independent calibration procedures:
  Calibration of the BSRH magnification (M) and point spread function (PSF)
    Only assumption – the PSF is Gaussian (not valid in H-plane)
    For the calibration used 6 different bunches (3 different emittances)
    Two parameters optimized – M(BSRH) and σPSF(BSRH)
  Calibration of the charge scaling on the BSRH (meaning protons/counts on camera)
    No assumptions at the moment

## Slide 11: Magnification and point-spread function
Comparison between “true” bunch profile and BSRH profile
Preliminary
Vertical profiles
Orange = BWS ⊗PSF
Blue = BSRH profile
Results V: σ = (277 ± 8)μm
m = (0.64 ± 0.006)
ps = (18.3 ± 0.2) μm/px
Problematic tail
Horizontal profiles
Orange = BWS ⊗PSF
Blue = BSRH profile
Used a subset of the profile – left of the blue line
Results H (L-BFGS-B): σ = (320 ± 30)μm
m = (0.68 ± 0.03)
ps = (17.0 ± 0.8) μm/px

## Slide 12: Charge scaling calibration
Simple:
total sum of camera counts * calibration factor = FBCT population
Take into account the exposure time!
cam_counts * c_factor*max_exposure/exposure = population
= 44.5

## Slide 13: Machine development session - overview
How to asses the performance of the instrument?
Scrape the beam to known size  beam halo = 0
Blow up a bunch (ADT) to populate the halo region
Measure charge in halo by two instruments (BWS, BSRH)

## Slide 14: MD results - analysis
Analysis of the BWS – straight forward
Raw data
Getting the center
Calculate integration region
Counts*c_factor = population in halo

## Slide 15: MD results - BSRH
20 times faster than real-life acq.

## Slide 16: MD results– BSRH analysis
Raw image
Projection + fit to get center
Calculate integration region,
Calculate the population in halo

## Slide 17: MD results - figures
Preliminary
V-plane results (3.5𝜎 to ∞):
BSRH data – moving average over 40 seconds (loss of exact timing information)
(gating on 10 pilot bunches while blowing up only one  contrast of 0.1%)

## Slide 18: MD results - figures
Preliminary
H-plane results (3.5𝜎 to ∞):
BSRH data – moving average over 2 seconds
(gating on 1 pilot bunch)

## Slide 19: MD results - remarks
Pretty good agreement, no?
Problems with the camera intensifier (minimized by moving average)
Additional data to be analysed
These results will be presented in December during a BHM review

## Slide 20: Outlook + improvements
Hardware during YETS:
  Exchange the image intensifier (+ maybe trigger cable)
  Make the BSRH parasitic to the BSRT (currently it is possible to send light to only one of the two instruments)
Software:
  Compare profiles from BWS and BSRH (using the “known” PSF)