## Slide 1: Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Xuan Tung Nguyen*, Long Chen, Tommaso Dorigo, Nicolas R. Gauger, Federico Nardi, Julien Donini
Fifth MODE Workshop on Differentiable Programming for Experiment Design
Kolymbari, Crete, Greece
June 12th, 2025

## Slide 2: Objectives
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Surrogates for Calorimeter Optimization?
Goal: Gradient-based optimization of calorimeter designs.
Challenge: GEANT4 is not natively differentiable ongoing efforts.
Proposal: Develop a high-fidelity, differentiable surrogate model.
Candidate: State-of-the-art generative model
Diffusion Models (DMs) Strong conditioning capabilities
    Fully differentiable via backpropagation
T.Dorigo et al., “Toward the End-to-End Optimization of Particle Physics Instruments with Differentiable Programming”, arXiv:2203.13818.

## Slide 3: Diffusion model for the surrogate
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Prompt: “a physicist developing machine learning application for future detector collider”
Decoder
Diffusion model
Text Encoder
RNG
Encoded text
loop

## Slide 4: Diffusion model for the surrogate
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Decoder
Diffusion model
Text Encoder
RNG
Encoded text
loop

## Slide 5: Challenge with Surrogate for Design Optimization
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Challenge: Surrogate model training in design optimization ideally requires exponentially many samples as the design-space increases.
Need to model entire design space accurately (Inputs are multi-dimensional DM must learn over this space).
Full simulation for whole design space is intractable (Can't cover all configurations with data alone).

## Slide 6: Pre-training + Post-training
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Pre-train a foundation model → learns global landscape approximately.
Pre-train model

## Slide 7: Pre-training + Post-training
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Pre-train a foundation model → learns global landscape approximately.
Post-train on current design point → learns local landscape accurately.
Pre-train model
Post-train model

## Slide 8: Pre-training + Post-training
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Pre-train a foundation model → learns global landscape approximately.
Post-train on current design point → learns local landscape accurately.
Backpropagation of diffusion model to its conditioning gives us gradient surrogate.
Enables gradient-based optimization.
Pre-train model
Post-train model
Optimization
Pezzulla, A., et al. “Inverse Design of Mechanical Metamaterials.” Nature Communications,

## Slide 9
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Denoising Diffusion Probabilistic Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Forward process: gradually add noise.
Reverse process: gradually remove noise.
Diffusion Model

## Slide 10
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Diffusion Model
Denoising Diffusion Probabilistic Models
Song, Yang. “Generative Modeling by Estimating Gradients of the Data Distribution.” yang‑song.net, 5 May 2021, https://yang-song.net/blog/2021/score/.
General generative model is built based on probability density function:
DDPMs use score function instead score-based model:
The sampling process of DM is iterative:
We can add an extra parameter y to the score-function to guide the model based on our design toward conditional denoising diffusion probabilistic models.
Notes: Most generative models start by modeling the probability distribution of the data. One common way is to define a probability density function pθ(x)pθ​(x), which is built from an energy function fθ(x)fθ​(x). This is shown here as:

## Slide 11: Methods
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Conditional Denoising Diffusion Probabilistic Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Conditioning = guide the generation process.
Learn the conditioned data distribution.
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Diffusion Model

## Slide 12: Methods
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Efficient Sampling
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Sampling
X3
X2
X1
X0
Notes: In standard DDPMs, generating a single takes hundreds or even 1,000 denoising steps. This is slow and inefficient, especially when you want to optimize over design parameters or deploy the model in practical scenarios.
Denoising Diffusion Implicit Models, or DDIMs, solve this. The key idea is to redefine the reverse process to be deterministic and non-Markovian, allowing us to skip steps in the denoising process.
Think of DDPMs as a strict chain: each step depends on the previous one, like dominoes falling. DDIMs break that chain and allow us to jump ahead — generating samples in, say, 25 or 50 steps instead of 1000.

## Slide 13: Methods
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Efficient Sampling
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Sampling
X3
X2
X1
X0
Efficient sampling.
Requires fewer steps.
Deterministic: can be differentiated.

## Slide 14: Methods
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Efficient Sampling
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Sampling
X3
X1
X0
Efficient sampling.
Requires fewer steps.
Deterministic: can be differentiated.
X2

## Slide 15: Methods
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Post-train model: Adapter
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Post-training: Adapter
Notes: So far, we've trained a powerful, conditioned generative model — and we've made it efficient and differentiable using DDIM. But now comes a practical question: what if the detector design changes? For example, what if a new experiment proposes a slightly different cell size or material?
Do we retrain the whole model from scratch? No — that’s expensive and unnecessary.
Instead, we use post-training techniques to quickly adapt our model to a new design configuration using only a small amount of data and compute.

## Slide 16: Methods
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Post-train model: Low-rank Adaptation (LoRA)
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Post-training: Adapter

## Slide 17: Methods
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Post-train model: Low-rank Adaptation (LoRA)
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Post-training: Adapter
Outputpretrain = W * X
WLoRA = W + r
Where r is low-rank update
r = WA * WB

## Slide 18: Methods
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Post-train model: Low-rank update (LoRA)
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Post-training: Adapter
Outputpretrain = W * X
WLoRA = W + r
Where r is low-rank update
r = WA * WB
We can adapt our model with different configuration (eg. CRILIN, PANDA, etc.) using LoRA post-training, require only small amount of data and training time

## Slide 19
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Muon Collider
CRILIN project: Optimization of FbF2 calorimeter (ECAL).
Pre-train on 5x5x5 Geant4 datasets with diverse cell sizes, materials, energies.
Post-train on 1x1x4cm3 cells (CRILIN baseline).
Used in loop: update design post-train compute gradient next iteration.
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
A Case Study

## Slide 20
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Training Data:
Simulation: Generated using GEANT4.
Dataset Size: 100,000 calorimeter shower images.
Energy levels: 1, 10, 50, 100, 200 GeV.
Granularity: 5 x 5 x 5 cells.
Material: Lead fluoride (PbF2 ), Lead Tungstate (PbWO4 ).
Addition labels: 5 different cell size configurations:
                2 x 2 x 6 cm3
                3 x 3 x 8 cm3
                4 x 4 x 10 cm3
                5 x 5 x 15 cm3
                6 x 6 x 20 cm3
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Training Setup

## Slide 21: Results
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
GEANT4 Ground-truth
CDDPMs Generated (at 300 epochs)
Comparison of GEANT4 and DDPM-generated showers:
DDPMs accurately reproduces GEANT4-generated showers.
No significant visual differences across energy levels.
Shows that our diffusion model effectively learns that shower distributions.
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Pre-training Results

## Slide 22: Results
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Energy profile at early epoch
Energy profile at later epoch
Huge mismatch between generated and ground-truth profiles.
Energy depositions are underestimated, and peak positions are deviate.
Two distributions closely matched across all energy levels.
Improved peak alignment and energy deposition spread.
Our model significantly enhances fidelity and successfully learns the shower calorimeter showers characteristics over time.
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Results
Pre-training Results

## Slide 23
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Pre-training Results
x
y
Quantify the physical fidelity of the generated shower,
we use physics-motivated metrics.
Total Energy (E):
Sum of intensities (energy deposits) over the full grid.
Energy-Weighted Radius (Rₑ):
Describes spread of the shower around its center.
Shower Dispersion (σᵧ):
Measures vertical spread using energy profile Iy (y).

## Slide 24
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Pre-training Results
These results demonstrate that the model not only learns to generate visually plausible showers, but it generate highly accurate HEP simulation data it can serve as high fidelity surrogate.
Mean Squared Error of each metric across training epochs

## Slide 25
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Results
Model performance on unseen cell size configurations
The conditional DDPMs was tested on cell size configuration that were not included in the training set to evaluate its ability to generalize.
Model captures the overall distribution but exhibits some deviate in shape.
The transverse profiles are well-aligned with the ground-truth.
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Results
Pre-training Results

## Slide 26: Results
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Pre-trained Energy profile
LoRA post-trained Energy profile
Generated energy deposition tends to overshoot the ground truth.
LoRA fine-tuning align closely with the ground truth across all energy levels.
Post-training reduces discrepancies with little training time.
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Posttraining Results
Results on Unseen Data post-train

## Slide 27
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Conclusion of working progress
Advantages of the Pre-train + Post-train Approach
Achieves high fidelity across a wide design space.
Requires only limited data for local adaptation.
Speed Benefit
For simple designs (e.g., homogeneous calorimeters), the speed gain is modest.
For complex or hybrid geometries, surrogate-based sampling will be significantly faster.
Next Steps
Evaluate the quality of gradients from the surrogate.
Apply gradient-based optimization to real design tasks.

## Slide 28
Differentiable Diffusion Models as Surrogate for Homogenous Calorimeter Design Optimization
Summary
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
A diffusion model surrogate can generate high-fidelity calorimeter showers, conditioned on design.
Pre-train + post-train to account for the large design space.
DDIM sampling makes inference fast and differentiable.
Gradients can be obtained through backpropagated through diffusion model to the conditioning parameters.
Optimization with surrogate gradients is ongoing.
Differentiable Modeling for Calorimeter Simulation using Diffusion Models
Summary

## Slide 29: Thank you for your attention!