## Slide 1: Towards differentiable GEANT with EM physics: addressing challenges with Multiple Scattering
Jeff Krupa1, Max Aehle2, Yiyang Zhao3, Mihaly Novak4, Max Sagebaum2, Long Chen2, Nicolas Gauger2, Mia Liu5, Lukas Heinrich6, Michael Kagan1
5th MODE Workshop
June 9, 2025
1
3
2
4
6
5

## Slide 2: Gradient-based optimization
An efficient and powerful way to optimize high dimensional functions like those used in HEP
Differentiable GEANT simulation would have far-reaching applications in topics like detector design
N parameters

## Slide 3: Detector optimization example
As an example, consider an e- beam with energy Ebeam incident on a sampling calorimeter with 2 parameters:
Can we tune θ to optimize an energy deposition profile?
  Eg to target a specific average shower depth
Pb
LAr
Ebeam
⍺
e-
⍺
⍺
…
2405.07944

## Slide 4: Detector optimization example
2D example of gradient descent in a realistic calorimeter
Loss surface
Gradients
START
END
2405.07944
Pb
LAr
Ebeam
⍺
e-
⍺
⍺
…

## Slide 5: GEANT
High fidelity software for simulating the passage of particles through matter, used in HEP and more!
50 layer sampling calorimeter
5
Pb
LAr
Ebeam
⍺
e-
⍺
⍺
…

## Slide 6: GEANT
DNA
~100nm
High fidelity software for simulating the passage of particles through matter, used in HEP and more!

## Slide 7: Making GEANT differentiable
Using AD tools built at Kaiserslautern
CoDiPack AD: operator-overloading tool which defines derivatives of all functions and operations
  G4double type inherits all of these operations
First: integrate the tool
Second: dig deep into the application to understand the implementation
see 2405.07944 2407.02966
Forward operator *(Forward a, Forward b){
return {a.val*b.val, a.dot*b.val+a.val*b.dot};
}
Multiplication operation
Forward cos(Forward a){
return {cos(a.val), -sin(a.val) * a.dot};
}
Cosine function
Illustrative example

## Slide 8: Lightning intro to EM GEANT
Multiple coulomb scattering
Bremsstrahlung
Discrete interactions for electrons*
Ionisation loss (Bethe-Bloch)
+
*positrons can also undergo annihilation *photons can also undergo photoelectric, Compton, pair production
Electron propagating through a volume = track
Propagate track through steps with defined length. At each step, perform:
  Discrete loss: sample discrete interaction probabilistically
  Continuous loss: calculate mean energy loss over entire step length
Transport particle to next step
Continue this until energy is exhausted or track leaves volume
Check if this includes brem

## Slide 9: Multiple Coulomb Scattering
Electron traveling through volume undergoes elastic scattering with very short mean free path
  Computationally infeasible to be treated discretely
Instead, an average deflection is estimated at each step
In 2405.07944 we observed large unphysical derivatives with MSC and it was turned off→address this challenge in this talk!
2405.07944
Multiple scattering OFF
Numerical derivative Automatic derivative
Automatic derivative
Multiple scattering ON

## Slide 10: Multiple Coulomb Scattering
Consider a detector with two layers of Pb, boundary at X = 0
  Boundary here carries no physical meaning→but plays a key role in GEANT navigation
e-
Layer 1 Pb
Layer 2 Pb

## Slide 11: Multiple Coulomb Scattering
e-
Layer 1 Pb
Layer 2 Pb
Consider a detector with two layers of Pb, boundary at X = 0
  Boundary here carries no physical meaning→but plays a key role in GEANT navigation
Track 7444
Step
X coordinate

## Slide 12: Multiple Coulomb Scattering
Step
Track 7444
Track 7444
X coordinate
Energy deposit derivative
Step
e-
Layer 1 Pb
Layer 2 Pb
Consider a detector with two layers of Pb, boundary at X = 0
  Boundary here carries no physical meaning→but plays a key role in GEANT navigation
Early observation: pathological tracks where derivatives become unstable

## Slide 13: Geometry and Stepping in GEANT
Step length cannot exceed the distance to boundary
  This folds navigation into derivative calculation

## Slide 14: Geometry and Stepping in GEANT
Pb volume 1
Pb volume 2
Start
End
Proposed step real physics
Step length cannot exceed the distance to boundary
  This folds navigation into derivative calculation

## Slide 15: Geometry and Stepping in GEANT
Pb volume 1
Pb volume 2
Start
End (post-MSC)
End
Proposed step real physics
Real step with MSC
Step length cannot exceed the distance to boundary
  This folds navigation into derivative calculation

## Slide 16: Geometry and Stepping in GEANT
Pb volume 1
Step length cannot exceed the distance to boundary
  This folds navigation into derivative calculation
Pb volume 2
Start
End (post-MSC)
End
Real step with MSC
Final step length geometry-limited
Proposed step real physics

## Slide 17: The Boundary in 1D
Initialize Ekin > 0 and track position/direction.
while (Ekin > 0) do
distToPhysics ← sample physics interaction length
distToBoundary ← distance to volume boundary
if (distToPhysics < distToBoundary) then
stepLength ← distToPhysics
else
stepLength ← distToBoundary
end if
…propagate track by stepLength
…do physics interactions
end while
tb
t

## Slide 18: The Boundary in 1D
Initialize Ekin > 0 and track position/direction.
while (Ekin > 0) do
distToPhysics ← sample physics interaction length
distToBoundary ← distance to volume boundary
if (distToPhysics < distToBoundary) then
stepLength ← distToPhysics
else
stepLength ← distToBoundary
end if
…propagate track by stepLength
…do physics interactions
end while
t
tb

## Slide 19: The Boundary in 1D
Initialize Ekin > 0 and track position/direction.
while (Ekin > 0) do
distToPhysics ← sample physics interaction length
distToBoundary ← distance to volume boundary
if (distToPhysics < distToBoundary) then
stepLength ← distToPhysics
else
stepLength ← distToBoundary
end if
…propagate track by stepLength
…do physics interactions
end while
→
→
!!!
tb
t

## Slide 20: The Boundary in 1D
Initialize Ekin > 0 and track position/direction.
while (Ekin > 0) do
distToPhysics ← sample physics interaction length
distToBoundary ← distance to volume boundary
if (distToPhysics < distToBoundary) then
stepLength ← distToPhysics
else
stepLength ← distToBoundary
end if
…propagate track by stepLength
…do physics interactions
end while
At a step length that transports to the boundary, there is a discontinuity in the derivative→instability in AD computations
We can remediate this by pausing gradient computation to boundary-limited steps
length t
tb
t

## Slide 21: Derivatives
After controlling gradient through navigation computations, noise in derivatives decreases substantially
  No change to primal (physics energy deposits remains unchanged)

## Slide 22: Simple Optimization
Define a target shower shape
Update primary energy to minimize loss
Optimization now using full EM physics processes in GEANT including multiple scattering
Pb
LAr
Ebeam
⍺
e-
⍺
⍺
…

## Slide 23: Simple Optimization

## Slide 24: Conclusion
Presented latest results on differentiable GEANT with full EM physics
Developed a solution for high-variance derivatives related to multiple scattering
  Understood these results in the context of a detector optimization
  Still studying the effects of derivatives w.r.t. geometry
Paper forthcoming