## Slide 1: Wrap up on beam halo monitoring status, options and path forward
F. Roncarolo
HL-LHC Beam Halo Monitor Review, 18-Dec-2024

## Slide 2: Specs and beam optics
about specifications and related discussions
  Distinction between tails close to the core and halo close to collimators.
  Presently not possible to follow halo formation during the cycle.
     important are simulations predicting beam halo formation
  can any of studies can include reduced collimator scans to benchmark BI techniques?
on possible beam optics at IR4
  Riccardo’s options promising: what can we test before LS3?
  A larger beam size enhances the performance of all monitors. For BSR: a reduced PSF/sigma ratio improves absolute accuracy in both contrast and integrated halo measurements. A beam size increase of a factor 1.5 or 2 (w.r.t. present optics) yields significant improvements

## Slide 3: BSRH
Phase | Deliverables | Dependencies
Pre-LS3 | Enhance knowledge of BSRH B2 Validate BSRTMB B1 light extraction Complete integration, procure vacuum chambers | - Given priority in MD list allocated MD time - -optimize time during commissioning (e.g. loss maps), propose/obtain eof studies
During LS3 | Deploy BSRH beam1/2 | 
Post-LS3 | Commission, tuning optimize system according to learning curve | 

## Slide 4: BGC
Take-home message for BGC imaging:
limited performance in acquisition rate and contrast
robust and reproducible thanks to its simplicity
→ insufficient as single halo monitor, might provide a solid cross-reference for other monitors
Take-home message for BGC profiler:
using BGC as beam profiler is a very recent concept
BGC profiler configuration very similar to existing one, already validated in the machine
→ instrument has potential, but further investigations needed (before LS3) to quantify performance

## Slide 5: BGC
Phase | Timeline | Deliverables | Dependencies | Budget Status
Pre-LS3 | Baseline Instrument Q1 2025 | Designs, Technical Specification, Cabling Requests, Test with BLMs | Optical Systems Collaborations | Manpower required
During LS3 | Installation in Phased approach | BGC for beam 2 | Geometers, Vacuum, Beam Loss Monitor System | Instrument from HL-LHC UK2 contribution CERN infrastructure budget identified
Post-LS3 | Operation as of start of run 4 | Optimise signal/noise ratio in fluorescence mode. Operation beam debris and BLMs | Beam Operation, Vacuum | 

## Slide 6: Low density materials
R&D very relevant for beam profile measurements both at LHC and in FT facilities
Need to find compromise among enough signal, detector lifetime, losses and quenches
Phase | Timeline | Deliverables | Dependencies | Budget Status
Pre-LS3 | By 2026 | HRMT test Material sim Material chemistry optimization Ball bonding | No dependencies | Covered
During LS3 | By 2028? | Proto for SPS | R&D dependecies | Not Covered
Post-LS3 | ? | Proto for LHC | R&D dependencies | Not Covered

## Slide 7: Best estimate of expected performance
Performance Metric | Required Range | Use Case(s) | BSR | BGI | BGC
Contrast | 10^-4 to 10^-6 | Collimation: 10^-4 at upper bound | Under study | Signal = 10 kHz (residual gas) or 5 MHz (injected gas) Background = tbd. | ~1%
 |  | MP: 10^-6 at 6.7σ |  |  | 
Relative Integral | 0.2% to 5% | Collimation: 5% to 0.5% | <0.1% | See slide #14 | tbc
 |  | MP: 1.4% to 0.2% |  |  | 
Absolute Integral | 10^10 to few 10^12 | Collimation: 1.5×10^12 | 1.5% during MD | See slide #14 | tbc
 |  | MP: (1-4)×10^10 |  |  | 
1D Profile Capability | Yes/No | Required for Beam-Beam | Yes |  | Yes
2D Image Capability | Yes/No | Required for Beam-Beam | Yes |  | No
Max. Acquisition Rate | 10-60 seconds | MP: ~10s | ~20Hz (time for full beam depends on the gated sample - >100s for full machine bunch per bunch, around 3s for 48b., limited by data processing) | 5 MHz with injected gas → 1800 electron / bunch / s. | 1 min
 |  | Others: ~60s |  |  | 
Bunch-by-Bunch Gating | Yes/No | Required for Beam-Beam | Yes | B-b-B via electrons timestamp | no
Number of Turns Needed | - | All cases accept multi-turn | Yes | With gas injection 5 MHz → 440 samples / turn. | -
Interlock Capability | Yes/No | Required for MP | tbc | tbc | SW

## Slide 8: General remarks questions
BSRs: need to balance pro and cons of second light source
BGC: can we have one version for beam emittance and beam halo
BGI is in HL-LHC baseline as profile monitor. If it works as profile monitor, functionality as BHM comes ‘for free’. Are there BGI design choices that depend on BHM specs? Question about ageing.
General: risks, for each technique what are the risks of not achieving what ‘promised’ today
From discussion: can we have more systematic studies on what happens during physics (Oliver’s comment on if we can use dump line monitors?)

## Slide 9: General questions
Q: Is there a monitor fulfilling all specs
A: no (as of today). ++points of each technique:
    BGC and BGI : self calibrated , all energies, including for ion
    BSR: high signal, high relative accuracy, bunch per bunch
Q: are there decisions that can’t be postponed?
A:
Approval / funding of BGC activities (?)
BSR:
  Complete BSR integration studies, procure enlarged beam pipes
  Assess if resources are enough to maintain two additional extraction sources
  Assess optical lines will work
Q: top importance milestones 2025?
A:
BGC tests as a profiler with BLM
BSRH MDs and operation during physics
Q: Do we continue with BH WG ?
A: topical meetings to update studies and preparation work ?