## Slide 1
RF sources and efficiency
I. Syratchev

## Slide 2
Tristron Efficiency vs. P out for different HV
For the required RF power modulation feedback (by LLRF only), the HV set point can be selected so that average efficiency will stay ultimately high: 88.7% (Z) and 91% (W,H). With HE TS klystron average efficiency will stay at 67% (Z).
MB Tristron – a unique gridded tube for FCCee collider
400MHz, 0.5MW
Cavities RF power modulation, 88MV
Z
Z, FOC, 88MV
Z, DeFOC,88MV
Tristron transient efficiency
46kV
Very efficient: >90%
Low Voltage: <50kV
Compact: ~ 1m3
Cost effective (compared to klystron)
No power consumption in sleeping mode (without RF)
Low power in collector (<50kW) and solenoid (3kW)
https://indico.cern.ch/event/1449294/
More reading:
+/- 20% modulation depth

## Slide 3
Issues with transient loading of the HV power supply
HV
Tristron
Transient power drain from HV power supply
It will be hard to provide such a bandwidth in HV unit.
Common HV
Tristron#1
Tristron#2
Transient power/2 drain from common HV power supply
50kV; 83%
46kV; 88.7%
With this layout we can set HV point and negotiate modulator bandwidth vs. average efficiency.
46kV, 88MV

## Slide 4
One cavity out of operation;103MV
Failure mode mitigation
46kV; 89%
50kV; 86%
RF power modulation; 88MV
Power sweep range: 320kW-540kW!
46V
50kV
Tristron transient efficiency
Average efficiency 86%
Working scenario: in the case of failure, slow (200-300 µsec) ramp up of the tristron modulator voltage from 46kV to ~50kV will provide efficient operation in the failure mode.

## Slide 5
Tristron for FCCee. Implementation scenarios.
Technology demonstrator (low cost at short time): Retrofit upgrade of existing ESS 0.7GHz, 1.2 MW MB IOT, anticipating efficiency increase from 70% to ~85%.
Full recycling of the exiting components (gridded cavity, output cavity and collector).
RF circuit and optics design and optimization at CERN.
Tube refurbishment at Thales – introducing extra cavity and compact external solenoid.
Testing at ESS using existing facilities.
Estimated schedule is about 18 month.
* Potential candidate for the graceful replacement of ESS klystrons along accelerator life-time.
** Frequency is close to 800MHz needed for FCC.
FCCee 0.5 MW Tristron prototype at 400MHz.
RF circuit and optics design and optimization at CERN.
Common input cavity vs. clustered option design and cost optimization (Thales+ ? + CERN)
Tube fabrication at Thales+?.
Estimated schedule is about 36 month.