## Slide 1: Particle motion in Hamiltonian Formalism I Yannis PAPAPHILIPPOU Accelerator and Beam Physics group Beams Department, CERN
CERN Accelerator School
Introduction to Accelerator Physics
Santa Susanna, Spain
September 21st – October 4th, 2025

## Slide 2: Purpose
The objective is finding methods to derive and solve (integrate) equations of motion, in order to describe the evolution (dependence with “time”) of a system (“particle”)
Introduce formalism of theoretical (classical) mechanics for analysing motion in general (linear or non-linear) dynamical systems, including particle accelerators
Connect this formalism with concepts already studied in the introductory CAS (matrices for transverse motion, synchrotron motion, invariants,…)
Prepare the ground for approaches followed for studying non-linear particle motion in accelerators (in the advanced CAS)

## Slide 3: Principles of classical mechanics
Some key concepts of classical (analytical) mechanics reviewed in this lecture, including
  Integrals of motion
  Integration by quadrature
  Period and Frequency
  Hamilton’s principle
  Lagrangian, Euler-Lagrange equations
  Hamiltonian, Hamilton’s equations
  Canonical variables, Symplecticity
  Poisson brackets
  Canonical transformations
Euler
Lagrange
Hamilton

## Slide 4: Equations of motion
Notes: Tabor 53-54

## Slide 5: Reminder: Newton’s law
The motion of a “classical” particle in a force field is described by Newton’s law:
with the position
the momentum
the force
the corresponding potential
It is essential to solve (integrate) the differential equation for understanding the evolution of the physical (dynamical) system

## Slide 6: Reminder: Harmonic oscillator
with
u
u
A linear restoring force (Harmonic oscillator) is described by

## Slide 7: Reminder: Harmonic oscillator
A linear restoring force (Harmonic oscillator) is described by
The solution obtained by substitution
with

## Slide 8: Reminder: Harmonic oscillator
A linear restoring force (Harmonic oscillator) is described by
The solution obtained by substitution
  through the characteristic polynomial , which yields the general solution
with the ”velocity”
with

## Slide 9: Reminder: Harmonic oscillator
A linear restoring force (Harmonic oscillator) is described by
The solution obtained by substitution
  through the characteristic polynomial , which yields the general solution
with the ”velocity”
Note that a negative sign in the differential equation provides a solution described by hyperbolic sine/cosine functions
Note also that for no restoring force , the motion is unbounded
with

## Slide 10: Matrix solution
The amplitude and phase depend on the initial conditions
The solutions can be re-written thus as

## Slide 11: Matrix solution
The amplitude and phase depend on the initial conditions
The solutions can be re-written thus as
or in matrix form

## Slide 12: Matrix solution
The amplitude and phase depend on the initial conditions
The solutions can be re-written thus as
or in matrix form
By replacing and , this becomes the solution of a quadrupole (see Transverse Linear Beam Dynamics lectures)

## Slide 13: Matrix formalism
General transfer matrix from s0 to s
Note that
which is always true for conservative systems (”energy” is constant)
Note also that

## Slide 14: Matrix formalism
General transfer matrix from s0 to s
Note that
which is always true for conservative systems (”energy” is constant)
Note also that
The general solution can be built by a series of matrix multiplications
from s0 to s1
from s0 to s2
from s0 to s3
from s0 to sn
…
S0
S1
S2
S3
Sn-1
Sn
(see Transverse Linear Beam Dynamics lectures)

## Slide 15: Integral of motion
Rewrite the differential equation of the harmonic oscillator as a pair of coupled 1st order equations

## Slide 16: Integral of motion
Rewrite the differential equation of the harmonic oscillator as a pair of coupled 1st order equations.
  By dividing the two sides of the equations, they can be combined to provide
  and by integrating
  with an integral of motion
  identified as the mechanical energy of the system

## Slide 17: Integral of motion
The equation describes in general an ellipse in phase space
see link
Solving the previous equation for , the system can be reduced to a first order equation

## Slide 18: Integration by quadrature
The last equation can be solved as an explicit integral or “quadrature”
  , yielding
  or the well-known solution

## Slide 19: Integration by quadrature
The last equation can be solved as an explicit integral or “quadrature”
  , yielding
  or the well-known solution
Note: Although the previous route may seem complicated, it becomes more natural when non-linear terms appear, where an ansatz of the type is not applicable

## Slide 20: Integration by quadrature
The last equation can be solved as an explicit integral or “quadrature”
  , yielding
  or the well-known solution
Note: Although the previous route may seem complicated, it becomes more natural when non-linear terms appear, where an ansatz of the type is not applicable
The ability to integrate a differential equation is not just a nice mathematical feature, but deeply characterizes the dynamical behavior of the system described by the equation

## Slide 21: Frequency of motion
The period of the harmonic oscillator is calculated through the previous integral after integration between two extrema (when the velocity vanishes), i.e. :

## Slide 22: Frequency of motion
The period of the harmonic oscillator is calculated through the previous integral after integration between two extrema (when the velocity vanishes), i.e. :
The period (or the frequency) of linear systems is independent of the integral of motion (energy)

## Slide 23: Frequency of motion
The period of the harmonic oscillator is calculated through the previous integral after integration between two extrema (when the velocity vanishes), i.e. :
The period (or the frequency) of linear systems is independent of the integral of motion (energy)
Note that this is not true for non-linear systems, e.g. for an oscillator with a non-linear restoring force
The integral of motion is and the
integration yields

## Slide 24: Frequency of motion
The period of the harmonic oscillator is calculated through the previous integral after integration between two extrema (when the velocity vanishes), i.e. :
The period (or the frequency) of linear systems is independent of the integral of motion (energy)
Note that this is not true for non-linear systems, e.g. for an oscillator with a non-linear restoring force
The integral of motion is and the
integration yields
This means that the period (frequency) depends on the integral of motion (energy) i.e. the maximum “amplitude”

## Slide 25: The pendulum
An important non-linear equation which can be integrated is the one of the pendulum, for a string of length L and gravitational constant g
For small displacements it reduces to a harmonic oscillator with frequency
By appropriate substitutions, this becomes the equation of synchrotron motion (see Longitudinal beam dynamics lectures)

## Slide 26: Solution for the pendulum
The integral of motion (scaled energy) is
and the quadrature is written as assuming that for

## Slide 27: Solution for the pendulum
The integral of motion (scaled energy) is
and the quadrature is written as assuming that for
Using the substitutions with , the integral is
and can be solved using Jacobi elliptic functions:
with “ ” representing the Jacobi elliptic sine

## Slide 28: Solution for the pendulum
Minima and maxima of the potential correspond to stable and unstable fixed points

## Slide 29: Period of the pendulum
For recovering the period, the integration is performed between the two extrema, i.e. and , corresponding to and

## Slide 30: Period of the pendulum
For recovering the period, the integration is performed between the two extrema, i.e. and , corresponding to and
The period is i.e. the complete elliptic integral multiplied by four times the period of the harmonic oscillator

## Slide 31: Period of the pendulum
For recovering the period, the integration is performed between the two extrema, i.e. and , corresponding to and
The period is i.e. the complete elliptic integral multiplied by four times the period of the harmonic oscillator
By expanding with , the “amplitude” dependence of the frequency becomes apparent

## Slide 32: Period of the pendulum
The deviation from the linear approximation becomes important at large amplitudes
The dependence of frequency with amplitude (spread) is useful for (Landau) damping (“beam”) instabilities

## Slide 33: Langrangian and Hamiltonian
Notes: Tabor 53-54

## Slide 34: Lagrangian formalism
Describe motion of particles in qn coordinates (n degrees of freedom) from time t1 to time t2
It can be achieved by the Lagrangian function with the generalized coordinates and the generalized velocities
Notes: Tabor 53-54

## Slide 35: Lagrangian formalism
Describe motion of particles in qn coordinates (n degrees of freedom) from time t1 to time t2
It can be achieved by the Lagrangian function with the generalized coordinates and the generalized velocities
The Lagrangian is defined as , i.e. difference between kinetic and potential energy
The integral defines the action
Hamilton’s principle: system evolves so as the action becomes extremum (principle of stationary action)
Notes: Tabor 53-54

## Slide 36: Euler- Lagrange equations
By using Hamilton’s principle, i.e. , over some time interval t1 and t2 for two stationary points (see appendix), the following differential equations for each degree of freedom are obtained, the Euler-Lagrange equations
Notes: Tabor 53-54

## Slide 37: Euler- Lagrange equations
By using Hamilton’s principle, i.e. , over some time interval t1 and t2 for two stationary points (see appendix), the following differential equations for each degree of freedom are obtained, the Euler-Lagrange equations
In other words, by knowing the form of the Lagrangian, the equations of motion can be derived
Notes: Tabor 53-54

## Slide 38: Lagrangian mechanics
For a simple force law contained in a potential function, governing motion among interacting particles, the (classical) Lagrangian is (or as Landau-Lifshitz put it “experience has shown that…”)
For velocity independent potentials, Lagrange equations become i.e. Newton’s equations.
Notes: Tabor 53-54

## Slide 39: From Lagrangian to Hamiltonian
Some disadvantages of the Lagrangian formalism:
  No uniqueness: different Lagrangians can lead to same equations
  Physical significance not straightforward (even its basic form given more by “experience” and the fact that it actually works that way!)
Note: The (relativistic) Lagrangian is very useful in particle physics (invariant under Lorentz transformations)
Notes: Tabor 48-52

## Slide 40: From Lagrangian to Hamiltonian
Some disadvantages of the Lagrangian formalism:
  No uniqueness: different Lagrangians can lead to same equations
  Physical significance not straightforward (even its basic form given more by “experience” and the fact that it actually works that way!)
Note: The (relativistic) Lagrangian is very useful in particle physics (invariant under Lorentz transformations)
Lagrangian function provides in general second order differential equations (coordinate space)
Already observed advantage to move to system of first order differential equations, which are more straightforward to solve (phase space)
Derived by the Hamiltonian of the system
Notes: Tabor 48-52

## Slide 41: Hamiltonian formalism
The Hamiltonian of the system is defined as the Legendre transformation of the Lagrangian where the generalised momenta are
Notes: Tabor 53-54

## Slide 42: Hamiltonian formalism
The Hamiltonian of the system is defined as the Legendre transformation of the Lagrangian where the generalised momenta are
The generalised velocities can be expressed as a function of the generalised momenta if the previous equation is invertible, and thereby define the Hamiltonian of the system
Notes: Tabor 53-54

## Slide 43: Hamiltonian formalism
The Hamiltonian of the system is defined as the Legendre transformation of the Lagrangian where the generalised momenta are
The generalised velocities can be expressed as a function of the generalised momenta if the previous equation is invertible, and thereby define the Hamiltonian of the system
Example: consider
From this, the momentum can be determined as which can be trivially inverted to provide the Hamiltonian
Notes: Tabor 53-54

## Slide 44: Hamilton’s equations
The equations of motion can be derived from the Hamiltonian following the same variational principle as for the Lagrangian (“stationary” action) but also by simply taking the differential of the Hamiltonian (see appendix)
Notes: Tabor 53-54

## Slide 45: Hamilton’s equations
The equations of motion can be derived from the Hamiltonian following the same variational principle as for the Lagrangian (“stationary” action) but also by simply taking the differential of the Hamiltonian (see appendix)
These are indeed equations describing the motion in the “extended” phase space
Notes: Tabor 53-54

## Slide 46: Properties of Hamiltonian flow
The variables are called canonically conjugate (or canonical) and define the evolution of the system in phase space
These variables have the special property that they preserve volume in phase space, i.e. satisfy the well-known Liouville’s theorem
The variables used in the Lagrangian do not necessarily have this property
Notes: Tabor 53-54

## Slide 47: Properties of Hamiltonian
The variables are called canonically conjugate (or canonical) and define the evolution of the system in phase space
These variables have the special property that they preserve volume in phase space, i.e. satisfy the well-known Liouville’s theorem
The variables used in the Lagrangian do not necessarily have this property
Hamilton’s equations can be written in vector form with and
The matrix is called the symplectic matrix
Notes: Tabor 53-54

## Slide 48: Poisson brackets
Crucial step in study of Hamiltonian systems is identification of integrals of motion
Consider a time dependent function of phase space. Its time evolution is given by
where is the Poisson bracket of with
Notes: Tabor 48-52

## Slide 49: Poisson brackets
Crucial step in study of Hamiltonian systems is identification of integrals of motion
Consider a time dependent function of phase space. Its time evolution is given by
where is the Poisson bracket of with
If a quantity is explicitly time-independent and its Poisson bracket with the Hamiltonian vanishes (i.e. commutes with ), it is a constant (or integral) of motion (as an autonomous Hamiltonian itself)
Notes: Tabor 48-52

## Slide 50: Summary of Lecture I
2nd order dif. equations of motion from Newton’s law (configuration space) can be solved by transforming them to pairs of 1st order ones (in phase space)
Natural appearance of invariant of motion (“energy”)
Non-linear oscillators have frequencies which depend on the invariant (or “amplitude”)
Connected invariant of motion to system’s Hamiltonian (derived through Lagrangian)
Shown that through the Hamiltonian , the equations of motions can be derived
Poisson bracket operators are helpful for discovering integrals of motion

## Slide 51: Appendix

## Slide 52: Derivation of Lagrange equations
The variation of the action can be written as
Taking into account that , the 2nd part of the integral can be integrated by parts giving
The first term is zero because so the second integrant should also vanish, providing the following differential equations for each degree of freedom, the Lagrange equations
Notes: Tabor 53-54

## Slide 53: Derivation of Hamilton’s equations
The equations of motion can be derived from the Hamiltonian following the same variational principle as for the Lagrangian (“least” action) but also by simply taking the differential of the Hamiltonian
Notes: Tabor 53-54

## Slide 54: Derivation of Hamilton’s equations
The equations of motion can be derived from the Hamiltonian following the same variational principle as for the Lagrangian (“least” action) but also by simply taking the differential of the Hamiltonian or
By equating terms, Hamilton’s equations are derived
These are indeed equations describing the motion in the “extended” phase space
Notes: Tabor 53-54

## Slide 55: Poisson brackets’ properties
The Poisson brackets between two functions of a set of canonical variables can be defined by the differential operator
Notes: Tabor 48-52

## Slide 56: Poisson brackets’ properties
The Poisson brackets between two functions of a set of canonical variables can be defined by the differential operator
From this definition, and for any three given functions, the following properties can be shown bilinearity
anticommutativity
Jacobi’s identity
Leibniz’s rule
Poisson brackets operation satisfies a Lie algebra
Notes: Tabor 48-52