## Slide 1
General Introductory Course, Santa Susanna (ES), 2025
Time & Frequency Domain Signals & Measurements
H.Schmickler, ex-CERN
With slides from:
M.Gasior, R.Jones, M.Wendt
(CERN)

## Slide 2
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to post them on the CAS website.
The author hereby confirms that to his best knowledge the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution. Nevertheless the material represent entirely standard teaching material known for more than ten years. Naturally some figures will look alike those produced by other teachers.
Copyright statement and speaker’s release for video publishing

## Slide 3
Introduction: What Is time domain and frequency domain?
Fourier synthesis and Fourier transform
Time domain sampling of electrical signals ( ADCs)
Bunch signals in time and frequency domain a) single bunch single pass b) single bunch multi pass (circular accelerator) c) multi bunch multi pass (circular accelerator)
Oscillations within the bunch (head-tail oscillations)  advanced course
Part I

## Slide 4
Fourier transform of time sampled signals a) basics
  b) aliasing c) windowing
Methods to improve the frequency resolution a) interpolation b) fitting (the NAFF algorithm) c) influence of signal to noise ratio d) special case: no spectral leakage + IQ sampling
Analysis of non stationary signals/spectra: - STFT (:= Short time Fourier transform) (Gabor transform) also called: Sliding FFT, Spectrogram - multi-BPM combined signal analysis
  - PLL tune tracking - wavelet analysis (if time permits, not really relevant for accelerators, but really cool stuff)
Part II

## Slide 5: Introduction 1/3
At first: everything happens in time domain, i.e. we exist in a 4D world, where 3D objects change or move as a function of time.
And we have our own sensors, which can watch this time evolution: eyes  bandwidth limit: 1 Hz
For faster or slow processes we develop instruments to capture events and look at them: oscilloscopes, stroboscopes, cameras…

## Slide 6: Introduction 2/3
But we have another sensor: ears
What is this?

## Slide 7: Introduction 3/3
Once we perceive the material in frequency domain (our brain does this for us), we can better understand the material.
Non matter whether we describe a phenomenon in time domain or in frequency domain, we describe the same physical reality. But the proper choice of description improves our understanding!

## Slide 8: Jean Baptiste Joseph Fourier (1768-1830)
Had a crazy idea (1807):
 Any periodic function can be rewritten as a weighted sum of Sines and Cosines of different frequencies
Don’t believe it?
  Neither did Lagrange, Laplace, Poisson and other big wigs
  Not translated into English until 1878!
But it’s true!
  called Fourier Series
  Possibly the greatest tool
  used in Engineering

## Slide 9: Fourier Series
A periodic function f(x) can be expressed as a series of harmonics, weighted by Fourier coefficients cn

## Slide 10: What about non-periodic functions ?
Mathematically this is « interesting »
Physicists « just assume it works »
1) In a time limited window any non periodic function can be expressed as Fourier series. Problem: Outside this window the function reproduces, since the sinus and cosinus functions are periodic and infinite.
2) In an infinite time window there are functions for which a Fourier series does not converge. But those seem to be irrelevant for the description of physical problems.
 Just do it
The tool: Fourier Transforms of time domain functions (next slide)

## Slide 11
Note:
Fourier Transforms (FT)
There is also the term FFT := Fast Fourier Transform This is nothing else than a DFT with N=2m; useful to speed up the computation

## Slide 12: Fourier Transform Pairs
Image taken from
https://wiki.seg.org/wiki/Dictionary:Fourier_transform
Will use this when we come to “windowing”
Gaussian gives a Gaussian!
Not surprising
Somewhat surprising!
Remember this when we will treat bunches!

## Slide 13: Time pulse = infinite spectrum of sin-waves
A pulse at t=0 corresponds to an overlap of an infinite number of sin-waves with all possible frequencies of infinite length!
In the example at left a base wave is generated and then new waves are added each time with a 1% higher frequency.
Nice example to show that a correct mathematical model not necessarily corresponds to reality!
Imagine an electrical pulse of a generator: The waves generated should already have existed before the generator was built!
So “infinity” is not always “infinity”

## Slide 14: Now we need some definitions in order to treat particle bunches
In real accelerators not all available RF-buckets are filled with particle bunches. - a gap must be left for the injection/extraction kickers
- Physics experiments can impose a minimum bunch distance, which is larger than one RF period (i.e. LHC)
Revolution frequency: ωrev = 2π frev
RF frequency: ωRF = 2π fRF = h* ωrev (h=harmonic number)
Bunch Repetition frequency: ωrep = 2π frep = ωRF /n (n= number of RF buckets between bunches)
(frep = 1/bunch spacing)

## Slide 15: Example LHC beam

## Slide 16: Single bunch single pass
Time and frequency domain description
Measurement of bunch length in time domain
 Sampling electrical signals with ADCs
Measurement of bunch length in frequency domain
Understanding beam signals in time and frequency domain
We start with:

## Slide 17: Particle beam with gaussian longitudinal distribution
A0, pick amplitude
σt
bunch length
σf
Time domain
Frequency domain

## Slide 18: Bunched beam longitudinal signal shape I
In many cases the description of the longitudinal bunch signal as “Gaussian” is adequate and sufficient. Depending on the study, more sophisticated descriptions are needed (next slide).
Typical bunch length for circular (high energy accelerators):
Protons: ~50 ns…0.5 ns (LHC) electrons: 1ns … ~10 ps (LEP)…10 fs (FEL)

## Slide 19: Bunched beam longitudinal signal shape II

## Slide 20: Beam Intensity Measurement in time domain
Sampling (=measurement) of an electrical signal in regular time intervals. The electrical signal is obtained from a monitor, which is sensitive to the particle intensity.

## Slide 21
Time domain observation of a
“short” electrical pulse
Ver: 50 mV/div, Hor: 2 ns/div
2 pairs of 10 mm button electrodes
Most often one uses an « oscilloscope », i.e. an electronic device that measures at a regular time-interval (called sampling-time) the applied voltage and converts it internally into a numerical sample. Keyword: ADC:= Analog Digital Converter
Example below: 4 « button » signals of a beam position monitor in the CERN SPS. Note the « red and yellow » signals have been artificially delayed in a cable for better visibility of the signals

## Slide 22: ADC performance chart (2015!!!)

## Slide 23: Frequency domain measurement
Pulses (bunches) can become very short in electron linacs (as low as a few femto-seconds)
This corresponds to a frequency content in the THz domain
No way to mesure any time domain signal (see last chart)
Make use of electromagnetic radiation and try to get information through optical ( ex: streak camera) or RF signals
Next slide example of a linac with pulses in the ps domain

## Slide 24: Frequency domain measurement of single bunch
Nice example from R&D work in CTF3 (CERN)
A.Dabrowski et al., Proc of PAC07, FRPMS045
Primary signal is EM wave of beam extracted through a thin window
Subdivision into 4 frequency bands
Measurement of rms amplitude in the 4 bands

## Slide 25: CTF3 results
Time domain measurements of 4 bands
FFT of down-converted signals
fit

## Slide 26: Deeper Analysis of bunch signals
After these introductory remarks we shall look at signals produced in an accelerator and understand them:
Single bunch single passage: Already done
Now to come:
2. Single bunch - multi pass
3. Multi bunch – multi pass…is a bit mind boggling, but still very relevant  complete slides as appendix

## Slide 27: Single bunch multi pass (circular accelerator)
Time domain
Frequency domain
frev
2frev
Remember:

## Slide 28: Understanding the revolution harmonics
The continuous spectrum of a single bunch passage becomes a line spectrum.
The line spacing is frev= 1/Trev . (Trev = revolution time)
The amplitude envelope of the line spectrum is the “old” single pass frequency domain envelope of the single bunch.
Why? - short answer: Do the Fourier transform! - long answer: Understand in more detail 2,3,4…N consecutive bunch passages in time and frequency domain (next slides)

## Slide 29: Bunch pattern simulations (1/4)
1 bunch 0.5 nsec
2 bunches
0.5 nsec
Δt = 5 nsec
Frequencies in this range make a constructive interference (no phase difference)
Frequencies in this range cancel each other (1800 phase difference)
Other frequencies intermediate summation/cancelation

## Slide 30: Bunch pattern simulations (2/4)
Δt= 5 nsec
Δt= 10 nsec
Δt= 20 nsec
First harmonic @ 200 MHz
First harmonic @ 100 MHz
First harmonic @ 50 MHz

## Slide 31: Bunch pattern simulations (3/4)
From top to bottom:
3, 5, 10 bunches (0.5nsec long, Δt = 10 nsec)

## Slide 32: Last bunch pattern simulation
100 equidistant bunches (Δt = 10 nsec)
Resulting spectrum is a line spectrum with the fundamental line given by the inverse of the bunch distance

## Slide 33
  Circular accelerator
    Beam signal periodic with revolution frequency: wrev
  Spectral components at:
A Measured Longitudinal beam spectrum
wrev
Spectrum of single bunch
Multi-bunch beam
wRF
2wRF
3wRF
Bunch not Gaussian.
Somewhat between triangular and parabolic

## Slide 34: LHC longitudinal frequency spectrum

## Slide 35: And if this was not enough: amplitude modulation of bunch signals
m= modulation index 0…1 (Venv = Vc)
Using trigonometric identity:
Any amplitude modulation in time domain leads to sidebands in frequency domain

## Slide 36: Relevant example of amplitude modulation: stimulated betatron oscillation(or: tune measurement) this means an amplitude modulation of the intensity signal by transverse excursions
Beam centre of charge makes small betatron oscillation around the closed orbit (- stimulated by an exciter or by a beam instability)
Depending on the proximity to an EM sensor the measured signal amplitude varies.
taken from R.Jones, proc. of BI-CAS 2018

## Slide 37
taken from R.Jones, proc. of BI-CAS 2018

## Slide 38: One bunch/several bunches?
In the case of more than one bunch (N) in the accelerator (assume equal intensities filled at equal distances!) one cannot distinguish between - an accelerator with 1 bunch and a revolution time of trev - an accelerator with N bunches and a revolution time of trev /N
!

## Slide 39: Multi-bunch multi-pass
If one has N bunches of equal intensity circulating in an accelerator with Trev and those bunches only move coherently without any phase difference, then this is undistinguishable from an accelerator with Trev/N as revolution time and one bunch in this accelerator
In reality the oscillations of individual bunches are not correlated and in consequence the time domain and frequency domain signals get really mind-boggling.
The study of these oscillations is important in case of multi-bunch instabilities or in case of the design of transverse active feedback systems

## Slide 40: Why do we worry about this?
The additional bunches will create additional spectral lines in frequency domain. Depending on the number of bunches the spacing between these lines can become so narrow, such that overlap of the beam spectral lines with the resonance of structures around the beam pipe (HOM modes of cavities for example) can excite the beam to oscillations.
This can lead to beam blow up or even particle losses.

## Slide 41
Multi-bunch modes: 10 stable bunches
Ten identical equally-spaced stable bunches
The spectrum is a repetition of frequency lines at multiples of the bunch repetition frequency: wrep = 10 wrev (bunch repetition frequency)
. . . . .
. . . . .
wrep
2wrep
3wrep
-wrep
-2wrep
-3wrep
0
Pickup

## Slide 42
Multi-bunch modes: 10 unstable bunches (m=0)
Ten identical equally-spaced unstable bunches oscillating at the tune frequency nw0 (n = 0.25)
M = 10  there are 10 possible modes of oscillation
Ex.: mode #0 (m = 0) DF=0 all bunches oscillate with the same phase
Pickup
m = 0, 1, .., M-1
wrep/2
0
wrev
2wrev
4wrev
Mode#0
3wrev

## Slide 43
Ex.: mode #1 (m = 1) DF = 2p/10 (n = 0.25)
w = pwrep ± (n+1)wrev - < p < 
wrep/2
0
wrev
2wrev
4wrev
Mode#1
3wrev
Pickup
Multi-bunch modes: 10 unstable bunches (m=1)

## Slide 44
Multi-bunch modes: summary (10 bunches)
If the bunches have not the same charge, i.e. the buckets are not equally filled (uneven filling), the spectrum has frequency components also at the revolution harmonics (multiples of wrev). The amplitude of each revolution harmonic depends on the filling pattern of one machine turn
wrep/2
0
wrev
2wrev
4wrev
9
3wrev
8
7
6
5
1
2
3
4
0
wrep
6wrev
7wrev
9wrev
4
8wrev
3
2
1
0
6
7
8
9
5
Lower sidebands of first revolution harmonics

## Slide 45
ELETTRA Synchrotron: frf=499.654 Mhz, bunch spacing≈2ns, 432 bunches, f0 = 1.15 MHz
nhor= 12.30(fractional tune frequency=345kHz), nvert=8.17(fractional tune frequency=200kHz) nlong = 0.0076 (8.8 kHz)
Spectral line at 512.185 MHz
Lower sideband of 2frf, 200 kHz apart from the 443rd revolution harmonic
 vertical mode #413
200 kHz
Rev. harmonic
Vertical mode
#413
Spectral line at 604.914 MHz
Upper sideband of frf, 8.8kHz apart from the 523rd revolution harmonic
 longitudinal mode #91
Rev. harmonic
Long. mode
#91
8.8kHz
Real example of multi-bunch modes

## Slide 46
Fourier transform of time sampled signals a) recap of basics
  b) aliasing  limitation of usable bandwidth to 50% of sampling frequency c) windowing
Methods to improve the frequency resolution a) interpolation b) fitting (ex: NAFF algorithm) c) influence of signal to noise ratio
Analysis of non stationary signals/spectra: - STFT (:= Short time Fourier transform) (Gabor transform) also called: Sliding FFT, Spectrogram - multi-BPM combined signal analysis - PLL tune tracking - wavelet analysis (if time permits, not really relevant for accelerators, but really cool stuff)
Part II

## Slide 47
Discrete Fourier Transform basics
Discrete Fourier Transforms
In general: We use DFTs of N equidistant time sampled signals; A FFT (Fast Fourier transform) is a DFT with N= 2k

## Slide 48: Aliasing
Periodic signals, which are sampled with at least 2 samples per period, can be unambiguously reconstructed from the frequency spectrum. (Nyquist-Shannon Theorem)
In other words, with a DFT one only obtains useful information up to half the sampling frequency.
Antialiasing filters need to be inserted upstream of the sampling in order to suppress unwanted higher spectral information.

## Slide 49: Spectral leakage caused by windowing
By measuring a continuous signal only over a finite length, we apply a “data window” to signal, which leads to spectral artefacts in frequency domain.

## Slide 50: Windowing = Convolution of continuous signal with window function
Recall: The Fourier transform of a product in time domain is the convolution of the individual Fourier transforms in Frequency domain

## Slide 51: Rectangular window example
signal = amp1* sin (2π ω1t) + amp2 * sin(2π ω2t)
amp1 =1
amp2=0.01
ω1= 2π * 9990 Hz
ω2= 2π * 10010 Hz
The small signal component is completely masked by the sidelobe of the large signal
ZOOM
FFT

## Slide 52: Applying the Blackman-Harris window
signal = window * amp1* sin (2π ω1t) + amp2 * sin(2π ω2t)
amp1 =1
amp2=0.01
ω1= 2π * 9990 Hz
ω2= 2π * 10010 Hz
The small signal component is nicely resolved
ZOOM
FFT

## Slide 53: Popular window functions
The following link contains many frequently used window functions, their main features and application:
https://en.wikipedia.org/wiki/Window_function
The actual choice of the window depends on:
The signal composition
The required dynamic range
The signal to noise ration remark: every window except the rectangular window is linked to a loss in amplitude (we multiply many samples with almost “zero”)  reduced S/N up to 6 dB

## Slide 54: Improving the frequency resolution of a DFT spectrum
Recall: basic frequency resolution: Δf = 2*fsamp/Nsamp
We can interpolate between the frequency bin with maximum content and the left and right neighbouring bins
We limit the discussion to “three point interpolation methods”
The interpolation function is either:
A) a parabola of the measurements (:= parabolic interpolation) B) a parabola of the log of the measurements (:= Gaussian interpolation)
Can get up to 1/N2 resolution
Details: https://mgasior.web.cern.ch/mgasior/pap/FFT_resol_note.pdf

## Slide 55: Improving the frequency resolution of a DFT spectrum
from: https://mgasior.web.cern.ch/mgasior/pap/FFT_resol_note.pdf

## Slide 56: Even higher frequency resolution: fitting the data
Assume a model function for the data (sample 1…N) (i.e. in the most simple case a monochromatic sin wave), in general samplei =f (i * Δt)
Get frequency and peak (or interpolated peak) from FFT: fmax and amax
Minimize: 2 – (amax * sin (2πfmax * Δt))2 by varying amax and fmax (NAFF algorithm:= Numerical Analysis of Fundamental Frequencies  NAFF algorithm can get up to 1/N4 resolution)
Very good convergence for noise free data (i.e. predominantly in simulations)

## Slide 57: A little summary on frequency resolution
Frequency measurement error ε(N) as function of log (N) for different S/N ratios
Basic FFT resolution proportional to 1/N
Plot shows result for interpolation using Hanning window.
With interpolation and no noise proportional to 1/N2
Data fitting (NAFF algorithm ) also very sensitive to S/N
1/N
1/N2
Taken from: R. Bartolini et al, Precise Measurement of the Betatron tune, Proceedings of PAC 1995, Vol. 55, pp 247-256

## Slide 58: Special case: no spectral leakage
The FFT of the so called background signal has no spectral leakage!!!!
All pictures: M.Gasior

## Slide 59: Special case continued:
In the shown example the following relation holds: = (ratio of rational numbers)
This means that with the 1024 samples exactly 110 full periods of the background signals have been measured.
The mathematical equivalent is that we have not applied a window function (no truncation), we get as result of the FFT the pure sine wave corresponding to the background frequency.
In accelerators we often know the frequency of a signal for which we want to measure the amplitude (=multiple of RF frequency)  we can avoid spectral leakage.
Important application of 4: IQ-sampling at 4*f (next slide)

## Slide 61: Other method: Network analysis
Excite beams with a sinusoidal carrier
Measure beam response
Sweep excitation frequency slowly through beam response

## Slide 62: Analysis of non-stationary spectra
Stationary Signal
  Signals with frequency content unchanged in time
  All frequency components exist at all times  ideal situation for Fourier transform (FT) ( orthonormal base functions of Fourier transform are infinitely long, no time information when spectral component happens)
Non-stationary Signal
  Frequency composition changes in time  need different analysis tools
  Illustration on the 3 following slides

## Slide 63: Example of non-stationary signals
Two stationary signals (single frequency) changing at one point in time.
Blue: lower freqeuncy first
Red: higher frequency first.
FT spectra identical; impossible to say which signal was first.

## Slide 64: Sliding time window (and FT each time window advances)
Originally called Short Time Fourier Transform (STFT) or spectrograms

## Slide 65: Spectrogram of two consecutive signals at two distinct frequencies

## Slide 66
Short Time Fourier Analysis
In order to analyze small section of a signal, Dennis Gabor (1946), developed a technique, based on the FT and using windowing : Short Time Fourier Transform:= STFT
A compromise between time-based and frequency-based views of a signal.
both time and frequency are obtained in limited precision.
The compromise between time and frequency resolution is given by the length of the time window.
Usually one chooses a fixed length of the observation window during the analysis.

## Slide 67
3D view
Not much readable information, but nice for publications

## Slide 68
STFT Measurement examples I
A trace of a transverse tune signal over several seconds during the energy ramp of the CERN SPS proton accelerator.

## Slide 69: STFT Measurement Examples II
Even older:
Left: horizontal and vertical tunes during LEP acceleration Right: Machine experiment: all 3 tunes and synchro-betatron coupling

## Slide 70: Some more cool stuff:
Sampling in time and space in a circular accelerator + retransform of data as new set of samples only in time, but at a higher sampling frequency.
Phase locked loop measurements of a single frequency (this way “in the old days” a radio receiver worked); if you still now what this is?
Wavelet analysis; not really used in accelerators, but used for example to find oilfields!

## Slide 71: A recent development: MultiBPM analysis
P.Zisopoulos et al, Phys. Rev. Acc.&Beams 22, 071002 (2019)
Refined betatron tune measurements by mixing BPM data
Basic idea: Create additional samples per turn by using data from neighbouring BPMs (up to 500 in the LHC) and transforming them from samples in space to samples in time.

## Slide 72: MultiBPM: Result for CERN-PS
During the injection process into the CERN PS strong orbit deflectors are activated. In addition to the wanted orbit change this leads also to an unwanted tune change: Needs to be measured
Single BPM measurements do not have enough time resolution at high frequency resolution  use several BPMs
With remarkable resolution for 40 turns

## Slide 73: recall: Network analysis (BTF:=Beam transfer function)
So far all methods use exclusively the amplitude information (BTW: in the case of self excited oscillations this is the only way!)
But if you drive a betatron oscillation of the beam oscillation through an external force, one can use the phase between the exciter and the beam response as observable
BTF

## Slide 74
What is Wavelet Analysis ?
And…what is a wavelet…?
A wavelet is a waveform of effectively limited duration that has an average value of zero.
In a Fourier transform (FT) we represent the data by the weighted sum of infinite sine waves with different frequencies.
So the “signal analyzing” functions are infinite sine waves.
In the continuous wavelet transform (CWT) we represent the data by the weighted sum of appropriately scaled and shifted wavelets.
So instead of only infinite sine waves we take frequency dependent wavelets (by scaling) and time dependent wavelets (by shifting)
as “two dimensional set of analyzing functions”

## Slide 75
Wavelet Scaling
Time stretching or frequency scaling:

## Slide 76
Wavelet Shifting
Time shifting:

## Slide 77
Wavelet Analysis by Shifting and Scaling

## Slide 78: Historical Development of wavelet transforms (main contributors)
Pre-1930
  Joseph Fourier (1807) with his theories of frequency analysis
The 1930s
  Using scale-varying basis functions; computing the energy of a function
1960-1980
  Guido Weiss and Ronald R. Coifman; Grossman and Morlet
Post-1980
  Stephane Mallat; Y. Meyer; Ingrid Daubechies; wavelet applications today

## Slide 79: Various transforms
The variables in red are linked to frequency resolution,
the variables in blue to time resolution.

## Slide 80: COMPARSION in terms of time and frequency resolution
From http://www.cerm.unifi.it/EUcourse2001/Gunther_lecturenotes.pdf, p.10

## Slide 81: Example (STFT vs WT)
In a continuously sampled sine wave two artefacts (values set to 0) are introduced at two different times.
In the result of the STFT (top trace: Spectrogram) there is no effect visible,
In the result of the WT (bottom trace: Scalogram) the location of the irregularities can be spotted.

## Slide 82: Which tool to use?
(Almost) Stationary Signals: windowed FFT with interpolation/fitting.
!!! Depending on the S/N the gain from very sophisticated methods needs to be evaluated!!!
Non stationary Signals: ω = f(t) - Good S/N + lots of data: STFT (spectrograms) i.e. most of the accelerator applications - Small S/N + few data: (typical examples: instabilities at threshold, effects of kickers, resonance crossing…)
 sampling in time and space + FFT  tracking only the main beam resonance (tune) using phase-lock techniques)

## Slide 83: Summary
Single beam passage in a detector produces a signal with a continuous frequency spectrum. The shorter the bunch, the higher the frequency content.
Repetitive bunch passages produce a line spectrum. The individual spectral lines are called revolution harmonics. Details of the bunch pattern, differences in bunch intensities etc. determine the final spectral distribution.
Transverse or longitudinal oscillations of the bunch around the equilibrium produce sidebands around all revolution harmonics.
These sidebands are used for the measurement of the betatron tunes and/or the synchrotron tune.
The standard tool for obtaining spectral information is a Fourier transform (FFT) of time sampled signals.
Windowing and interpolation allow measurements with higher frequency resolution.
Spectograms or STFTs are consecutive FFTs of larger datasets, which allow to follow time varying spectra. A compromise has to be found between time resolution and frequency resolution.
Phase locked loops can be used for continuous tune tracking, hence one obtains the time evolution of the main beam resonance (tune). No other spectral information!
Wavelet analysis instead of Spectograms are an alternative analysis tool.
This is really useful in the case of few time samples.

## Slide 84: Appendix I: Python Code for bunch pattern display

## Slide 85: Appendix Ia: Python code for bunch pattern simulation 1st part
import numpy as np
from numpy import fft
import matplotlib.pyplot as plt
N=16384
NBUNCH=100
sigmax = 0.5
deltax=10
T=1/N
NLEFT=-50
NRIGHT=50
x1= np.linspace(NLEFT,N-NLEFT,N)
xtime=np.linspace(NLEFT,NBUNCH*deltax + NRIGHT,N)
IB=0
y=NBUNCH*np.exp(-(x1*x1)/(2*sigmax*sigmax))
ytime=NBUNCH*np.exp(-(xtime*xtime)/(2*sigmax*sigmax))
y1=0
y2=0
y3=0
ytime=0
while True:
y1=y1+np.exp(-(x1-IB*deltax)*(x1-IB*deltax)/(2*sigmax*sigmax))
ytime=ytime+np.exp(-(xtime-IB*deltax)*(xtime-IB*deltax)/(2*sigmax*sigmax))
IB=IB+1
if IB==NBUNCH:
break

## Slide 86: Appendix Ib: Python code for bunch pattern simulation 2nd part
ffty=(fft.fft(y))
ffty1=(fft.fft(y1))
x2=np.linspace(0.0,500,N/2)
y2=2.0*np.abs(ffty1[:N//2])/float(N)
y3=2.0*np.abs(ffty[:N//2])/float(N)
plt.rcParams["figure.figsize"] = [15,4]
plt.subplot(1,2,1)
plt.plot(xtime,ytime,'b-')
plt.ylabel('amplitude')
plt.xlabel('time [nsec]')
plt.subplot (1,2,2)
plt.plot (x2,y3,'r-')
plt.plot (x2,y2,'b-')
plt.ylabel('amplitude')
plt.xlabel('frequency [MHz]')
plt.tight_layout()
plt.savefig (‘whatever.png')
plt.show()

## Slide 87: Appendix II
Tune tracking with PLL technique

## Slide 88: recall: Network analysis (BTF:=Beam transfer function)
So far all methods use exclusively the amplitude information (BTW: in the case of self excited oscillations this is the only way!)
But if you drive a betatron oscillation of the beam oscillation through an external force, one can use the phase between the exciter and the beam response as observable
BTF

## Slide 89: Principle of PLL tune measurements
Beam
VCO
Voltage controlled oscillator
A sin(t)
BPM
B sin(t+)
Phase detector (=product)
½*AB(cos()-cos(2 t +))
Lowpass
Frequency control:
½*ABcos()
Due to cos () =0 at resonance this system “looks” to the 90 deg. point of the BTF
VCO changes ω until control input ==0
Control system can read tune betatron tune at regular intervals by reading the VCO frequency
Recall: sin a sin b = 1/2 (cos(a − b) − cos(a + b))

## Slide 90: Illustration of PLL tune tracking
A
q

q
Single carrier PLL locks on 900 point of BTF;

## Slide 91: Q’ Measurement via RF-frequency modulation (momentum modulation)
Applied Frequency Shift  F (RF)
 Qh
 Qv
Amplitude & sign of chromaticity
calculated from continuous tune plot

## Slide 92: Measurement example during changes on very strong quadrupoles in the insertion: LEP -squeeze
qh
qv

## Slide 93: Appendix III multibunch – multi passage

## Slide 94: Multi-bunch multi-pass
If one has N bunches of equal intensity circulating in an accelerator with Trev and those bunches only move coherently without any phase difference, then this is undistinguishable from an accelerator with Trev/N as revolution time and one bunch in this accelerator
The time domain and frequency domain signals get really mind-boggling, if the bunches start to do individual uncorrelated betatron oscillations
The study of these oscillations is important in case of multi-bunch instabilities or in case of the design of transverse active feedback systems

## Slide 95
Multi-bunch modes
Let us consider M bunches equally spaced around the ring
Any oscillation pattern of these bunches can be decomposed into a set of eigenmodes of oscillation, the so called multi-bunch modes.
Each multi-bunch mode is characterized by a bunch-to-bunch phase difference of:
m = multi-bunch mode number (0, 1, .., M-1)
Each multi-bunch eigenmode is characterized by a set of frequencies:
Where:
p is and integer number - < p <  ; p=0 = baseband
wrev is the revolution frequency
Mwrev = wrep is the bunch repetition frequency
ν is the tune
Hard to understand like this…needs some graphics

## Slide 96
Multi-bunch modes: single stable bunch
transverse. One single stable bunch
Every time the bunch passes through the pickup ( ) placed at coordinate 0, a pulse with constant amplitude is generated. If we think it as a Dirac impulse, the spectrum of the pickup signal is a repetition of frequency lines at multiple of the revolution frequency: pwrev for - < p < 
wrev
2wrev
3wrev
. . . . .
. . . . .
-wrev
-2wrev
-3wrev
0
Pickup position

## Slide 97
Multi-bunch modes: single oscillating bunch
One single unstable bunch oscillating at the tune frequency nw0: for simplicity we consider a vertical tune n < 1, ex. n = 0.25. M = 1  only mode #0 exists
The pickup signal is a sequence of pulses modulated in amplitude with frequency nw0
Two sidebands at ±nw0 appear at each of the revolution harmonics
wrev
2wrev
3wrev
. . . . .
. . . . .
-wrev
-2wrev
-3wrev
0
Pickup

## Slide 98
Multi-bunch modes: 10 stable bunches
Ten identical equally-spaced stable bunches (M = 10)
The spectrum is a repetition of frequency lines at multiples of the bunch repetition frequency: wrep = 10 wrev (bunch repetition frequency)
. . . . .
. . . . .
wrep
2wrep
3wrep
-wrep
-2wrep
-3wrep
0
Pickup

## Slide 99
Multi-bunch modes: 10 unstable bunches (m=0)
Ten identical equally-spaced unstable bunches oscillating at the tune frequency nw0 (n = 0.25)
M = 10  there are 10 possible modes of oscillation
Ex.: mode #0 (m = 0) DF=0 all bunches oscillate with the same phase
Pickup
m = 0, 1, .., M-1
wrep/2
0
wrev
2wrev
4wrev
Mode#0
3wrev

## Slide 100
Ex.: mode #1 (m = 1) DF = 2p/10 (n = 0.25)
w = pwrep ± (n+1)wrev - < p < 
wrep/2
0
wrev
2wrev
4wrev
Mode#1
3wrev
Pickup
Multi-bunch modes: 10 unstable bunches (m=1)

## Slide 101
wrf/2
0
w0
2w0
4w0
Mode#2
3w0
Ex.: mode #2 (m = 2) DF = 4p/10 (n = 0.25)
w = pwrep ± (n+2)wrev - < p < 
Pickup
Multi-bunch modes: 10 unstable bunches (m=2)

## Slide 102
wrep/2
0
wrev
2wrev
4wrev
Mode#3
3wrev
Ex.: mode #3 (m = 3) DF = 6p/10 (n = 0.25)
w = pwrep ± (n+3)wrev - < p < 
Pickup
Multi-bunch modes: 10 unstable bunches (m=3)

## Slide 103
wrf/2
0
wrev
2wrev
4wrev
Mode#5
3wrev
Ex.: mode #5 (m = 5) DF = p (n = 0.25)
w = pwrep ± (n+5)wrev - < p < 
Pickup
Multi-bunch modes: 10 unstable bunches (m=5)
Mode#5
Aliasing!!!

## Slide 104
wrf/2
0
w0
2w0
4w0
Mode#6
3w0
Ex.: mode #6 (m = 6) DF = 12p/10 (n = 0.25)
w = pwrf ± (n+6)w0 - < p < 
Pickup
Multi-bunch modes: 10 unstable bunches (m=6)

## Slide 105
Multi-bunch modes: summary (10 bunches)
If the bunches have not the same charge, i.e. the buckets are not equally filled (uneven filling), the spectrum has frequency components also at the revolution harmonics (multiples of wrev). The amplitude of each revolution harmonic depends on the filling pattern of one machine turn
wrep/2
0
wrev
2wrev
4wrev
9
3wrev
8
7
6
5
1
2
3
4
0
wrep
6wrev
7wrev
9wrev
4
8wrev
3
2
1
0
6
7
8
9
5
Lower sidebands of first revolution harmonics

## Slide 106
Multi-bunch modes: coupled-bunch instability
One multi-bunch mode can become unstable if one of its sidebands overlaps, for example, with the frequency response of a cavity high order mode (HOM). The HOM couples with the sideband giving rise to a coupled‑bunch instability, with consequent increase of the sideband amplitude
nwrev
Response of a cavity HOM
Effects of coupled-bunch instabilities:
increase of the transverse beam dimensions
increase of the effective emittance
beam loss and max current limitation
increase of lifetime due to decreased Touschek scattering (dilution of particles)
Synchrotron Radiation Monitor showing the transverse beam shape

## Slide 107
ELETTRA Synchrotron: frf=499.654 Mhz, bunch spacing≈2ns, 432 bunches, f0 = 1.15 MHz
nhor= 12.30(fractional tune frequency=345kHz), nvert=8.17(fractional tune frequency=200kHz) nlong = 0.0076 (8.8 kHz)
Spectral line at 512.185 MHz
Lower sideband of 2frf, 200 kHz apart from the 443rd revolution harmonic
 vertical mode #413
200 kHz
Rev. harmonic
Vertical mode
#413
Spectral line at 604.914 MHz
Upper sideband of frf, 8.8kHz apart from the 523rd revolution harmonic
 longitudinal mode #91
Rev. harmonic
Long. mode
#91
8.8kHz
Real example of multi-bunch modes