## Slide 1: Impedance modelling and equipment design
Chiara Antuono, Michela Neroni on behalf of
H. Bursali, E. De La Fuente, M. Diaz, G. Favia, L. Giacomel, I. Karpov, P. Krkotic, A. Lasheen, N. Mounet, B. Salvant, L. Sito, C. Vollinger, M. Zampetakis, C. Zannini.
Many thanks to: W. Andreazza, M. Barnes, G. Bregliozzi, S. Calatroni, A. Perillo Marcone, D. Mirarchi, C. Pasquino, R. Seidenbinder, J. A. Ferreira Somoza, R. Franqueira Ximenes.
11th December 2024, JAP Workshop, Montreux

## Slide 2: Introduction

## Slide 3: Introduction
Equipment degradation or damage due to beam induced heating and/or sparking
Beam quality degradation and beam instabilities
Impedance-induced effects
When facing cross section variations of the vacuum chamber wall, as well as its finite resistivity, charged particles travelling in the accelerator, induce electromagnetic fields mainly left behind the source particle.
 Wakefield
Effect can be quantified through
Beam coupling impedance
Dependent on beam spectrum
Total accelerator impedance
Impedance of single a component
Can be triggered by
FFT
Accurate and up-to-date accelerator impedance model is crucial

## Slide 4: Methodology
It requires close collaboration between impedance team and equipment owners to allocate time needed for impedance validation.
Impedance modelling of each component and optimization
Accelerator impedance model
Electromagnetic simulations
CST Studio Suite®
Beam dynamics simulations
Accurate prediction of accelerator performance
New equipment design
Bench measurements
 Needed for validation of component before any installation
Ʃ
Beam dynamics observations and accelerator upgrades

## Slide 5: Methodology
Beam dynamics observations and accelerator upgrades
Complex loads installation on 630 MHz HOM-couplers - SPS 200 MHz cavity
P. Kramer, PhD Thesis
PSB horizontal instability post LIU
New region explored
SPS dark impedance
E. De La Fuente, et al., HB2023
C. Antuono, et al., IPAC24

## Slide 6: Impedance studies in the CERN complex
 | 2023 | 2024
Unshielded pumping manifold |  | 
Rotary wire scanners |  | 
Injection kicker MKI-cool |  | 
TDIS |  | 
Vacuum modules |  | 
Not limited beam operation with no hardware failure
Limited beam operation with no hardware damage
Limited beam operation with hardware damage
PS
SPS
LHC
Impedance modelling is a constant work on going and it often requires dedicated students' projects.
Here covering impedance related studies and observations in the CERN complex for 2023-24.
Many other accelerator components to be followed up…
 Complete overview for 2025 and HL-LHC in conclusions
Close to limit, requires impedance optimization

## Slide 7: Impedance-related observations in the CERN complex in 2023/24

## Slide 8
Unshielded pumping manifold (PS)
Observations in 2023 and 2024 of high frequency modulation at transition crossing for ion and proton beams (AWAKE)*.
Impedance source identified in high frequency range (1.2 GHz)  vacuum equipment: unshielded pumping manifold.
Close to longitudinal stability limit also for AWAKE beam: about 15-20% margin in longitudinal emittance (~7.5-10% bunch length from linear scaling).
See talk by A. Lasheen at IPP
 Follow up for prototype shield ongoing
E. Vinten, et al., IPAC23
ILHC75ns#3b
28/11/2024
Avoided through emittance blow up
However, uncaptured beam observed at flat top.
Courtesy of J. Flowerdew
Current operational conditions close to the instability limit. Further improvements in beam quality or performance requires impedance optimization.
Combined impedance and beam dynamics study necessary for a full understanding of limitations and possible future bottlenecks.
* Impact on other beams to be evaluated.

## Slide 9
Rotary wire scanners (SPS)
  Following the failure of 4 wire scanners in April 2023, impedance mitigation was put in place with 5 ferrite tiles and RF feedthrough.
 No limitations foreseen if the fork in parking position, thanks to task force study element is fully mitigated.
Wire breakage happened with 4x72b, Nb~1.6e11 p/b  was predicted with accurate impedance simulations and beam induced heating calculations*.
Observations in 2024 run:
Task force impedance study 2023:
RF feedthrough
Fork in parking position
Fork in stuck configuration in July 2024 for one wire scanner (more info on control of fork positioning in BI talk).
strong resonance at 380 MHz, lead to 70% power dissipated on the wire
Up to 10 kΩ
*L. Sito, ABP meeting
*E. De La Fuente, IPP

## Slide 10
LHC injection kickers - MKI-cool
MKI-cool:
2 MKI-cool already installed and successfully tested in 2023 and 2024 in Point 8 (more info in G. Favia talk, “ABT Equipment: Operational Insights and Future Perspective”).
2 more MKI-cool to be installed in Point 8 during YETS24/25.
  Full upgrade of Point 2 with 4 MKI-cool foreseen for LS3 (plus 4 additional spares)
water cooling of RF damper was necessary in view of HL-LHC beams
Reduction of beam induced heating in view of HL-LHC beams required an impedance optimization of the design* verified with simulations and benchmarked through stretched wire measurements.
* M. J. Barnes, et al., IPAC18
* H. Day, PhD Thesis
RF Damper
(ferrite ring)
Magnet
Beam
Screen conductors
Alumina tube
Cooling pipes
Metallization
Courtesy of G. Favia

## Slide 11: TDIS high temperature readings
2023: Unexplained high temperature signals in the RF screen: caused interlocks and limited LHC filling
In the LHC injection beam dumps protection elements are installed, particularly two Target Dump Injection Segmented (TDIS):
  TDIS002 in point 2
  TDIS001 in point 8
Carbajo Perez, David, et al. at IPAC2021
For each TDIS module:
  6 temperature probes : 2 on screen and 4 on jaws
Module A
Module B
Module C
5.8 m

## Slide 12: TDIS high temperature readings
Fast temperature decrease when opening jaws
2023: Unexplained high temperature signals in the: caused interlocks and limited LHC filling
Closed jaw
Closed jaw

## Slide 13: TDIS : correlations with impedance measurements
Impedance measurements*:
  Electro Magnetic (EM) coupling with probes
  Correlations with temperature readings:
    Em coupling higher with closed jaws
    Em coupling higher with screen probes (interlock)
    Em coupling significantly higher for TDIS in point 8 (interlock)
  Unexpected low frequency resonance detected
Visual inspection:
  Presence of non-conformities :
    Partially lost finger contact
    melted spring
L. Giacomel et al. at the 81st IWG
L. Sito et al. at the 92nd IWG

## Slide 14: TDIS: 2023 Vs 2024
2023: Unexplained high temperature signals in the RF screen: caused interlocks and limited LHC filling
2023 TDIS: presence of non-conformities:
  Partially lost finger contact
Spare TDIS were installed:
  supposed to be identical to old 2023 TDIS
2024: significantly lower temperature signals in the RF screen: no limitations in the LHC operation
Different temperature readings behavior might come from non-conformity observed on 2023 TDIS

## Slide 15: TDIS in 2025 Run
2025 TDIS will benefit of several improvements
  Improved shielding of existing screen temperature probes
  Two additional fully shielded screen temperature probes (same as MKIs)
Impedance measurements*:
  Contrary to 2023, no correlations with jaw aperture, probe type and TDIS device
  Moreover, the unexpected low frequency resonance not detected
Development of an accurate impedance model ongoing to investigate the issue (fine details such as RF fingers etc..)
  Preliminary impedance studies in case of finger contact missing:
    Presence of low frequency resonances
    Beam induced power on the probe: factor 4 higher with missing contact
For conformal TDIS no impedance induced issues are expected
* L. Sito, TDIS impedance measurements presented at the 92nd IWG meeting
Courtesy of J. Li
Preliminary model results
Given the findings so far, the issue in 2023 seems to be correlated with the observed non-conformities
Impedance measurements

## Slide 16: LHC vacuum module: incident and impedance understanding
Pipe tube
RF fingers
Tension spring
Presence of two beams
beam offset
defects/irregularities finger spacing
non ideal contact fingers/tube
2023: Pressure spikes during the fill ID 8828 (1.63 1011 p/b – 2358 bunches)
lead to a beam dump and impossibility to fill the LHC
Localized heating on the tension spring of ID212
Impedance studies revealed EM field leakage inducing localized heating on the spring compatible with the spring breakage
beam
In presence of
Intensity limitation posed to 1.6 1011 p/b
1 week downtime for LHC
Big effort to build an accurate impedance model to address the issue
  impedance bench measurements
  impedance simulations
  Analytical computations*
  *E. de la Fuente et al. , A Python package for Beam Induced Heating
More info at the 2023 JAP talk-C.Antuono and P.Krkotic
2023 JAP talk, C.Antuono & P.Krkotic
ID212

## Slide 17: LHC vacuum module in 2024 Run
Intensity limitation posed to 1.6 1011 p/b
Mitigation strategy:
  beam operation:
    intensity limitation at 1.6e11 p/b
    interlock for bunch length lower than 1.2 ns (never achieved)
  Replace/transform the 71 modules in the ID212 spring+fingers with newly designed modules wherever it is possible
Deformable RF fingers (DRF)
Transformed anchored solution
Optimized unshielded bellows
2024 run
24 ID212 with spring+fingers design
No pressure spikes or failure in 2024
YETS 23/24
2023 Run…
71 ID212 modules
YETS 24/25
More info at the 2023 JAP talk-C.Antuono and P.Krkotic
Calculations consider the failure reference heating given by the ID212 modules
2358

## Slide 18: LHC vacuum module in 2025 Run
Beam induced heating at least halved compared to the failure heating of the ID212
1 beam and smaller offset
4 modules with original spring+finger design of ID212
2025 run
YETS 23/24
2023 Run…
71 ID212 modules
YETS 24/25

## Slide 19: LHC vacuum module in 2025 Run
Beam induced heating at least halved compared to the failure heating of the ID212
1 beam and smaller offset
4 modules with original spring+finger design of ID212
2025 run
YETS 23/24
2023 Run…
71 ID212 modules
YETS 24/25
The most critical elliptical modules (bigger apertures 128-53)
significantly less critical compared to circular ID212
failure can still be reached depending on the contact quality
Smaller ID expected to be less critical (C. Zannini talk at Chamonix ‘24)
The bottleneck is the circular ID212
These curves can be lifted up by removing the remained 4 ID212
Do we expect failures from different modules in the critical design spring+fingers?
Expected failure range
2400
2700

## Slide 20
Impact on LHC impedance
 | Longitudinal | Transverse
Unshielded bellows |  | 
DRFs |  | 
TWO CRYST |  | 
Rotated Roman Pots |  | 
CMS Double bellows |  | 
MKIs-cool |  | 
LHC: Impact on stability with p/b is:
  Negligible in transverse
  Acceptable in longitudinal
HL-LHC: longitudinal stability is more critical *
  Higher intensity and HOMs from crab cavities
Machine developments (MD) studies are needed to
  test and refine the impedance model of the LHC
  refine the longitudinal stability limit
MD in 2024 with p/b with 1000 bunches at injection looked promising
  In 2025/26 MDs with increased number of bunches, particularly for HL-LHC, are needed
Devices to be installed during YETS 24-25
*M. Zampetakis's talk at the HiLumi annual meeting
*C. Lannoy’s talk at the HiLumi annual meeting
Vacuum module consolidation
Double crystal experiment in IR3
In only with stable beams
In only for low Intensity-MDs
To be filled, ongoing

## Slide 21: Conclusions
 | 2023
Unshielded pumping manifold | 
Rotary wire scanners | 
Vacuum module | 
TDIS | 
Beam impedance limitations observed in the LHC and injectors during RUN 3
PS
SPS
LHC
2023
Not limited beam operation with no hardware damage
Limited beam operation with hardware damage
2024
Limited beam operation with no hardware damage

## Slide 22: Conclusions
 | 2023
Unshielded pumping manifold | 
Rotary wire scanners | 
Vacuum module | 
TDIS | 
Not limited beam operation with no hardware damage
Limited beam operation with hardware damage
Beam impedance limitations observed in the LHC and injectors during RUN 3
  Most of them have been addressed, particularly thanks to the development of accurate impedance models
PS
SPS
LHC
2024
Limited beam operation with no hardware damage

## Slide 23: Conclusions
 | 2023 | 2024
Unshielded pumping manifold |  | 
Rotary wire scanners |  | 
Vacuum module |  | 
TDIS |  | 
Not limited beam operation with no hardware damage
Limited beam operation with no hardware damage
Limited beam operation with hardware damage
To be followed up for Run 3
Not expected limitations for 1.8e11 p/b
Not expected limitations for MDs with 2.3e11 p/b at inj.
Others… | 2023 | 2024 | 2025/26
Extraction kicker KFA14 |  |  | 
MKP-S |  |  | 
Beam Gas Ionization (BGI) |  |  | 
MKDH |  |  | 
IR7 crystal goniometers |  |  | 
Injection kicker MKI-cool |  |  | 
TCLD |  |  | 
To be followed up for HL
The release of p/b is a key step to further exploit possible limitations during the remaining time of Run 3
  MDs with p/b at injection provide valuable input for refining impedance models and stability limit
Step forward the readiness of HL-LHC
Beam impedance limitations observed in the LHC and injectors during RUN 3
  Most of them have been addressed, particularly thanks to the development of accurate impedance models
2025/26
PSB
PS
SPS
SPS
LHC
LHC
- Mitigation studies (e.g. hardware modifications etc.)
- Continuous monitoring
- Finalizing understanding
- Finalizing installations

## Slide 24: Backup

## Slide 25: Backup

## Slide 26
Titanium coated ceramic rod
NEG coated ceramic cathode
SPS-BGI Impedance Study
Impedance reduction of the beam gas ionization monitors for the CERN SPS
Simulation and RF Measurement Report to Determine the Longitudinal Beam Coupling Impedance in the SPS-BGI
Info from BI team
Courtesy of H. Bursali and J. Storey

## Slide 27: Comparison with simulations
1) Case above the LLD threshold
,
Expected impedance does not explain the observed oscillation amplitude
is expected to be around 4-5 GHz (beam screen cut-off)
Courtesy of M. Zampetakis