## Slide 1: Elliptical cavities simulations for MuCol
Sophie Pierron
Dec. 10th 2024

## Slide 2: Elliptical cavities simulations for MuCol
Constraints to be met :
  A frequency of 704.4 MHz, .
  A cavity length Lacc of
  Limited to 3 cells
An elliptical cavity as an alternative approach
Cells not separated by windows to allow electrical coupling.
Walls are not parallel Reduces the multipactor.
Irises are optimized to minimize the electric peak field.
N.B.: the geometry of the designs shown below is axisymmetrical.

## Slide 3
Elliptical cells (walls are not parallel):
Design ESS, a 5 cells cavity – as reference
cavity end
cavity end
cavity center
β= 0.86 and the resonant frequency is closed to 704 MHz.
ESS cavities designed to minimize Epeak/Eacc .
inner_rint = 62 mm
end_rint = 70 mm
rext = 189 mm
Lacc = 915.05
ESS | Comsol
frequency [MHz] | 704.48 MHz
High beta, β | 0.86
Q0 | Not simulated
Epeak/Eacc | 1,89990683
Bpeak/Eacc | 4.36 E-09 s/m
R/Q [Ω] | 455.84896
an alternative approach
N.B.: rint for the inside radii of the cavity,
rext, for the extrern ones.

## Slide 4: Design with a 3 cells cavity
With tubes at both ends:
- Same elliptical cavity, with β= 0.884, only 3 cells.
Magnetic field (T)
Electric field (V/m)
N.B.: This is an axisymmetric geometry.
- The walls are in copper.
inner_rint = 62.72 mm
end_rint = 77.5 mm
rext = 191.77 mm
Lacc = 3Lcell
where Lcell =
an alternative approach
MuCol 3cells | Comsol
frequency [MHz] | 704.08 MHz
High beta, β | 0.884
Q0 | Not simulated
Epeak/Eacc | 1.9366
Bpeak/Eacc [s/m] | 4. 463 E-09
R/Q [Ω] | 274.1516

## Slide 5: Design with a 3 cells cavity + Windows
Without tube:
- Same elliptical cavity, with β= 0.884 and 3 cells but
closed by two windows in Al.
N.B.: This is an axisymmetric geometry.
The walls are in copper
If the tubes still exist, the RF cavity is enclosed by two Al windows (at either end).
inner_rint = 55.5 mm
end_rint = 78 mm
rext = 188 mm
Lacc = 3 Lcell
where Lcell =
Electric field (V/m)
an alternative approach
MuCol 3cells | Comsol
frequency [MHz] | 704.08 MHz
High beta, β | 0.884
Q0 | Not simulated
Epeak/Eacc | 1.8822
Bpeak/Eacc [s/m] | 4. 01 E-09
R/Q [Ω] | 349.41
Magnetic field (T)

## Slide 6: Comparative work
For a perfect pillbox, where Each cell is separated and walls are parallel, the ratio Epeak/Eacc is 1.55.
The simulation of the pillbox with Comsol gives a bit more (1.59).
an alternative approach
Comsol | Epeak/Eacc
1 cell pillbox | 1.59
ESS 5 cells | 1.8999
3 cells w. tubes | 1.9366
3 cells w.o. tube | 1.8822
In an electrically coupled system, the Epeak/Eacc ratio increases compared with a pillbox cavity, which however does not allow electrical coupling.
Enclosing the 3 cells reduces this ratio from 19.4% to 18.8%.
So, for an electrically coupled system, the 3-cell elliptical cavity with windows gives a “good” Epeak/Eacc ratio.

## Slide 7: Simulation of field emission/breakdown
Next step: Simulating the field emission with an elliptical 3 cells cavity and a pillbox cavity.
We are working with CST to simulate flows of particles.
Simulation of electrons with constant DC E field.
Simulation of electrons in an ECR ion source at 2.45 GHz.

## Slide 8: Questions?
…