## Slide 1: First studies of beam loss distributions from fast instabilities WORK IN PROGRESS
G. Nigrelli1,2,3, M. Boscolo2, G. Broggi1,2,3, R. Bruce1, X. Buffat 1, S. Redaelli1
1 CERN, Geneva, Switzerland,
2 INFN-LNF, Frascati, Italy,
3 Sapienza Università di Roma, Roma, Italy
16/12/2024 FCC-ee MDI meeting
Giulia Nigrelli

## Slide 2: Table of contents
Introduction to Fast Instability
Horizontal Instability Characteristics
Vertical Instability Characteristics
Conclusions
Next steps
2
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 3: Fast instability Introduction
The ring impedance can generate an instability that leads the beam to oscillate coherently with an exponentially growing amplitude, potentially losing the beam within few turns.
A feedback system is under development to damp the instability. However, feedback failures might happen and need to be investigated.
Effects on machine and detectors need to be understood to avoid damage.
Collimation system must protect the machine/detectors also in this scenario and shouldn’t be damaged by it.
If not, both collimation and feedback systems must be improved or the beam must be dumped before any damage occurs.
3
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 4: Simulation setup
Impedance model and single bunch interactions not simulated, but it is under studying within the collective effects group.
Fast instability modeled by 8 exciters, giving dipole kicks, placed along the ring (one per arc, shown as green points).
Exciters are synchronized such that the kicks (H/V) are equally distributed in phase advances across 90° and 180° (smooth
change in amplitude within 1 turn).
The exciter strengths change with time as:
, where is the rise time.
Resulting in betatron oscillations exponentially growing with time.
Performed with Xsuite-BDSIM simulation tool, as for the other collimation studies with combined tracking and scattering routines.
Beam loss distributions along the ring are produced as outputs.
4
IPA
IPF
IPG
IPJ
IPD
IPB
Simulation parameters:
45.6 GeV electrons
(Z-mode).
SR (mean model), RF cavities, magnet tapering.
detailed aperture model, halo and tertiary collimators, SR collimator, wiggler.
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting
Notes: All the kickers are in phase?

## Slide 5: Case studies
Fit of the amplitude growth to the average centroid of the beam.
Since the instability can start at any point, it is relevant to explore the phase dependence.
Exciters shifted along the ring to have four different phase advances between the first exciter and the primary collimator.
16 different cases have been investigated:
5
Rise time |  | 
Horizontal |  | 
Vertical |  | 
Rise time |  | 
Horizontal |  | 
Vertical |  | 
Horizontal: 6 turns
Vertical: 3 turns
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 6: Horizontal instability CHARACTERISTICS
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 7: Transverse beam position at primary collimator
7
The beam oscillates coherently in the horizontal plane until collimator apertures are reached.
This animation does not include scattering in the collimators, so the distribution would be even more spread.
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting
Notes: EXAMPLES PICTURES OF WORST TURN FOR BOTH VERTICAL/HORIZONATLA ND 3/6 TURNS
HIGLITH THAT 50% OF THE ENRìTIRE BEAM IS LOST IN 1 TURN
Highligth that the entire beam is lost within 20 turn but losses are observed only uring the last few turn
GIVE RANGE OF ENERGY LOST BEFORE THE BOOM, IS IT DETECTABLE?

## Slide 8: Beam intensity
8
Entire beam is lost in few turns.
Most of the configuration presents a turn where up to of the beam is lost.
Order of MJ lost across collimators and apertures in one turn.
The energy lost in first turns might be detected to dump the beam before damages.
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 9: Lossmaps: worst case
9
Primary particles on tertiary collimator → current collimation system in PF cannot intercept this fast losses.
From turn 19 () to turn 20 ().
Losses in the aperture ( of total losses) coming from secondary particles or scattered primaries.
Giulia Nigrelli
PF
PB
PH
IPA
IPD
IPJ
PL
IPG
IPA
16/12/2024 FCC-ee MDI meeting

## Slide 10: Lossmaps: Interaction regions (IPG)
10
Significant losses close to the IPs, more than in the collimator insertion.
Possible solution:
  Shower absorber after tertiary collimator to protect detectors.
Giulia Nigrelli
IPG
TCT
SR
16/12/2024 FCC-ee MDI meeting

## Slide 11: Losses across collimators
11
anchor
Total loss on same type of collimator shows:
  Primary collimators not always absorb most of the energy lost → primaries on tertiary collimators.
  Significant losses in the tertiary collimators, efficiently protecting SR collimators.
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 12: Vertical instability CHARACTERISTICS
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 13: Transverse beam position at primary collimator
13
The beam oscillate coherently along the vertical axis for many turns until the dynamic aperture is reached → beam distribution blows up.
Ongoing studies to tighten the vertical collimator’s apertures up to the DA.
This animation does not include scattering in the collimators.
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting
Notes: EXAMPLES PICTURES OF WORST TURN FOR BOTH VERTICAL/HORIZONATLA ND 3/6 TURNS
HIGLITH THAT 50% OF THE ENRìTIRE BEAM IS LOST IN 1 TURN
Highligth that the entire beam is lost within 20 turn but losses are observed only uring the last few turn
GIVE RANGE OF ENERGY LOST BEFORE THE BOOM, IS IT DETECTABLE?

## Slide 14: Beam intensity
14
Entire beam is lost in few turns.
Most of the configuration presents a turn where up to of the beam is lost.
Order of MJ lost across collimators and apertures in one turn.
Losses are more spread in time due to the beam blow up.
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 15: Lossmaps: worst case
15
Entire beam lost within
() turns for .
First loss at turn 21 () then turn 22 ().
Less losses in the aperture compared to the horizontal case().
Giulia Nigrelli
PF
PB
PH
IPA
IPD
IPJ
PL
IPG
IPA
16/12/2024 FCC-ee MDI meeting

## Slide 16: Lossmaps: Interaction regions (IPJ)
16
Primary particles on tertiary collimator ().
Solutions:
  Shower absorber after tertiary collimator to protect detectors.
  Tightening of vertical collimators apertures.
Giulia Nigrelli
IPJ
TCT
SR
16/12/2024 FCC-ee MDI meeting

## Slide 17: Losses across collimators
17
anchor
Total loss on same type of collimator shows the same characteristic of the horizontal case:
  Primary collimators not always absorb most of the energy lost → primaries on tertiary collimators.
  Significant losses in the tertiary collimators, efficiently protecting SR collimators.
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 18: Integrated lossmaps over all turns H vs V
18
Vertical 0° 3 turns
Horizontal 0° 3 turns
Giulia Nigrelli
PF
PB
PH
IPA
IPD
IPJ
PL
IPG
IPA
16/12/2024 FCC-ee MDI meeting

## Slide 19: Conclusions
Fast instability modeled by synchronized kicks placed along the ring with raising strength:
  Reproduced exponential growth of betatron oscillation amplitudes.
  Studied beam loss distributions around the ring and across multiple turns.
THIS IS A WORK IN PROGRESS, affected by collimation optics updates and impedance modeling as well as potential tightening of the vertical collimator cut.
The fast instability could be dangerous if the feedback system fails.
  Full beam potentially lost within few turns.
  Almost 50% of beam energy lost in one turn, losses of order of MJ in the collimator can be expected.
  The effects depend also on the phase advance.
  High losses in tertiary collimators hence nearby experiments.
This instability could potentially cause damage both at the machine and detectors further investigation is needed.
19
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 20: Next steps
Energy deposition studies → impact distributions on collimators jaws provided to the FLUKA team.
High losses nearby experiments, shower calculation in the detector regions are needed.
Mitigating potential damage: the machine needs to be design such that this instability doesn’t occur:
  redundancy in damper system,
  Interlocks,
  reduced impedance,
  high chromaticity,
  …
20
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 21: Thank you for your attention!
Giulia Nigrelli
16/12/2024 FCC-ee MDI meeting

## Slide 22: Backup

## Slide 23
23
Horizontal: 3 turns
Vertical: 6 turns
Giulia Nigrelli
At primary collimator.

## Slide 24: Fast instability: Introduction
Assuming the beam as a single particle of charge (no coupling) under the influence of an external force(wake fields/impedance) and neglecting the longitudinal motion.
A complex tune shift is generated due to the impedance of the ring :
The betatron motion is influenced by such
impedance.
The real part of the impedance define
growth/damping rate of the betatron oscillation.
The instability rise-time is given by:
If betatron oscillations grow
exponentially.
For more detalies X. Buffat.
24
04/11/2024 / 2nd FCC Italy & France Workshop
Giulia Nigrelli

## Slide 25: Lossmaps: Time distribution
25
28/11/2024 10th FCC-ee Machine Protection Task Force meeting
Giulia Nigrelli
IPA
PF
PB
PH
IPA
IPD
IPJ
PL
IPG
PF
PB
PH
IPA
IPD
IPJ
PL
IPG

## Slide 26: Collimator impact distributions
26
anchor
Considering the configuration :
Impact distributions have been provided to the FLUKA team for energy deposition studies.
Note: Axes are with respect to the collimator system.
28/11/2024 10th FCC-ee Machine Protection Task Force meeting
Giulia Nigrelli

## Slide 27: Losses at the primary collimator (tcp.h.b1)
27
To compare the various cases is useful to look at the losses in the primary with respect to time:
28/11/2024 10th FCC-ee Machine Protection Task Force meeting
Giulia Nigrelli

## Slide 28: Losses at the tertiary collimator (tct.h.1.b1)
28
To compare the various cases is useful to look at the losses in the primary with respect to time:
28/11/2024 10th FCC-ee Machine Protection Task Force meeting
Giulia Nigrelli

## Slide 29: Lossmaps: Time distribution
29
28/11/2024 10th FCC-ee Machine Protection Task Force meeting
Giulia Nigrelli
IPA
PF
PB
PH
IPA
IPD
IPJ
PL
IPG
PF
PB
PH
IPA
IPD
IPJ
PL
IPG
Notes: Lossmaps at each turn have been generated to study the time distribution of the losses:

## Slide 30: Collimator impact distributions
30
For the configuration :
Impact distributions have been provided to the FLUKA team for energy deposition studies.
28/11/2024 10th FCC-ee Machine Protection Task Force meeting
Giulia Nigrelli

## Slide 31: Losses at the primary collimator (tcp.v.b1)
31
To compare the various cases is useful to look at the losses in the primary with respect to time:
28/11/2024 10th FCC-ee Machine Protection Task Force meeting
Giulia Nigrelli

## Slide 32: Losses at the tertiary collimator (tct.v.1.b1)
32
To compare the various cases is useful to look at the losses in the primary with respect to time:
28/11/2024 10th FCC-ee Machine Protection Task Force meeting
Giulia Nigrelli

## Slide 33
Colors
Backgrounds
Radiant Blue
Flash
Energy
Green
Red
Deep Blue
Use for Layout
Background Blue
Background Purple
Background Yellow
Background Grey

## Slide 34
Graphical Elements
Badges
Infographics
Separation lines 1.5 pt
Arrows
Use light badges on dark backgrounds
Use blue badges on light backgrounds
This information is a badge because it is important!
This information is a badge because it is important!
This information is a badge because it is important!
This information is a badge because it is important!