## Slide 1
Vitaly Chepel
LIP and University of Coimbra
Developments on micropattern structures for liquid xenon detectors
2024.00269.CERN
A. Breskin, G. Martinez Lema, A. Roy, V. Solovov, F. Neves

## Slide 2
Two-phase liquid detectors are probably the most versatile detectors for low energies and rare events
Double-phase liquid noble gas detector
> 1 m
S1
S2
Measurement of the two signals is the basis for e/nuclear recoils discrimination
WIMP signature
S1
S1
S2
S2
Neutrons (nuclear recoils)
Gammas/electrons
The threshold is determined by S1 (usually 2 or 3 phe are required in coincidence)
S2 provides energy and position in (x,y) – typically 300 ph/e
Typical configuration of a two-phase WIMP detector

## Slide 3
Two options: dive or float
“No surface, no problem” – back to single (liquid) phase
Liquid surface – inconvenient but worth of suffering (at least it was until now)
Problems associated with the surface:
A strong E field is required for electron extraction  the surface should be between two multiwire electrodes with the distance of 5 mm between them  wire sagging matters
Under surface charge drift/diffusion
Possible ripples, acoustic effects, local deformations, instabilities in a strong E field
The bigger the detector the bigger the problem
“We are one” – electrodes & surface – floating electrodes
Motivation
Take the best of it and enjoy
OR

## Slide 4
Double-phase: development of floating electrodes for LXe
Single phase: electroluminescence of LXe (LAr) on narrow strips:
Results with a microstrip plate
Results with a VCC – Virtual Cathode Chamber
Outline

## Slide 5
LXe density 2.9 g/cm3
FR4 density 2.00.2 g/cm3 - dielectric material used to make THGEM
If copper cladding is not too heavy  THGEM should float on the surface of LXe
copper
FR4
THGEM
0.4 mm holes
Chepel e.a. JINST 18(2023)P05013
1. Floating electrodes – THGEM
Field near the LXe surface:

## Slide 6
Experimental setup - schematics
THGEM position with LXe below the cathode
Floating THGEM
1. Floating THGEM – setup
34 mm
THGEM:
0.4 mm thick
0.3 mm holes, 0.1 mm rim
1.0 mm pitch
Two 20 m wires
connected to the two THGEM electrodes
source

## Slide 7
1. Floating THGEM – results
Chepel e.a. JINST 18(2023)P05013
S1
S2
No S2 for fully covered THGEM
Increase LXe thickness  S2 moves right
Increasing extraction field (above THGEM)  electroluminescence in the uniform field shows up

## Slide 8
Light in the uniform field
Chepel e.a. JINST 18(2023)P05013
1. Floating THGEM – results
LXe in the hole: does it really look like this?
Generated in the hole:
1 phe/drifting electron
20-50 ph/drifting electron in
Not very impressive…
Vmesh(V)
zoom
Light in THGEM holes
Assumed LXe level
(see my talk in WP3.2)
Computation model

## Slide 9
Significantly smaller free liquid surface – reduced probability of any kind of surface instabilities (ripples, waves, microexplosions, local deformations, etc.)
Electron drift/diffusion under the surface – eliminated or made local (within the hole pitch)
High electron extraction probability thanks to high field at the interface (unreachable in uniform field)
Positive ion feedback (if any) – likely to end up at the floating electrode
Result – reduced single electron noise
Parallelism between the gate and extraction electrodes – guaranteed for any dimensions
No sagging
No need for fine detector levelling and liquid level control
1. Floating multihole electrodes – benefits

## Slide 10
Opacity for VUV (S1 problem) – CsI photocathode? Quartz substrate?
Physics – meniscus profile, wettability, field effects, electron transmission efficiency
Structure optimization – thicker THGEM? Bigger holes?
Works in LAr (1.4 g/cm3)?
floaters
LAr or LXe
LAr or LXe
Some plastics do float in LAr, e.g. polycarbonate (1.2 g/cm3).
The question is whether one can make a THGEM-like electrode from them and put into a cryogenic liquid.
Other possible configurations:
1. Floating electrodes – remaining questions/further work
Prove of principle – successful. Open questions:
(a collaboration with AstroCeNT, Warsaw, is established)

## Slide 11
2a. Microstrip plate in LXe (WIS)
Anode 8
Cathode 400
1 mm
5x5 cm2 D263 Schott glass 0.5 mm thick
(same as we used to observe electron multiplication in LXe back in 1995)
=2000 V
Martinez-Lema e.a. JINST 19(2024)P02037
Policarpo e. a. NIMA365(1995)568
source
microstrips

## Slide 12
2a. Microstrip plate in LXe (LAr preliminary)
35.52.6 VUV phot/drifting e- in
Energy resolution (light)
Martinez-Lema e.a. JINST 19(2024)P02037
Policarpo e. a. NIMA365(1995)568
Light
Anode voltage
Charge
Anode voltage
Martinez-Lema e.a. JINST 19(2024)P02037
LXe
preliminary
LAr
Martinez-Lema e.a. LIDINE2024
Same geometry as for LXe (PMT quartz window covered with TPB)
S2 signall by a factor of 100 smaller
Light

## Slide 13
2b. Virtual Cathode Chamber (VCC) vs Microstrip plate
No cathode strips; the cathode is on the other side of the plate (Capeans e. a. NIMA400(1997)17)
VCC
Computations using
Distance from strip
(kV/cm)
Photon yield (per electron)
Anode voltage (kV)
10 m
20 m
For same voltage, microstrip is better than other configurations
However, higher voltages can be applied to VCC than to a microstrip plate
Our best
Good chance to get
Martinez-Lema e.a. JINST 19(2024)P02037

## Slide 14
2b. VCC – results in LXe
Martinez-Lema e.a. LIDINE2024
anode strip (Cr) 2 m wide
Vsource = -2.0 kV
Vcathode = ground
Vback = -2.0 kV
Vanode = +1.6 kV
Vsource = - 2.0 kV
Vback = - 1.75 kV
Vanode = +3.25 kV
ΔV = 1.6 kV
ΔV = 5.0 kV
Our VCC plate
S2 drops x5 in 1h
photons/drifting e–
At more or less stable conditions (in small steps, after waiting a few min)
Max photons/electron observed
Time since ramp up, min
S2 integral (mV)
S2 integral (phe)
(V)
expected
Preliminary

## Slide 15
2b. VCC – possible explanations for signal degradation
Martinez-Lema e.a. LIDINE2024
VCC
Fixed drift field (
(
Fixed
Drift
S2
S2
Charging up? – 40 Bq source, …
Glass conductivity too low?
(1011 at room T, in LXe)
Effect of glass polarization?
Glass – kind of Pestov black glass
One thing is clear – the substrate matters
?
?
?

## Slide 16
2. Microstrips and VCC vs wires
Wires:
0.1-0.5 ph/e = “Light/Charge” single wire 4 to 25 mm, up to 5 kV -- Masuda e.a. 1979
20 ph/e @ ~3.6 kV
100 ph/e @ 5 kV
300+-80 ph/e @ 6.7 kV
17 ph/e @ 3.6 kV - single 10 mm anode wire; cylidrical geometry (wire cathodes) -- Qi e.a. 2023
29 ph/ie @ 4.4 kV -- Tönnies et al 2024
Us: photons/drifting e– ( >500 possible with VCC?)
10 mm anode wire between two plane multiwire cathodes, 8 mm between them -- Aprile 2014
As a footnote: first report on electroluminescence of LXe (in uniform field) – Dolgoshein e.a. 1967

## Slide 17
Substrate polarization/charging up/…? – clarify
Would higher conductivity of the substrate help?
Is it possible to do on a VUV transparent substrate?
Works in LAr ?
How do we maximize electroluminescence and avoid charge multiplication?
2. Microstrips: what next
Prove of principle – successful.
Breskin JINST 17 (2022) P08002
Advantage - No liquid-gas interface
    Reduced instabilities (interface ripples)
    No delayed e- emission or e- transfer inefficiency through interface
    No gate-interface-anode alignment problems
    Potential improvement for S2-only events (e.g. lower background)
Drawbacks
  Electric fields ~few 100 kV/cm required for electroluminescence (EL)
  So far, lower light yield than dual-phase detectors (except VCC right after applying the voltage)
Open questions:

## Slide 18
Conclusions
FHM – prove of principle in LXe successful, structure optimization and material studies are needed; floating in LAr is interesting but challenging – will try soon
Microstrips and VCC – prove of principle successful in LXe and LAr; light yield in LXe is comparable or higher of that with 10 m wires; signal degradation in time with VCC needs to be understood; much higher ligh yield seems possible
Thank you