## Slide 1: 2nd CERN Advanced Training School on Operation of Accelerators @ ELENA
D. Gamba, L. Ponce, et al.
12/05/2025 – ATSOA2025

## Slide 2: Outline
The Antimatter Complex at CERN: AD/ELENA
  What it is and how it works
  Chosen specificity: e-cooling
Expectations for the week
Where is the control room?!
For the groups coming to ELENA:
  Recall on tune and coupling
  How does an e-cooler look like?
  Tune and Cooling interplay: is this important?
  Your tools, and what you should be careful about

## Slide 3: AD/ELENA: a Unique pbar Facility!
The only place in the world with low energy pbars in a synchrotron!
Serving 60 Research Institutes/Universities – 350 Scientists – 6 Active Collaborations
ALPHA,
Spectroscopy of 1S-2S in antihydrogen
ASACUSA, ALPHA
Spectroscopy of GS-HFS in antihydrogen
ALPHA, AEgIS, GBAR
Test free fall weak equivalence principle with antihydrogen
antihydrogen
ASACUSA
Antiprotonic helium spectroscopy
BASE, BASE-STEP
Fundamental properties of the proton/antiproton, tests of clock WEP / tests of exotic physics / antimatter-dark matter interaction, etc...
PUMA
Antiproton/nuclei scattering to study neutron skins
antiprotons
26 GeV protons on iridium target
Momentum selection (3.57 GeV/c) chicane
AD deceleration (to 5.3 MeV)
- since 1999 -
ELENA decelerator
(to 100 keV)
- since 2018 -
Electrostatic transfer line to experiments
- since 2021 -
AD ring length: 182 m
30 m
Six collaborations, pioneering work by Gabrielse, Oelert, Hayano, Hangst, Charlton et al.

## Slide 4: From 25 GeV p to 100 keV pbar: 4e7 pbars/2’
Generating pbars from 26 GeV/c protons (yield of the order of 3e-6 pbar/p)
Up to 80% deceleration efficiency from 2.75 GeV (3.57 GeV/c) to 100 keV (13.7 MeV/c)
  Requiring several stochastic and electron cooling steps
AD Cooling and
Deceleration
p-pbar yield
p from
PS
AD s-cooling
AD e-cooling
ELENA e-cooling
ELENA Cooling and Deceleration
to users
p
PS eje
FTA9053
(AD target)
Transfer to
ELENA
2e13
1.8e13

## Slide 5: Serving 4 Users at a Time
Pbars from AD
H- from local source
Up to 4 experiments served at the same time with 1e7 pbars/bunch
  24/7 beam availability was the key game changer for AD users since ELENA is online (2021)
  Users are taking beam right now !
    We will need to be careful !
AD produces 1 bunch at 5.3 MeV
ELENA can use H- from a local source:
  Instrumental for commissioning, but also used for physics
  It will be the source of beam during the school !
ELENA: 4 bunches at 100 keV
  <150 ns FWHM
  <1e-3 RMS dp/p
  <3 um emit.

## Slide 6: The ELENA cycle
Running with two (magnetically-equal) ~15-second-long pbar or H- cycles:
Second H- injection to increase beam intensity @100 keV before extraction
h=4
h=1
h=4
h=1
E-cooling
E-cooling
E-cooling
n bunches extracted on demand by users
Repetition rate is too slow, and all pbar cycles “taken” for physics
    You can use H- cycles, still with a “poor” repetition rate: one cycle every about 2 minutes
    H- lifetime strongly affected by vacuum levels in the ring (typically 10-11 mbar)
    We will concentrate on the final 2-s long plateau, where you will play with cooling !

## Slide 7: ELENA: A Toy Ring for Optics, e.g. Tune and Coupling
What you will be able to explore:
Measure and change basic beam properties, e.g. Tune:
Is there any coupling in the machine?
Can you try to correct it? How?

## Slide 8: Cooling: Why?
Beam size depends on β (depends on the machine optics) and 𝜖 (property of the beam)
Normalised emittance is constant with energy
  Good for colliders: the higher the energy the smaller the beam size, hence higher luminosity:
  Bad for decelerators: beam size increases, but the vacuum pipe remains the same ➔ losses!
A “cooling” mechanism to reduce beam emittances is the fundamental ingredient for AD/ELENA
Example: transverse phase-space
Acceptance
Beam
  You will have a unique chance to play with such a technique in ELENA !

## Slide 9: History: First Idea of Electron Cooling
G.I. Budker is discussing electron cooling
Electron cooling was proposed by G.I.Budker in 1965 as a method for preparing of the beams for hadron colliders.
The electron beam moving with the same average velocity as proton beam absorbs the kinetic energy of heavy particles (protons or ions).
Budker, G. I. (1967), Soviet Atomic Energy 22 (5): 438–440

## Slide 10: E-Cooling: What?
Simple analogy (by I. Meshkov): a bullet (“ion”) shot at a heap of sand (“electrons”!) flying with average velocity v0 :
Vion  v0  ve
ion
e-
v0
Vion ≠ v0
To be efficient, it requires a good alignment (both in terms of longitudinal “speed” and transverse position/angle) between e- trajectory and ion beam closed orbit !
YOUR EXERCISE: check the impact of misalignments on cooling and optimise it !

## Slide 11: Understanding E-Cooling at ELENA
What you will be able to explore:
What is the impact of trajectory misalignments between ions and e-?
What is happening here?
A possible strategy to optimise cooling.
Find the best configuration to minimise final beam size (emittance)

## Slide 12: Expectations from Your Stay in the ACR
First half a day:
  Visit of the facility with one operator in charge of the facility
  Walking through the machine settings, beam observables, and control system of AD and ELENA
  Questions and answer: profit of machine experts around you!
Second day:
  Split in two groups: one using ELENA user “MD4”, one using “MD6”, looking at final e-cooling plateau
  Measure and correct transverse coupling
  Characterise e-cooling
  Optimise e-cooling for faster cooling and smaller final emittances
  (Optional) More advanced optimisations?
    Can you find a better machine setup? (lower emittance? Faster cooling? Shorter bunches?)
  “Take home” some data for further analysis, … and questions …

## Slide 13: Where is the Antimatter Complex ?
CERN Entrance B
CERN Globe
CLEAR Control Room
AD Control Room
Meeting Room(s)
CERN Restaurant 2
ISOLDE Control Room
CERN Restaurant 1
Suggested path to reach the AD Control Room (ACR)

## Slide 14
For the Groups Coming to ELENA

## Slide 15: Tune and Coupling Observation in Practice
  The simplest method to determine if there is coupling is to excite a beam oscillation in one plane (by kicking the beam), and then observe the oscillations or the frequency content
  If there is coupling, then for a horizontal kick there will be a vertical oscillation (and vice-versa).
Example from the LHC

## Slide 16: Quantifying Coupling with Closest Tune Approach
  Coupling makes it impossible to approach the measured tunes closer than , where is referred to as the coupling coefficient
  can be measured by trying to approach the tunes and measure their minimum distance
measured
(recall )
programmed Qx
programmed Qy
programmed Qx
programmed Qy
minimum tune separation
minimum tune separation
e.g. in the CERN PS

## Slide 17: How to Realise Electron Cooling in Practice
ions
e-
Source: electron gun
E- beam transport: solenoids, toroids, steering magnets
Beam dump:
collector
The LEAR (now ~AD) e-cooler, CERN-EP/90-04
A guiding magnetic field carries a DC electron beam from a cathode into the ion beam and then to a collector.

## Slide 18: Other Properties of Generated Electron Beam: Electron velocities
The longitudinal energy a of the electron beam is not constant along its radius (r), but it typically follows the relation:
Details on CERN-EP/90-04
where E0 is the energy in the center of the beam and r0 is the beam radius.
This effect can be partially cured by trapping positive ions in the electron beam along the interaction region!
It can be of a few %!
(details not discussed here. See CERN-EP/90-04 )

## Slide 19: E-cooling studies in ELENA
Test bed for Xsuite e-cooling model benchmark (P. Kruyt)
  Generally, good agreement between measurements and simulations
  Still to test impact of field quality degradation (introduced with correction coils) on cooling efficiency
ELENA magnetic field quality somewhere in this range
Simulations at 35 MeV/c
Measurements and simulations at 13.7 MeV/c

## Slide 20: More complex example: ELENA emittance at ejection
Up to 4th order resonances
ELENA Design
A typical challenge in low energy synchrotrons:
Possibly excited resonance limit the possible tunes that one can use in a machine, e.g. ELENA
Space-charge effect induces a tune spread experienced by the beam depending on particle particle density within the beam
  i.e. smaller beam size (or emittance) = higher tune spread
An optimisation example:
Observation: the beam emittance at ELENA extraction was above the design value
We simulated expected tune spread due to space charge, and measured excitation state of resonance by scanning the tune diagram
We identified a more robust working point
Factor 2 emittance reduction obtained in 2023
Used in operation since 2024
Plots assuming beta_x = 7.7 m and betay = 1.3 m irrespectively from working point => big assumption! Optics is actually diffferent
x2 emittance reduction!
Initial working point
Third order resonance found to be excited

## Slide 21: Your Main Tools…
Measuring beam properties
Setting machine parameters
Beam intensity
Beam size – after extraction
Beam Tunes
Energy(Frequency) Spread
“Knobs”:
mainly to control beam extraction time for e-cooling studies
“All machine parameters” editor
(Please, be careful at what you touch!)

## Slide 22: LSA Settings Management: some words
Only act on MD4/MD6 cycles which you find under “TEST” !
Parameters under “Device Group” “EUROLABS” are normally “safe” to touch
You can see
(and can re-load) the “history” of a parameter settings under “Trim History”
Typically, you are meant to look at / modify (“trim”) “target” settings

## Slide 23: A Quick Eye on the Operational (Physics!) Pbar Cycles
Keep an eye on the AD Vistar: live – and short history – check that all is well.
Numbers that should never really change…
Last pbar cycle in ELENA:
Users taking beam can change
Intensity “shape” should remain “constant”

## Slide 24: A Quick Eye on ELENA cycles (all!)
Keep an eye on the ELENA Vistar: live – and short history – check that all is well
  at least on the the “production” cycles: HMPROD1 and PBMD1 (or PBPRD1) …
“Your” cycles: MD4/6
Physics H-: HMPROD1
Physics pbar: PBMD1
LIVE VIEW
Showing which cycle is being played, and a short history of performance

## Slide 25
APPENDIX

## Slide 26: Overview of AD and ELENA rings and instruments
AD ring length: 182 m
30 m
Slow machines
  Featuring cooling: i.e. no emittance preservation
Mostly relying on destructive transverse measurements: scrapers
  IPM in AD seems to work since this yets!
  Neutrals monitor in ELENA (H- only): usable?
  SEMs in ELENA for ejected beam characterization
  BTVs partially used for optics matching
Intensity (and Schottky) monitoring essential!
  Several “BCT”s, and BCCCA in AD, (using BPMs in ELENA)
SCRAPERs
IPM
Neutral H monitor
AD s-cooling
AD e-cooling
ELENA e-cooling
SEMs
BTVs
BCCCA
BCT/LPU Schottky
+BPMs +Tune Meters (AD/ELENA)

## Slide 27: CERN Coolers Main Parameters
 | LEIR | AD |  | ELENA | 
(Main) Ion particle | 208Pb54+ | pbar | pbar | pbar | pbar
Ion momentum | ~88 MeV/c/u | 300 MeV/c | 100 MeV/c | 35 MeV/c | 13.7 MeV/c
Electron kinetic energy | 2.3 keV (<6.5 keV) | 25.5 keV (<35 keV) | 2.9 keV | 355 eV | 55 eV
Relativistic beta | 0.094 | 0.305 | 0.106 | 0.037 | 0.015
Electron current | 600 mA | 2.5 A | 100 mA | 5 mA | 1 mA
Cooling length | 2.5 m | 1.5 m |  | 1 m | 
Ring length | 78.54 m | 182.43 m |  | 30.41 m | 
Gun magnetic field | Up to 2.3 kG | 590 G |  | Up to 1 kG | 
Drift magnet field | 750 G | 590 G |  | 100 G | 
Electron beam radius (drift) | 14 - 25 mm | 25 mm |  | 8 to 25 mm | 
Each cooler is designed with specific parameters to match the accelerator needs
Notes: For LEIR we typically speak about 4.2 MeV/u kinetic energy