## Slide 1: LHC - Beam Wire Scanner Impedance Study Update
18/02/2025
H. Bursali, C. Vollinger, W. Andreazza, C. Pasquino, H. Sullivan
SY-RF-BR
96th IWG Meeting

## Slide 2: Outline
Legacy Model
Improvements on the Model
  Follow up
  RF Absorber Usage
  Studied Models
  Updated Model
  Previous vs Updated Model
Beam-induced RF Power Loss
Conclusion & Future Work
1
96th IWG Meeting

## Slide 3: Legacy Model
2
Wire Scanner
Ferrites (TT2-111 R)
Wire is located behind the ferrites!
4 wire scanners
96th IWG Meeting

## Slide 4: Follow up
3
For more info: ‘LHC BWS Impedance Study’, 93rd IWG Meeting
96th IWG Meeting

## Slide 5: RF Absorber Usage
4
No RF absorber
With RF absorber
96th IWG Meeting
50 Ω NEG coated ceramic (macor)

## Slide 6: Studied Models
5
Ferrites (TT2-111 R)
50 Ω NEG coated ceramic (macor)
RF absorbers with different lengths on bottom chamber
30 mm
20 mm
10 mm
5 mm
Absorber -> 50 Ω NEG coated ceramic (macor)
Models with different absorber configurations
96th IWG Meeting

## Slide 7: Updated Model
6
Panels
RF Absorber Locations
RF Absorber and Panel Locations
50 Ω NEG coated ceramic (macor)
96th IWG Meeting

## Slide 8: Previous vs Updated Model
7
Previous Model (93rd IWG)
Updated Model
96th IWG Meeting

## Slide 9: Remark (1)
8
Current Design
Current Design + Absorbers on the middle panel
96th IWG Meeting
There will be wire with copper track on the card. -> Loop!

## Slide 10: Remark (2)
9
96th IWG Meeting
Current model
Additional absorbers

## Slide 11: Beam-Induced RF Power Loss
10
Bunch length -> 1 ns
Number of particles/bunch -> 2.2e11
q-Gaussian Distribution
Power Loss -> 4.59 W
Max. Power Loss -> 5.03 W
Beam Induced Heating Computation code – BIHC
Power Loss
Power Spectral Density over Frequency
96th IWG Meeting

## Slide 12: Conclusion & Future Work
The BWS model is equipped with RF absorbers both in the lower and upper chambers. All the peaks in the previous model (presented in 93rd IWG meeting) has mitigated.
The panels are updated for better mechanical assembly and RF contact.
Calculated beam-induced RF power loss is ~5 W for q-Gaussian beam distribution with 1 ns bunch length and 2.2e11 p/b intensity.
Integration model and transverse impedance simulations will be performed.
11
96th IWG Meeting
Previous Model
Updated Model

## Slide 13: Thanks for your attention!
SY-RF-BR
Special thanks to Leonardo Sito for the help on the BIHC code.
96th IWG Meeting

## Slide 14: Backup Slides

## Slide 15: BWS Model
Mechanical Model
Simplified CST Model

## Slide 16: BWS Model - Dimensions
350 mm
185 mm
250 mm
62 mm

## Slide 17: BWS Legacy Model

## Slide 18: BWS Model Trial with Wire (1)
Front View
CST Model with Wire & Feedtrough
Mode # | Frequency (MHz)
1 | 71
2 | 75
3 | 338
4 | 446
5 | 532
Eigen Solver

## Slide 19: BWS Model Trial with Wire (2)
Mode #1 -> 71 MHz
Surface Current
Electric Field
Magnetic Field

## Slide 20: BWS Model Trial with Wire (3)
Mode #5 –> 532 MHz
Surface Current
Electric Field
Magnetic Field

## Slide 21: Models with Absorbers at Bottom Chamber (1)
RF absorber -> 50 Ω NEG coated ceramic (5 mm thickness)

## Slide 22: Models with Absorbers at Bottom Chamber (2)
30 mm
20 mm
10 mm
Absorber width

## Slide 23: Models with Absorbers at Bottom Chamber (3)
30 mm
20 mm
10 mm
5 mm

## Slide 24: Absorber Width Change
10 mm
20 mm
30 mm
40 mm
50 mm
60 mm
Absorber width

## Slide 25: Modified Bottom Chamber (1)
Impedance responses of modified model with different absorbers
50 Ω NEG coated ceramic (macor)
Ferrites (TT2-111 R)
Ferrites (TT2-111 R)
50 Ω NEG coated ceramic (macor)
Model with NEG coated absorbers
Model with ferrites
Model with combined absorbers

## Slide 26: Modified Bottom Chamber (2)
Impedance responses of modified model with different absorbers
Model with NEG coated absorbers
Model with ferrites
Model with combined absorbers

## Slide 27: Updated Model