## Slide 1: ALICE GAS SYSTEMS
  2024 Activities
  03 February 2025
  Louis-Philippe De Menezes
  ED/DT/FS – Gas Group

## Slide 2: TOPICS
  * Piquet Interventions
  Louis-Philippe De Menezes
  ED/DT/FS – Gas Group
  * One specific intervention
  * M&O interventions
  * On going activities

## Slide 3
Piquet interventions
  ED/DT/FS – Gas Group
  Louis-Philippe De Menezes
87 piquet interventions in 2023
Chart: interventions
| TPC | TRD | TOF | HMPID | CPV | MCH | MID | PGS | Analysis / All
Sales | 26 | 9 | 15 | 3 | 0 | 3 | 15 | 12 | 4
Chart: Stop hours/ system
Chart: Work hours
| TPC | TRD | TOF | HMPID | CPV | MCH | MID | PGS | Analysis
Sales | 15.5 | 7.5 | 11 | 1.5 | 0 | 1.5 | 13 | 8.5 | 2
5.5h00 of stop
60.5 of direct work
Chart: Stop hours
| Gas ssytem faillure | External reasons
Sales | 4.5 | 1
82% / 18%
Chart: Stop Hours
| TPC | TRD | TOF | HMPID | CPV | MCH | MID | PGS | Analysis / All
Sales | 2.5 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0
TPC
MID

## Slide 4
Piquet interventions
  ED/DT/FS – Gas Group
  Louis-Philippe De Menezes
Example of intervention on MID
The system stopped due to the fact that the pressure sensor had a strange behavior and suddenly went to the minimum of the scale (-15 mbars). We swopped the regulation from this chamber sensor to the output distribution sensor. It was running like this before the installation of the chamber sensor.

## Slide 5
M&O interventions
  ED/DT/FS – Gas Group
  Louis-Philippe De Menezes
130 M&O interventions
Chart: 
| TPC | TRD | TOF | HMPID | CPV | MCH | MID | All | PGS
Sales | 17 | 19 | 18 | 6 | 3 | 24 | 23 | 18 | 3

## Slide 6
  ED/DT/FS – Gas Group
  Louis-Philippe De Menezes
Example of activities
Safety valves checks
Analyzers checks calibration / cells changes or calibration
Pump membranes changes
Filters change / cleaning
Power supply change MCH
Periodic checks
Festo changes
Safety valves checks
TOF Exhaust filter
FESTO Modules
replacement
M&O interventions

## Slide 7
Specific intervention
  ED/DT/FS – Gas Group
  Louis-Philippe De Menezes
Example of intervention on TPC
Construction and installation of a new small filtration low delta P filter ( 0.02 microns and 20mbars)

## Slide 8
Activities 2025 ( On going)
  ED/DT/FS – Gas Group
  Louis-Philippe De Menezes
TRD Leak search
TPC pump dumper

## Slide 9
ThANK you