## Slide 1: Introduction to Particle Accelerators
Simon Albright
Accelerator Physicist
03/12/2025

## Slide 2: What is a Particle Accelerator?

## Slide 3: According to Wikipedia:
A particle accelerator is a machine that uses electromagnetic fields to propel charged particles to very high speeds and energies to contain them in well-defined beams.

## Slide 4
Maltese cross
Electric field
Cathode ray
(electron beam)
A particle accelerator is a machine that uses electromagnetic fields to propel charged particles to very high speeds and energies to contain them in well-defined beams.
Electron source

## Slide 5
Magnetron
Electric field
A particle accelerator is a machine that uses electromagnetic fields to propel charged particles to very high speeds and energies to contain them in well-defined beams.
Electron source
Electron beam
Magnetic field

## Slide 6
Cyclotron
A particle accelerator is a machine that uses electromagnetic fields to propel charged particles to very high speeds and energies to contain them in well-defined beams.
Hydrogen
Proton beam
Electromagnetic field
Magnet
Proton source

## Slide 7
Large Hadron Collider
A particle accelerator is a machine that uses electromagnetic fields to propel charged particles to very high speeds and energies to contain them in well-defined beams.
Proton/ion beams
Magnets

## Slide 8: Particle Accelerators:
Can be almost any size
Use electromagnetic fields to manipulate beams of charged particles
Range from household appliances to multi-national research facilities, and everything in between

## Slide 9: Electrostatic Acceleration
-
+
Negative particle:
e-, H-, anti-proton, …
Positive particle:
e+, H+, Pb82+, …
A charged particle in an electric field will experience a force, and therefore accelerate
An electron crossing a potential difference of 1 Volt gains 1 electron-Volt (eV) of energy (1.6x10-19 J)
Change of energy
Charge
Potential difference

## Slide 11: Van de Graaf Accelerator
H. V.
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Positive ion
source
Particle beam
Ion source raised to Van de Graaf (VdG) potential
Ions accelerated towards ground

## Slide 12: Tandem Van de Graaf Accelerator
H. V.
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Negative ion
source
Positive particle
beam(e.g. H+)
Negative ions accelerated from ground towards the VdG
Excess electron(s) removed by a charge stripper
Positive ions accelerated from VdG towards ground
Charge stripper
Negative particle
beam (e.g. H-)

## Slide 13: The limits of Electrostatic Acceleration
Western Michigan University: 6 MV
Brookhaven National Laboratory: 15 MV
Daresbury Laboratory: 20-30 MV

## Slide 14
Several methods to generate high electrostatic voltage exist (Van de Graaf, Cockroft-Walton, Pelletron, …)
Limited by maximum field to the Mega-Volt scale, typically 10s – 100s kV
Need Tera-Volts for the LHC

## Slide 15: From DC to AC
+
-
+
-
Crossing multiple electrostatic gaps does not allow further acceleration
Electric field points in the “wrong” direction between the gaps
Need to change the direction of the electric field

## Slide 16: From DC to AC
Crossing multiple electrostatic gaps does not allow further acceleration
Electric field points in the “wrong” direction between the gaps
Need to change the direction of the electric field
+
-
+
-
-
+
-
+

## Slide 17: Radiofrequency Acceleration
Confine radio frequency (kHz – GHz) electromagnetic fields in a cavity
Pass bunched beams through either a line of cavities or the same cavity multiple times
Accumulate many small steps in energy, no need for extreme static fields

## Slide 18: Radiofrequency Acceleration
Change of energy
Charge
Potential difference
Particle phase
Phase
Amplitude
The voltage experienced depends on the phase (time) of arrival at the cavity
Particles must cross at the phase that gives the correct voltage
Requires precise synchronisation

## Slide 20: A Light Tour of relativity
c
When this approaches 1
This approaches infinity
Newton
Einstein

## Slide 21: Impact on Acceleration and Energy Gain
The electric field adds kinetic energy to the particles
c
From Newton to Einstein
Newton
Einstein

## Slide 22: Change of Speed vs Change of Energy
At high energy, speed is almost constant
At low energy, increased kinetic energy means increased speed
Light particles (electrons) become relativistic very quickly
Heavier particles (protons) require a lot more energy to become relativistic

## Slide 23: Change of Speed vs Change of Energy – Increasing Mass

## Slide 24: Drift Tube Linac
Drift tubes
Beam is accelerated in the gaps between the drift tubes
And shielded from the field in the “wrong” direction in the drift tubes
The drift tubes get longer because the particles get faster (low energy)

## Slide 25
Widerøe Linac
(PhD Thesis 1927)
Gaps
Drift tubes
CERN: Linac4
GSI: UNILAC

## Slide 26
Instead of going in a straight line and using lots of accelerating gaps
Go in a circle and use the same gap lots of times

## Slide 28
Index = fIeld
seCond = Current
Fumb = Force
N
S
Force applied
Magnetic field
Current
Bending Magnets - Dipoles

## Slide 29: The Cyclotron
Dee
(magnet)
Dee
(magnet)
RF Cavity
Moving charge follows a curved path in the Dee
On each crossing of the gap, energy and path radius increase
Increased path length and increased speed cancel out, fixed time between crossings

## Slide 30: The Cyclotron
Dee
(magnet)
Dee
(magnet)
RF Cavity
Cyclotron frequency
Charge
Magnetic field
Mass
Particle revolution frequency (cyclotron frequency) independent of radius
Excite the RF cavity at (or a multiple)
Increment the particle energy at each crossing of the cavity

## Slide 31: The Cyclotron - Limits
Dee
(magnet)
Dee
(magnet)
RF Cavity
Cyclotron frequency
Charge
Magnetic field
Mass
As the energy increases, relativity starts to matter
By a few tens of MeV, protons become a bit too relativistic and the frequency drops
Lose synchronism, acceleration stops
Relativistic gamma

## Slide 32
4-inch Cyclotron
80 keV protons
11-inch Cyclotron
1.2 MeV protons
60-inch Cyclotron
16 MeV deuterium
Some Lawrence (et al) Cyclotrons

## Slide 33: Fancy Cyclotrons
Synchrocyclotrons:
Adapt the RF frequency to compensate for relativistic effects
Sector cyclotrons:
Non-uniform magnetic field reshapes the orbit to maintain frequency for longer
CERN (1957-1990)
600 MeV protons
TRIUMF (1974-Present)
520 MeV protons

## Slide 35: Beyond the Cyclotron
Classical cyclotrons are limited to around 20 MeV
With further developments, energies pushing 1 GeV can be reached
Need an accelerator that can operate through to the ultra-relativistic regime
Synchrotrons:
Constant orbital radius
Magnetic field varies with time
RF frequency changes synchronously with the magnetic field

## Slide 36: Dipole Magnetic Field And Momentum
Magnetic
field
(B)
Momentum
Charge
Magnetic field
Bending radius
Speed of light
Bending
radius
()

## Slide 37: Create a Synchrotron
Create a ring of dipoles to define the path for a given energy/momentum

## Slide 38: Create a Synchrotron
The momentum defines the speed, add one or more RF cavities with a frequency at an integer multiple of the revolution frequency.
Increase magnetic field and RF frequency synchronously: Synchrotron

## Slide 39
Particle beams are never perfectly laminar
Like-charges repel each other
Lenses are used to focus the beam
Focusing

## Slide 40: Focusing Magnets - Quadrupoles
S
S
N
N
N
N
S
S
Focusing quadrupole:
Focuses in the horizontal plane
Defocuses in the vertical plane
Defocusing quadrupole:
Defocuses in the horizontal plane
Focuses in the vertical plane

## Slide 41: Focusing Channel
Horizontal
Vertical
D
F
D
D
F
F
F

## Slide 42
Add quadrupoles around the ring to keep the beam focused

## Slide 44: Dispersion
The particles have a range of energies (momenta)
For a given magnetic field, high momentum particles bend less than low momentum particles, causing the beam to spread out
Dipole

## Slide 45: Chromaticity
High energy particles are focused less
Low energy particles are focused more
For correct focusing, another magnet is added
F

## Slide 46: Chromaticity Correction - Sextupole
D
F
S
S
N
N
S
N
This side focuses
This side defocuses
F

## Slide 47
Add sextupoles to correct for chromaticity

## Slide 48: Beam Instrumentation
Beam Position Monitors:
Measure the beam’s horizontal/vertical offset
Beam Loss Monitors:
Localise and quantify lost beam
Beam profile measurement
Measure the beam distribution in 3D

## Slide 49
Add beam instrumentation

## Slide 50: Vacuum

## Slide 51
Add vacuum systems

## Slide 52: Anything Else?
Injection and extraction systems
  Fast pulsing magnets to get beam in and out of the accelerator
Collimators
  Absorb lost beam in a controlled way at predefined locations
Higher order magnets
  Correct additional errors and influence more beam parameters
Additional RF systems
  Manipulate the longitudinal beam parameters
Feedbacks
  Identify and correct errors that might degrade the beam
…..

## Slide 53
Linacs
Synchrotrons
Plasma Wakefield Accelerator

## Slide 54: Linac4
High voltage platform:
H- ion source
Electrostatic acceleration
Radiofrequency Quadrupole (RFQ):
Structure that both accelerates and focuses at the same time
Drift Tube Linac (DTL)

## Slide 55: PS Booster
H- from Linac4
H-
H+
Charge strippers
Dipole
Quadrupole
Sextupole

## Slide 56: Low Energy Ion Ring
Dipole
Dipole
Dipole
Dipole
Quadrupoles
Quadrupoles
Quadrupoles
Quadrupoles
Quadrupoles
Injection system
Extraction system
RF Cavities
Electron cooling

## Slide 57: Proton Synchrotron
Combined function magnet: Both a dipole and a quadrupole
Variable frequency (~10MHz) cavity
20 MHz cavity
40 MHz cavity
80 MHz cavity
200 MHz cavity
Multi-frequency cavity

## Slide 58: Super Proton Synchrotron
Dipole
Sextupole
Quadrupole
200 MHz Cavity
(Travelling Wave Structure)
Beam dump

## Slide 59: Large Hadron Collider
Dipole
Quadrupole
Beam loss monitor
400 MHz RF cavities

## Slide 60: Industrial Applications
The future of Industrial Accelerators and Applications, B. Doyle et al, Reviews of Accelerator Science and Technology Vol. 10 (2019)
Many thousands of accelerators in the world
The vast majority are used in industry and medicine
The underlying physics and engineering requirements are universal, the rest is a matter of context

## Slide 61
Linear
Circular
DC
AC
Very flexible (no need for synchronism)
Energy limited by electric field strength
Cavity design depends on , varies along the linac
Increasing energy requires more RF cavities
Very fast acceleration
Fixed frequency and field (usually)
Large magnets and vacuum vessels
Energy limited by relativity and size
Cyclotron
Synchrotron
Magnetic field and RF frequency ramp synchronously
Energy limited by magnet strength and ring size

## Slide 62: Other types of accelerator
Betatron: Magnetic field for steering and accelerating
Plasma wakefield: Particles accelerated in bubbles of plasma
Induction: Magnetic induction accelerates the beam
Laser radiation pressure: High powered laser pushes particles
Fixed field accelerator: Best bits of cyclotrons and synchrotrons
…

## Slide 63: Summary
Particle accelerators can be small (fit in a microwave), very very large (27 km) and anything in between
Electric fields add energy to the beam, magnetic fields steer and focus the beam (with exceptions)
Electrostatic accelerators can accelerate “anything” but are limited to a few MV, typically 10s-100s kV
Radiofrequency cavities allow many sequential energy increments in linear or circular accelerators
Only a small fraction of accelerators are used for fundamental research, most are tools for industry and medicine