## Slide 2: HI-ECN3 Target complex 13th NBI Workshop - 7-10 October 2024 AYA’s Laboratory, Tokai, Japan
Jean-Louis GRENARD - CERN - on behalf of HI-ECN3 WP4 Target complex

## Slide 3: Content
BDF Target complex
Target exchange principle
Service building integration
Service cell
Summary

## Slide 4: BDF/SHiP Target
New
Service Building
~ 1000 m2
ECN3
Beam Dilution System
New
Access Shaft
(material only)
88 m2
TCC8
170m
Existing
Access Shaft
48 m2
B918
B911
New Target Complex
containing the Beam Dump Target
13 x TZM blocks (580 mm)
5x W blocks (780 mm)
Baseline Design  Improvement during TDR
(Rui Franqueira Ximenes)
BDF/SHiP experiment
(Richard Jacobsson)
Also at NBI 2024
The new ECN3 high intensity facility for the BDF/SHiP experiment and high intensity beam transfer (Matthew Fraser)
Radiation protection studies and considerations for the ECN3 high intensity project (Claudia Ahdida)

## Slide 5: BDF Target complex integration
Target area
Confinement wall
Access chicane
Mobile Shielding
Above Coil Shielding
Magnetized
shielding
Water cooled proximity shielding
Target
Upstream Shielding
Collimator
Target station
SHIP experiment
Muon shield magnet
Diluted Proton beam from SPS
Space for shielding temporary storage
Beam instrumentation
Vacuum confinement

## Slide 6
BDF Target complex integration - shielding
~12m
~8m
~4,8m
~ 180 m³ (~1400t) of cast iron + US1010
~ 360 m³ (~800t) of concrete / marble
Now establishing a bill of material to cross check what we will recover from other CERN facilities

## Slide 7: Target Complex in an existing facility
Benefit of being below ground level and having soil on top of the cavern
Existing overhead travelling crane 30t capacity
TCC8 cross section (length 170m)
8m soil

## Slide 8: BDF Target complex integration - extraction
~30m

## Slide 9: Target station vacuum confinement
Utilities feedthroughs
Mechanical design ready to build a prototype
Design of radiation tolerant gaskets
Decommissioning plan
Overall dimensions: ~6.36 x 2.05 x 2.95 m
Can be fully fabricated and tested at a contractor premisses
Primary vacuum to optimize air activation around target
(Water containment in case of water leak)

## Slide 10: BDF Target complex integration extraction development
Trolley mounted on full stainless steel chain action rollers
Extraction / insertion mechanism based on a motorized rigid chain
Door tooling installation
Door removal
Mobile rails installation
Chains connectors orientation
Chains connectors connection
Trolley extraction

## Slide 11: Target handling
Target utilities removed to fit cask

## Slide 12: Target Complex handling
Existing overhead travelling crane 30t capacity replaced
  Redundancy on the 3 movements of the crane
  Integration of a video system
  Integration of a positioning system for the 3 movements
  Off-board control cubicles
  Cable festoon routing
  Remote tools connection on the hook
  Auxiliary hoist
  Investigation on possibility to optimize crane size
  Ongoing specification

## Slide 13: The target service building
Nuclear ventilation system of the target complex
  Air handling units, filters, dehumidifiers (outside)
Target cooling systems
  Pumps, Filters, Heat exchanger, Cooling instrumentation, He circulation system
  Target controls systems
  Target monitoring (sensors), Target control valves, vacuum vessel confinement
  Service cell / hot cell
  Buffer area
Safety systems
Electrical distribution system
Control and safety systems
(Evaporator)
~1000m²

## Slide 14
Service building within the BDF/SHiP complex

## Slide 15
Shielded buffer zone
Material access
Cooling equipment
Service cell (~60m²)
with a movable roof
Power room
Personnel access
Lorry access
Service building – ground floor
HotCell
Access shaft

## Slide 16: Service building – 1rst level
30t overhead traveling crane
Control racks
Mobile shielded hatches
Filter room
Definition of the envelops by end of 2024

## Slide 17: HI-ECN3 service cell - context
HI-ECN3 project need to have a facility to prepare objects for final disposal
  BDF target
  Proximity shielding
  Hadron stopper coil
  Why do we need a specific facility to prepare HI-ECN3 object for final disposal (waste packaging)?
  Level of radiation (~few Sv/h after 1year of cool down)
  Characteristics of materials (W)
  Presence of radiological critical spallation products
  Size and weight of the objects doesn’t fulfil elimination path requirement towards PSI (container size limitation)
  Understanding of failure modes to improve future designs
  Lessons learnt from waste packaging of highly radioactive objects (ISOLDE target, LHC TDE, n_TOF spallation targets)
  Currently such facility does not exist at CERN
Main justification

## Slide 18: Service building – Service cell
Purpose
  Repair of activated components
  Size reduction and material separation for final disposal to optimize cost using different elimination path
  Post Irradiation Examination
Tools envisaged
  Master-slave manipulators
  Robots (fixed and mobile)
  Custom built machinery
Example of a
possible service cell
internal arrangement

## Slide 19: Service cell definition – BDF target disposal draft sequence

## Slide 20: Summary
Significant benefit by reusing an existing infrastructure
Preliminary shielding study have been designed and optimized according to radioprotection requirement
TDR is in progress to finalize the design now focused on defining the process to define Civil Engineering aspects
A service building will be implemented to support the target complex
Part of this building will be dedicated to a service cell for size reduction, waste packaging and to perform PIE
A wide range of remote handling technics will be used within the HI-ECN3 target complex taking the benefit of all the recent developed made across various projects at CERN

## Slide 21
Thank you