## Slide 2: Radiation Protection Considerations for HI-ECN3
C. Ahdida, F. Luoni, F. Malacrida, G. Mazzola, O. Pinto, H. Vincke (HSE-RP), HI-ECN3 Project Team
NBI2024 - 13th International Workshop on Neutrino Beams and Instrumentation AYA'S LABORATORY Quantum Beam Research Center, Japan October 7th to 10th, 2024

## Slide 3
Overview of RP Challenges at HI-ECN3
Target Complex Design Optimization
Target Studies
Beam Transfer Studies
Dismantling studies
Outline

## Slide 4
CERN’s SPS North Area
HI-ECN3 at ECN3
Key beam parameters of BDF/SHiP
 | BDF
Intensity (p/spill) | 4×1013
Spill duration (s) | ≥1
Cycle length (s) | ≥7.2
Avg. beam power (kW) | 356
Average intensity (p/s) | ≤5.6×1012
Annual POT | 4×1019
Duration (years) | 15
Total POT | 6×1020
8m soil
TCC8 cross-section
High Intensity ECN3 (HI-ECN3) project for a new state-of-the-art high intensity experimental facility housing BDF/SHiP in ECN3
    exploiting the available high intensity SPS 400 GeV/c p+ beam
    benefiting from an existing cavern of comfortable size incl. its infrastructure
    using the advantage of the shielding created by the soil
RP challenges
    High beam energy and intensity as well as high POT leading to high prompt radiation and activation levels
    Proximity to surface, experimental and public areas
    High-intensity beam transfer
    Dismantling of current TCC8/ECN3 equipment
400 GeV p+ from SPS
See talks about the SHiP experiment by R. Jacobsson and the BDF target station design by J.L. Grenard

## Slide 5
Target Complex Optimization

## Slide 6
RP studies based on FLUKA MC simulations were performed for a design optimization of BDF/SHiP@HI-ECN3
ALARA approach Optimization required to ensure that exposure of personnel to radiation and radiological impact on environment are As Low As Reasonably Achievable
Prompt radiation Reduce prompt radiation to comply with radiation area classification in the surrounding accessible areas as well as the 1 mSv/y limit at the CERN fence
residual radiation Limit activation of target and experimental area to reduce residual dose rates to be compatible with an adequate area classification
Air and soil activation Reduce activation of air and its releases into the environmental. Limit soil activation (3H<1000 Bq/kg, 22Na<50 Bq/kg) and transfer to groundwater
Environmental impact Reduce environmental impact from prompt radiation and releases of activated air to fulfill CERN’s dose objective for the public of <10 uSv/year
Radiation area classification
BDF/SHiP design optimization

## Slide 7
Stainless steel
Concrete
US1010
Cast iron
Target complex & muon shield, Created using FLAIR [4]
Moraine
TCC8
W-TZM target
Magnetic part of hadron stopper 1.6 T
11 m
Moraine
1.6 m
1.6 m
8 m
Muon shield 1.7 T
ECN3
A detailed BDF/SHiP target complex together with the muon shield was implemented in FLUKA
Optimized BDF dump with reduced shielding and re-use of existing, already activated TCC8/TT7 shielding blocks, while maintaining SHiP physics performance
Shielding embedded in vacuum vessel
FLUKA geometry includes the full underground TCC8/ECN3 cavern and surrounding galleries, tunnels, rooms, etc.
Ground profile data from CERN’s Geographic Information System and technical drawings were used to model the surrounding ground
FLUKA hosted by CERN [1-3]
4.8 m
Floor shielding (13.3 m3)
1 m
Vacuum vessel
Muon shield
~180 m³ of cast iron + US1010
~360 m³ of concrete
BDF/SHiP FLUKA model

## Slide 8
Cross-sectional view
Side view
Along y-axis
Shielding design is well optimized for the prompt radiation
Limit of Non-designated Area on CERN domain is by far met
Avg. intensity of 5.6×1012 p/s
(-20 cm < x < 80 cm)
(13260 cm < z < 134380 cm)
(-20 cm < x < 80 cm)
(13260 cm < z < 13380 cm)
Prompt radiation in target area
100 rem = 1Sv

## Slide 9
Cross-sectional view, target level
Along x-axis, working height
Upstream of vessel w/o upstream shielding Preliminary worst case manual intervention scenario
The shielding design contains well the high residual dose rates reaching in the central target region several 10 Sv/h after 1 month of cool-down
The residual dose rates outside the shielding are < 1 µSv/h
1 month cool-down
x [0,40]
x_beam = 26 cm
Shielding removed
After removal of the shielding upstream of the vessel, residual dose rates of several 100 µSv/h are expected
Supervised Radiation Area on the sides
Further optimization by movable shielding
Total PoT 6×1020
(13240 cm < z < 13390 cm)
(15 cm < y < 45 cm)
(13240 cm < z < 13390 cm)
1 month
(-15 cm < x < 80 cm)
Residual radiation in target area
100 rem = 1Sv

## Slide 10
Soil activation
Specific activity of 3H and 22Na in the soil below TCC8 (most critical area)
3H
22Na
Thanks to floor iron shielding, 3H and 22Na activity concentrations in the soil are below respective conservative design limits
A hydro-geological study is underway allowing to refine the design limits and possibly allow to reduce the required shielding
Total PoT 6×1020
1
Floor shielding (13.3 m3)
1 m
(-120 cm < x < 120 cm)
(13148 cm < z < 13364 cm)
(-120 cm < x < 120 cm)
(13148 cm < z < 13364 cm)
Most critical area for soil activation
100 rem = 1Sv

## Slide 11
Air activation
PoT 4×1019 per year
Activation of air in target complex area was studied
Production of radionuclides evaluated with FLUKA in combination with ActiWiz [5]
Two cases were investigated:
CASE 1: build-up of radionuclides during yearly operation without air extraction and 30 min cooldown time before air release
CASE 2: constant immediate release of air (worst-case for upper limit of environmental impact)
Even without any cooldown time, the air activity concentration in the target complex would be compatible with access (< 0.1 CA1)
Flush of target complex with fresh air before any access
1 Person working 40h/w, 50w/y with standard breathing rate in activated air with CA = 1 receives 20 mSv
1
Air activation
Activities of main radionuclides with % contribution to total activity
In red main contriubtors to CA (>4%)
1
See talk by H. Vincke

## Slide 12
Worst-case immediate air release (CASE 2) yields 3 nSv/year (main contributors: N-13, Ar-41, C-11, O-15) and is thus well below the annual dose objective of CERN
Exposure of members of the public due to air releases is negligible
Environmental impact
Muon prompt radiation aboveground downstream ECN3
Dose from air releases
Used max. dose coefficients from different age groups [6]
Positions of nearby population groups
Effective dose estimates
Dose from stray radiation
Release point
Annual limit of Non-designated Area on CERN domain and at CERN fence (1 mSv/y) as well as dose objective for members of the public (10 uSv/y) is by far met
CERN fence
H-3 release due to air activation of ~80 kBq
100 rem = 1Sv
PoT 4×1019 per year
Annual effective dose from muons

## Slide 13
BDF Target Studies

## Slide 14
Baseline Design (CDS)
Water-cooled target: TZM (0.08% titanium – 0.05% zirconium – molybdenum alloy) and W blocks cladded with Ta2.5W
Pursued during the comprehensive design phase → C. Ahdida et al., SPS Beam Dump Facility - Comprehensive Design Study, CERN-2020-002
Prototype + test with beam in 2018 + Post irradiation examination
TDR phase for CDS design improvement
Alternatives with pure W and He cooling under investigation
BDF target baseline design
D 250 mm
~ 1500 mm
See talk “Design considerations for the BDF/SHiP production target” by R. Ximenes on Wednesday

## Slide 15
Longitudinal cut along the target
The residual dose rates of the target were studied for 5 years of operation and different cool-down times
The highest dose rates are in the order of 100 Sv/h after 4 hours of cooling and a few Sv/h after 1 year
Even after 30 years, dose rates at 40 cm still of the order of a few mSv/h → dedicated storage place in facility for irradiated target
For radioactive transport the max. dose rate level at any point on the external surface of a package shall not exceed 2 mSv/h
Dedicated casks for transportation and storage as well as during handling will be designed
Total PoT 4×1019 (5 yrs)
4 hours cool-down
1 year cool-down
30 years cool-down
1 day cool-down
Residual radiation of CDS target

## Slide 16
LA multiples of BDF target materials,
TZM
Ta
W
Total PoT 2×1020 (5 yrs)
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
CDS target radionuclide inventories
Radionuclide inventory of target materials evaluated with FLUKA in combination with ActiWiz → important for radioactive transport and waste considerations (characterization, processing, disposal)
Comparison to Authorization Limits (LA) and Swiss Clearance Limits (LL)

## Slide 17
BDF target prototype w/ in total 14 h irradiation in TCC2, leading to 2.4E16 PoT
Target activation was measured and compared to FLUKA simulations showing excellent agreement
Cooling water activation was estimated w/ FLUKA
Estimated residual dose rate after 1h of cooling at 40 cm from the cartridge is 18.7 mSv/h, while the PMI monitor measured 16.9 mSv/h
Both samples showed the presence of high-Z spallation products some of them could have been produced in the target materials
Water-cooling filter with debris was analysed via EDX
  No peaks were found for Ta, W, Mo or Ti
  Metallic particle (Al, Ca, Fe, Cl, Fe, Cr)
Benchmark of residual dose rates (mSv/h)
Radionuclides in water samples
Water samples were analysed by liquid scintillation and gamma spectrometry
Prototype target tests

## Slide 18
Beam Transfer Studies
See talk on HI-ECN3 by M. Fraser on Wednesday

## Slide 19
P42 beam dump
FLUKA model of P42 dump
400 GeV p+ from SPS
A new beam dump will be installed in the P42 beamline
It shall allow commissioning the most critical part of the dedicated beam transfer (SPS → P42 beamline), while works in TCC8/ ECN3 are ongoing
The former, already activated SPS beam dump is to be reused
Additional shielding is placed around the dump to allow complying with the RP constraints related to prompt radiation, residual radiation, soil and air activation
Key beam parameters of P42 dump
Intensity (p/spill) | 2.2×1012
Cycle length (s) | 7.2
Average intensity (p/s) | 2.8×1011
Operational hours/year | 100
Duration (years) | 3
Total POT | 1.8×1017
Former SPS beam dump
Max. contact dose rate in Apr. 24 amounted to 0.5 mSv/h
Graphite
CuCrZr
GG20
W
Iron shielding
Concrete shielding
2.4 m
0.8 m
0.2 m
0.4 m

## Slide 20
P42 beam dump
Prompt dose rates Side view, 2.8×1011 p/s
All particles
TT83
TT84
Prompt dose rates (<30 uSv/h w/ safety factor 3) in the accessible downstream part of TT84 would be compatible with a Simple Controlled Radiation Area (50 uSv/h)
A radiation monitor is in the accessible part of TT84 to monitor the dose rates during access conditions
An additional benchmark of the dose rates measured in TT84 during a deliberate full beam loss on a collimator showed very good agreement with dedicated FLUKA simulations
FLUKA model of collimator Cross-sectional view
Prompt dose rates Side view, 1.25×1010 p/s
All particles
Collimator benchmark
1 m long
Simulated dose rate: 22.7 uSv/h
Measured dose rate: 27.8 µSv/h

## Slide 21
P42 beam dump
1 week
Prompt dose rates (<30 uSv/h w/ safety factor 3) in the accessible downstream part of TT84 would be compatible with a Simple Controlled Radiation Area (50 uSv/h)
A radiation monitor is in the accessible part of TT84 to monitor the dose rates during access conditions
An additional benchmark of the dose rates measured in TT84 during a deliberate full beam loss on a collimator showed very good agreement with dedicated FLUKA simulations
Residual dose rates 1.8×1017 POT, 1 week cool-down
1 week
1 week
After 1 week, the residual dose rates close to the dump require a Controlled Radiation Area
After 1 month, most of the accessible area is compatible with a Supervised Radiation Area
Even for unlikely unforeseen accesses to TT83 with 2h cool-down only, the dose for walking past the dump would be acceptable
1 month
1 month
Soil activation was evaluated for 3 years of operation (1.8×1017 POT) and found to be acceptable
Soil activation
Considering 3 years of operation and 10 min of cool-down the air activation in the tunnel is compatible with a 0.1 CA even without considering additional fresh air injection into the tunnel
The total activity for 5 min of cool-down amounts to 0.2 MBq (N-13, O-15, C-11)
Environmental impact of released air activation is negligible
Air activation
All particles
TT83
TT84
Prompt dose rates Side view, 2.8×1011 p/s

## Slide 22
Dismantling Studies

## Slide 23
TCC8/ECN3 today
B918
B911
TCC8
400 GeV p+ from SPS
Be target generates a secondary beam of kaons
ECN3
NA62 experiment is currently located in ECN3, while its target area is situated upstream in TCC8
It is in operation since 2009 searching for rare kaon decay modes
p+ [1012 /spill] | POT [1018 / yr] | Exp. tot. POT (2026)
~ 3 | ~0.07 – 2.3 | ~1.4×1019
NA62 beam parameters

## Slide 24
TCC8 dismantling
Dismantling of the highly radioactive TCC8 target area in 2026
Evaluation of residual dose rates and radio-nuclide inventories for operational RP as well as radioactive transport and waste studies
TCC8 FLUKA model
Residual H*(10) – Sep 2027
TCC8 dismantling
Concrete composition studies
Concrete samples were taken and analyzed via gamma spec and XRF measurements
Particle fluences were scored at the given locations via FLUKA, which were then used for subsequent ActiWiz studies to match the measured radionuclide production
Evaluation of refined elemental concrete composition

## Slide 25
Summary
Main radiological aspects regarding an implementation of BDF/SHiP in ECN3 were investigated
First shielding design for an optimization of exposure of personnel to radiation and radiological impact on environment
Additional studies for the beam transfer and the TCC8 dismantling were conducted
Further detailed studies and optimization in the Technical Design Phase until 2026 to achieve first beam on target in 2031

## Slide 27
[1] Website: https://fluka.cern
[2] C. Ahdida, D. Bozzato, D. Calzolari, F. Cerutti, N. Charitonidis, A. Cimmino, A. Coronetti, G. L. D’Alessandro, A. Donadon Servelle, L. S. Esposito, R. Froeschl, R. García Alía, A. Gerbershagen, S. Gilardoni, D. Horváth, G. Hugo, A. Infantino, V. Kouskoura, A. Lechner, B. Lefebvre, G. Lerner, M. Magistris, A. Manousos, G. Moryc, F. Ogallar Ruiz, F. Pozzi, D. Prelipcean, S. Roesler, R. Rossi, M. Sabaté Gilarte, F. Salvat Pujol, P. Schoofs, V. Stránský, C. Theis, A. Tsinganis, R. Versaci, V. Vlachoudis, A. Waets, M. Widorski, New Capabilities of the FLUKA Multi-Purpose Code, Frontiers in Physics 9, 788253 (2022)
[3] G. Battistoni, T. Boehlen, F. Cerutti, P.W. Chin, L.S. Esposito, A. Fassò, A. Ferrari, A. Lechner, A. Empl, A. Mairani, A. Mereghetti, P. Garcia Ortega, J. Ranft, S. Roesler, P.R. Sala, V. Vlachoudis, G. Smirnov, Overview of the FLUKA code, Annals of Nuclear Energy 82, 10-18 (2015)
[4] V. Vlachoudis, FLAIR: A Powerful But User Friendly Graphical Interface For FLUKA, in Proc. Int. Conf. on Mathematics, Computational Methods & Reactor Physics (M&C 2009), Saratoga Springs, New York (2009)
[5] H. Vincke, C. Theis, ActiWiz – optimizing your nuclide inventory at proton accelerators with a computer code, Progress in Nuclear Science and Technology (2014)
[6] P. Vojtyla, Models for assessing the dosimetric impact of releases of radioactive substances from CERN facilities to the environment – Air, CERN Internal report (2021)
Bibliography

## Slide 28
Activities of BDF target materials
TZM
Ta
W
Total PoT 2×1020 (5 yrs)
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
Activities – CDS target

## Slide 29
LL multiples of BDF target materials
TZM
Ta
W
Total PoT 2×1020 (5 yrs)
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
Multiples of Swiss Clearance Limits (LL)
CDS Target

## Slide 30
CDS target radionuclide inventories
1 month cool-down
Target | Material | Mass [kg] | Multiple LL | Multiple LA | A [Bq]
CDS | W | 695 | 1.9E+08 | 2.6E+08 | 9.2E+14
 | TZM | 271 | 1.1E+09 | 8.4E+07 | 1.8E+14
 | Ta | 28 | 1.7E+11 | 6.9E+08 | 9.8E+14
Ta cladding dominates for 1 month of cool-down due to Ta-182 (t½ - 115 d)
30 years cool-down
Target | Material | Mass [kg] | Multiple LL | Multiple LA | A [Bq]
CDS | W | 695 | 1.9E+05 | 1.1E+08 | 1.3E+12
 | TZM | 271 | 3.4E+05 | 3.1E+05 | 2.1E+12
 | Ta | 28 | 6.5E+05 | 1.5E+07 | 1.7E+11
Total PoT 2×1020 (5 yrs)
For 30 years of cool-down, the LL for Ta and W is dominated by Ba-133 (t½ - 10.5 y), while the LA by Gd-148 (t½ - 74.6 y)
For all materials, the total activity is dominated by H-3 (1.5E12 Bq for TZM, t½ - 12.3 y)

## Slide 31
Activation of water from cooling circuits was estimated
Shielding estimate around demineralization cartridges was performed assuming Be-7 to be stopped, but no target debris
  → 50 cm cylindrical concrete shielding was foreseen and for the roof of the area 165 cm concrete
Remaining water in circuit mostly contains H-3 with a concentration of around 0.5 GBq/l per year of operation
Due to the high H-3 production in the target (~18 TBq during 5 yrs operation), a significant contribution to the H-3 concentration in the water can come from H-3 out-diffusion from the target disks and subsequent trapping in the cooling water
In case of 1% of out-diffusion every 2 months (guess, currently no data available) and 100% trapping, the H-3 concentration from out-diffusion amounts to ~60 MBq/l every 2 months
The exchange of cooling water (1 m3) in one year would result in ~220 GBq of H-3 activity
PoT 1×1019 (1 yr)
Total Activity (Bq) for H-3 and Be-7
Results above do not take out-diffusion from target into account
Water activation – CDS

## Slide 32
Baseline Design (CDS) – Water cooled, W + TZM cladded w/ Ta2.5W
Investigation of alternative claddings (Nb, Nb-1Zr, Nb-10Hf-1Ti) → Nb-94 (half-life of 20k yrs) w/ higher waste disposal challenges
Alternative BDF target design studies
Alternative designs currently being studied in the TDR
Enclosed compact
Cu + W Target
W Helium cooled Target
D = 33 cm, L = 201 cm
Investigation of radionuclide inventories
Expected to be less critical from a radiological point of view
See talk “Design considerations for the BDF/SHiP production target” by R. Ximenes

## Slide 33
Total PoT 2×1020 (5 yrs) + 1 month cool-down
Tungsten – Total Activity (Bq)
Tungsten – Multiple of LL
Tungsten – Multiple of LA
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
Tungsten part
Radionuclide inventory of large W target

## Slide 34
Total PoT 2×1020 (5 yrs)
Tungsten – Multiple of LA
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
1 hour
1 day
Radionuclide | Halflife | 1h
Hf-178m | 4s | 1.2E+09
Gd-148 | 74.60y | 4.3E+08
W-187 | 23.9h | 3.2E+08
W-185 | 75.1d | 1.9E+08
Hf-172 | 1.87y | 1.5E+08
Ta-182 | 114.7d | 3.8E+07
Sum of all |  | 2.52E+09
Radionuclide | Halflife | 1d
Gd-148 | 74.60y | 4.3E+08
W-185 | 75.1d | 1.9E+08
W-187 | 23.9h | 3.2E+08
Hf-172 | 1.87y | 1.5E+08
Ta-182 | 114.7d | 3.8E+07
Yb-169 | 32.0d | 1.7E+07
Ta-183 | 5.1d | 1.7E+07
Hf-175 | 70.0d | 1.3E+07
Sum of all |  | 1.13E+09
For 1 h of cool-down, Hf-178m is dominant (48%) and wrt. to 1 month of cool-down also W-187 and W185 are relevant (Hf-178m comes from the decay of Ta-178m (2.36h half-life)
For 4 hours of cool-down, the important radionuclides are as for 1 hour
For 1 day of cool-down, Gd-148 becomes most important (38%)
Large W target – LA for short cool-down
Tungsten part

## Slide 35
Cladding materials:
  Tantalum –16.6 g/cm3
  Nb (ASTM R04210 – Type 2) – 8.6 g/cm3
  Nb-1Zr (ASTM R04261 – Type 4) – 8.6 g/cm3
  Nb-10Hf-1Ti (ASTM R04295) – 8.86 g/cm3
Total PoT 2×1020 (5 yrs), 1y cool-down
Total PoT 2×1020 (5 yrs)
Residual dose rates (uSv/h)
No difference in the residual dose rates for the various Nb claddings
Includes residual dose rates from surrounding material
Waste classification as FA-MA waste to be disposed of in Switzerland (no open pathway so far for such activation of Ta/Nb)
* LMA: Acceptance Activity Limits, if activity levels < LMA candidate for elimination in France
Alternative Claddings
Nb-94 half-life of 20300 yrs