## Slide 2: Beam Transfer for the High Intensity facility at ECN3 for the Search for Hidden Particles experiment
M. Fraser (SY-ABT-BTP) presenting on behalf of the HI-ECN3 Project Team
13th International Workshop on Neutrino Beams and Instrumentation (NBI2024)
AYA'S LABORATORY Quantum Beam Research Center (AQBRC), Tokai, Japan
7 – 10th October 2024
https://hiecn3.web.cern.ch

## Slide 3
Study Project Approved Project
Upgrade of beam intensity at North Area and SHiP beam-dump (BDF/SHiP) experiment approved recently…
… with ~ 62 MCHF (over 7 years) reserved for the HI-ECN3 project in CERN’s Medium-Term Plan ratified by CERN Council in June 2024.
Approved together with ~ 170 MCHF for consolidation of the North Area (NA-CONS project)
The HI-ECN3 project is a part of CERN’s…
“…broad diverse scientific programme, complementary to the collider and carried out mainly at the injectors: continuously upgraded and expanded (e.g. recently the ECN3 beam intensity upgrade at the North Area).”
Fabiola Gianotti

## Slide 4
SHiP has a bow wave…

## Slide 5
Francesco VELOTTI & Laurie NEVAY
Rui FRANQUEIRA XIMENES
Jean-Louis GRENARD
Francois BUTIN
Claudia AHIDIDA
Project Safety Officer (PSO): Melania AVERNA
Project & Experiment Safety Support (PESS) Correspondent: Jamie CURRIE
Fernando PEDROSA
Luigi ESPOSITO
Other HI-ECN3 contributions at NBI 2024
The Search for Hidden Sector experiment and its tau neutrino program
Current & future facilities session: Richard JACOBSSON
Radiation protection studies and considerations for the ECN3 high intensity project
Radiological & safety issues session: Claudia AHDIDA
BDF target station design
Secondary beamline session: Jean-Louis GRENARD
Design considerations for the BDF/SHiP production target
Target and beam window session: Rui Franqueira XIMENES
Experiment Project Leader: Richard JACOBSSON
SHiP Experiment Safety Correspondent: Letizia DI GIULIO
PL: Matthew FRASER
DPL: Claudia AHDIDA
HI-ECN3 Project Structure

## Slide 6
HI-ECN3 Operation
Operation out to late 2040s:
beyond HL-LHC
(frequency & length of LS’s TBC)
HI-ECN3
Commissioning
HI-ECN3
Operation
Today
NA available exclusively for EHN1/2 from mid-2029:
Test-beam users & other POT demanding experiments
(e.g. AMBER, MuonE)
ECN3 beam to dump in P42 for commissioning of TCC2
whilst construction ongoing
CERN Accelerator Schedule
NA-CONS
NA-CONS Phase II
(TBC)
NA-CONS Phase I
M. Lamont, Updated schedule for CERN’s accelerators, CERN Bulletin, 4 October 2024

## Slide 7
Consolidation & Upgrade
Transfer Tunnel (TT) 20:
inc. TT20 TED
TDC2: TT20 splitters
TCC2 Targets:
T2 / T4 / T6
SPS Extraction Straight
Timeline = completion in LS3 (2026-2029)
NA-CONS consolidation project
ECN3
TCC8: T10 / TAX
→ BDF
New Beam Dump (TIDVG4)
HI-ECN3 project
Timeline = completion before 2031
~ 1.7 km !

## Slide 8
BDF/SHiP in ECN3
L. Krzempek, BDF-SHiP Integration in ECN3, EDMS #2936008
ECN3
New
Access
Shaft
TCC8
Existing
Access Shaft
B918
B911
Beam from SPS
BDF’s Target Complex
containing a “thick” high-Z target (Mo/W)
Beam Dilution System
~ 300 kW (avg.)
~ 2.3 MW (spill)
1 second spill
4 Hz sweep
New Target
Service Building
SHiP experiment

## Slide 9
HI-ECN3 Project Timeline
TDR Phase
(Facility)
TDR extension?
Long Shutdown 3
Upgrades to NA with NA-CONS
LS4
Below freezing design for SCE!
(Detailed design for consultant before contractor Invitation to Tender)
July 2026
Critical path:
CE procurement & works
Dismantling
Beam on BDF Target

## Slide 10
SHiP beam parameter request
BDF Parameter | Value
POT / year [1019] | 4.0 (similar to CNGS)
Spill intensity [1013] | 4.2 (including conservative transmission)
Spill length [s] | ~ 1.0 on a 1.2 s flat-top (longer spills reduce achievable POT)
Spill quality | … to be formailsed with SHiP
BDF spills / year [106] | 1.0
Vertical emittance | can be as bright as possible for transmission, no splitting: final focus will be adjustable (~ 8×8 mm spot size, swept on target)
Total POT on BDF | 60×1019
Duration [years] | 15 (at 4×1019 POT/year)
BDF Parameter | Value
POT / year [1019] | 4.0 (similar to CNGS)
Spill intensity [1013] | 
Spill length [s] | ~ 1.0 on a 1.2 s flat-top (longer spills reduce achievable POT)
Spill quality | … to be formailsed with SHiP
BDF spills / year [106] | 1.0
Vertical emittance | can be as bright as possible for transmission, no splitting: final focus will be adjustable (~ 8×8 mm spot size, swept on target)
Total POT on BDF | 60×1019
Duration [years] | 15 (at 4×1019 POT/year)

## Slide 11
Field-free region
Horizontally deflected by the B-field
Continues straight: no B-field
Losses (~5%)
Shared delivery:
splitting
11
Matthew FRASER | HI-ECN3 Beam Transfer
NBI 2024 AQBRC, Tokai Japan 7 – 10 October 2024
T2
T4
T6
TT23
TT24
TT25
H2
H4
H6
H8
P4
P42
M2
EHN1
ECN3
EHN2
LSS2
P41, P61
SPS
TCC8
NA62
TT21
TT22
Shared Beam Delivery to ECN3

## Slide 12
T2
T4
T6
TT23
TT24
TT25
H2
H4
H6
H8
P4
M2
EHN1
ECN3
EHN2
LSS2
SPS
No interaction with TCC2 Target
No splitting
in TDC2
TT21
TT22
Dedicated Beam Delivery to ECN3: commissioning
P4 Beam Dump
TBIU
target
TBID
Dedicated delivery:
no splitting
B

## Slide 13
T2
T4
T6
TT23
TT24
TT25
H2
H4
H6
H8
P4
P42
M2
EHN1
ECN3
EHN2
LSS2
P41, P61
SPS
TCC8
No interaction with TCC2 Target
BDF/SHiP
No splitting
in TDC2
TT21
TT22
Dedicated Beam Delivery to ECN3

## Slide 14
How many protons for BDF / SHiP? (i)
Short CNGS-like 7.2 s SFTPRO cycle with a 1.2 s FT (~ 1 s spill)
SPS Page 1 during BDF prototype target test at T6 in 2018

## Slide 15
How many protons for BDF / SHiP? (ii)
Protons to ECN3 (BDF/SHiP)
Protons to TCC2 (other NA users)
North Area needs
~ 51019 protons/year…
a la CNGS (~41019 p+/y)
… but, slow extracted…
…unprecedented !
T. Prebibaj et al., SPS Operation and Future Proton Sharing Scenarios for the ECN3 facility, CERN-PBC-Notes-2023-001

## Slide 16
Slow Extraction from LSS2 in SPS

## Slide 17
Correlation between end of year activation dose rate (peak at electrostatic septum) and annual POT
Objective: to achieve a beam loss reduction factor of ~ 4 in stable, in long-term operation
SY-ABT mandated to investigate losses in 2015
?
Slow extraction beam loss reduction

## Slide 18
Radiation hazards of future operational scenarios can be predicted using data driven models: fit measured prompt beam loss [Gy] & proton flux [p+] to RP monitor [Sv/h]
Modelling induced radioactive in the SPS
Machine Learning: LightGBM: A Highly Efficient Gradient Boosting Decision Tree
F.M. Velotti, Induced radioactivity predictions from prompt beam loss readings, Slow Extraction Workshop 2024, Wiener Neustadt, February 2024
Semi-analytic:
t(function call) ~ minute
t(function call) ~ ms

## Slide 19
LSS4 gonio R&D:
~ 55% loss reduction
To be deployed operationally in 2024
Crystal Shadowing of electrostatic septa
L. Esposito et al., Progress on optimised TECA and MVRA production, SLAWG #76: Crystal shadowing and production, August 2024
F. M. Velotti et al., Phys. Rev. Accel. Beams 22, 093502 (2019)
down
To SPS
x
s
ZS
Unaffected beam
Deflected beam
up
TECS (LSS2)
(...)
Deflected beam
TECA (LSS4)
To TT20
circulating
deflected
LSS2 gonio already operational with 20% loss reduction
Thin, bent silicon crystal ~ 2 mm thick, 2 mm long

## Slide 20
Objective: achieve an even higher loss reduction factor (x10?!) with advanced crystal technology (multiple thin, bent crystals aligned for Volume Reflection) installed in SPS
Prototype might be available for tests in 2025 (mechanics developed in-house at CERN)
Crystal Shadowing of electrostatic septa (ii)
L. Esposito et al., Progress on optimised TECA and MVRA production, SLAWG #76: Crystal shadowing and production, August 2024
F. M. Velotti et al., Phys. Rev. Accel. Beams 22, 093502 (2019)

## Slide 21
Low-density septa
Today
Residual dose rate after 1 week
Dream world
20x reduction!
Efforts focused on tank material as the best candidate: feasible + factor 2 dose reduction
Selection of alloy → Al 5083
Design of low-Z flanges → Bimetallic flange
Buckling tests → mass reduction of 2.7x w.r.t. current tank
Manufacturing → mock-up + welding tests
H. Vincke, Radiological impact of the material choice of the ZS element, SLAWG #74, Nov 2023
F. Lackner et al, Improvements of the SPS slow extraction electrostatic septum, TUPC72, IPAC2024

## Slide 22
TCC2 Upgrades

## Slide 23
Beam transfer from SPS to EC3
A huge effort is ongoing to improve understanding of old 1970’s transfer line equipment
A. Gorn et al., Optics rematching between TT24 and P42 primary beam lines within the HI-ECN3 study project at CERN 2024, TUPC71, IPAC 2024
L. Dyks, Characterisation of the optics of the TT24 and P42 beamlines in the CERN SPS North Area, IPAC 2024

## Slide 24: Existing TCC2 Target T4 Region
Today, operation of EHN1 (H6/H8 test beams) is coupled with ECN3 (NA62)
Secondary particles for EHN1 are selected using magnet wobbling system, whilst protons not interacting with the target are transmitted to NA62
x
s
T4 Target
To EHN1: H8
T4 XTAX
To ECN3: NA62
To EHN1: H6
F. Metzger et al, Beam line and parameters, 30th SHiP collaboration meeting, ALU Freiburg, 1 – 4 October 2024

## Slide 25
Upgrade for BDF/SHiP
T4
A pulsed magnet allows us to decouple proton beams on the dedicated HI-ECN3 cycle in the horizontal plane (in addition to vertical separation to avoid target)
To EHN1: H8
To ECN3: NA62
To EHN1: H6
F. Metzger et al, Beam line and parameters, 30th SHiP collaboration meeting, ALU Freiburg, 1 – 4 October 2024

## Slide 26
T4 XTAX absorber in TCC2
Looking downstream from on top of T4 target
H6
H8
To ECN3
To avoid scattering BDF/SHiP beam on air the ECN3 side of XTAX will be replaced by a fixed absorber with a vacuum chamber
Urgent design effort ongoing !

## Slide 27: TCC2 Target System Upgrade
  Reduce beam loss in P42 transfer line to ECN3:
    Putting XTAX under a continuous primary vacuum of ~10-3 mbar will reduce the beam loss in the shallow transfer tunnels from TCC2 to ECN3 caused by scattering of BDF/SHiP (by up to a factor ~ 50!)
L. Dyks, Beam loss studies for the P42 beamline at the CERN SPS north area, TUPC73, IPAC 2024
TCC2: T4
TCC8: BDF
P42 transfer line
Detailed design underway

## Slide 28
Dilution

## Slide 29: BDF Dilution System
Y. Dutheil, SPS BDF CDS, CERN Yellow Report, CERN-2020-002
Present baseline:
Slow sweep = 4 Hz over a 1 second spill
/2 scheme: independently powered laminated dipole magnets:
  2H + 2V magnets (~ 0.5 mrad, 0.7 Tm per plane)
  de-phased by 90 degrees to give circular spill
Beam profiler(s) to check beam position, size & sweep post-operation
Challenge: protection of the target critical, loss of dilution during single spill will likely damage the target
Independent interlock system needed for redundancy:
  Independent DCCTs measurement current in dilution dipole magnets
  Dedicated “live” beam position monitoring of beam during its sweep
Failure 2H OR 2V
Failure 1H OR 1V
Failure 1H AND 1V
Failure Scenario:

## Slide 30
Summary
BDF/SHiP was approved in 2024
CERN has reserved budget in its MTP for a new facility in ECN3 under the project named HI-ECN3
We are under pressure to meet NA-CONS deadlines for Long Shutdown 3 and in the last 6 months we have focused on beam delivery in the North Area
Some ~ 10 years of slow extraction R&D will converge into a Technical Design Report as part of the HI-ECN3 TDR
HI-ECN3 TDR to be published in 2026, aiming at beam on target in 2031 !