## Slide 1: Beam Delivery to the Target
L. Nevay, F. Velotti, D. Banerjee, M. Fraser, A. Gorn, F. Metzger, T. Prebibaj.
21st February 2025
Final focus system, instrumentation and dilution

## Slide 2: BDF / SHiP in the CERN Complex
SPS
PSB
PS
ISOLDE
nTOF
East Area
North Area
including BDF/SHiP
AD
LHC
HiRadMat
AWAKE
Linac4
Schematic not to scale
“PSB” = “booster”
1
2
3
4
5

## Slide 3: Supercycles
The injector complex delivers protons to multiple facilities in parallel, typically over ~31 weeks per year
  PSB → PS, ISOLDE
  PS → SPS, nTOF, EAST, AD
  SPS → LHC, North Area, AWAKE, HiRadMat
A supercycle is a sequence of cycles directed to the different facilities
The supecycles are defined based on the accelerator capabilities & facility requests
The proton sharing between facilities is achieved using supercycles
Below is a typical supercycle
See T. Prebibaj’s talk for details:
https://indico.cern.ch/event/1469359/contributions/6233099/
T. Prebibaj

## Slide 4: SPS Slow Extraction
The beam in the SPS is excited with a 3rd order resonance in the horizontal plane
RF gymnastics are performed first to reduce momentum spread and give the most uniform distribution in time
High amplitude particles are extracted with a thin electro-static septum
The beam extracted is nominally uniform in time with no bunch structure
Electrostatic Septum
(ZS)
Quad
QFA216
Magnetic
Septum (MST)
TPST
mask
North
Area
Magnetic
Septum (MSE)
Quad
QDA217
Bumper
Quad
QFA218
Quad
QDA219
horizontal phase space

## Slide 5: Shared and Dedicated Beam
The beam from the SPS is normally split with magnetic splitters twice
  the vertical position on the splitter determines the sharing ratio
  the 3 beams are directed onto 3 targets producing 5 secondary beams and 1 left-over primary beam
For BDF / SHiP, a new set of optics will be used that bypass the splitters without splitting (low losses)
Shared with splitting:
Dedicated delivery:
no splitting
B
field free region
horizontally deflected
straight ahead
losses (~5%)
B
vertical beam envelopes
SPS
P42

## Slide 6: BDF Beam and SPS Supercycle Composition
Nominal 4 x 1013 protons in a 1s spill to BDF/SHiP
  the 1 s of continuous beam is inside a 7.2 s overall cycle
A study has shown 5 x 1013 protons / spill would mean ~40% more spills to other North Area users
  MDs this year will investigated SPS intensity limits
  previously operated at 4.8 x 1013 for CNGS (fast extraction)
  greater North Area availability from a proton-sharing point of view
Nominal Design Parameter | Value
Beam type | proton
Beam momentum [GeV/c] | 400
Beam pulse intensity [1013 p] | 4.0
Spill length [s] | 1
Beam pulse power [kW] | 2560
Average beam power [kW] (7.2 s) | 356
POT [1020 p over 15 years] | 6.0
Nominal Design Parameter | Value
Beam type | proton
Beam momentum [GeV/c] | 400
 | 4.0
Spill length [s] | 1
Beam pulse power [kW] | 2560
Average beam power [kW] (7.2 s) | 356
 | 6.0
SFTSHiP
SFTPRO
356 kW
232 kW
Beam power
on BDF target
15.6 s
7.2 s
T
T2
T4
T6
H2
H4
H6
H8
M2
EHN1
ECN3
EHN2
SFTSHiP
cycle
P42
splitters
BDF/SHiP
Rest of North Area

## Slide 7: P42 Final Focus & Dilution System
The beamline “P42” that delivers protons to ECN3 will be modified in the final 200 m
  quadrupoles will be removed and shifted to create a much larger beam
  beam size and ratio will be adjustable independently
  100 m from last magnet to front of BDF target
A dilution system of N dipoles will sweep the beam in a circle
  number of magnets / plane depends on possible failures and being studied
No sweeping and a large beam size is possible, but we must stay clear of the aperture
dilution system
today
future
BDF
Beam size can easily be produced from 𝜎 = 1 - 20 mm, but choice affects design of vacuum chamber
There will be beam halo and the aperture must be clear of this

## Slide 8: Nominal and Accident Scenarios
Magnets along the beamline can fail
  change in beam position and size as the field drops
Beam loss monitors will be placed on each quadrupole to cut the beam quickly if losses high
A crucial failure mode will be that of the dilution system magnets and power supplies
1 magnet per plane
2 magnets per plane
Patterns on target vary depending on the magnet and exact time of failure

## Slide 9: Beam Instrumentation Requirements
Beam Delivery & Experiment
Beam position during spill
    can be given after each spill to the experiment
    ensure sweeping radius
  Beam intensity (< 3% absolute error)
Target
Beam position to ensure sweeping
Beam spot size each spill
Avoid front-mounted diagnostics as complicated to access / maintain
The strategy for beam instrumentation immediately before BDF is being studied
Background for the experiment created by matter interaction with the beam being studied
  muons far from the axis could possibly be captured into the experiment (to be studied)
We must align the beam axis well w.r.t. the target and know the beam size and sweep radius
Foresee an instrumentation package 10 - 20 m upstream of the front of the target
Diagnostics must give feedback during the spill on a short time-scale
  avoid slow, high-level software interlocks

## Slide 10: Interlocking
The baseline maximum intensity allowed without sweeping is 2 x 1012 protons
  this corresponds to a maximum of a 50 ms spill at the nominal extraction intensity
Fast interlocks can act on the time-scale of O(100 μs) and cut the SPS extraction
The current of most transfer line power converters will be monitored
  this includes the ramp across the spill to compensate for the shift in momentum
Beam loss monitors (BLMs) will be placed beside each quadrupole and in key locations
We will consider an independent method of verifying the beam sweeping pattern on the target
  e.g. an independent current measurement
  or, 4 beam loss monitors for position via asymmetry of back-splash

## Slide 12: Tunnel Names
TT83
TCC2
TDC8
TT85
TCC8
ECN3