## Slide 1: Beam Matter studies for the target system
G. Mazzola, L.S. Esposito (SY-STI-BMI) Acknowledgements: M. Calviani, J-L. Grenard, R. Franqueira Ximenes, M. Parkin, A. Romero Francia (SY-STI-TCD), M. Fraser, F. Velotti (SY-ABT-BTP), R. Jacobsson (EP-SME-SHP), C. Ahdida, O. Pinto (HSE-RP-AS)
1st Beam Dump Facility (BDF) Targetry Systems Advisory Committee (TSAC) – March 4-6, 2025

## Slide 2: Outlook
FLUKA simulations and motivation
Geometry and beam parameters
Particle yields and energy deposition in various systems
DPA and gas production in target
Radiation fields around target complex and R2E considerations
Conclusion and outlook

## Slide 3: FLUKA simulations and motivation
FLUKA is a general-purpose Monte Carlo code for particles transport and interaction with matter
Results coming from FLUKA.CERN simulations are used as input for Finite Element Analysis (FEA) to validate the design of different Beam Intercepting Devices (BID) distributed along the accelerator lines

## Slide 4: Geometry and beam parameters
Top view of FLUKA model for BDF/SHiP
Top view of BDF/SHiP integration model – EDMS 2936008
Geometry design
Beam parameters
Target complex
Magnetized Hadron Stopper (MHS)
Warm Muon Shield (MS)
Beam parameters of the BDF target operation – CDS (Comprehensive Design Study) book
Representation of beam sweep (left) and CDS design target for BDF (right)

## Slide 5
Target
Magnetized Hadron Stopper (MHS)
Warm Muon Shield (MS)
Vacuum vessel
Concrete shielding
Iron shielding
Proximity shielding
Particle yields and energy deposition in various systems

## Slide 6: Geometry: Target core designs
TZM 64 cm
25 cm
W 80 cm
25 cm
33 cm
201 cm
123 cm
25 cm
Different core designs evaluated to maintain/improve the SHiP physics reach with respect to the CDS design
  Option 1) CDS target – sweep σ = 8 mm Option 2) CDS target – sweep σ = 16 mm
  Option 3) W target 1.2 m – sweep σ = 8 mm Option 4) W target 2 m – sweep σ = 8 mm
W-He target
  Option 5) Optimum W target – sweep σ = 8 mm
33 cm
201 cm
119 cm

## Slide 7: Geometry: Reduction of MHS length
As requested by SHiP, a shorter MHS would allow to reduce the aperture of the SC magnet
  Full W target 1.5 m long, ⍴ = 19.3 g/cm3, ⌀ = 25 cm
  Cast-iron proximity shielding length downstream 25 cm
  W plug ⍴ = 18.5 g/cm3, ⌀ = 30 – 25 cm
  Hadron absorber: 2.3 m long (from 4.5 m)
  sweep σ = 8 mm
2.3 m
Option 6) New baseline
4.5 m
CDS geometry

## Slide 8: Geometry: Reduction of MHS length
As requested by SHiP, a shorter MHS would allow to reduce the aperture of the SC option:
  Full W target 1.5 m long, ⍴ = 19.3 g/cm3, ⌀ = 25 cm
  Cast-iron proximity shielding length downstream 25 cm
  W plug ⍴ = 18.5 g/cm3, ⌀ = 30 – 25 cm
  Hadron absorber: 2.3 m long (from 4.5 m)
  sweep σ = 8 mm
2.3 m
Option 6) New baseline
4.5 m
Option 1) CDS target + MHS + MS

## Slide 9: Target: Physics parameter metrics
For each target design, signal production and background suppression are evaluated – SHiP CM
Spectra of charmed particles produced in target Metrics used as trace for SHiP desired signal
Spectra of pions exiting target downstream Metrics used for background suppression evaluation
Spectra of muons exiting MHS Metrics used for background suppression evaluation
Note the excess of 1 GeV muons after the shorter MHS for the new baseline.
Option 1) CDS target – sweep σ = 8 mm
Option 2) CDS target – sweep σ = 16 mm
Option 3) W target 1.2 m – sweep σ = 8 mm
Option 4) W target 2 m – sweep σ = 8 mm
Option 5) Optimum W target – sweep σ = 8 mm
Option 6) W target 1.5 m – MHS 2.3 m – sweep σ = 8 mm
MHS
MHS -

## Slide 10: MS: Neutrino distributions
Comparison Spectra of ν exiting MS
Option 1 Phase space distribution ν
Considered all neutrinos and anti-neutrinos flavors
Simulated 40 M protons on target
Downstream the MHS, similar reduction factor obtained going from CDS to full W target
The new baseline sits in between CDS and Options 3/4
Option 1) CDS target – sweep σ = 8 mm
Option 2) CDS target – sweep σ = 16 mm
Option 3) W target 1.2 m – sweep σ = 8 mm
Option 4) W target 2 m – sweep σ = 8 mm
Option 5) Optimum W target – sweep σ = 8 mm
Option 6) W target 1.5 m – MHS 2.3 m – sweep σ = 8 mm
MHS

## Slide 11: Target: Energy deposition
Evaluation of energy deposited in the core for the different target designs
Verification of thermo-mechanical properties and design optimization
Maximum energy density deposited by beam W target with different beam delivery (sweep 50 mm radius, 8 mm and 16 mm σ)
Maximum energy density deposited by beam For all designs same beam delivery (sweep 50 mm radius, 8 mm σ)
Results normalized to 4e13 p/cycle with 7.2 s/cycle

## Slide 12: Target: Decay heat
Residual maximum power density deposited W-He target, beam sweep 50 mm radius 8 mm σ for 5 years with 4e19 p/year
For CDS design, the decay heat in the target material is considerable and it is significantly driven by the cladding.
The possibility of a Loss-of-Coolant Accident (LOCA) poses a critical safety risk. This risk leads to several potential problems
  Uncontrolled temperature and pressure increase
  Potential risk of core melting (due to decay heat)
  In case of cladding rupture, the release of radioactive material
Reducing/avoiding Ta cladding as mitigation strategy

## Slide 13: Proximity shielding: Energy deposition
The proximity shielding is placed inside the vacuum vessel, and it surrounds the whole target → high energy deposited, and active cooling required
Proximity shielding
Top view and side view of BDF target complex Proximity shielding highlighted
Cast iron
Top view and side view for energy density deposited in BDF target complex. Results normalized with 4e13 p/spill
Parameters and integral energy deposited in proximity shielding

## Slide 14: MHS and MS: Energy deposition
The Magnetized Hadron Stopper (MHS) and the Muon Shield (MS) are fundamental elements in the background suppression for SHiP:
  MHS aims to stop all hadrons escaping the target and applies a first sweep to the muons through a magnetic field. Energy deposition evaluated in the coil and yoke to appropriately design the element.
  MS is composed by a series of magnetized blocks which sweep horizontally the muons exiting downstream BDF creating the “ship” shape. Options for a fully warm and hybrid (super conducting + warm) MS are being investigate.
Effect of 1.5 m W target + plug + reducing the MHS
CDS geometry. Cross section for energy density deposited. Results normalized to 4e13 p/spill
at the start of MHS
at the start of MS
Yearly value of TID for the coil and yoke’s center at start and at the end of MHS. 4e19 p/year considered.
MHS
MHS
MHS
MHS

## Slide 15
DPA and gas production in target
Core (W blocks)
Vessel
Window

## Slide 16: DPA in target
Evaluation of displacement per atom in the target’s core evaluated with different models and used as figure of merit for the radiation induced damage:
    ARC-DPA model assigns an energy-dependent damage cross section. Parameters are needed for DPA evaluation.
Maximum yearly DPA, computed with different models, along W target Beam sweep 50 mm radius, 8 mm σ
Distribution of DPA-NRT in W target with beam sweep 50 mm radius, 8 mm σ. Values averaged angularly.
Maximum yearly DPA-NRT along W target with different beam delivery (sweep 50 mm radius, 8 mm and 16 mm σ)
For W with ARC-DPA model, parameters: Ed = 70 eV, barc = -0.564 and carc = 0.119 (ref)

## Slide 17: Gas production in target
Evaluation of residual gas (H and He) production in target core. Gas production can generate concern in safety and can change material properties
Maximum density of hydrogen isotopes along W target with beam sweep 50 mm radius, 8 mm σ after 5-year operation
Maximum density of helium isotopes along W target with beam sweep 50 mm radius, 8 mm σ after 5-year operation

## Slide 18
BDF target complex
Muon Shield (MS)
Ventilation room
911 shaft door
SHiP detectors
TCC8
ECN3
Radiation fields around target complex and R2E considerations

## Slide 19: R2E lesson from CNGS experience
During the 2007 CNGS physics run, 8×1017 p.o.t. delivered, i.e., ~2% of a nominal CNGS year
Single event upsets (SEU) in the electronics of the ventilation units caused control failure and interruption of communication
Critical review of installation of all electronics in CNGS:
installing thick radiation shields in situ
moving all the control systems into a protected area
Electronics
Ventilation Units
CV,crane,
fire
This triggered the creation of the R2E Project, with large impact for LHC operation and HL-LHC
 This must be considered for any new facilities

## Slide 20: Radiation field around the target complex
Protons of 400 GeV/c impacting on a 12 λ long target (CDS) generate a high radiation field all around the target and the target complex
  Constraints for radiation protection and radiation to electronic aspects → Great amount of shielding required
  On the other side, the radiation field can be exploited for material and electronics irradiation tests → (backup slide)
Side view of neutron (left) and pions (middle) around target complex. Right, top view of muons fluence. Results normalized considering 4e13 p/spill. Plots averaged around BDF target (CDS design).
Radiation field results to be dominated by neutrons, pions stopped in MHS while muon exit downstream BDF

## Slide 21: R2E in TCC8
The radiation field generates constrains due to radiation to electronic effects mainly leading to cumulative damage and Single Event Effect (SEE)
Some general limits (EDMS) are defined for specific R2E quantities (Indico) to characterize an area as radiation-safe for electronics.
General limits for R2E considerations
The radiation levels in different areas which will store active electronics has been evaluated:
  Ventilation room above BDF in TCC8
  911 shaft door
  SHiP detector in ECN3
Similar plots present also in BDF/SHiP proposal, considering previous integration model of BDF
Side view of BDF and ventilation room in TCC8. ThNeu yearly fluence averaged along target. Grey color represents the limit of 3e7 cm-2/year

## Slide 22: R2E in 911 shaft and ECN3
The radiation levels in different areas which will store active electronics has been evaluated:
  Ventilation room above BDF in TCC8
  911 shaft door
  SHiP detector in ECN3
Top view of BDF and 911 access shaft. ThNeu yearly fluence averaged at beam height. Grey color represents the limit of 3e7 cm-2/year
General limits for R2E considerations
Top view of yearly thermal neutron equivalent fluence (left) and Total Ionizing dose in one year (right) in ECN3. For left plot, the grey color represents the limit of 3e7 cm-2/year. In the right plot, value of 10 Gy/year represented by red contour

## Slide 23: Conclusion and outlook
Different studies have been conducted for BDF target: building upon the solid baseline design (CDS), the goal was to optimize it and explore new solutions
This presentation summarizes the main results (energy deposition, DPA, and radiation levels).
In addition, studies have been performed on future targets for irradiation, the SC MS, and parasitic irradiation facilities (info in backup slide)
Target design optimization is nearly finalized. A tungsten-helium (W-He) cooled target offers promising benefits in terms of mechanical properties and background reduction
New simulations are planned after incorporating the updated design into the target facility model for the TDR

## Slide 25: Radiation field and irradiation stations
The neutron-dominated radiation field generated around BDF is of interest for Electronics and Materials irradiation and Nuclear Activation
Parasitic irradiation of samples in well-defined irradiation stations
HI-ECN3 Irradiation Opportunities Workshop
BHFIM2
BHFIM1
(BEAS) R2E@4m
Vacuum
vessel
Rabbit channel
BRIS
Top view of the BDF target complex with CDS design for target. Highlighted the proposed irradiation stations.
Integral particles fluence in different irradiation stations