## Slide 2: Radiation protection considerations for the target complex
C. Ahdida, P. Bertreix, G. Dumont, F. Malacrida, G. Mazzola, O. Pinto, C. Theis, Hl. Vincke, Hz. Vincke, P. Vojtyla
1st BDF Targetry Systems Advisory Committee (TSAC) 4-6th March 2025

## Slide 3
Overview of RP Challenges at HI-ECN3
Target Complex Design Optimization
Target Studies
Service building considerations
Outline

## Slide 4
CERN’s SPS North Area
HI-ECN3 at ECN3
Key beam parameters of BDF/SHiP
 | BDF
Intensity (p/spill) | 4×1013
Spill duration (s) | ≥1
Cycle length (s) | ≥7.2
Avg. beam power (kW) | 356
Average intensity (p/s) | ≤5.6×1012
Annual POT | 4×1019
Duration (years) | 15
Total POT | 6×1020
8m soil
TCC8 cross-section
HI-ECN3: a state-of-the-art high intensity experimental facility in ECN3 with RP optimization for full lifecycle
Advantage of underground cavern with shielding created by the soil and beam dump concept
RP challenges
    High beam energy and intensity as well as high POT leading to high prompt radiation and activation levels
    Proximity to surface, experimental and public areas
    Losses during beam transfer (not covered here)

## Slide 5
Target Complex Optimization

## Slide 6
RP studies based on FLUKA MC simulations were performed for a design optimization of BDF/SHiP@HI-ECN3
ALARA approach Optimization required to ensure that exposure of personnel to radiation and radiological impact on environment are As Low As Reasonably Achievable
Prompt radiation Reduce prompt radiation to comply with radiation area classification in the surrounding accessible areas as well as the 1 mSv limit at the CERN fence
residual radiation Limit activation of target and experimental area to reduce residual dose rates to be compatible with an adequate area classification
Air and soil activation Reduce activation of air and its releases into the environmental. Limit soil activation (3H<1000 Bq/kg, 22Na<50 Bq/kg) and transfer to groundwater
Environmental impact Reduce environmental impact from prompt radiation and releases of activated air to fulfill CERN’s dose optimization objective for the public of <10 uSv/year
CERN’s radiation area classification
BDF/SHiP design optimization

## Slide 7
Stainless steel
Concrete
US1010
Cast iron
Target complex & muon shield, Created using FLAIR [4]
Moraine
TCC8
W-TZM target
Magnetised Hadron Stopper (MHS) 1.6 T
11 m
Moraine
1.6 m
1.6 m
8 m
Muon shield 1.7 T
ECN3
A detailed BDF/SHiP target complex together with the muon shield was implemented in FLUKA [1-3]
Optimization of BDF shielding and re-use of existing, already activated TCC8/TT7 shielding blocks, while maintaining SHiP physics performance
Shielding embedded in vacuum vessel allowing to reduce air activation
Floor shielding reinforcement to limit soil activation
FLUKA geometry includes the full underground TCC8/ECN3 cavern and surrounding galleries, tunnels, rooms, etc.
Ground profile data from CERN’s Geographic Information System and technical drawings were used to model the surrounding ground
FLUKA hosted by CERN [1-3]
4.8 m
Floor shielding (13.3 m3)
1 m
Vacuum vessel
Muon shield
~180 m³ of cast iron + US1010
~360 m³ of concrete
BDF/SHiP FLUKA model

## Slide 8
Cross-sectional view
Side view
Along y-axis
Shielding design is well optimized for the prompt radiation
Annual limit of Non-designated Area on CERN domain
Avg. intensity of 5.6×1012 p/s
(-20 cm < x < 80 cm)
(13260 cm < z < 134380 cm)
(-20 cm < x < 80 cm)
(13260 cm < z < 13380 cm)
Prompt radiation in target area

## Slide 9
Cross-sectional view, target level
Along x-axis, working height
Upstream of vessel w/o upstream shielding Preliminary worst case manual intervention scenario
The shielding design contains well the high residual dose rates reaching in the central target region several 10 Sv/h after 1 month of cool-down requiring remote handling
The residual dose rates outside the shielding are < 1 µSv/h
1 month cool-down
x [0,40]
x_beam = 26 cm
Shielding removed
After removal of the shielding upstream of the vessel, residual dose rates of several 100 µSv/h are expected
Supervised Radiation Area on the sides
Further optimization by movable shielding
Future detailed handling studies planned
Total PoT 6×1020 (15 years)
(13240 cm < z < 13390 cm)
(15 cm < y < 45 cm)
(13240 cm < z < 13390 cm)
1 month
(-15 cm < x < 80 cm)
Residual radiation in target area
100 rem = 1Sv

## Slide 10
Radioactive waste production
To distinguish areas of radioactive waste from conventional ones the Swiss clearance limits (LL) were used
The following sum rule was applied for material containing a mixture of radionuclides
The most activated parts are the target and the iron shielding elements (also for 30 years of cooling)
The minimisation of radioactive waste is being considered in the shielding design by having a modular shielding such that activated parts can easily be separated from non-radioactive parts
1 year of cooling (CDS design)
ai - specific activity (Bq/g) of the ith radionuclide LLi - respective Swiss clearance limit for the radionuclide i n - number of radionuclides present
SPS Beam Dump Facility - Comprehensive Design Study, CERN-2020-002
Notes: An activation study was performed to predict the amount and the characteristics of the radioactive material present in the bdf target area. To distinguish areas of radioactive material from conventional ones the liberation limits from the Swiss legislation [7] were used. To exempt a material containing a mixture of radionuclides of artificial origin from any further regulatory control, the following sum rule shall be respected ∑1_(𝑖=1)^𝑛▒〖𝑎_𝑖/〖𝐿𝐿〗_𝑖 <1〗
where a𝑖 is the specific activity (Bq/g) of the ith radionuclide of artificial origin in the material, LL𝑖 is the respective Swiss liberation limit for the radionuclide i in the material and n is the number of radionuclides present. If the sum rule is not fulfilled, the material is radioactive according to the Swiss legislation.
Either this unit is wrong or a conversion factor is missing in the formula as the LL is given in Bq/g.
I would also be careful talking about total activity as then the rule is different as one compares to a fraction of kilo-LL.
Thanks for spotting. It was from an old document with LE (Bq/kg).

## Slide 11
Soil and air activation
Specific activity of 3H and 22Na in the soil below TCC8 (most critical area)
3H
22Na
Air activation
Thanks to floor iron shielding, 3H and 22Na activity concentrations in the soil are below respective design limits
A hydro-geological study is underway, which will allow to refine the design limits and possibly allow to reduce the required shielding
Total PoT 6×1020
PoT 4×1019 per year
Activation of air in target complex area were studied
Production of radionuclides evaluated with FLUKA in combination with ActiWiz [5]
Air recycling: build-up of radionuclides during operation w/o air extraction and 30 min cooldown time before air release
Continuous release: long-term continuous releases without delay (very conservative for environmental impact)
Flush of target complex with fresh air before any access will further reduce specific airborne radioactivity
H-3 out-diffusion/ejection nor potential leakage of He-cooling system not yet considered here
1 Person working 40h/w, 50w/y with standard breathing rate in activated air with CA = 1 receives 20 mSv
1

## Slide 12
Continuous air release yields 3 nSv/year (main contributors: N-13, Ar-41, C-11, O-15) and is thus well below the annual dose optimization objective of CERN
Additional contribution from H-3 out-diffusion/ejection and potential leakage of He-cooling system to be quantified
Environmental impact
Prompt radiation aboveground downstream ECN3
Dose from air releases
Used max. dose coefficients from different age groups [6]
Positions of nearby population groups
Effective dose estimates
Dose from stray radiation
Release point
Annual limit of Non-designated Area on CERN domain and at CERN fence (1 mSv/y) as well as dose optimization objective for members of the public (10 uSv/y) are by far met
CERN fence
H-3 release due to air activation of ~80 kBq (w/o out-diffusion)
100 rem = 1Sv
PoT 4×1019 per year
Annual effective dose

## Slide 13
BDF Target Studies

## Slide 14
CDS target design
D 250 mm
~ 1500 mm
Water-cooled W + TZM target (136 cm) cladded with Ta2.5W
Pursued during the comprehensive design phase → C. Ahdida et al., SPS Beam Dump Facility - Comprehensive Design Study, CERN-2020-002
Prototype + test with beam + post irradiation examination (see talk R. Ximenes)

## Slide 15
Longitudinal cut along the target
The residual dose rates of the target were studied for 5 years of operation and different cool-down times
The highest dose rates are in the order of 100 Sv/h after 4 hours of cooling and a few Sv/h after 1 year
Even after 30 years, dose rates at 40 cm still of the order of a few mSv/h
Shielding cask for handling to be designed allowing to also contain potential contamination
Shielded storage area and service cell to be designed
Shielding further to be foreseen for transport and final disposal (< 2 mSv/h)
Total PoT 4×1019 (5 yrs)
4 hours cool-down
1 year cool-down
30 years cool-down
1 day cool-down
CDS target – Residual radiation

## Slide 16
LA multiples of CDS target materials
TZM
Ta
W
Total PoT 2×1020 (5 yrs)
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
CDS target – Radionuclide inventories
Total PoT 2×1020 (5 yrs) + 1 month cool-down
Target | Material | Mass [kg] | Multiple LL | Multiple LA | A [Bq]
CDS | W | 695 | 1.9E+08 | 2.6E+08 | 9.2E+14
 | TZM | 271 | 1.1E+09 | 8.4E+07 | 1.8E+14
 | Ta | 28 | 1.7E+11* | 6.9E+08 | 9.8E+14
*Dominated (99.9%) by Ta-182 (115 d half-life)
Authorization Limit (LA) means the value corresponding to the abs. activity level of a material above which handling of this material is subject to mandatory licensing. It is based on the risk of inhalation.
Clearance Limit (LL)

## Slide 17
Cladding materials:
  Tantalum –16.6 g/cm3
  Nb (ASTM R04210 – Type 2) – 8.6 g/cm3
  Nb-1Zr (ASTM R04261 – Type 4) – 8.6 g/cm3
  Nb-10Hf-1Ti (ASTM R04295) – 8.86 g/cm3
Total PoT 2×1020 (5 yrs), 1y cool-down
Total PoT 2×1020 (5 yrs)
Residual dose rates (uSv/h)
No difference in the residual dose rates for the various Nb claddings
Includes residual dose rates from surrounding material
Waste classification as FA-MA1 waste to be disposed of in Switzerland (no open pathway so far for such activation of Ta/Nb)
LMA: Acceptance Activity Limits, if activity levels < LMA candidate for elimination in France
1 Low and intermediate activation waste for elimination in Switzerland
CDS target – Alternative Claddings
Nb-94 half-life of 20300 yrs

## Slide 18
CDS target – Water activation
Activation of water from cooling circuits was estimated
Shielding estimate around demineralization cartridges was performed assuming Be-7 to be stopped, but no target debris
  → 50 cm cylindrical concrete shielding was foreseen and for the roof of the area 165 cm concrete
Remaining water in circuit mostly contains H-3 with a concentration of around 20 MBq/l per year of operation (~4000 litres)
High production of H-3 in target materials (~15 TBq during 5 years of operation)
Quantification of out-diffusion/ejection with given operational conditions are crucial for evaluating the actual amount of H-3 activity in the cooling water
PoT 4×1019 (1 yr), 4 hours cool-down
Total Activity (Bq) for H-3 and Be-7
Results above do not take out-diffusion from target / shielding into account

## Slide 19
BDF target prototype w/ in total 14 h irradiation in TCC2, leading to 2.4E16 PoT
Target activation was measured and compared to FLUKA simulations showing excellent agreement
Cooling water activation was estimated with FLUKA
Estimated residual dose rate after 1h of cooling at 40 cm from the cartridge is 18.7 mSv/h, while the PMI monitor measured 16.9 mSv/h
Both samples showed the presence of high-Z spallation products some of them could have been produced in the target materials
Water-cooling filter with debris was analysed via EDX
  No peaks were found for Ta, W, Mo or Ti
  Metallic particle (Al, Ca, Fe, Cl, Fe, Cr)
Benchmark of residual dose rates (mSv/h)
Radionuclides in water samples
Water samples were analysed by liquid scintillation and gamma spectrometry
CDS target – Prototype tests

## Slide 20
19x W blocks (L1500 mm) (D250 mm)
He
cooling
P+
W target design
He-cooled, Pure W Core, potentially cladded (tbd)
Improved physics performance (see talk G. Mazzola)
Prototype and beam testing in 2025 and 2026 (see talk R. Ximenes)

## Slide 21
LA multiples of W target
Total PoT 2×1020 (5 yrs), 1 month cool-down
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
W target – Radionuclide inventories
Radionuclide | Half-life | Multiple of LA | Contribution
Gd-148 | 74.60 y | 4.8E+08 | 59%
Hf-172 | 1.87 y | 1.5E+08 | 18%
W-185 | 75.1 d | 8.8E+07 | 11%
Ta-182 | 114.7 d | 2.7E+07 | 3%
Yb-169 | 32.0 d | 9.7E+06 | 1%
Hf-175 | 70.0 d | 9.2E+06 | 1%
Sum of all |  | 8.0E+08 | 
LA for short-cool-down times:
For 1h (4h), Hf-178m (4s half-life) produced via Ta-178m (2.36h half-life) is dominant
For 1d, Gd-148 (74y half-life) becomes most important (as for 1 month)
Investigation of outgassing of radionuclides (incl. H-3) and possible formation of volatile chemicals ongoing → important for understanding of radiological risks connected to He-cooling circuit
  Measurements during prototype target tests (e.g. analysis of filters/cartridge, quantification of contamination, H-3 measurements, inline gas spectrometer, etc.) are to be defined
Comparison to CDS target
Target | Material | Mass [kg] | Multiple LL | Multiple LA | A [Bq]
W target | W | 1420 | 2.7E+08 | 8.0E+08 | 2.6E+15
CDS target | W | 695 | 1.9E+08 | 2.6E+08 | 9.2E+14
 | TZM | 271 | 1.1E+09 | 8.4E+07 | 1.8E+14
 | Ta | 28 | 1.7E+11* | 6.9E+08 | 9.8E+14
*Dominated (99.9%) by Ta-182 (115 d half-life)
Authorization Limits (LA)
Swiss Clearance Limits (LL)

## Slide 22
Surface building

## Slide 23
RP considerations for service cell
A HI-ECN3 service cell is crucial for safe packaging and disposal of highly radioactive equipment, as mandated by French and Swiss authorities
The only available disposal pathway for the BDF target currently involves cutting it to fit within a KC-T12 container designated for disposal in Switzerland
Alternatives such as transport to external facilities would require significant investments in transport casks and infrastructure, expected to cost several MCHF
The cutting of the BDF target vessel requires a destructive technique (e.g. cable saw) causing contamination
The total resuspended activity was estimated by assuming that 4 cuts on the vessel (stainless steel/Inconel) removing ~7.8 kg
Resuspended activity
Total PoT 2×1020 (5 yrs) + 1 y cool-down
Material | Multiple LA
Inconel | 1.2E+06
Stainless steel | 1.3E+05

## Slide 24
Service building area classification
Work sector | Maximum Activity
Normal | LA
Type C | 1E+02 LA
Type B | 1E+04 LA
Type A | Depending on authorization
A
C
C
C
Controlled Radiation Area with Contamination Risk
Simple Controlled or Limited Stay Radiation Area with Contamination Risk
If required, dedicated room for hotcell
Simple Controlled or Limited Stay Radiation Area with Contamina-tion Risk
Class A and C working areas will in addition have a Controlled Radiation Area classification with contamination risk (Limited Stay or High Radiation Area)
At CERN, laboratories or working areas in which radioactive substances are manipulated are classified according to the Swiss Radiological Protection Ordinance (RPO)
This area classification is in addition to the standard CERN area classification
The work sector classification is based on the radionuclide dependent authorization limit LA
→ Specific working area requirements, e.g. ventilation, filters, fire resistance, decontami-nation possibilities, changing rooms, etc.
EN-CV service for cooling system:
  He-cooling: system with filters. In underground target area already HEPA filters + heat exchanger
  Water-cooling: ion exchanger cartridges w/ shielding underground
Ongoing design definition together with FIRIA

## Slide 25
Conclusions and outlook
Main radiological aspects regarding an implementation of BDF/SHiP in ECN3 were investigated
First shielding design for an optimization of exposure of personnel to radiation and radiological impact on environment
Further detailed studies and optimization in the Technical Design Phase including amongst others:
  BDF handling studies and target cask requirements
  Service building and service cell studies including shielding requirements (walls, storage, waste container, etc.)
  Evaluation of risks related to H-3 out-diffusion/ejection, and volatile radionuclides in the He-cooling system

## Slide 27
[1] Website: https://fluka.cern
[2] C. Ahdida, D. Bozzato, D. Calzolari, F. Cerutti, N. Charitonidis, A. Cimmino, A. Coronetti, G. L. D’Alessandro, A. Donadon Servelle, L. S. Esposito, R. Froeschl, R. García Alía, A. Gerbershagen, S. Gilardoni, D. Horváth, G. Hugo, A. Infantino, V. Kouskoura, A. Lechner, B. Lefebvre, G. Lerner, M. Magistris, A. Manousos, G. Moryc, F. Ogallar Ruiz, F. Pozzi, D. Prelipcean, S. Roesler, R. Rossi, M. Sabaté Gilarte, F. Salvat Pujol, P. Schoofs, V. Stránský, C. Theis, A. Tsinganis, R. Versaci, V. Vlachoudis, A. Waets, M. Widorski, New Capabilities of the FLUKA Multi-Purpose Code, Frontiers in Physics 9, 788253 (2022)
[3] G. Battistoni, T. Boehlen, F. Cerutti, P.W. Chin, L.S. Esposito, A. Fassò, A. Ferrari, A. Lechner, A. Empl, A. Mairani, A. Mereghetti, P. Garcia Ortega, J. Ranft, S. Roesler, P.R. Sala, V. Vlachoudis, G. Smirnov, Overview of the FLUKA code, Annals of Nuclear Energy 82, 10-18 (2015)
[4] V. Vlachoudis, FLAIR: A Powerful But User Friendly Graphical Interface For FLUKA, in Proc. Int. Conf. on Mathematics, Computational Methods & Reactor Physics (M&C 2009), Saratoga Springs, New York (2009)
[5] H. Vincke, C. Theis, ActiWiz – optimizing your nuclide inventory at proton accelerators with a computer code, Progress in Nuclear Science and Technology (2014)
[6] P. Vojtyla, Models for assessing the dosimetric impact of releases of radioactive substances from CERN facilities to the environment – Air, CERN Internal report (2021)
Bibliography

## Slide 28
Activities of BDF target materials
TZM
Ta
W
Total PoT 2×1020 (5 yrs)
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
Activities multiples – CDS target

## Slide 29
Radionuclide inventory of W target
Total PoT 2×1020 (5 yrs) + 1 month cool-down
Tungsten – Total Activity (Bq)
Tungsten – Multiple of LL
Tungsten – Multiple of LA
D = 25 cm, L = 150 cm
H-3 |  | 2.23E+13
W-185 | 67%, | 1.75E+15
W-181 | 13%, | 3.49E+14
Ta-178 | 3%, | 8.80E+13
W-178 | 3%, | 8.79E+13
Ta-179 | 3%, | 8.34E+13
Hf-175 | 2%, | 5.54E+13
Sum of all |  | 2.60E+15
H-3 |  | 1.57E+05
Ta-182 | 49% | 1.32E+08
Hf-175 | 15% | 3.90E+07
W-181 | 9% | 2.45E+07
Lu-173 | 5% | 1.46E+07
Lu-172 | 4% | 1.06E+07
Ta-178 | 2% | 6.19E+06
W-178 | 2% | 6.19E+06
Ta-179 | 2% | 5.87E+06
Re-184m | 2% | 4.53E+06
Eu-146 | 1% | 3.06E+06
Gd-146 | 1% | 2.77E+06
Sum of all |  | 2.69E+08
H-3 |  | 2.23E+05
Gd-148 | 59% | 4.78E+08
Hf-172 | 18% | 1.48E+08
W-185 | 11% | 8.77E+07
Ta-182 | 3% | 2.68E+07
Yb-169 | 1% | 9.67E+06
Hf-175 | 1% | 9.23E+06
Sum of all |  | 8.03E+08

## Slide 30
LL multiples of BDF target materials
TZM
Ta
W
Total PoT 2×1020 (5 yrs)
Main contributors (>1%), sum for all radionuclides
Pure alpha/beta emitters are shown in bold
Dominant radionuclide is shown in red
Multiples of Swiss Clearance Limits (LL)
CDS Target

## Slide 31
CDS air and He activation
A helium purification system provides a purity of at least 99.9% He (<0.1% air contamination)
Air and He regions in the target complex
He vessel
Target pit
Annual releases from the target pit and the He vessel
Effective dose to reference groups
1.4 GBq H-3 released to the air would lead to 5 nSv

## Slide 32
Alternative cladding materials
Material: |  | Niobium | Nb-1Zr | Nb-10Hf-1Ti |  | 
 |  | (ASTM R04210 | (ASTM R04261 | "C103" |  | 
 |  | Type 2) | Type 4) | (ASTM R04295) |  | 
Density (g/cm3): |  | 8.6 | 8.6 | 8.86 |  | 
Composition: | C | 0.01 | 0.01 | 0.015 |  | 
Max Weight % | N | 0.01 | 0.01 | 0.01 |  | 
 | O | 0.025 | 0.025 | 0.025 |  | 
 | H | 0.0015 | 0.0015 | 0.0015 |  | 
 | Zr | 0.02 | 0.8-12 | 0.7 |  | 
 | Ta | 0.3 | 0.5 | 0.5 |  | 
 | Fe | 0.01 | 0.01 | - |  | 
 | Si | 0.005 | 0.005 | - |  | 
 | W | 0.05 | 0.05 | 0.5 |  | 
 | Ni | 0.005 | 0.005 | by difference |  | 
 | Mo | 0.02 | 0.05 | - |  | 
 | Hf | 0.02 | 0.02 | 9-11" |  | 
 | Ti | 0.03 | 0.03 | 0.7-1.3" |  | 
Reference: |  | [1] | [2] | [3] |  | 
[1] | https://www.navstarsteel.com/niobium-sheet.html |  |  |  |  | 
[2] | https://www.tantalum-niobium.com/niobium/nb-1zr-wire-rod.html |  |  |  |  | 
[3] | Ximenes Franqueira R., Internal communication, (2021) |  |  |  |  | 

## Slide 33
Target vessel materials
Inconel - AW3.7 - 8.4 g/cm3 | 
ALUMINUM | 1.15E-02
BORON | 6.00E-05
CARBON | 8.00E-04
CHROMIUM | 2.10E-01
COBALT | 1.00E-02
COPPER | 8.00E-03
IRON | 1.11E-01
MANGANESE | 3.50E-03
MOLYBDENUM | 3.30E-02
NICKEL | 5.50E-01
NIOBIUM | 5.50E-02
PHOSPHORUS | 1.50E-04
SILICON | 3.50E-03
SULFUR | 1.50E-04
TITANIUM | 3.00E-03
SS316LN - AW3.7 - 8 g/cm3 | 
CARBON | 3.00E-04
COBALT | 1.00E-03
CHROMIUM | 1.73E-01
IRON | 6.39E-01
MANGANES | 2.00E-02
MOLYBDEN | 2.50E-02
NITROGEN | 1.70E-03
NICKEL | 1.30E-01
PHOSPHO | 2.25E-04
SULFUR | 7.50E-05
SILICON | 1.00E-02

## Slide 34
Beam transfer
TT7 shielding recovery
TCC8 dismantling
Shielding recovery from discontinued CERN PS Neutrino Facility (PSNF)
~100 m3 std. cast iron blocks
~50 m3 non-std cast iron blocks
~3 MCHF, investment <1/3
Residual H*(10)
Radioactive waste zoning
Several RP studies for the high intensity SPS-ECN3 beam transfer were performed
This includes studies for a bridge above the TDC85 transfer tunnel near ECN3
Prompt H*(10)
Various beamline and shielding configurations were investigated
Dismantling of the highly radioactive TCC8 target area in 2026
Evaluation of residual dose rates and radio-nuclide inventories for operational RP as well as radioactive transport and waste studies
TCC8
Residual H*(10)
Some additional studies

## Slide 35
Optimization of MHS length
Ongoing optimization of MHS length to enhance SHiP’s physics performance, while maintaining optimization goals for radiation (RP, radiation to material) in the downstream area
FLUKA model w/ reduced MHS length
Along z-axis
Along z-axis
Prompt radiation
Residual radiation
MHS length and dump reduced from 4.5 m to 2.3 m with full W target and Cu plug
Prompt dose rate for the reduced length is ~7 times higher than for the longer version
Along beamline dose rates are compatible with Supervised Radiation area after 1 day. On sides expected to be lower
2.3 m
1.5 m
25 cm
40 cm distance
Preliminary
Preliminary
<X> = [-12:12] cm, <Y> = [-20:15] cm
<X> = [-12:12] cm, <Y> = [-13:15] cm​

## Slide 36
Radioactive Material
Specific and total activity exceed clearance limits (LL values)
as given in the Annex of EDMS 942170 (adopted from Swiss legislation)
OR
Net ambient dose equivalent rate > 0.1 µSv/h in 10 cm distance
OR
Surface contamination exceeds limits
as given in the Annex of EDMS 942170 (> 1 CS)
When is a material radioactive?
Sum rule for mixture
of radionuclides:
Sum rule for mixture
of radionuclides:
Examples: 0.1 Bq/g for 22Na, 54Mn, 60Co
1000 Bq/g for 55Fe