## Slide 2
Test of new BB Finemet
controller
T. Gavric, B. Woolley, H. Damerau, Y. Brischetto, M. Vadai
IPP MD Days
05/02/25
Many thanks to PSB/PS operations team

## Slide 3
Outline
Previous work
Synchronization scheme
New features
Change in the current setup
Plans for 2025
MD topics

## Slide 4
Previous work
Diagram from M. Vadai, A. Alomainy, H. Damerau: Barrier Bucket Studies in the CERN PS (CC-BY 3.0) - https://doi.org/10.18429/JACoW-IPAC2019-MOPTS106
Barrier-bucket MTE scheme significantly reduces beam loss in PS extraction region
Non-PPM barrier waveform
  Lacked flexibility
2 consolidation boards
  h16 measurement
  h1 measurement

## Slide 5
Synchronization scheme
Conventional synchronisation not possible
  RF voltage of the wide-band cavity generating the BB would be too low for a conventional synchronisation
Synchronisation concept in use:
  Synchronising in h16 using feed-forward cogging
  Lower accuracy sufficient for barrier buckets
  Synchronisation in h1: phase measurement and communicating phase information within a cycle to set the correct barrier position
Notes: 590-600 Loops off,ℎ16 phasemeasurement 600 ℎ1 phase measurement 600-620 Cogging 620-650 Radial steering to central orbit 650-770 Constant offset for MTE 770-800 Radial steering to extraction orbit 800-815 Hand-over ℎ16 to barrier bucket 800-815 Debunching 835 Extraction

## Slide 6
New features (1)
Full control of RF drive voltage
  PPM
  Arbitrary waveform
  16-bit waveform memory
Acquisition of gap voltage
  Single turn
  Hard trigger (from CTRV through backplane)
    PAX.SACQ-ALLRFM
Arbitrary gain function of the waveform
  FGC: Internal function generator – new preferred option (makerule from old function)
  CVORB
Chart: 

## Slide 7
New features (2)
Following features are yet to be tested with the beam:
New extraction synchro for PS: h1 measurement w.r.t. SPS derived h1
  Updates BB azimuth during the cycle (C620 ms)
PS acquisition core
  Gain function
  h1 measurement – phase between SPS derived h1 and PS h1
Accordion sweep of the waveform
  Time in which sweep happens can be set
    Used for smooth batch compression – interesting for possible ion chain upgrade

## Slide 8
Change in h1 measurement
h=1
controller
SPS h=1 RF
PS h=1 RF
Network
BB
drive
φh1 mod h16
To wideband
cavity
h=1 controller measures the phase w.r.t. SPS and sends it real-time via C programs on front-ends to the barrier bucket drive
New Finemet cavity controller
Non-standardized hardware removed
Enables remote intervention
h=1 diagram: M. Vadai, H. Damerau, M. Giovannozzi, A. Huschauer, A. Lasheen: IMPLEMENTATION OF SYNCHRONISED PS-SPS TRANSFER WITH BARRIER BUCKET (CC-BY 4.0) https://arxiv.org/abs/2210.05416
Notes: - Hardware only used for synchronization.
- Hand-made electronics, conforms to no rack standard.
- Power and comms: FEC via USB.

## Slide 9
Deploy new firmware during commissioning period
Deploy operational FESA class for the new cavity controller during 24/25 YETS
Increase number of turns acquired – up to 16 turns
Test new features with the beam
Add relay for remote interventions on NIM crate powering h16 controller??
Develop BB IP as a part of new digital PS beam control
  Removes remaining controller used for h16 measurement
Plans for 2025

## Slide 10
Explore the benefits of Finement cavity with new software and firmware beyond barrier buckets
  Transient beam loading compensation
  Smooth batch compression (h21 → h42) for Oxygen ion run
MD topics