## Slide 1: Beam based measurements of cavities impedance (C80, C10)
Mathieu Taquet
Acknowledgments : A. Lasheen, B. Woolley, V. Desquiens, PS operators
05/02/2025

## Slide 2: Outline
Introduction
Measurement principle
C80
C10
Conclusions

## Slide 3: Introduction
Is the new PSpice model of the amplifier chain reproducing the beam cavity interaction throughout the complete power range?
C80
C10
What are the dynamics of the impedance when the gap relay is switched on ?
Is the shunt impedance with wideband feedback around 500 Ω ?
Measure the system with the beam until it starts to compress

## Slide 4: Measurement principle (for C80-88)
While the 40 MHz cavities and C80-89 and C80-08 follow the bunch rotation program
Current calibration
Voltage Calibration

## Slide 5: Results (for C80-88)
Compression of the shunt resistance
Anodic current during BR
Induced voltage in C80-88 during BR

## Slide 6: Results (for C80-88)
All good !!

## Slide 7: Measurement principle (for C10)
While the gap relays are switched on
Current calibration
Voltage Calibration

## Slide 8: Results: Dynamic impedance behavior
Example of cavity 56 – tuned on h8

## Slide 9: Results: wideband feedback only
Impedance is too high!! Factor 2-3, depending on cavities
1
2
Issues with calibration of voltage due to cable compensator: measurements to be repeated but central frequency is reliable
A few cavities for illustration
Impedances of C10 have been measured, but some issues to be tackled/understood next year

## Slide 10: Conclusion
The new PSpice model reproduces correctly the dynamic impedance behavior
C80
C10
Impedance is too high: work will be done on the RF side to better estimate the impedance and tune the loop
No more measurement to be redone
Need to remeasure the impedances
In general, we did not experience any relevant problem

## Slide 11: Backup Slides

## Slide 12: Pspice model (for C80-88)

## Slide 13: Power limitations (for C80-88)