## Slide 1: Pushing intensity with LHC-type beams
H. Bartosik, I. Karpov, I. Mases, L. Mether, G. Papotti, K. Paraschou, G. Rumolo, C. Zannini,
F. Asvesta, X. Buffat, H. Damerau, A. Lasheen, K. Li, M. Barnes, R. Calaga,
E. de la Fuente, G.P. Di Giovanni, A. Huschauer, G. Iadarola, V. Kain, B. Mikulec, B. Salvant,
M. Schenk, F.M. Velotti, PSB-PS-SPS OP teams

## Slide 2: Intensity reach in the last three years
Intensity reach at flat top with nominal bunch length [] |  | 
Year | 8b4e (4 x 56 bunches) | LHC25ns (4 x 72 bunches)
2022 | 1.5 | 1.52
2023 | 2.15 | 2.2
2024 | x | 2.3
Year | 8b4e (4 x 56 bunches) | LHC25ns (4 x 72 bunches)
2022 | 1.5 | 1.52
2023 | 2.15 | 2.2
2024 | x | 2.3
Consolidation of LIU beam and exploration of intensity limits with 8b4e beam
LIU beam (288 bunches with ~2.3e11 ppb and ~1.6ns bunch length) accelerated to 450 GeV
During 2024 scrubbing we demonstrated the LIU intensity
LIU beam at 2.3e11 ppb never fully restored
Beam availability during MDs, struggling with RF cavity limits, beam readiness from injectors after long gaps, magnet exchanges, ….
Key to be well prepared for the 2026 reliability run

## Slide 3
Horizontal instability studied in detail in 2018 for 1.8e11 p/b
  Mitigation strategy developed in simulations: high chromaticity + octupoles
Extremely fast vertical coupled bunch instability predicted in simulations
  Threshold depends on the set vertical tune and chromaticity
Trasverse stability at injection energy
Criticality of short bunches at injection (<4 ns) to ensure stability, also confirmed in simulations

## Slide 4
Horizontal instability studied in detail in 2018 for 1.8e11 p/b
  Mitigation strategy developed in simulations: high chromaticity + octupoles
Extremely fast vertical coupled bunch instability predicted in simulations
  Threshold depends on the set vertical tune and chromaticity
Trasverse stability at injection energy
Criticality of short bunches at injection (<4 ns) to ensure stability, also confirmed in simulations
Transverse stability successfully tested in 2024 (~30h with ~2.7e11 ppb injected and 4 x 72 bunches)
With some exceptions 2024 bunch lengths from PS were consistently below 4 ns

## Slide 5: Observation of vertical instability
  Experimentally confirmed with 1 batch and low intensity in 2021 and 2022
  Studies with 4 batches in 2024
At tune Qv = 20.18, and QPV = 0.6 (knob),
we reduced gradually the gain of the damper
SCAN OF THE VERTICAL CHROMATICITY AT NOMINAL DAMPER GAIN
Vertical chromaticity (knob) needs to be QPV >= 0.6
Plot of I. Mases

## Slide 6
At tune Qv = 20.18, and QPV = 0.6 (knob),
we reduced gradually the gain of the damper
SCAN OF THE VERTICAL CHROMATICITY AT NOMINAL DAMPER GAIN
Vertical chromaticity (knob) needs to be QPV >= 0.6
4 x 72bunches, N = 2.6e11 p/b
Observation of vertical instability
Plot of I. Mases

## Slide 7: Horizontal and vertical chromaticity
Could Q22 optics help to reduce the needed chromaticity for transverse stability?
Investigation with Q22 optics revealed that indeed horizontal stability can be improved as predicted by Xavier (stability reached for a 0.1-0.15 lower H chromaticity). Stability become more critical in the vertical plane (0.1-0.15 higher V chromaticity)
Standard beam
BCMS beam
Higher chroma needed for transverse stability with BCMS beam in both planes due to the smaller emittances
Standard beam
BCMS beam

## Slide 8: SPS injection kicker beam induced heating mitigation
Circulating
beam
Offsetting the circulating beam towards the ground conductor is expected to be beneficial in terms of beam induced heating
After the optimization of the MKP-L, MKP-S became the major bottleneck in term of beam induced heating
Scrubbing run 2023 and 2024 had to be modulated to accommodate cool down of the MKP-S magnet
Ground conductor
Experimental verification with orbit bump during scrubbing run 2024

## Slide 9: Desiderata for 2025
Consolidation of LIU beam (scrubbing + at least 4-5 MD slots)
  Starndard (during scrubbing) and BCMS (dedicated MD cycle)
Exploration of intensity margins for LIU beam – at least 2-3 MD slots
Pushing intensity with 8b4e beam (goal is to give 2.3e11 ppb to LHC for 2026 high intensity studies) - at least 2 MD slots
Beam quality optimization (emittance, tails, batch-by-batch tune correction)
Minimization of PS-SPS mismatch (tuning of transfer line optics)
meas. time | Standard |  |  |  | BCMS |  |  | 
 | epsn [ | Intensity [] | Brightness [] | Target brightness [] | epsn [ | Intensity [] | Brightness [] | Target brightness []
PS extr. | 2.05 | 2.64 | 1.29 | - | 1.59 | 2.64 | 1.66 | -
SPS inj. | 2.25 | 2.59 | 1.15 | 1.36 | 1.73 | 2.59 | 1.50 | 1.71
meas. time | Standard |  |  |  | BCMS |  |  | 
PS extr. | 2.05 | 2.64 | 1.29 | - | 1.59 | 2.64 | 1.66 | -
SPS inj. | 2.25 | 2.59 | 1.15 | 1.36 | 1.73 | 2.59 | 1.50 | 1.71

## Slide 10: Thank you for your attention

## Slide 11: Additional studies

## Slide 12
SPS Wire scanner failure
YETS 23/24: installation of ferrites and coupler in all 4 wire scanners tanks
As predicted from power loss calculations, no issues observed in parking position up to LIU intensities
An SPS wire scanner get stuck close to beam halo during 2024 operation
The stuck wire broke with significantly lower intensity than LIU, consistently with the advanced model predictions
Development of an advanced model that can reproduce the beam induced power loss over the relevant frequency range
Beam type | Parking position [W] | Stuck position [W]
Operational | <0.9 | <4.5
MD beam (breakage) | <2.4 | >6.8
LIU | <5 | >14
Breakage expected for >6.5 W
L. Sito, E. de la Fuente

## Slide 13
SPS Wire scanners: expectations for coming years
YETS 23/24: installation of ferrites and coupler in all 4 wire scanners tanks
From power loss calculations, no issues are expected if considering
peak power on the wire along the cycle.
L. Sito, E. de la Fuente
800 MHz

## Slide 14: Appendix

## Slide 15: MKP-S beam induced heating mitigation

## Slide 16: MKP-S beam induced heating mitigation

## Slide 17: MKP-S beam induced heating mitigation

## Slide 18: MKP-S beam induced heating mitigation
Projection on limitations during scrubbing

## Slide 19
Horizontal instability @26 GeV studied in detail in 2018 for 1.8e11 p/b
  Mitigation strategy developed in simulations: high chromaticity + octupoles
Extremely fast vertical coupled bunch instability @26 GeV predicted in simulations
  Threshold depends on the set vertical tune and chromaticity
SPS transverse stability
Courtesy of I. Mases
With some exceptions 2024 bunch lengths from PS were consistently below 4 ns
Criticality of short bunches at injection (<4 ns) to ensure stability, also confirmed in simulations

## Slide 20
Horizontal instability studied in detail in 2018 for 1.8e11 p/b
  Mitigation strategy developed in simulations: high chromaticity + octupoles
Extremely fast vertical coupled bunch instability predicted in simulations
  Threshold depends on the set vertical tune and chromaticity
Trasverse stability at injection energy
Criticality of short bunches at injection (<4 ns) to ensure stability, also confirmed in simulations
Transverse stability successfully tested in 2024 (~30h with ~2.7e11 ppb injected and 4 x 72 bunches)