## Slide 1
Florian Henkes – Technical University of Munich
Oliver Schulz – Max-Planck Institute for Physics
Julia HEP Workshop 2025– Princeton University

## Slide 2: Outline
Introduction to LEGEND and 0νββ-decay physics
What is the JuLeAna Software Stack?
Features and highlights in the latest LEGEND analysis
Summary & Outlook

## Slide 3: Outline
Introduction to LEGEND and 0νββ-decay physics
What is the JuLeAna Software Stack?
Features and highlights in the latest LEGEND analysis
Summary & Outlook

## Slide 4: Matter Antimatter Asymmetry
+
-
-
+
-
+

## Slide 5: Neutrinoless Double Beta Decay
2νββ
0νββ
 Lepton-Number Violation (LNV) by two units
 Neutrino = Majorana
 Matter-antimatter asymmetry explanation?
Single -decay
* Only Possible in ~35 isotopes
BSM physics
“Creation of matter without anti-matter”

## Slide 6: The challenge: Low Statistics
Energy of both electrons
Continuous energy spectrum
Peak at Q𝛽𝛽 -value (76Ge: 2.039 MeV)
Total Background in ROI:
⇒ ↑ High
requires
Low ↓
Background Index
Energy Resolution
Total Mass
Run Time
Current best limits:
Notes: Make 2 slides out of one

## Slide 7: 0νββ Decay Physics

## Slide 8: 76Ge: The ideal material?
High-Purity Germanium detectors enriched in 76Ge
  Source = detector ⟼ high efficiency
  Intrinsically pure ⟼ low background
  High enrichment (~90%) ⟼ high active mass
  Ge crystal ⟼ excellent FWHM (~0.1%)
  “solid-state TPC” ⟼ topological discrimination
  ⇒ Technology proven by GERDA and MAJORANA
Enriched 76Ge bulk
n+ contact (lithiated) @ 3- 5 kV
p+ contact (boron implanted)
Point-like ββ interactions
Notes: Make 2 slides out of one

## Slide 9: The - Experiment
200kg of enrGe (x 5yr), in GERDA cryostat
Physics data taking since March 2023
BI ~ 2 10-4 cts / (keV kg yr)  1027 yr
1t of enrGe (x 10yr)
BI < 10-5 cts / (keV kg yr)  1028 yr
Fully cover inverted ordering region
“The collaboration aims to develop a phased,76Ge-based
double-beta decay experimental program with discovery potential at a half-life beyond 1028yr, using existing resources as
appropriate to expedite physics results.”
LEGEND-200
LEGEND-1000

## Slide 10: The - 200 Experiment
Liquid Argon cryostat
Water tank/ -veto
HPGe readout electronics
Larger mass
(inverted coaxial)
HPGe detectors with up to 4 kg
Detector mount: underground copper, optically active PEN plates and radiopure PEI
Liquid Argon instrumentation:
inner & outer fiber barrels with silicon photomultiplier (SiPM) readout at top & bottom
Source funnels
for 228Th calibration sources
Notes: Get some more picture from luigis slides

## Slide 11: The - 200 Experiment
Liquid Argon cryostat
Background radiation

## Slide 12: Outline
Introduction to LEGEND and 0νββ-decay physics
What is the JuLeAna Software Stack?
Features and highlights in the latest LEGEND analysis
Summary & Outlook

## Slide 13: The Analysis Strategy
2 analysis frameworks
New primary software stack in python
Secondary Julia software stack for validation and comparison
In blinded analysis
&

## Slide 14: The - 200 Data Taking
Installed first 142 kg of HPGe detectors (Oct ’22)
130 kg operational (12 kg OFF due to hardware issues)
Exposure accumulated over 1 year
Total exposure:
Weekly calibrations with Th-228 sources
Latest results:
https://arxiv.org/pdf/2505.10440

## Slide 15: The Software Stack
raw
RadiationDetectorSignals.jl
LegendHDF5IO.jl / LegendDataTypes.jl
LegendSpecFits.jl
BAT.jl
RadiationSpectra.jl
dsp
hit
evt
sim
SolidStateDetectors.jl
LegendGeSim.jl
LegendDataManagement.jl
LegendDSP.jl
LegendEventAnalysis.jl
DataTier
Official
-physics
ana
legend-julia-dataflow / ParallelProcessingTools.jl
Registry
IO
Metadata & Pars
HPC Computing
LegendML.jl
ZeronuFit.jl
RadiationDetectorDSP.jl
LegendMakie.jl
Plotting
Notes: Was ist aktuell im Software Slack?
4 Teile/Kästchen: Daten einlesen (raw), DSP, Fits/SpecFits /Hit, tcm (event building)
4 Kästchen erklären (Alles bildlich darstellen)
Dadrunter die Paketnamen ?
Mostly feature complete for LEGEND analysis …
… but we’ll still add, improve lots of stuff
Covers whole span from Geant4-output and lab control to final analysis

## Slide 16: HPC Computing
Can scale cluster up and down repeatedly, even from interactive Julia session
Timeout/retry mechanism + atomic file I/O with optional local caching
Best LH5 write performance achieved so far 1.2 TB in 70 seconds
Ran up to 4000 parallel multi-cpu worker processes
Under development: improved distributed progress and performance monitoring
Custom dataflow with simple graph and dependency handling
Markdown log reports and debug plot capabilities
Interactive HPC Computing in a REPL:
All performed on MPCDF Munich HPC systems Raven/Viper
legend-julia-dataflow / ParallelProcessingTools.jl
HPC Computing

## Slide 17: Outline
Introduction to LEGEND and 0νββ-decay physics
What is the JuLeAna Software Stack?
Features and highlights in the latest LEGEND analysis
Summary & Outlook

## Slide 18: Analysis workflow overview
waveforms
waveform level
Legend
raw data
detector-wise
file-wise

## Slide 19: LEGEND Data
All waveform data saved for offline processing
  O (100) of HPGe channels
  O (50) of SiPM channels
Metadata in JSON or YAML
raw data in HDF5 with custom compression
julia > using LegendDataManagement, LegendHDF5IO
julia > raw = lh5open(“data.lh5”, “r”)
julia > l200 = LegendData(:l200)
julia > raw = read_ldata(l200, DataTier(:raw), DataPeriod(3), ChannelId(111000))
julia > using CairoMakie, LegendMakie
julia > waveformplot!.(raw.waveform[1:10])
LegendHDF5IO.jl / LegendDataTypes.jl
IO
Notes:   7 days of physics data taking
  + Calibration run with 4 Th-228 calibration sources
  form a run

## Slide 20: Detector Simulation
Detector geometry
Bias voltage
Impurity
density
Electric potential
Charge drift model
Drift paths
Weighting potentials
3
Raw pulses
Electric field
electrons holes
SolidStateDetectors.jl
Notes: So let us start with a slide on pulse shape simulation and the different steps to get from the detector geometry and crystal properties to “raw simulated pulses”.
As this is an SSD talk, I will also show the julia commands that are used to perform the different steps of the pulse shape simulation chain on the right.
To start the simulation, the user has to define the detector setup. Let us assume that our detector geometry is defined in a configuration file called, for example, “BEGe.yaml”.
This files contains information like the physical dimensions of the crystal, the geometries of the contacts, possible boreholes, etc. We will have a closer look at the structure of such a configuration file at the end of my talk.
In this file, (*PUSH*) the user can also define the impurity density profile of the detector, the potentials applied to the contacts to bias the detector, and any object in the vicinity of the detector (holding structures, cryostat walls and so on) that have an influence on the electric potential (if SSD should include them in the simulation).
SSD calculates the electric potential from all that information using a successive over relaxation algorithm. The implementation of this algorithm is optimised for fast computation AND we recently added support for performing the calculations on GPUs for further speed-up. I should note here that SSD can perform both 2D AND 3D calculations of the electric potential. Especially, 3D simulations can be quite important to simulate detectors or setups which are not fully phi-symmetric (segmented surfaces, non-centered boreholes, holding structures, etc.).
The first derivative of the electric potential then gives the electric field.
To simulate the drift paths of the charges created in an event with given hit positions and energies, SSD needs the electric field and a charge drift model for both electrons and holes. The energy deposits are converted to electron-hole pairs that then drift according to the electric field and the charge drift model in pre-given time steps of e.g. 1 ns.
Together with the weighting potentials, that are defined by the detector geometry, we can apply the Schockley-Ramo theorem to calculate the raw pulses to which we could later apply an electronics model to obtain the “real” pulses (but especially applying an electronics model is not part of SSD).
And as said, these simulated pulses can then be used to test pulse shape discrimination algorithms.
While this might sound very trivial there are quite some uncertainties on the input to the simulation and that will influence the outcome.

## Slide 21: SolidStateDetectors.jl on GitHub
Find the latest version of the documentation on GitHub:
https://juliaphysics.github.io/ SolidStateDetectors.jl/stable/
36

## Slide 22: Simulating Group Effects
julia > using SolidStateDetectors, Unitful
julia > sim = Simulation{Float64}(“BEGe.yaml”)
julia > calculate_electric_potential!(sim)
julia > calculate_electric_field!(sim)
julia > for i in 1:2 calculate_weighting_potential!(sim, i) end
julia > locations = [CartesianPoint(0.035,0,0.02)] julia > energies = [1000u”keV”]
julia > evt = Event(NBodyChargeCloud(locations, energies, 100)) julia > simulate!(evt, sim, diffusion = true, self_repulsion = true)
40
SolidStateDetectors.jl

## Slide 23: Support for Geant4.jl
julia > using SolidStateDetectors, Unitful julia > using Geant4
julia > sim = Simulation{Float64}(“ivc.yaml”)
julia > simulate!(sim)
41
SolidStateDetectors.jl

## Slide 24: Support for Geant4.jl
julia > using SolidStateDetectors, Unitful julia > using Geant4
julia > sim = Simulation{Float64}(“ivc.yaml”)
julia > simulate!(sim)
julia > source = MonoenergeticSource(
“gamma”, 2.615u”MeV”, CartesianPoint(0.05, 0.0, 0.05), CartesianVector(-1, 0, 0), 10u”°”
)
41
SolidStateDetectors.jl

## Slide 25: Support for Geant4.jl
julia > using SolidStateDetectors, Unitful julia > using Geant4
julia > sim = Simulation{Float64}(“ivc.yaml”)
julia > simulate!(sim)
julia > source = MonoenergeticSource(
“gamma”, 2.615u”MeV”, CartesianPoint(0.05, 0.0, 0.05), CartesianVector(-1, 0, 0), 10u”°”
)
julia > app = G4JLApplication(sim, source) julia > evts = run_geant4_simulations(app, 10000)
41
SolidStateDetectors.jl

## Slide 26: Support for Geant4.jl
julia > using SolidStateDetectors, Unitful julia > using Geant4
julia > sim = Simulation{Float64}(“ivc.yaml”)
julia > simulate!(sim)
julia > source = MonoenergeticSource(
“gamma”, 2.615u”MeV”, CartesianPoint(0.05, 0.0, 0.05), CartesianVector(-1, 0, 0), 10u”°”
)
julia > app = G4JLApplication(sim, source) julia > evts = run_geant4_simulations(app, 10000)
julia > simulate_waveforms(sim, evts)
41
SolidStateDetectors.jl

## Slide 27: Analysis workflow overview
waveforms
waveform level
Legend
raw data
detector-wise
file-wise
data
quality cuts
Remove non-physical waveforms

## Slide 28: Quality Cuts: Identify non-physical Events
Machine Learning
based QC:
Affinity Propagation with Support Vector Machine
Re-labeling by hand with interactive Pluto.jl notebooks during shifts
LegendML.jl
Notes:   7 days of physics data taking
  + Calibration run with 4 Th-228 calibration sources
  form a run

## Slide 29: Analysis workflow overview
waveforms
waveform level
Legend
raw data
detector-wise
file-wise
data
quality cuts
Remove non-physical waveforms
digital signal processing
(dsp)
filter to extract parameters, e.g. energy

## Slide 30: Digital Signal Processing
First step in analysis chain
  Signal height : Energy information
  Signal derivative: Pulse Shape information
  Signal integral: Charge-trapping information
  Time points: Drift Information
Custom GPU-accelerated DSP routines
julia > using LegendDSP
julia > dsp = dsp_icpc(raw, DSPConfig(“config.json”), 400.0u”µs”, PropDict(:trap => (:rt => 10.0u”µs”, :ft => 3.0u”µs”)))
LegendDSP.jl
RadiationDetectorDSP.jl
Notes:   7 days of physics data taking
  + Calibration run with 4 Th-228 calibration sources
  form a run

## Slide 31: Analysis workflow overview
waveforms
waveform level
Legend
raw data
detector-wise
file-wise
data
quality cuts
Remove non-physical waveforms
digital signal processing
(dsp)
filter to extract parameters, e.g. energy
dsp parameter level
energy calibration
(ecal)
Fit calibration data: γ-lines with known energies
run-wise

## Slide 32: Th-228 Calibration Spectra
DEP
Bi-212 FEP
SEP
FEP
julia > using LegendSpecFits, LegendMakie
julia > r_simple, p_simple =
simple_calibration(e_uncal,
th228_lines, th228_windows)
julia > lplot(p_simple)
LegendSpecFits.jl
RadiationSpectra.jl

## Slide 33: Peak Fits
Signal (γ)-line peak: Gaussian
  mean: µ
  standard deviation: std
  amplitude: n
Low-energy tail: Exponentially modified Gaussian
  width skew width
  rel. amplitude: skew fraction
Background:
  Energy-independent (flat) background
  Step-function Compton continuum
4. High energy tail:
  for escape peaks only: Compton scattering of annihilation photon in transition layer
_________________________
very small + not significant
-> reduce residuals to literature value
julia > r_fits, p_fits = fit_peaks(peakhists, peakstats, th228_names)
julia > lplot(p_fits)
Bayesian Guided MLE fits
LegendSpecFits.jl
RadiationSpectra.jl

## Slide 34: Energy Calibration
Literature values with uncertainties
Linear fit
Performed per run and per detector
peak centroid =
Excellent residuals
julia > r_cal, p_cal = fit_calibration(1, r_fits.centroid, th228_lines)
julia > lplot(p_cal)
LegendSpecFits.jl
RadiationSpectra.jl

## Slide 35: Energy Resolution
Excellent residuals
√ of 1st-order
polynomial fit
julia > r_fwhm, p_fwhm = fit_fwhm(1, th228_lines, r_fits.fwhm)
julia > lplot(p_fwhm)
Literature values with uncertainties
Numerical FWHM of signal components
LegendSpecFits.jl
RadiationSpectra.jl

## Slide 36: Energy Resolution
Current LEGEND-200 Dataset:
  47 calibration runs
  89 HPGe usable detectors
  6 different energy extractors
   More than 25,000 spectra auto-calibrated (!)
LegendSpecFits.jl
RadiationSpectra.jl

## Slide 37: Analysis workflow overview
waveforms
waveform level
Legend
raw data
detector-wise
file-wise
data
quality cuts
Remove non-physical waveforms
digital signal processing
(dsp)
filter to extract parameters, e.g. energy
dsp parameter level
energy calibration
(ecal)
Fit calibration data: γ-lines with known energies
run-wise
pulse-shape analysis (psd)
Remove
background events

## Slide 38: The A/E Classifier to Discriminate SSEs and MSEs
SSE
MSE
→ only applicable in ICPC, PPC and BEGe detectors
A: maximum current amplitude of event
E: height of charge pulse
Notes: - “The A/E classifier is a PSD classifier that can distinguish between signal-like single-site events (SSEs) and background-like multi site events (MSEs) based on the charge and current signal of the events.”
Detetcor and run/partition specific
– determine cut value below everything is rejected (low A/E cut) and a certain value like 3 or 9 above all events are rejected (high A/E cut)
Discriminate between SSEs and MSEs based on charge and current signal. Current is derivative of charge and has several peaks for MSEs -> maximal current pulse is lower compared to the signle current pulse we get from an event with same energy (plus charge signal i.e. waveform has multiple kinks for MSEs)

## Slide 39: Pulse Shape Discrimination
Double Escape Peak (DEP) as proxy for Single Site Events (SSE)
 Fully automated cut generation
FEP
p+ events
SSEs
SEP
DEP
MSE and n+ events
LegendSpecFits.jl
RadiationSpectra.jl
Notes:   7 days of physics data taking
  + Calibration run with 4 Th-228 calibration sources
  form a run

## Slide 40: Pulse Shape Discrimination - A/E
SEP
Current LEGEND-200 Dataset:
  3 different A/E extractors
   More than 12,000 auto-tuned cuts (!)
julia > r_sf, p_sf = get_peak_surrival_fraction(
aoe, e, 2103u”keV”, 20.0u”keV”, -2.0)
julia > lplot(p_sf)
LegendSpecFits.jl

## Slide 41: Analysis workflow overview
waveforms
waveform level
Legend
raw data
detector-wise
file-wise
data
quality cuts
Remove non-physical waveforms
digital signal processing
(dsp)
filter to extract parameters, e.g. energy
dsp parameter level
energy calibration
(ecal)
Fit calibration data: γ-lines with known energies
run-wise
pulse-shape analysis (psd)
Remove
background events
cal. energy spectrum
event building
Put everything together:
- Germanium dets
- LAr
- all cuts
partition-wise
all LEGEND instrumentation

## Slide 42: SiPM Calibration
Gaussian Mixture Model
 Effective Peak Positions
julia > r_si, p_si = sipm_simple_calibration(e_uncal)
julia > lplot(p_si)
julia > r_fit, p_fit = fit_sipm_spectrum(
r_si.pe_simple_cal, 0.5, 3.5)
julia > lplot(p_fit)
julia > r_cal, p_cal = fit_calibration(
1, r_fit.positions, 1:1:3)
julia > lplot(p_cal)
*9 SiPMs/channel
LegendSpecFits.jl

## Slide 43: Event Building
Software trigger condition:
  Any{EnergyHPGe} > 25keV && waveform passes QC
Physical event condition:
  All{HPGeNo-Trigger} == “Baseline-Only”
LAr anti-coincidence:
  Sum{EnergySiPM} > 4 PE
Define Anti-Coincidence
  Number{TriggerHPGe} == 1
Define PSD cut
  All{HPGeTrigger} == Single-site events
40K
42K
212Bi
208Tl
α-events
Custom software trigger and event reconstruction with all three detector subsystems
LegendEventAnalysis.jl

## Slide 44: Analysis workflow overview
cal. energy spectrum
dsp parameter level
waveforms
data
quality cuts
digital signal processing
(dsp)
energy calibration
(ecal)
pulse-shape analysis (psd)
event building
0νββ analysis
Remove non-physical waveforms
filter to extract parameters, e.g. energy
Fit calibration data: γ-lines with known energies
Remove
background events
Put everything together:
- Germanium dets
- LAr
- all cuts
T1/2 ,
background index
waveform level
Legend
raw data
detector-wise
run-wise
partition-wise
file-wise
all LEGEND instrumentation

## Slide 45: Data in the Region of Interest
7 events surviving in LEGEND-200 ROI:
Background Index
GERDA, MAJORANA + LEGEND combined
LEGEND-200 contribution
+30% of limit median expectation
event at 1.4 𝜎 from 𝑄ββ weakens limit
Observed | Sensitivity
Observed | Sensitivity
ZeronuFit.jl

## Slide 46: Outline
Introduction to LEGEND and 0νββ-decay physics
What is the JuLeAna Software Stack?
Features and highlights in the latest LEGEND analysis
Summary & Outlook

## Slide 47: Summary & Outlook
LEGEND features full Julia based Software Stack
LEGEND tools will become more and more JuliaPhysics tools, e.g. SolidStateDetectors.jl to be used by the community
Julia ecosystem demonstrates its versatility and power for fast and easy scaling
High acceptance by new students and beginners due to simplicity of code, software and API layout
And of course we have T-shirts

## Slide 48: 0νββ Decay Physics with 76Ge

## Slide 49
BACKUP

## Slide 50: Role of Julia Software Stack
Primary LEGEND software stack in Python, alternative in Julia
  Validation: Independent code guards physics results against bugs in primary stack
  Experimentation: Primary stack needs stable interface, alternative can use bleeding-edge technology and change/evolve more freely
  Future perspective: Find out what’s possible for LEGEND-1000
Community-wide and LEGEND-specific open-source packages
Custom dataflow and management routines for throughput cluster computing
raw
dsp
hit
evt

## Slide 51: Background Reduction Strategy
MJD, GERDA, LEGEND
Pulse shape discrimination (PSD) for multi-site and surface events
ββ decay signal: single-site event energy deposition in a ~1 mm3 volume
Ge detector anti-coincidence
LAr veto based on
Ar scintillation light
read-out by fibers
Muon veto based on Cherenkov light and plastic scintillator
Liquid Ar
Pure water
Fibers
PEN
MJD, GERDA, LEGEND
MJD, GERDA, LEGEND
MJD, GERDA, LEGEND
GERDA, LEGEND
MJD, GERDA, LEGEND
Scintillating PEN
plate detector holders
LEGEND

## Slide 52: Sensitivity
“…an era in which a discovery could come at any time!”
: Effective Majorana mass
: Decay half-life
: Nuclear matrix element
: Phase space factor

## Slide 53: LEGEND Experiment

## Slide 54
The - 1000 Experiment

## Slide 55: Th-228 Calibration Spectra
julia > using LegendSpecFits, LegendMakie
julia > r_simple, p_simple =
simple_calibration(e_uncal,
th228_lines, th228_windows)
julia > lplot(p_simple)

## Slide 56: A/E Digital Signal Processing

## Slide 57: Energy Dependence of Raw A/E
Model energy-dependence with:
“high A/E region”
“low A/E region”
SSE band
Notes: Savitzky golay filter for A/E, cusp filter for energy
Then normalize A/E to get values around 1
2D histogram (explain it -> every point is one event that has a certain A/E value, x axis energy)
Explain different A/E zones i.e. high A/E (close to surface??), low A/E (MSE) and SSE band
-> SSEs: populate gaussian shaped peak with mean mu and standard deviation sigma
Normalized and calibrated A/E classifier is to be centered around 0 and should have standard deviation of 1

## Slide 58: Definition of Compton Bands and Fit
Divide Compton continuum: 47 bands
Each band 20 keV range
From 520 keV – 2170 keV
GitHub: fit_aoe_compton
Fit function:
EMG:
Notes: EMG Formel ausschreiben

## Slide 59: Combined Fit
GitHub: fit_aoe_compton_combined
Combined Bayesian-guided MLE fit
Notes: MLE = Maximum Likelihood Estimation (Bayesian guided -> pseudo priors), starting values from single fits
Frequentist fit aber nutze Konzept von Priorn um Fitter zu guiden (fügen Prior Knowledge ein aber haben trotzdem kompletten Frequentist fit)
Take mu and sigma values of each CB as pseudo priors for optimization of a combined neg log likelihood
Visualize this -> e.g. bubble around three single CB fits to indicate that all CB together are used to determine the ‘optimal’ fit parameters (not every single CB optimized itself but all together)

## Slide 60: Energy Correction
Notes: Result: mu and sigma value for every CB -> fit these distributions with the mu and sigma functions to obtain the values for correcting for the energy dependence
This method “individual fits”, since all CB are fitted individually. But: prone to outlayers that could influence the result negatively
Therefore: new method was developed: the combined fit
Combined fit: residuals are 0 (no single points anymore)

## Slide 61: Charge Trapping Correction (CTC)
GitHub: ctc_aoe
CTC based on Compton bands:
Fit function:
Proportional to Charge trapping
Notes: Auf Basis der Compton Bänder und nicht DEP (Unterschied zu Pygama)
Numerische Optimierung ctc

## Slide 62: Charge Trapping Correction (CTC)
Notes: Effect of CTC
Higher drift time means lower A/E which we don‘t want since it could be leading to the rejection of a signal-like event

## Slide 63: Tuning of Low A/E Cut and the High A/E Cut
GitHub: get_low_aoe_cut
Low A/E: 90% SF of Tl208DEP
High A/E: cut off at 3 (or 9)
Notes: How to tune low A/E?
Swipe through DEP distribution and reject everything below it until we reach 90% SF since events in the DEP window should me mostly due to SSEs

## Slide 64: Survival Fractions after Low and DS A/E Cut
GitHub: get_peak_survival_fraction
LOW
DS

## Slide 65: Application of A/E Cut on Calibration Spectrum

## Slide 66: SiPM Analysis – LAr Cut
4x4 classifier
LAr anti-coincidence cut
in [-1µs, 5µs] around t0*
*(After discharge removal per SiPM trigger)
Total LAr Efficiency
94.29 ± 0.001 %*
*(Based on forced-trigger after DC removal)

## Slide 67: SiPM Analysis – LAr Cut

## Slide 68: LAr anti-coincidence cut
40K
42K
Liquid Ar
Fibers
42K
40K
Before
After
LAr anti-coincidence
Energy (keV)
40K
EC
42K
40K
Notes: Small graphics for potassium peaks
Monitoring plot with bigger font

## Slide 69: Muon Veto Analysis – DSP + Calibration
Custom DSP routines
Calibration based on 1 P.E. peak fit
Muon veto flag
Multiplicity > 12 || Sum(PE) > 30 P.E*
*(in [-10µs, 10µs] around t0)

## Slide 70: Muon Veto Analysis

## Slide 71: LEGEND Experiment