## Slide 1: Linear Colliders Lecture 3 Subsystems II
Main Linac (cont.)
  Accelerating gradient – NC/SC
Beam / bunch structure
Beam Delivery System
Alignment and Stabilization
Damping rings
NC/SC driven differences

## Slide 2: Previous Lecture
Particle production
Damping rings with wiggler magnets
Bunch compressor with magnetic chicane
small, short bunches to be accelerated w/o emittance blowup
Main linac:
  longitudinal wakefields => energy spread, chromatic effects
  Transverse wakefields, minimized by structure design
Now: Acceleration in the linac
Electron Gun Deliver stable beam current
Damping Ring Reduce transverse phase space (emittance) so smaller transverse IP size achievable
Bunch Compressor Reduce σz to eliminate hourglass effect at IP
Positron Target Use electrons to pair-produce positrons
Main Linac Accelerate beam to IP energy without spoiling DR emittance
Final Focus Demagnify and collide beams

## Slide 3: SC Technology
In the past, SC gradient typically 5 MV/m and expensive cryogenic equipment
TESLA development: new material specs, new cleaning and fabrication techniques, new processing techniques
Significant cost reduction
Gradient substantially increased
Electropolishing technique has reached ~35 MV/m in 9-cell cavities
31.5 MV/m ILC baseline
  limited by critical magnetic field Hcrit above which no superconductivity exists
=>
Chemical polish
Electropolishing

## Slide 4: Achieved SC accelerating gradients
Large progress by R&D program to systematically understand and set procedures for the production process
reached goal for a 50% yield at 35 MV/m by the end of 2010
90% yield at 28 MV/m exceeded in 2012
Tests for higher gradient ongoing
  limited certainly below 50 MV/m (Hcrit)
  X-FEL running with 23.6 MV/m
1st pass
2nd pass

## Slide 5: Limitations of Gradient Eacc
Surface magnetic field
  SC structures become normal conducting above Hcrit
  NC: Pulsed surface heating => material fatigue => cracks
Field emission due to surface electric field
  Vacuum arcs - RF break downs
  Break down rate => Operation efficiency
  Local plasma triggered by field emission => Erosion of surface
  Dark current capture => Efficiency reduction, activation, detector backgrounds
RF power flow
  RF power flow and/or iris aperture apparently have a strong impact on achievable Eacc and on surface erosion. Mechanism not fully understood

## Slide 6: NC Structure conditioning
Material surface has some intrinsic roughness (from machining)
Leads to field enhancement b field enhancement factor
Need conditioning to reach ultimate gradient RF power gradually increased with time
RF processing can melt field emission points
  Surface becomes smoother
  field enhancement reduced
  => higher fields less breakdowns
More energy: Molten surface splatters and generates new field emission points!
Excessive fields can also damage the structures
from S.Doebert

## Slide 7: Breakdown-rate vs gradient
C. Adolphsen /SLAC
Strong increase of breakdown rate for higher gradient

## Slide 8: Breakdown-rate vs pulse length
100
200
300
400
500
600
700
800
900
10
-3
10
-2
10
-1
10
0
10
1
Pulse length (ns)
Breakdown rate
SLAC 70 MV/m
SLAC 65 MV/m
SLAC 60 MV/m
KEK 65 MV/m
exp. fit
Higher breakdown rate for longer RF pulses
Summary: breakdown rate limits pulse length and gradient

## Slide 9: Accelerating gradient
Normal conducting cavities have higher gradient with shorter RF pulse length
Superconducting cavities have lower gradient (fundamental limit) with long RF pulse
SC
WARM

## Slide 10: Bunch structure
SC allows long pulse, NC needs short pulse with smaller bunch charge
ILC
2625
0.370
970
0.156
312
20000
ILC
12
0.0005
0.37

## Slide 11: Beam Delivery: Final Focus
Need large demagnification of the (mainly vertical) beam size
by* of the order of the bunch length σz (hour-glass effect)
Need free space around the IP for physics detector
Assume f2 = 2 m => f1 ≈ 600 m
Can make shorter design but this roughly sets the length scale
f1
f2 (=L*)

## Slide 12: Final Focus: chromaticity
Need strong quadrupole magnets for the final doublet
Typically hundreds of Tesla/m
Get strong chromatic aberations
for a thin-lens of length l:
change in deflection: change in IP position: RMS spot size:

## Slide 13: Final focus: Chromaticity
Small β* => βFD very large (~ 100 km)
for δrms ~ 0.3%
Definitely much too large
We need to correct chromatic effects
=> introduce sextupole magnets
Use dispersion D:

## Slide 14: Chromaticity correction
Combine quadrupole with sextupole and dispersion
x + Dδ
IP
quad
sextup.
KS
KF
Quad:
Sextupole:
Second order
dispersion
chromaticity
Could require KS = KF/D
=> ½ of second order dispersion left
Create as much chromaticity as FD upstream
=> second order dispersion corrected
y plane straightforward
x plane more tricky

## Slide 15: Final Focus: Chromatic Correction
Relatively short (few 100 m)
Local chromaticity correction
High bandwidth (energy acceptance)
FF tested at ATF2 (KEK Japan)
  44 nm achieved (37 nm design)
  scales to 6 nm at ILC (5 nm)
Correction in both planes
“2001 Report on the Next Linear Collider”, SLAC-R-0571

## Slide 16: Final focus: fundamental limits
From the hour-glass effect:
For highest energies, additional fundamental limit: synchrotron radiation in the final focusing quadrupoles => beamsize growth at the IP
so-called Oide Effect: minimum beam size:
for
for 3 TeV CLIC
λe is the Compton wavelength of the electron
F is a function of the focusing optics: typically F ~ 7 (minimum value ~0.1)

## Slide 17: Stability and Alignment
Tiny emittance beams, nm vertical beam size at collision
Any quadrupole misalignment ΔyQ,i and jitter will cause orbit oscillations and displacement at the IP (designated by *)
=> Tight component tolerances
  Field quality
  Alignment
Vibration and Ground Motion issues
Active stabilisation
Feedback systems
Demonstrate Luminosity performance in presence of motion
Some numbers (CLIC):
  Cavity alignment (RMS) 17 µm
  Main Beam quad alignment: 14 µm
  vert. MB quad stability: 1.5 nm @>1 Hz
  hor. MB quad stability: 5 nm @>1 Hz
  Final quadrupole: 0.15 nm @>4 Hz !!!
kQ,I quad. strength
𝛾 rel. gamma
β opt. beta funct.
Δɸi opt. phase adv.

## Slide 18: Active stabilization
Test bench reaches required stability of CLIC MB quadrupole

## Slide 19: Ground Motion
Site dependent ground motion with decreasing amplitude for higher frequencies

## Slide 20: Ground motion: ATL law
Need to consider short and long term stability of the collider
Ground motion model: ATL law
This allows you to simulate ground motion effects
Relative motion smaller
Long range motion less disturbing
Absolute motion
Relative motion over dL=100 m
1nm

## Slide 21: Beam-Beam feedback
Use the strong beam-beam deflection kick for keeping beams in collision
Sub-nm offsets at IP cause well detectable offsets (micron scale) a few meters downstream

## Slide 22: Other IP issues
Collimation:
    Beam halo will create background in detector
    Collimation section to eliminate off-energy and off-orbit particle
    Material and wakefield issues
Crossing angle:
    NC small bunch spacing requires crossing angle at IP to avoid parasitic beam-beam deflections
    Luminosity loss (≈10% when θ = σx/σz )
Crab cavities
    Introduce additional time dependent transverse kick to improve collision
Spent beam
    Large energy spread after collision
    Design for spent beam line not easy

## Slide 23: Post-Collision Line (CLIC)

## Slide 24: Bunch structure
SC allows long pulse, NC needs short pulse with smaller bunch charge
ILC
2625
0.370
970
0.156
312
20000
ILC
12
0.0005
0.37

## Slide 25: TESLA/ILC damping ring
Long pulse: 950µs * c = 285 km!!
Compress bunch train into 17 km (or less) “ring”
kick individual bunches
Min. circumference by ejection/injection kicker speed (≈20 ns)
“Dog bone” ring with ≈ 400m of 1.67 T wigglers
3.2 km circular rings in the baseline ILC design
Very demanding kicker rise + fall time < 6 ns

## Slide 26: CLIC damping ring layout
167.3
Total length 421m (much smaller than ILC), beam pulse only 47m
Racetrack shape with
  96 TME arc cells (4 half cells for dispersion suppression)
  26 Damping wiggler FODO cells in the long straight sections
Slide 26

## Slide 27: Warm vs Cold RF Collider
Normal Conducting
High gradient => short linac 
High rep. rate => ground motion suppression 
Small structures => strong wakefields 
Generation of high peak RF power 
Small bunch distance 
Superconducting
long pulse => low peak power 
large structure dimensions => low WF 
very long pulse train => feedback within train 
SC structures => high efficiency 
Gradient limited <40 MV/m => longer linac  (SC material limit ~ 55 MV/m)
low rep. rate => bad GM suppression (εy dilution) 
Large number of e+ per pulse 
very large DR 