## Slide 1
Mel-BOX Summary
Line 3 - PC (new cups) => ~23MW conditioning
  Hot spot ~ 40C @ piston flange
Line 4 - TD24 N1 No BO conditioning:
  Reach 38MW
  Pulsing 24/7
  LABview update: choose line, EPIC interface… etc
Oil leak (modulator)
VNA measurement + bead pool (preliminary) of TD24 N2 BO (seams good)
Linkage grant application & Australia’s Economic Accelerator (AEA) grant submitted

## Slide 2
TD24 N2 Conditioning plot (Update Code)
Melbourne
450M Pulses
350 M Pulses
CERN
~450M
Now is back to 33MW
Structure BDs
PC BDs
PC BDs
TD24 BDs

## Slide 3
New cups pulse compressor conditioing
Unusual reflection (~15 dB) and outgassing have been observed on the new PC cups.
  The reflection follows the PSI pulse shape ⇒ the issue is likely downstream of the PC (possibly a bad gasket?).
  Stop condition occurred around 10 MW.
TD24 was pulsed alone for a long period (~300 M pulses).
  The PC was sharing vacuum and power; leaks were observed only at the hybrid.
A few days ago, we restarted PC conditioning, within one day, we reached 23 MW.
  Interlocks were triggered due only to vacuum.
  Vacuum conditioning algorithm is being used.
PLR
PSI
Gain factor ≈ 3 at 1.5 µs pulse width, flat-top ≈ 50 ns.
Gain factor ≈ 4 at 2.5 µs pulse width, flat top ≈ 50 ns.
Vacuum conditioning only so far; only a few breakdowns

## Slide 4
Power & Vacuum

## Slide 5
We observe different temperature on the left and right plunger; the hottest point isn’t at the cup level but on the plunger flange of the left cavity
Right Cavity (R) NOT Calibrated should be -5C
Left (L) Cavity ~ Calibrated
L
R
Start pulsing chiller temperature
~ 30C, power ~16MW
Hot plunger
Calibration done with FLUKE Thermo-Gun

## Slide 6
We observe different temperature on the left and right plunger; the hottest point isn’t at the cup level but on the plunger flange of the left cavity
Right Cavity (R) NOT Calibrated should be -5C
Left (L) Cavity ~ Calibrated
~40C @ L Flange
Had a temp. probe to the flange
Note: If change the plunge position, we have vacuum spike even a low power.

## Slide 7
Possible reason of temperature difference
The 3 dB hybrid doesn’t split the klystron power equally.
Cavity frequency detuning
Coupling imbalance (β mismatch)
Outgassing and vacuum differences
  If one cavity has slightly worse vacuum (e.g. 10⁻⁷ mbar instead of 10⁻⁸ mbar):
  There are more residual gas molecules inside.
  These molecules absorb part of the RF energy through ionization or dielectric loss, especially near the field maxima.
  The absorbed energy appears as additional heating on the cavity wall (mostly at the iris or coupling port, where fields are strongest).
There might be a leak at the gasket, which also doesn’t look perfectly aligned when touched.

## Slide 8
Modulator D - Oil leak
Problem should be just the gasket
Contacted Scandinova for more details
Modulator C Oil level 8mm
Modulator D Oil level 2mm
Oil level should be just above the screwheads that fastens the tunings.
oil just so that the level is just above the screwheads that fastens the tunings,
D
C
Leak
D
C

## Slide 9
After fill ~1cm of the oil in both KLYs.
oil just so that the level is just above the screwheads that fastens the tunings,
D
C
D
C
C
D
D oil level decrease!!! Should not be calibration only the problem. BTW with the refill we have safe to pulse.
Just check regularly the oil lavel on the lids
The oil level is decreasing! It shouldn’t be just a calibration issue. By the way, with the refill we’re safe to pulse. Just check the oil level on the lids regularly.

## Slide 10
Code updated (Marca)
Reload configuration file with fixed phase
Epic INTERFACE
Choose the line
Show both lines
Reset to zero the SSA values when turned off.
Epic INTERFACE

## Slide 11
Beam line