## Slide 1
Name of the legal entity | Type | Country | Main contact person
INFN, Bologna | Institute | Italy | Gilda Scioli
Picotech SAS | Company | France | Crispin Williams
LIP-Coimbra | Institute | Portugal | Alberto Blanco
University of Clermont Ferrand | University | France | Cristina Carloganu
EUROPEAN MEMBERS
AIDAinnova (7.2)
MRPCs for fast timing at high incident flux of charged particles
Muon tomography: Low power, minimal gas use, excellent time resolution
Tsinghua University | University | China | Yi Wang
Shenzhen Institute of Advanced Technology, Chinese Academy of Sciences | Institute | China | Zheng Liu
Seoul National University Bundang Hospital | Institute | South Korea | Do-Won Kim
Gangneung-Wonju National University | University | South Korea | Yongwook Baek
Benemérita Universidad Autónoma de Puebla | University | Mexico | Cecilia Uribe Estrada
EXTERNAL MEMBERS

## Slide 2
AIDAinnova (7.2)
MRPCs for fast timing at high incident flux of charged particles
Muon tomography: Low power, minimal gas use, excellent time resolution
Highlights
  Gas: Need ‘streamer-free’ plateau
  Ecological
  Aging
  Low resistivity glass
  Excellent time resolution: picoTDC
  Muon tomography : minimum channels with excellent position and time resolution
AidaInnova 06/05/2025 slide 2

## Slide 3
Grant Agreement No: 101004761
AIDAinnova
Advancement and Innovation for Detectors at Accelerators
Horizon 2020 Research Infrastructures project AIDAINNOVA
deliverable report
Characterisation of small size MRPC prototypes for fast timing and high rates
Deliverable: D7.2
Many thanks to Yongwook Baek and Jinsook Kim for this report
AidaInnova 06/05/2025 slide 3

## Slide 4
Beam test :
  T10 line at PS CERN
  Two MRPC tested :
    8-gap (2 stacks of 4-gaps) chamber (HRG)
      standard float glass, thickness 400μm
      gap size 250 μm
      nylon fishing lines as spacers
    10-gap (2 stacks of 5 gaps) chamber (LRG)
      Low resistive glass (109 Ωcm), thickness 500μm
      gap size 235 μm
      ceramic coated fishing lines as spacers
  Two mixtures of gas tested :
    98% C2F4H2 and 2% SF6
    100% HFO-1234ze
AidaInnova 06/05/2025 slide 4

## Slide 5: Efficiency vs. Rate
Beam: 7 GeV pions
Beam profile : 1.3 cm FWHM
Rates :
  up to 28 kHz/cm2 for standard gas
  up to 63 kHz/cm2 for eco gas
Rate has no effect on LRG chamber (as expected)
difference between low resistivity and soda lime glass
AidaInnova 06/05/2025 slide 5

## Slide 6: Efficiency in a beam spill (ps spill 400 ms long)
HRG
LRG
AidaInnova 06/05/2025 slide 6

## Slide 7
HRG vs. LRG
  A distinct difference in the rate capability at high rate flux
Ecological gas vs. Standard gas
  No conspicuous difference in efficiency and timing performance (but significant increase of voltage)
A realistic test on the rate capability needs to be carried out in the further test by irradiating the larger detector area instead of a focused beam on a small spot.
AidaInnova 06/05/2025 slide 7

## Slide 8
neutron RPCs
200 mm
200 mm
Cathode: 0.3mm thick aluminium plate with both sides coated with 10B4C @ ESS Detector coatings workshop
Anodes: 0.3mm thick Float Glass plates OR 0.4mm thick Low Resistivity Glass
Spacers: 0.28mm diameter PEEK monofilament
10B4C layers thickness: 0.6 - 2.2μm
n
n
XY-coordinates readout
Cu-strips mutually orthogonal on 25μm thick FLEX-PCB
0.3mm strip width, 1mm Pitch
AidaInnova 06/05/2025 slide 8

## Slide 9
nRPC Detector - stack of 10 nRPCs
9 x nRPC units made with float glass
1 x nRPC unit made with Low Resistivity Glass
Detector on CT2 neutron beamline (λn=2.5 Å) at ILL
AidaInnova 06/05/2025 slide 9

## Slide 10
Cd slit
0.5 mm width
Count rate: LR-Glass vs Float Glass nRPCs
Beam collimated by a Cd-Slit & Neutron flux adjusted with plexiglass attenuators
Reconstructed Image
(XY)-2D Map
Integral of histograms normalized to unity
Float-Glass (9 x nRPCs)
For the LR-Glass the slit image profile remains unchanged by decreasing
the number of attenuator (Increasing the neutron flux):
Capable to sustain count rates > 40 kHz/cm² (0 attenuators)
AidaInnova 06/05/2025 slide 10

## Slide 11
Multilayer nRPC Detector
The detector's active area increased 4-fold compared to the first prototype, with spatial resolution remaining unaffected by scaling (staying < 0.3 mm FWHM)
Total detection efficiency (~42 %, λn=2.5 Å) agrees well with the simulation prediction.
The LR-Glass nRPC is shown to sustain máx. count rates > 40 kHz/cm2
  Suggests potential for count rates in the hundreds of kHz/cm² with multilayer nRPC detectors
Note that each neutron detection affects only a single gas gap at a time
AidaInnova 06/05/2025 slide 11

## Slide 12
Q amplifiers, X
Q amplifiers, Y
T amplifiers
Raw (X,Y)
illustration (partial) of readout
24 X channels + 24Y + 10 timing.
X, Y readout in parallel sub-groups,
group disentanglement via raw position from time Raw (X,Y).
130x90 cm² detector
Detector scheme 2x 6 gaps (0.3mm).
98% C2H2F4 and 2 % SF6
Detector Concept
10.1016/j.nima.2025.170466
AidaInnova 06/05/2025 slide 12
Large area Muon detectors

## Slide 14
2D position map of the 8×3×2 cm3 scintillators over the full
detector area, created with a 1.0 mm bin size in both dimensions.
(a) 2D position map of the 8×3×2 cm3 scintillators. The red arrow identifies the location of the spacer. (b) Projection of the 2D event map onto the X-axis, showing a clear reduction in the number of events at the location of the 300-μm gas gap spacers.
2D position map of the 8×3×2 cm3 and 8×4×1 cm3 scintillators
2D Spatial resolution
Timing precision
89 ps
Distribution of time differences
MRPC and scintillators
AidaInnova 06/05/2025 slide 14

## Slide 15: Some words on the picoTDC development
INFN Bologna
AidaInnova 06/05/2025 slide 15

## Slide 16
Update on picoTDC card (128 channels)
Firmware suite fully developed for PolarFire FPGA
I2C programming of picoTDC
Data acquisition via Ethernet (IPBUS)
Resolution tests using calibrated delayed line (EM) (0 – 600 ps)
1. power supply (12 V)
2. picoTDC board with 2 picoTDC
3. FMC adapter card (includes VHDCI connectors getting inputs from ALICE TOF FEA cards)
4. SiLab low-jitter clock (used to pulse at 30 KHz)
5. Electromagnetic trombone (Colby XT-200)
s2ch ≅ 1.34 LSB
Delay (TDC bins)
s2ch (TDC bins)
s1ch ≅ 0.95 LSB
Note :
LSB is 3 ps
AidaInnova 06/05/2025 slide 16

## Slide 17
Additional custom card: FMC adapter for Weeroc LIROC
LIROC is an ASIC (preamp+disc) optimized for SiPM
64 channels naturally “coupled” with picoTDC
8 discriminated output available on ext. connectors
I2C programming of LIROC via picoTDC Board
The cards will be used for test beams at CERN both on MRPC
(from NINO FEA) and SiPM (from LIROC)
Delay line measurements with picoTDC Board
AidaInnova 06/05/2025 slide 17

## Slide 18: Main highlights
Suitable eco gas tested (needs higher voltage)
Low resisitivity glass – works well for charged particle + neutron detector
Intelligent readout of Muon detectors allows small number of channels for readout of large area with exceptional position and time resolution
PicoTDC - excellent time resolution
AidaInnova 06/05/2025 slide 18

## Slide 19: Thank you for your attention