## Slide 1: WP5.2 – Transport Analysis Collimator Jaws Updates & Further Proceedings
L. Hannemann, F. Carra, M. Guinchard, L. Puddu
10/03/2025

## Slide 2: Updates
Influence of gravity on natural frequencies
Vibrational Input in z-direction and x-direction
Other collimator components to be checked
Transportation frame proposal by CINEL
Experimental verification proposals

## Slide 3: Collimators Configurations
Considered collimator jaws:
Key Structural Elements Analysed:
Absorber blocks
Shafts
Cooling pipes
Overall stress evaluation
Collimator Design | Material
TCTPXH | Inermet180
TCTPM | 
TCLP | 
TCLPX | 
TCSPM | Copper Coated Graphite

## Slide 4: Structural & Vibrational Analysis Setup
Static Structural: Loads of the clamping system
Modal
Static Structural: Loads of the clamping system
Modal
Random Vibrations: Norm
Random Vibrations: Experimental Data
Jaw without shaft
Jaw with shaft

## Slide 5: Comparison of Jaws Modal Analysis
Collimator | First Natural Frequency without shaft | First Natural Frequency with shaft
TCLP | 132 Hz | 77Hz
TCLPX | 88 Hz | 80.6 Hz
TCSPM | 146 Hz | 90 Hz
TCTPM | 126 Hz | 60 Hz
TCTPXH | 107 Hz | 78 Hz
Natural Frequency without shaft is higher than natural frequency with shaft for all collimators
Gravity had no influence on the natural frequencies

## Slide 6: Material Properties and Acceptance Criteria
A Safety Factor of 3 was used due to the high reliability needs for the components
Components | Material | Yield Strength | Compressive strength | Flexural Strength | Acceptance Criteria
Absorber Blocks | Inermet180 | 614 MPa | - | - | <205 MPa
 | Graphite | - | 130 MPa | 60 MPa | <43.3 MPa (compr.) / <20 MPa (flex.)
Shafts | SS-316L | 205 MPa | - | - | <68.3 MPa
Cooling pipes | Cu-Ni 90-10 | 109.2 MPa | - | - | <36.4 MPa
Housing | CuCrZr | 460 MPa | - | - | <153.3 MPa

## Slide 7: Random Vibrations – PSD Norm Input
ASTMD4169 Norm
Evaluate the durability of packaging for products transported by road (trucks, vans, etc.)
3 PSD levels provided by standard
High level PSD applied in z-direction and x- direction on the shafts.
Random Vibrations
Acceleration PSD
Input

## Slide 8: Absorber Blocks - Peak Stress Evaluation (ASTMD4169 Input)
Collimator | Block Material | Equivalent Von Mises Stress z- direction | Equivalent Von Mises Stress x- direction
TCLP | Inermet180 | 2.9 MPa | 2.5 MPa
TCLPX | Inermet180 | 0.9 MPa | 1.9 MPa
TCSPM | Graphite | 0.1 MPa | 0.6 MPa
TCTPM | Inermet180 | 1.7 MPa | 5.5 MPa
TCTPXH | Inermet180 | 2.9 MPa | 12 MPa
Acceptance Criteria:
​ for Inermet
​ for Graphite

## Slide 9: TCTPXH Stress on Absorber Blocks – ASTMD z-Direction Input

## Slide 10: Shafts- Peak Stress Evaluation (ASTMD4169 Input)
Collimator | Equivalent Von-Mises Stress z-direction | Equivalent Von-Mises Stress x-direction
TCLP | 5.0 MPa | 17.0 MPa
TCLPX | 10.6 MPa | 27.0 MPa
TCSPM | 4.5 MPa | 10.4 MPa
TCTPM | 8.6 MPa | 25.9 MPa
TCTPXH | 3.2 MPa | 13.1 MPa
Acceptance Criteria:
​ for SS-316 L

## Slide 11: TCSPM Stress on Shafts - ASTMD z-Direction Input

## Slide 12: Cooling Pipes- Peak Stress Evaluation (ASTMD4169 Input)
Collimator | Equivalent Von-Mises Stress z-direction | Equivalent Von-Mises Stress x-direction
TCLP | 0.6 MPa | 1.7 MPa
TCLPX | 1.8 MPa | 6.0 MPa
TCSPM | 0.4 MPa | 0.4 MPa
TCTPM | 0.9 MPa | 3.0 MPa
TCTPXH | 0.5 MPa | 1.4 MPa
Acceptance Criteria:
​ for Cu-Ni 90-10

## Slide 13: TCSPM Stress on Cooling Pipes - ASTMD z-Direction Input

## Slide 14: Peak Stress Evaluation Overalll (ASTMD4169 Input)
Collimator | Equivalent Von-Mises Stress z-direction | Equivalent Von-Mises Stress x-direction
TCLP | 6.7 MPa – on housing above shaft | 20.6 MPa - on housing over shaft
TCLPX | 10.4 MPa – on the end of the shaft | 27.0 MPa - on the end of the shaft
TCSPM | 5.1 MPa - on housing above shaft | 10.3 MPa – on the shaft
TCTPM | 8.7 MPa - on housing above shaft | 25.9 MPa - on the shaft
TCTPXH | 3.2 MPa - on the shaft | 13.1 MPa - on the shaft
Acceptance Criteria:
​ for CuCrZr
​ for SS-316 L

## Slide 15: TCSPM Overall Stress - ASTMD z-Direction Input

## Slide 16: TCLP Directional Overall Deformation – ASTMD Input
Collimator | Maximum deformation z- direction input | Maximum deformation x- direction input
TCLP | 3 in x-direction | 53 in x-direction
TCLPX | 34 in x- direction | 144 in x-direction
TCSPM | 13 in z-direction | 47 in x-direction
TCTPM | 31 in x-direction | 109 in x-direction
TCTPXH | 23 in x-direction | 100 in x-direction
Collimator | Maximum deformation z- direction input | Maximum deformation x- direction input
TCLP |  | 
TCLPX |  | 
TCSPM |  | 
TCTPM |  | 
TCTPXH |  | 
 No clash to be expected with other components

## Slide 17: TCLP Directional Overall Deformation – ASTMD z- Direction Input

## Slide 18: Random Vibrations – Experimental Input
EDMS reference: https://edms.cern.ch/document/2755675/2
Maximum PSD acceleration on the frame of the cryomodule in z-direction
Random Vibrations
Acceleration PSD
Input

## Slide 19: Absorber Blocks - Peak Stress Evaluation (Experimental Input)
Collimator | Equivalent Von- Mises Stress z- Direction | Equivalent Von-Mises Stress x- Direction
TCLP | 0.6 MPa | 1.8 MPa
TCLPX | 2.8 MPa | 7.7 MPa
TCSPM | 0.1 MPa | 0.3 MPa
TCTPM | 1.3 MPa | 3.9 MPa
TCTPXH | 1.6 MPa | 12.0 MPa
Acceptance Criteria:
​ for Inermet
​ for Graphite

## Slide 20: TCLP Stress on Absorber Blocks- Experimental Input Z-Direction

## Slide 21: Shafts- Peak Stress Evaluation (Experimental Input)
Collimator | Equivalent Von-Mises Stress z-direction | Equivalent Von-Mises Stress x-direction
TCLP | 7.9 MPa | 12.3 MPa
TCLPX | 7.9 MPa | 25 MPa
TCSPM | 9.8 MPa | 10.2 MPa
TCTPM | 16.0 MPa | 19.3 MPa
TCTPXH | 2.7MPa | 13.1 MPa
Acceptance Criteria:
​ for SS-316 L

## Slide 22: TCLP Stress on Shafts – Experimental Input Z-Direction

## Slide 23: Cooling Pipes- Peak Stress Evaluation (Experimental Input)
Collimator | Equivalent Von-Mises Stress z-direction | Equivalent Von-Mises Stress x-direction
TCLP | 0.2 MPa | 0.4 MPa
TCLPX | 1.9 MPa | 5.7 MPa
TCSPM | 0.9 MPa | 0.4 MPa
TCTPM | 0.9 MPa | 2.1 MPa
TCTPXH | 0.7 MPa | 1.4 MPa
Acceptance Criteria:
​ for Cu-Ni 90-10

## Slide 24: TCLP Stress on Cooling Pipes – Experimental Input Z-Direction

## Slide 25: Peak Stress Evaluation Overall (Experimental Input)
Collimator | Equivalent Von-Mises Stress z-direction | Equivalent Von-Mises Stress x-direction
TCLP | 9.4 MPa - on housing above shaft | 20.6 MPa - on housing over shaft
TCLPX | 7.9 MPa - on the end of the shaft | 27.0 MPa - on the end of the shaft
TCSPM | 11.08 MPa - on housing above shaft | 10.35 MPa - on the shaft
TCTPM | 16.3 MPa - on housing above shaft | 25.9 MPa - on the shaft
TCTPXH | 2.7 MPa - on the shaft | 13.1 MPa - on shaft
Acceptance Criteria:
​ for CuCrZr
​ for SS-316 L

## Slide 26: TCLP – Overall Stress Experimental Input Z-Direction

## Slide 27: TCLP Directional Overall Deformation – Experimental Input
Collimator | Maximum deformation z- direction input | Maximum deformation x- direction input
TCLP | 18 in x-direction | 76 in x-direction
TCLPX | 29 in x-direction | 132 in x-direction
TCSPM | 13 in z-direction | 47 in x-direction
TCTPM | 22 in z-direction | 81 in x-direction
TCTPXH | 15 in x-direction | 71 in x-direction
Collimator | Maximum deformation z- direction input | Maximum deformation x- direction input
TCLP |  | 
TCLPX |  | 
TCSPM |  | 
TCTPM |  | 
TCTPXH |  | 
 No clash to be expected with other components

## Slide 28: TCLP Directional Deformation – Experimental Input Z-Direction

## Slide 29: Conclusion of Simulations
The loads remain within the acceptance criteria in all cases.
Deformations are very low  no risk of clash
Load orientation in the Z-direction is preferable over the X-direction, though both remain acceptable.
Gravity has no influence on the natural frequencies.
The maximum load occurs on the housing or the shaft.

## Slide 30: CINEL Transportation Frame

## Slide 31: CINEL Transportation Frame

## Slide 32: CINEL Transportation Frame
To be confirmed:
  Final transportation frame layout
  Damper specifications and positioning

## Slide 33: Failure modes of other components to consider
Drift Tube: Buckling, resonance-induced vibration, localized stress concentrations leading to cracks.
Bolted/Fastened Connections: Loosening due to vibration

## Slide 34: Experimental Verification
Modal analysis of pre-series jaw
Monitoring of the first transport
Review the transportation frame provided by CINEL
Shaker test on jaw mock-up to check for screw loosening

## Slide 35: Experimental Verification
Why Perform Model Correlation?
Confirm the accuracy of the finite element model (FEM).
Identify discrepancies between simulations and real-world behavior.
Improve confidence in the model for further analyses.
Ensure reliable predictions for operational conditions and transport effects.
Simulation of natural frequencies of Jaws
Experimental Test of first natural frequencies
Model Correlation

## Slide 36: Thank you for your attention

## Slide 37: Background – Collimator Setup TCLP
TCLP Collimator cross Section
Jaw with shafts in vertical orientation
Assembly: The jaws are fixed to two shafts and are positioned within a housing.
Orientation: Vertical orientation during transport.
shafts
Absorber blocks
Clamping system
tapering

## Slide 38: First Step: Modal Analysis
Objective of Simulation:
  Conduct a modal analysis on the jaw without the shaft to evaluate its vibrational characteristics.
Reasoning:
  Benchmark simulation results against real measurements on a jaw in the same condition.
  Validate the accuracy of the simulation through comparison with actual data.
Expected Outcome:
  If the simulation accurately reflects real measurements, it confirms the reliability of further vibrational analysis.
  A successful modal benchmarking provides confidence that subsequent simulations will accurately predict vibrational behavior.
Jaw without shafts

## Slide 39: First Step: Modal Analysis
Objective of Simulation:
  Conduct a modal analysis on the jaw without the shaft to evaluate its vibrational characteristics.
Reasoning:
  Benchmark simulation results against real measurements on a jaw in the same condition.
  Validate the accuracy of the simulation through comparison with actual data.
Expected Outcome:
  If the simulation accurately reflects real measurements, it confirms the reliability of further vibrational analysis.
  A successful modal benchmarking provides confidence that subsequent simulations will accurately predict vibrational behavior.
Jaw without shafts

## Slide 40: TCLP First Bending Modes
Jaw without shaft
Jaw with shaft
First bending moment: 132Hz
First bending moment: 77Hz

## Slide 41: TCLPX First Bending Mode
First Bending Mode: 80.6 Hz
First Bending Mode: 88Hz

## Slide 42: TCSPM First Bending Mode
First Bending mode: 90.5 Hz
First Bending mode: 146 Hz

## Slide 43: TCSP First Bending Mode
First Bending Mode: 101 Hz
First Bending Mode: 136 Hz

## Slide 44: Second Bending Modes
Jaw without shaft
Jaw with shaft
Second bending moment: 228 Hz
Second bending moment: 114 Hz

## Slide 45: Maximum Stress on Components with Standard
Input: ASTMD High standard load in z-direction and in x-direction

## Slide 46: TCLP: Stress on Blocks for ASTMD4169 Input Z-Direction
Maximum stress: 1 MPa for a scale factor of 3 sigma

## Slide 47: TCLPX: Stress on Blocks for ASTMD4169 Input Z-Direction

## Slide 48: TCSPM: Stress on Blocks for ASTMD4169 Input Z-Direction
Maximum stress: 0.06 MPa for a scale factor of 3 sigma

## Slide 49: TCSP: Stress on Block for ASTMD4169 Input Z-Direction
Maximum stress: 0.12 MPa for a scale factor of 3 sigma

## Slide 50: TCSP: Stress on Blocks for ASTMD4169 Input Z-Direction
Maximum stress: 0.5 MPa for a scale factor of 3 sigma

## Slide 51: TCSP: Stress on Shafts for ASTMD4169 Input Z-Direction
Maximum stress: 5 MPa for a scale factor of 3 sigma

## Slide 52: TCLP: Max Stress for ASTMD4169 Input
Maximum overall stress: 6.7 MPa for a scale factor of 3 sigma

## Slide 53: TCLPX: Max Stress for ASTMD4169 Input
Maximum overall stress: 8.7 MPa for a scale factor of 3 sigma

## Slide 54: TCSPM: Max Stress for ASTMD4169 Input
Maximum overall stress: 5.1 MPa for a scale factor of 3 sigma

## Slide 55: Comparison ASTMD4169 Input Z- and X- direction
 | Directional Deformation in x-direction [mm] | Directional deformation in z- direction [mm]
Blocks | 0.095 | 0.026
Shaft | 0.05 | 0.002
Cooling pipes | 0.1 | 0.01

## Slide 56: TCLP: Stress on Blocks for Z-Frame Input

## Slide 57: TCLPX: Stress on Blocks for Z-Frame Input

## Slide 58: TCSPM: Stress on Blocks for Z-Frame Input
Very little response of the block to the acceleration PSD input

## Slide 59: TCSP: Stress on Blocks for Z-Frame Input

## Slide 60: Stress on Shafts for Z-Frame Input

## Slide 61: Stress on Cooling pipes for Z-Frame Input

## Slide 62: TCLP Material Properties and Collimator Setup
Material | Yield Strength [MPa] | Youngs Modulus [GPa]
Steel 304 L | 210 | 200
Steel 316L | 205 | 190
CuCr1Zr | 293 | 130
CuNi90/10 | 109.2 | 142
Inermet180 | 613 | 360

## Slide 63: TCLPX Material Properties and Setup
Material | Yield Strength [MPa] | Youngs Modulus [GPa]
Steel 316L | 205 | 190
CuCr1Zr | 293 | 130
CuNi90/10 | 109.2 | 142
Inermet180 | 613 | 360

## Slide 64: TCSPM Material Properties and Setup
Material | Yield Strength [MPa] | Youngs Modulus [GPa]
Steel 316L | 205 | 190
CuCr1Zr | 293 | 360
CuNi90/10 | 109.2 | 142
Graphite |  | 11.5
Glidcop |  | 128

## Slide 65: TCLP: Maximum Stress for Z-Frame Input
Maximum overall stress on the CuCr1Zr housing: 9.3 MPa for a scale factor of 3 sigma

## Slide 66: TCLPX: Maximum Stress for Z-Frame Input
Maximum overall stress on the CuCr1Zr housing: 8.1 MPa for a scale factor of 3 sigma

## Slide 67: TCSPM: Maximum Stress for Z-Frame Input
Maximum overall stress on the CuCr1Zr housing: 11.08 MPa for a scale factor of 3 sigma

## Slide 68: Summary TCLP
 | Max Equivalent Stress [MPa] |  | Max Directional Deformation [mm] | 
 | ASTMD4169 | Cryomodule z-frame | ASTMD4169 | Cryomodule z-frame
Blocks | 1 | 0.72 | 0.03 (x-direction) | 0.02 (z-direction)
Shaft | 4.97 | 7.87 | 0.0014 (x- direction) | 0.013 (x-direction)
Cooling pipes | 0.55 | 0.65 | 0.027 (x-direction) | 0.017 (z-direction)
Z-direction input