## Slide 1: Overview of ongoing and future studies for WP5.1
R. Bruce For WP5.1
WP 5.2 meeting, 07/04/2025

## Slide 2: Introduction
A lot of work has been done in the past to define the upgrade path for HL-LHC collimation
  Beam dynamics studies, energy deposition, thermo-mechanical analysis…
We have now a robust baseline collimation system for HL-LHC, but…
  HL-LHC baseline is constantly under development – need to ensure that collimation system is adequate
  Need to verify with beam tests that all works as expected in the LHC
    Tests under HL-LHC conditions where possible, test new hardware,
  Need to study and address any remaining open points
  Need to study alternative and backup scenarios
Main areas of the tasks of WP5.1 in simulations and measurements:
  Studies of proton collimation
  Simulation studies of Pb ion collimation
  Studies of beam halo

## Slide 3: Studies of proton collimation
Studies of baseline collimator settings: “Tight” vs “Relaxed”
  Tight: initial baseline; slightly better cleaning and better aperture protection – allows for smaller β*
  Relaxed: more open settings for better impedance and potentially better tolerance to beam jitter and failures with overpopulated halo
  Ongoing studies:
    Cleaning simulations, also with imperfections, and to reproduce experimental observations in 2024 MD
      Study cleaning with realistic sagittas, also from beam-induced deformation
      Load on graphite vs MoGr secondaries at most exposed slots
    MD proposed in 2025 with further beam measurements
Studies of collimation in alternative scenarios
  Flat optics proposed by WP2 for improved performance
  IR7 is unchanged, but this has potential implications on

## Slide 4: Studies of proton collimation
New IR7 optics
  Larger β-functions  Larger physical collimator gaps  reduced impedance
  Larger β-function at primary collimator  larger normalized kick in scattering; more likely to intercept scattered particles with downstream stages  better cleaning
  Hence, new optics developed for optimized cleaning and impedance
    Included in present HL-LHC baseline
  Further studies ongoing:
    Development for MD in 2025 and possible deployment in 2026
    Energy deposition studies to be done, potentially followed by thermomechanical studies
  In collaboration with WP2
Failures
  Tracking simulations of failure scenarios to study global loss pattern and impacts on collimators: asynchronous beam dump, injection failure, crab cavities, CLIQ…
  In collaboration with WP7
  verify protection of aperture and sensitive collimators
    Potential need for of energy deposition and thermomechanical studies

## Slide 5: Studies of proton collimation
Quench test
  Experimental test– excite high losses, corresponding to HL-LHC design beam loss power of ~1MW, and observe if the collimation system can handle this without quench
  First tests done with B2; could not reach 1 MW due to dumps on fast BLM running sums or collimator temperature
  2025: new test proposed on B1, hope some of the previous limitations are mitigated by new BLMs mounted on the tunnel wall
  Studied collimator robustness under these loads in the past – likely no new simulations needed in 2025
  Still of interest to study thermomechanical response of TCSPM during 2022 quench test
BLM thresholds
  Previous studies on operational thresholds for Pb ion operation
  Ongoing studies on proton losses at start of ramp
  Typically studies of tracking, energy deposition, and thermomechanical response to quantify allowed losses vs collimator robustness
  Proposed to implement ANSYS models for all collimator types to quickly react in case of encountered operational bottlenecks
  In collaboration with BLM threshold WG

## Slide 6: Studies of Pb ion collimation
All HL-LHC upgrades for ions installed – full HL-LHC performance should be available already
  Reminder: 11T dipoles not installed in LS2, now using crystal collimation to improve cleaning
  2023 operation limited by beam losses – a lot of follow-up studies done to eliminate source of losses and improve cleaning
  Strong improvement in 2024, but still ongoing work to optimize the cleaning setup
BLM thresholds for ions
  Simulation campaign of collimator robustness, together with BLM threshold WG, allowed increased BLM thresholds in 2024
  Tracking, energy deposition, thermomechanical response
Crystal collimation quench test
  Excite HL-LHC design losses, verify if they can be sustained without quench
  Planned in 2024, but not done due to machine downtime. Re-proposed for 2025
  Preparatory studies of collimator robustness (tracking + energy deposition + thermomechanical response) – strong synnergy with BLM threshold studies

## Slide 7: Studies of Pb ion collimation
New IR7 optics for ions and crystal collimation
  Similarly to protons, new IR7 optics developed for Pb ions
  Main goal: cleaning improvement (impedance not critical)
  Proposal for experimental test in 2025
Failure modes with crystals
  Presently using old CFC secondary collimators as crystal absorbers in the H plane, but new coated MoGr secondaries in V plane
  Can the channeled halo be sustained on coated secondary collimator in case of failures ?
  To be studied: channeled halo on coating in case of asynchronous beam dump

## Slide 8: Studies of Pb ion collimation
ALICE background studies
  Strong background observed in 2023, prevented data taking at ALICE
  Crash effort enabled understanding and mitigation of the main component (fragmented Pb207 ions from IR7 collimators hitting tertiary collimator and showering on ALICE)
  Some background still remains – acceptable for operation, but requests to reduce further if possible
  Ongoing studies to identify background source and further alleviation measures
Tracking of Pb ion losses in IR3
  halo and collisional losses
  Gives important inputs to IR3 dose estimates
Potentially study collimation of future ion beams in Run 5
  ALICE3 letter of intent asks for significantly higher NN-luminosity – potential to increase luminosity with with other ions than Pb and alternative production schemes
  Need to study collimation cleaning and collisional losses with these other ions
    Account for higher stored beam energy and higher luminosity!
    Tracking, energy deposition – to be seen if other studies are needed
  First experimental tests of crystal collimation proposed with oxygen and neon in 2025

## Slide 9: Pb ion collisional losses
In close collaboration with WP10
BFPP losses in Pb-Pb
  alleviated with new TCLD collimators in IR2 and orbit bumps in IR1/5
  Request for high luminosity in IR8 – re-use TCLDs built for IR7 but not used?
    Not part of HL-LHC baseline
Load from collisional losses in p-Pb
  Imposed limit on luminosity in 2016 p-Pb run
  Need to study if present TCL and TCLD collimators can alleviate these losses
  What is the limit at LHCb?

## Slide 10: Studies of beam halo
Reminder: HEL removed from baseline – presently no halo cleaning in HL-LHC
  Risk of over-populated tails and high losses during beam jitter or failures
  What are the implications for HL-LHC operation?
  Crucial to understand what halo population we can expect in HL-LHC
Experimental studies: halo measurements
  Using collimator scrapings, measure beam halo with operational beams
  MDs proposed: collimator scrapings at new points in the cycle; halo cleaning with stable islands
Theoretical studies on halo models and diffusion
  Complement to experimental studies, help extrapolating LHC measurements to HL-LHC

## Slide 11: Conclusions
We have a solid collimation baseline for HL-LHC, but a number of items remain to be studied
  For baseline and alternatives
Rich and interesting future program of WP5 studies
  Simulations and experimental studies of
    proton collimation
    Pb ion collimation
    Beam halo

## Slide 12: Thanks for the attention