## Slide 1: MolFlow and SynRad development update
2025-02-25 TE-VSC seminar
Márton Ady, Petar Trifunović

## Slide 2: MolFlow in one slide
Test-particle vacuum simulator
Uses Monte Carlo test particles
Assumes molecular flow
Written by Roberto Kersevan in 1990s
Modernized at ESRF in 2008
Developed at TE-VSC since 2012
Approx. 1000 users

## Slide 3: Today: 5 new functions
Physics
Visualization
Contamination
Geometry edit
Data extraction
2024
2025

## Slide 4
Entrance
Exit
A Monte Carlo simulation: Transmission probability

## Slide 5: MolFlow for sputtering simulations
C
C
Simple sputtering simulation
With background gas

## Slide 6: Collision between two particles
From Fabian Manke

## Slide 7
mass ratio = 0.5
mass ratio = 5
mass ratio = 50
collisions off
green lines: particle trajectories
purple dots: collision locations
red dots: absorption locations on walls

## Slide 8
mass ratio = 0.5
mass ratio = 50
mass ratio = 5
collisions off

## Slide 9
Sputtering seminar for SCC section
reference – no background
with background gas

## Slide 10: Water vapor sticking
Surface
Probability of sojourn time t:
where
f: Molecule's surface oscillation frequency [Hz]
E: Adsorption energy [J/mole]
A: Escape probability per oscillation: A=exp(−E/(RT))

## Slide 11: Time-dependent mode in MolFlow
CLIC cavity geometry: Cedric Garion
Problem: No connection between independent time moments

## Slide 12: New features
Add temperature-dependent residence time
Add reflection counters
Integrate over time
New plotter window

## Slide 13: Particle balance example
Mean residence time: 0.2s
Outgassing: from 0 to 0.1s

## Slide 14: Automation with MolFlow
Run MolFlow programmatically
molflowCLI
molflowCLI.exe --file inputFile.xml -t 3600 -o ./outputFile.xml
Extract results
Change physics or geometry
Parameter sweep
Iterative simulations
Result-based optimization
Python XML interface
Python XML interface

## Slide 15: Python XML interface
Python is an easy to learn, popular programming language
XML is a file format – both machine and human-readable
  Looks like a tree
  Non-linear, can be searched
MolFlow file
Geometry
Physics
Particle balance
Pressure
Facets
Vertices
Gas mass
Input
Results
Time

## Slide 16: Published as Python module or Jupyter notebook

## Slide 17: Examples
Set what to work on:
Read geometry:
Get results:
Change physics:

## Slide 18
Cross-section viewer

## Slide 19: Rich facet and vertex movement
SynRad movement using beam trajectory points
  Two points of a trajectory define the movement parameters:
    Direction,
    Distance,
    Rotation.

## Slide 20: Rich facet and vertex movement
SynRad movement using beam trajectory points
  Two points of a trajectory define the movement parameters:
    Direction,
    Distance,
    Rotation.
Example (top view):

## Slide 21: Rich facet and vertex movement
SynRad movement using beam trajectory points:
  Why add this feature?
Problem:
  Moving or duplicating smaller pieces of geometry along longer pipes.
  Long pipes usually contain beams whose trajectory is aligned with the pipe.
The old “solution”:
  Using the Move and Rotate options separately, manually calculating the rotation.
The new solution:
  Selecting the appropriate trajectory points while SynRad does the rest.

## Slide 22: Rich facet and vertex movement – a simple demo

## Slide 23: Rich facet and vertex movement – FCCee demo

## Slide 24: New feature – extracting data along a path
Problem:
  It is often required to extract simulation results (e.g. pressure, impingement rate…) along a certain path in the geometry.
The old solution:
  For straight paths, it could be sufficient to add a transparent facet that stretches along the desired path and “records” results.
  For curved paths, this can be hard:
Fenna Ukena, Experimental Measurements of Electron Capture and Loss Cross Sections of Ions with Gaseous Targets, CERN VSC group seminar, 21 January 2025

## Slide 25: New feature – extracting data along a path
Problem:
  It is often required to extract simulation results (e.g. pressure, impingement rate…) along a certain path in the geometry.
The old solution:
  For straight paths, it could be sufficient to add a transparent facet that stretches along the desired path and “records” results.
  For curved paths, this can be hard.
The new solution:
  Allow the user to define a data extraction path by specifying the points in space it consists of.
  Read simulation results from the surrounding facets.

## Slide 26: Extracting data along a path – a preview

## Slide 27: Extracting data along a path – an important use case
FCC-ee:
  Using curved geometries at CERN is a very common practice.
  The new feature will be useful for simulations for the FCC-ee.
  The SynRad version will include data extraction along trajectory points