## Slide 1
Tape status and strategy at CERN
Department
CERN
IT
DSS
Data Storage
Services
Germán Cancio, Vladimír Bahyl, Eric Cano, Steve Murray, Daniele Kruse - CERN
4x Oracle SL8500
40x T10KC drives
+legacy T10KBs
Setup and numbers
5x IBM TS3500
40x TS1140 drives
+ legacy TS1130s
62PB data in 208M files and 52K tapes
1.5 .. 3PB new data per month
Up to 6.9GB/s to tape during HI period
From nearline to archiving…
Tape technology is evolving…
Increased per-tape capacity and transfer speed
Large-scale archive market building up (legal, media, cloud providers)
… but library and drive mount/positioning times not improving!
Full deployment of ‘buffered’ tape marks (cf. poster 415, S. Murray)
Early 2011, reduced sync tape marks from 3 to 1 per CASTOR file
speed increase from ~15MB/s to ~40MB/s
Achieve near-native drive speed by writing data in effective chunks of ~32GB
eliminates “backhitch” (tape repositioning) inefficiencies
  Before:49MB/s avg
Speed up streaming access and minimise file/user based HSM
b) optimise data retrieval
Deployed “traffic lights” and “bus lanes” for prioritising bulk read requests
Access to robotics and drives is the bottleneck
  Define thresholds for tape mounts:
  minimum volume, max wait time, concurrent drive usage; group related tape requests
  Different thresholds + priorities for production coordinators and end users
3x files / volume per mount -> 3x increase in effective tape access speed
~50% less tape mounts (~7K to 3.5K mounts per day)
Additional ~30% less tape mounts expected when moving CMS end users to EOS
… now evaluating commodity tape
Tape usage at CERN was heavy-duty requiring enterprise-class tape equipment from IBM and Oracle
With far less demand in terms of small file writes and read mounts, “commodity” tape (LTO) becomes a serious option, i.e. for “dusty” archived data which is infrequently accessed
Market share: LTO (~90%) vs. enterprise media (~2%)
Since Nov 2011, testing a SpectraLogic T-Finity library (max 120 drives, 30K slots)
  Test configuration: 5-10 LTO-5 drives, 1000 cartridges (1.5PB)
Necessary CASTOR adaptations coded and released
  Field test drives, library, and vendor support – storing 2nd copies of experiment data
  So far satisfactory results in general
Active monitoring and verification
Automated handling of tape, drive and library malfunction
User activity is monitored and unusual/inefficient usage automatically reported
“bus lane” concept encourages users to pre-stage data
Top users causing tape mounts:
STAGER USER:GROUP #MOUNTS #TAPES RATIO Avg#FILES AvgFILESIZE(MB)
PUBLIC vkxxxxx:vy 2167 66 32.8 1.3 1047
ALICE alxxxxx:z2 834 85 9.8 1.7 4305
LHCb saxxxxxx:z5 285 5 57 1.4 160
CMS mpxxxxx:zh 119 2 59.5 1 202
Reliability (approximate!):
~0.0175% unavailable (under repair)
~0.000062% data loss (37.2GB)
higher throughput and efficiency allowing substantial
decrease of production tape drives (from 120 to 80)
a) boost write streaming
  After: 146MB/s avg
Archive verification:
re-read
all newly filled tapes
tapes not seen recently
turnaround time ~2 years
speed ~ 3PB / month