## Slide 1: Status update on RF duty factor studies at the FCC-ee booster
Ivan Karpov, Franck Peauger, and Lina Valle for FCC SRF WP1 with input from: Hannes Bartosik, Christian Carli, Antoine Chance, Frank Zimmermann
203rd Accelerator Design Meeting & 74th FCCIS WP2.2 Meeting, 27.02.2025

## Slide 2: Introduction
Two-stage approach for high-energy booster RF system:
112 cavities for Z-WW-ZH with one power source per four cavities or individual power sources
112 + 336 cavities for with individual power sources
Enormous RF voltage range to be covered (50 MV ~10 GV)
Main RF-related parameters
 | Unit | Z | W* | ZH | 
Beam current | mA | 16.2 | 6.2 | 2.0 | 0.4
RF voltage (FB) | MV | 50 |  |  | 
RF voltage (FT) | GV | 0.057 | 0.402 | 1.960 | 10.187
Max SR power | MW | 2.55 | 2.13 | 3.45 | 3.74
Max. cav. voltage | MV | 17.5 |  |  | 22.7
 | Unit | Z | W* | ZH | 
Beam current | mA | 16.2 | 6.2 | 2.0 | 0.4
RF voltage (FB) | MV | 50 |  |  | 
RF voltage (FT) | GV | 0.057 | 0.402 | 1.960 | 10.187
Max SR power | MW | 2.55 | 2.13 | 3.45 | 3.74
Max. cav. voltage | MV | 17.5 |  |  | 22.7
*Recent change of bunch charge
Courtesy of A. Chancé
Dynamic power loss:
Ohm (circuit definition),
Average dynamic loss depends on the cavity voltage evolution during the cycle
“RF duty factor” =
Energy programs for filling mode

## Slide 3: Optimal coupling: flattop considerations
RPO with four cavities per source leads to big discrete steps of the difference between the number of focusing and defocusing cavities,
is excluded due to very high RF voltage per cavity
is a reasonable compromise with less than 5% average power overshoot for W and ZH modes also reducing RF power for Z mode during the ramp (see later)
is chosen for to avoid too small cavity bandwidth (~30 Hz) at the cost of ~40% RF power overshoot
RF power requirements at the extraction energy

## Slide 4: Analysis for operating mode

## Slide 5: mode: RF voltage
RPO
Constant voltage
In-phase voltage
ramp
Voltage drop given by cavity filling time (11 ms)
Resetting phases for RPO
The total RF voltage and energy programs are provided by A. Chancé
Four regimes are required to cover RF voltage requirements during the ramp
Choice of constant voltage impact RF power and dynamic losses

## Slide 6: mode: RF power and detuning
Significant RF power imbalance for focusing and defocusing cavities
Low “constant” voltage leads to very low RF power

## Slide 7: mode: total RF power and dynamic losses
~40% RF power overshoot due the choice of loaded quality factor of
Peak dynamic losses up to 24 W, while average value is only 4.2 W

## Slide 8: Analysis for ZH operating mode

## Slide 9: ZH mode: RF voltage
RPO
Constant voltage
In-phase voltage ramp
Voltage drop given by cavity filling time (4 ms)
Resetting phases for RPO
The total RF voltage and energy programs are provided by A. Chancé
Four regimes are required to cover RF voltage requirements during the ramp
Choice of constant voltage impact RF power and dynamic losses

## Slide 10: ZH mode: RF power and detuning
Significant RF power imbalance for focusing and defocusing cavities
Low “constant” voltage leads to very low RF power

## Slide 11: ZH mode: total RF power and dynamic losses
A tiny RF power overshoot due the choice of loaded quality factor of
Peak dynamic losses up to 15 W, while average value is only 2.4 W

## Slide 12: Analysis for WW operating mode

## Slide 13: WW mode: RF voltage
RPO
Voltage drop given by cavity filling time (4 ms)
The total RF voltage and energy programs are provided by A. Chancé
RPO scheme allows to cover RF voltage requirements during the entire ramp (except no beam segment)

## Slide 14: WW mode: RF power and detuning
The same RF power for focusing and defocusing cavities
Significant RF power overshoot at the moment of extraction needs to be verified with dynamic mode (opening feedback loops might be required)
Cavity detuning becomes more significant

## Slide 15: WW mode: total RF power and dynamic losses
A tiny RF power overshoot due the choice of loaded quality factor of (excluding injection and extraction transients)
Peak dynamic losses up to 10 W, while average value is only 1.7 W

## Slide 16: Analysis for Z operating mode

## Slide 17: Z mode: RF voltage
RPO
The total RF voltage and energy programs are provided by A. Chancé
RPO scheme allows to cover RF voltage requirements during the entire ramp (except no beam segment)
overshoot

## Slide 18: Z mode: RF power and detuning
The same RF power for focusing and defocusing cavities
Significant RF power overshoot at the moment of extraction needs to be verified with dynamic mode (opening feedback loops might be required)
Cavity detuning becomes even more significant
Clamping at 50 kW
overshoot

## Slide 19: Z mode: total RF power and dynamic losses
A tiny RF power overshoot due the choice of loaded quality factor of (excluding injection and extraction transients)
Peak dynamic losses up to 3.8 W, while average value is only 0.7 W
overshoot

## Slide 20: Conclusions
Reverse phase operation and other schemes are necessary to provide the required RF voltage during HEB ramps
First analysis shows significant lower average dynamic loss values compared to the peak values
Analysis of RF power transients is necessary to clarify average RF power requirements
Further optimization to be done based on requirements for the cryogenic systems
Thank you for your attention!
 | Z | WW | ZH | 
(W) | 3.7 | 9.7 | 14.6 | 24.1
(W) | 0.7 | 1.7 | 2.4 | 4.2
 | 0.2 | 0.18 | 0.17 | 0.17
 | Z | WW | ZH | 
 | 3.7 | 9.7 | 14.6 | 24.1
 | 0.7 | 1.7 | 2.4 | 4.2
 | 0.2 | 0.18 | 0.17 | 0.17

## Slide 21: Backup slides

## Slide 22: RF system
A common RF system design for Z, W, and ZH modes of the collider was adopted as a new baseline:
2 RF systems with 50 MW RF power and 1 GV of RF voltage
A low RF voltage for Z is achieved using Reverse phase operation mode (RPO, Y. Morita et al., 2009)
Splitting and combining beams in the RF straight section covers the RF voltage range for W and ZH
 | Energy (GeV) | Current (mA) | RF voltage (GV)
Z | 45.6 | 1283 | 0.088
W | 80 | 135 | 1.05
ZH | 120 | 26.7 | 2.1
RPO at Z
(MV) | 
7.95 | 9.21e5
7.95 | 9.21e5
The Booster RF system requires similar flexibility to achieve a smooth switch between operational modes

## Slide 23: Design constraints
Booster RF system for Z-W-ZH modes:
Various RF voltages and beam currents must be covered without hardware modifications
112 6-cell cavities, four cavities per source (~50 kW per cavity)
Maximum cavity voltage is defined by ZH mode (17.5 MV)
Fixed should minimize RF power at flattop and ideally through the whole cycle
Reverse phasing mode should be used to cover an enormous RF voltage range (50 MV ~2 GV)
 | Unit | Z | W | ZH
Beam current | mA | 16 | 13 | 2
RF voltage (FB) | MV | 50 |  | 
RF voltage (FT) | MV | 57 | 402 | 1960
Max SR power | MW | 1.05 | 4.51 | 3.44
Main RF-related parameters

## Slide 24: Coupled-bunch instabilities at 20 GeV
No margin for beam stability with direct RF feedback activated
We could profit from installing wigglers (1 wiggler gain of 4)
Main RF-related parameters
Assuming the same , we need ~ 3.1 MV to get 50 MV at injection energy
Minimizing RF power by detuning the cavities can drive coupled bunch instabilities
Optimal detuning during injection for Z

## Slide 25: Detuning during cycle
Injection process
Ramp-up
Flattop
Ramp-down

## Slide 26: RF power at injection
Large transients with the full feedback gain due to high peak beam current

## Slide 27: RF power at injection
Reduction of gain by a factor of 5 significantly suppresses power transients
Feedback gain can be ramped up together with beam intensity
Additional margin with wigglers would be beneficial
Filling should be as uniform as possible

## Slide 28: High-Energy Booster cycle
Energy ramp and RF voltage programs were initially designed for Z (A. Vanel, FCC week, 2024) and later for modes
RF voltage and energy evolution for Z

## Slide 29: RF system block diagram
rf cavity
Load
Circulator
Generator
–
+
, rf component of the beam current
, reference voltage
, cavity voltage
, generator current
, Reflected current
, error signal
delay
Low-pass direct rf feedback
High-pass direct rf feedback
+
+
FCC feedback system assumed to be similar to one in the LHC (P. Baudrenghien et al, 2006)
BW of 2 MHz