## Slide 1: FCCee Collider DepolariZer Design Considerations
27.02.2025 FCCee Optics Design Meeting
W. Hofle
CERN SY-RF-BR
Acknowledgements:
I. Koop, G. Roy, D. Sittard
Epol WG

## Slide 2: FCCee collider needs depolarizer kicker
Basic functional requirements (for operation at Z and WW energies)
For resonant depolarization powerful transverse electromagnetic kickers are needed in FCCee that provide vertical kicks with fields that can be modulated to target witness bunches placed in gaps between the trains of bunches used for Physics
for Physics bunches the same type of kicker system can be used to continuously or on demand to shake the beam to prevent polarization build-up
The same kickers can also be used to fulfill the function of transverse feedback
Wolfgang Hofle
27.02.2025 2025 FCCee Optics Meeting

## Slide 3: Considerations for placement in ring
from the technical sites, locations where RF is located, offer advantages but space is an issue (in collider), and so are the large diameter beam pipes between cavities
experimental sites (PA, PG, PD, PJ)
  spaces considered:
    return arc (rejected, not good)
    regular arc
  implementation of any arc optics modification in four points preserves symmetry (4-fold)
PA:collider
transverse feedback kickers & depolarizer (1)
booster
transverse feedback kickers
Wolfgang Hofle
Update early of 2025:
PG: collider
transverse feedback kickers & depolarizer (2)
PD: collider
transverse feedback kickers & depolarizer (4)
PJ: collider
transverse feedback kickers & depolarizer (3)
27.02.2025 2025 FCCee Optics Meeting
no suitable space available (LSS)

## Slide 4: Depolarizer kickers and transverse feedback
Possible synergies with transverse feedback kickers
due to similar requirements for bandwidth synergy between the needed kickers for the transverse feedback and the depolarizer have been explored
long, O(m), stripline kickers operating at a multiple of the bunch repetition frequency offer good RF power efficiency and sufficient bandwidth
differences in requirements between transverse feedback and depolarizer kickers are
  depolarizer kicker only needed for vertical kicks, transverse feedback also for horizontal plane kicks
  implementation of depolarizer excitation as a modulated local orbit bump requires one or several sets of pairs of kickers with bending magnets in between
    no perturbation on experimental points permitted, may require tuning possibility with a third kicker per set of kickers
  kick strength required for depolarizer is high (total of 10 mrad) and adequate protection is needed to prevent acting on Physics bunches (loss of synchronisation with gaps)
Wolfgang Hofle
14.01.2025 FCCee Physics Workshop

## Slide 5: Stripline kicker: arc compatible version (1st version)
Characteristics (good for transverse feedback, but too low shunt impedance for depolarizer with arc compatible diameter)
four electrodes arranged at 45 degrees
leaves horizontal plane free for synchrotron radiation absorbers similar as for BPM designs
compatible with vacuum chamber diameters of 60-70 mm foreseen for arcs (initial proposal)
small diameter also desirable for increased shunt impedance, but matching to 50 Ohm must be considered for both differential mode and common mode
universal design that can be powered to provide vertical or horizontal kicks, even simultaneously, power can be directed to plane that needs high level kicks
device is a backward coupler, powered at beam downstream ports and terminated at upstream ports
action on beam provided in equal parts from magnetic and electric fields
length can be adjusted to match actual needs for bandwidth
total kick strength provided by set of kickers, placed at the appropriate phase advance / optics as needed
Wolfgang Hofle
D. Sittard (CST)
RF power
RF power
RF loads
RF loads
up to 1m long
27.02.2025 2025 FCCee Optics Meeting

## Slide 6: Stripline kicker: field plots (70 mm chamber)
Electric field (vertical)
Magnetic field field (horizontal)
Wolfgang Hofle
D. Sittard
vertical kick evenly split between electric and magnetic fields
27.02.2025 2025 FCCee Optics Meeting

## Slide 7: Shunt impedance kicker (four electrode version)
 power need reduced by factor 15.6
70 mm vacuum chamber diameter (directly arc compatible)
Adaptation of length to bandwidth also possible (using 1 m long kickers for 40 MHz +/- 20 MHz)
26 mm vacuum chamber ( 18 mm between electrodes)
40 MHz
80 MHz
160 MHz
D. Sittard
Wolfgang Hofle
@40 MHz, 700 kW
4x4x 2.26 kW
4x4x 35 kW
integrated transverse kick 450 kV needed (split voltage over four kickers):
looks feasible, 1 m length
beam impedance check with BE-ABP needed
total length per beam for kickers ~10 m (+ overhead tapers)
3 m per experimental point per beam (if split over four experimental points)
4 kickers
4 electrodes
RF power (peak)
for 10 mrad @ 45.6 GeV
27.02.2025 2025 FCCee Optics Meeting

## Slide 8: Stripline kicker: field plots (26 mm chamber)
Electric field (vertical)
Magnetic field field (horizontal)
Wolfgang Hofle
D. Sittard
vertical kick evenly split between electric and magnetic fields
18 mm diameter stay clear aperture
18 mm
27.02.2025 2025 FCCee Optics Meeting

## Slide 9: Placement in return arcs or in arcs?
positron beam outgoing (clockwise) / right of IPs
current optics plot: curtesy G. Roy
Wolfgang Hofle
return arcs would be suitable location for transverse feedback kickers
however, due to only two dipoles per FODO cell  less effect for depolarizer (according to I. Koop)
arc much better suited, but is space available?
Better to foresee to distribute depolarizers over eight locations
kickers 1-4
kickers 2-8
kickers 9
If concentrate in one experimental point  10 m per return arc (e.g. PA) !
dedicated optics needed in return arc(s) adapted to the needs of the depolarizer kickers
(local modulated bump)
Kicker #9 additional degree of freedom to adjust closing of bump (depolarizer function)
OR regular arc
27.02.2025 2025 FCCee Optics Meeting

## Slide 10: Placement in regular arcs re-visited
positron beam outgoing (clockwise) / right of IPs
Following proposal by I. Koop
Wolfgang Hofle
split system over eight locations, left and right of experimental points
chose kickers of lengths of 1 m, 26 mm chamber
 at least 8 kickers per beam for four full wave bumps per beam
+ the optional third kicker to ensure bump closure (another 4 kickers per beam)
24 kickers in total
Kicker 1
Kicker 2
Kicker 3
optional kicker 3 to ensure full wave bump is closed
https://indico.cern.ch/event/1471324/contributions/6220925/attachments/2963259/5212471/Koop-depolarizer%20review.pdf
if distributed over four locations only 2.5x10-6 rad
27.02.2025 2025 FCCee Optics Meeting

## Slide 11: Kick voltage and kick angle summary
10 mrad at 45 GeV  450 keV/c transverse momentum kick needed, at minimum two locations for implementing a closed bump with modulated amplitude can be provided by stripline kickers
  use sets of 1 m long kickers (RF matched to 50 W) with four electrodes for each location to create local modulated bump (2x4x2.26 kW = 18 kW peak RF power)
  four such systems per beam
  24 kickers in total for both beams combined, including the additional kicker to adjust closure
    for 16 main kickers: 144 kW peak RF power
    power needed for adjustment kickers is smaller
Wolfgang Hofle
27.02.2025 2025 FCCee Optics Meeting

## Slide 12: Next crucial steps – my view
confirmation needed on available space in arcs or for modified return arc optics suitable for depolarizer
feasibility of small diameter vacuum chamber kicker needs confirmation
  beam impedance, needed tapers, synchrotron radiation
follow-up on machine protection considerations
optimization of electrode design, possible consideration of advantages of higher line impedance kicker
Wolfgang Hofle
27.02.2025 2025 FCCee Optics Meeting

## Slide 13: Thank you for your attention.
13
Wolfgang Hofle
13.01.2025 FCCee Physics Workshop

## Slide 14: Spare
13.01.2025 FCCee Physics Workshop

## Slide 15: Filling pattern Z-pole – update of situation
C. Carli et al. @FCC SAC 19.11.24
e-cal bunches of at least one gap are affected by injection bump risetime, so effectively 175 (one beam), 176 (the other beam) useful bunches at maximum
Number of gaps was increased from 20 to 40
due to transient beam loading considerations in RF cavities
(I. Karpov)
14.01.2025 FCCee Physics Workshop
Wolfgang Hofle

## Slide 16: Machine Protection considerations (03.10.24)
What can go wrong?
Excitations not correctly synchronized
Excitation amplitudes not correct leading to not closed depolarizing bumps
any of the other excitations that will certainly be used (AC dipole mode etc.) need to be protected against failures
very strong kicks possible comparable or even larger than at LHC injection
protection with BLMs of limited or of no use due to small beam size
monitoring of positions at appropriate distance from kickers in phase
global monitoring of beam position required turn-by-turn, independent of pick-ups used for TFB
interlocks need to be derived from this monitoring
beam Stoppers?
Mitigation
Wolfgang Hofle
machine protection task force working group requested examination of failure scenarios and mitigations
from MP point of view not clear if entangling TFB and depolarizer system into one system is the optimum due to the different kick strength required for both systems and the possible failure scenario
  possibility to have common kickers, with combination of signals before kicker (pulsed system for de-polarizer, cw system for feedback function)
14.01.2025 FCCee Physics Workshop

## Slide 17: FCCee collider and booster transverse feedback systems
Key requirements
need bunch-by-bunch operation at 25 ns bunch spacing  defines bandwidth
can operate at multiple of bunch repetition frequency (short bunches)  no need to work in “base-band” as in LHC  helps as it reduces relative bandwidth
sets of RF matched strip-lines with carefully chosen length as kickers seem obvious choice
Booster:
  request to also operate to damp a significant transverse injection error  defines maximum kick requirements
    needs estimate of injection errors, filamentation time, … to define system
  moderate damping times only for instabilities (not beyond experience from LHC)
  single location in ring sufficient
Collider:
  need to damp very fast transverse instabilities  four turns risetime, high gain system
    favors distributed system with multiple pick-ups and kickers
    possibility of synergy with exciter for resonant depolarization (as in LEP)
Wolfgang Hofle
13.01.2025 FCCee Physics Workshop

## Slide 18: Transverse Feedback Kickers
Requirements
bunch-by-bunch operation calls for +/- 20 MHz minimum for 25 ns bunch spacing
high gain required, not necessarily high kick strength
low noise electronics
prefered to provide feedback kicks in a band at a multiple of the bunch repetition frequency, nx40 MHz or nx50 MHz depending on bunch spacing
  lowest betatron frequency is very low in frequency (~660 Hz)
possibilities to distribute kicker system over several collider points considered before but seems at present not required, but needs independent confirmation
fast damping rates required for low order modes only
have a set of kickers available at different phase advances is an advantage (if fractional tune options close to 0.5 or integer, it is a must)
highest beta function for given aperture, low dispersion for associated set of pick-ups
additional synergy to be explored for applications as in LHC (AC-dipole for optics measurements …)
Wolfgang Hofle
13.01.2025 FCCee Physics Workshop

## Slide 19
LHC ADT kicker (LHC transverse feedback)
  high impedance tetrode amplifiers
  kicks with electric field only
  6 m effective length split over 4 kickers twice as strong as depolarizer kicker system (2 mrad at 450 GeV/c)
  full amplitude not as bunch selective as needed for FCCee
  due to resonances not (readily?) suitable for short electron bunches
W. Hofle et al. PAC 2001
Wolfgang Hofle
13.01.2025 FCCee Physics Workshop