## Slide 1: The Tiny Triplet Finder: a low silicon resource usage pattern recognition scheme and its test implementation in a low-cost FPGA device
Jinyuan Wu
Fermilab
Nov. 2025

## Slide 2: Introduction
Applications of triplet finding
Problems with pairing
Tiny Triplet Finder
An example of track seeding engine using Tiny Triplet Finder
An implementation in Cyclone 5 FPGA

## Slide 3: The Triplet Finding

## Slide 4: From the Triplet Finder to Track Fitter
The triplets are group of at least 3 (but can be more than 3) hits that satisfy the first constraint.
The hits may arrive in arbitrary order.
A triplet finder reorganizes hits for further track fitting.
Track
Fitter

## Slide 5: Triplet Finding: Barrel Geometry, r-phi & r-z views
At least three hits are needed to determine a track.
Curved tracks can also be determined.
A 3D triplet finding engine is needed to eliminate fake tracks.

## Slide 6: Triplet Finding: Non-bend y-z view & y-t view
Consider a detector measuring both coordinates and time.
Three hits are needed for both y-z view and y-t view.
It requires a 3D triplet finding engine to eliminate fake tracks.

## Slide 7: Triplet Finding: Double TPCs
Two TPCs drifting toward opposite directions and a timing layer are used to identify high-rate tracks.
Earlier track may arrive TPC pad later and vise versa.
T0, T1 and T2 satisfy a constraint, forming a triplet.
T0
T1
T2
T1
T0+const.
T2
(T1+T2)/2 = T0+const.

## Slide 8: Pairing, Not Good

## Slide 9: Pairing
Mainstream tracking algorithms: find a pair => find third => fit and find others
Mark Pesaresi et. al. ACES 2020

## Slide 10: From Pairing to Triplet Seeding
Simple pairing will create more fake hit pairs, which must be eliminated in later stages.
When three or more hits (stubs) are picked up together in triplet seeding stage, less fake segments are expected.
fake
Seeding with
Pairs
Seeding with
Triplets
fake

## Slide 11: Pairing vs Triplet Finding
Pairing causes large number of fake segments.
  To eliminate fakes, narrow coincidence window is needed.
    => Low PT tracks is not triggered. Physics cases are limited.
Triplet finding controls fakes well, allowing triggering on low PT tracks and enables broader physics program.
Pairs
Pairing
Track
Fitter
Hits/
Stubs
Triplets
Triplet
Finding
Track
Fitter
Coincidence
Search
Window
L1
Hits/
Stubs
Low PT
Tracks
L2
L3

## Slide 12: Tiny Triplet Finder

## Slide 13: Computing Complexities of Hit Match Schemes
Hit Matching
  Doublet
  Triplet
  4-hits
 | Software | FPGA Typical | FPGA Resource Saving Approaches
 | O(n2) for(){ for(){…} } | O(n)*O(N) Comparator Array | Hash Sorter O(n)*O(N): in RAM
 | O(n3) for(){ for(){ for(){…} } } | O(n)*O(N2) CAM, Hugh Trans. | Tiny Triplet Finder O(n)*O(N*logN)
 | O(n4) for(){ for(){ for(){ for() {…} }}} |  | 

## Slide 14: The Tiny Triplet Finder for Cylindrical Detector Geometry
The Tiny Triplet Finer is a scheme to reuse a single set of track road coincidence logic for whole detector.
It uses shift (or rotate) to bring bit arrays to feed the track road coincidence logic.
C1
C2
C3

## Slide 15: General Structure of the Tiny Triplet Finder
A typical Tiny Triplet Finder includes:
  Bit arrays for different layers of the detector.
  Shifters
  Bitwise coincidence logic.
*R1/R3
*R2/R3
Triplet Map Output To Decoder
Bit Array
Shifter
Bit Array
Shifter
Bit-wise Coincident Logic

## Slide 16: A 3D Track Seeding Engine

## Slide 17: Structure of the Seeding Engine: Two RAM Banks + Tiny Triplet Finders
nZ375
nZ0
nPhi3
ROM
ROM
nZ1
nZ3
nZ375
(nZ2)
nZ0
nZ0
nZ375
RAM Banks
Tiny Triplet Finders

## Slide 18: Structure of the Seeding Engine: Single Physical RAM View
nZ375
nZ0
nPhi3
ROM
ROM
nZ1
nZ3
nZ375
(nZ2)
nZ0
nZ0
nZ375

## Slide 19: General Timing
nZ375
nZ0
nPhi3
ROM
ROM
nZ1
nZ3
nZ375
(nZ2)
nZ0
nZ0
nZ375
Event N
225 CLK
Event N+1
225 CLK
Event N+2
225 CLK
L1, L3
112 CLK
L2
112 CLK
R
Data Filling
Coincidence
Checking
Refreshing

## Slide 20: Operation: (1) Filling Hits
nZ375
nZ0
nPhi3
ROM
ROM
nZ1
nZ3
nZ375
(nZ2)
nZ0
nZ0
nZ375
L2
112 CLK
R
Event N
225 CLK
Event N+1
225 CLK
Event N+2
225 CLK
L1, L3
112 CLK
Data Filling

## Slide 21: Operation: (2) Checking Coincidence
nZ375
nZ0
nPhi3
ROM
ROM
nZ1
nZ3
nZ375
(nZ2)
nZ0
nZ0
nZ375
L1, L3
112 CLK
R
Event N
225 CLK
Event N+1
225 CLK
Event N+2
225 CLK
L2
112 CLK
Coincidence
Checking

## Slide 22: Pattern Shifting and checking
The bit patterns with the same z0 from Layer 1 and Layer 3 are shifted to align with the coincidence road array.
The amount of shift is determined by phi2.
Matching bits are output for further process.

## Slide 23: Operation: (3) Refresh Cycle
nZ375
nZ0
nPhi3
ROM
ROM
nZ1
nZ3
nZ375
(nZ2)
nZ0
nZ0
nZ375
L1, L3
112 CLK
L2
112 CLK
R
Event N
225 CLK
Event N+1
225 CLK
Event N+2
225 CLK
Refreshing

## Slide 24: The Seeding Engine & Clustering Buffer
To Kalman Filtering
P1
P2
P3
Full data of hits are stored in the clustering buffer.
After triplet finding, the full data are sent to the Kalman filter stage for further track fitting.
Clustering
Buffer
Clustering
Buffer
FIFO
Hugh
Transform
Cells
Hugh
Transform
Cells
Tiny
Triplet
Finder

## Slide 25: Implementation in Cyclone 5 FPGA

## Slide 26: Generated Events: r-z View
In 240 cm (z) x 10 degrees (phi) range, up to 112 hits per layer are generated, out of which, 10 are from good tracks.
The z0 of the vertices spread in +- 10 cm along beam axis.

## Slide 27: The Events: r-phi View
Minimum PT: 2GeV/c.
The hits on Layer 2 is limited to 10 degrees, but hits on Layer 1 and 3 spread up to 16 degrees.
The impact parameters of the tracks: +- 2 mm.

## Slide 28: Serving Range of Seeding Engine
In each TFP, 4 seeding engines are implemented, each serving 2.4 m (full length) x 10 degrees plus overlap.
Each engine sees <100 hits/layer per event.
The layer 2 is divided with exact 10-degree boundaries.
Overlapping in:
  Layer 1: +- 2.16 degrees, 14.3 degrees total
  Layer 3: +- 2.62 degrees, 15.2 degrees total

## Slide 29: Home Test Stand and the Evaluation Module
The seeding engine core firmware is implemented in Altera C5G evaluation module (179 USD ea.).
The FPGA is Cyclone V GX 5CGXFC5C6F27C7N (171 USD ea.).

## Slide 30: Structure of the seeding engine
The entire engine is organized as a pipeline so that it can run at high speed (250 MHz in Cyclone V).
Blocks: Address Generation; Hugh Trans. Cells; Shifter Bank; Road Coincidence

## Slide 31: Test Stand and Operation Timing
Data and signal bits are brought out to monitor operation timing.
Each event takes 225 clock cycles @ 250 MHz:
  112 clock cycles for filling
  112 clock cycles for coincidence checking
  1 clock cycle for refreshing RAMs.
Filling
Coincidence
Checking
Refreshing
DATA
CHK
CNT_CHK
REFRESH

## Slide 32: Register-Like Block RAM for Hit Patterns
The hit patterns are stored in the register-like BRAM.
Each hit is processed in a single clock cycle.
Single clock cycle refreshing allows fast preparation for next event.
L1, L3
112 CLK
L2
112 CLK
R
Event N
225 CLK
Event N+1
225 CLK
Event N+2
225 CLK
Single Clock Updating
Single Clock Reading
Single Clock Refreshing

## Slide 33: Resources
Search with keywords: “Tiny Triplet Finder”:
https://indico.cern.ch/event/418639/contributions/1018431/attachments/868807/1216592/TTF_lecc2004p-v3.pdf
https://arxiv.org/abs/2305.09834
https://inspirehep.net/literature/733063
https://inspirehep.net/literature/1980573
2004:
2006:
2021:
2023:

## Slide 34: Conclusion
Hardware triplet finding solution exists, so it is unnecessary to go through pairing.
The Tiny Triplet Finder uses O(n) operation time (2n+1 clock cycles per event) that matches data input rate and will not be jammed when messy events arrive.
The Tiny Triplet Finder uses O(N*log N) resources which can be implemented in intermediate sized FPGA for most applications.
A versatile 3D triplet finding engine based on Tiny Triplet Finder has been implemented that can be used for various detector geometries.

## Slide 35: The End
Thanks

## Slide 36: Introduction
Clustering is a doublet finding algorithm that consumes O(n^2) time if implemented in software.
The FPGA clustering scheme should match the data input rate, i. e., the resource usage is O(n)*O(N), where O(N) represents hardware portion.
The performance should not be affected by the number of hits and number of clusters: (no O(n^2) terms).

## Slide 37: The Clustering Engine
The input data are first used to fill the cluster ID RAM.
  Each isolated hit is giving a new cluster ID.
  Hits within certain distance in channel and time domain are assigned with same cluster ID.
The input data are looped through again and reorganized in the cluster output buffer.
Clustered data are output after reorganization.
Cluster
ID
Counter
Input
Buffer
Cluster
ID
Assignment
Logic
&
RAM
Cluster
Output
Buffer
Delay
Buffer

## Slide 38: The Cluster ID RAM
Hits stream into the cluster engine.
Cluster ID are to be assigned for each hit.
A memory array holds cluster ID.
Each cell holds a short time range.
Time
CH
{Cluster ID}

## Slide 39: The Filling Process
A hit is used to address a cell.
Neighboring cells are also addressed, and contents are readout.
The cluster ID of the cells are to be determined.
  If no cells are filled, a new cluster ID will be filled into the center cell.
  If several cells are filled, they will be updated to the lowest (oldest) cluster ID.
{Cluster ID}

## Slide 40: The Reading Process
Input hits are looped through again.
The cluster ID of each hit is readout.
Raw data are stored in cluster output buffer addressed by the cluster ID.
The clustered data are output from the cluster output buffer.
{Cluster ID}
Cluster
Output
Buffer
Input
Buffer
Delay
Buffer

## Slide 41: The Read-Update Timing
In slower applications, each hit is processed in 4 clock cycles:
  Clock cycle 1, 2: Read.
  Clock cycle 3: Process, choosing correct cluster ID.
  Clock cycle 4: Write back to cells.
The “register-like block RAM” is also available for faster applications, which process each hit in 1 clock cycle, instead of 4.
D Q
D
WA
WE
RA
Q
D Q
D Q
X
Address
Delay
Process
Update
Hit 0
Hit 1

## Slide 42: Register-Like Block RAM for Hit Patterns
The hit patterns are stored in the register-like BRAM.
Each hit is processed in a single clock cycle.
Single clock cycle refreshing allows fast preparation for next event.
L1, L3
112 CLK
L2
112 CLK
R
Event N
225 CLK
Event N+1
225 CLK
Event N+2
225 CLK
Single Clock Writing
Single Clock Reading
Single Clock Refreshing

## Slide 43: Task sharing
Cluster Engine
The cluster engine takes multiple clock cycle to process an input hit.
Multiple cluster engines can be used to match the input rate.
Input stream fills each engine in a rotational manner. Each engine process some sets of events.
Input
Buffer
Cluster
Output
Buffer
Cluster Engine
Input
Buffer
Cluster
Output
Buffer
Cluster Engine
Input
Buffer
Cluster
Output
Buffer
Cluster Engine
Input
Buffer
Cluster
Output
Buffer