## Slide 1: Designing ASICs for HEP Experiments: Turning painful mistakes into practical guidelines for future ASICs
Davide Ceresa
Thursday 9th of October 2025 – TWEPP 2025 – Rethymno, Creete, Greece

## Slide 2: About Me: 10+ years into ASIC design for HEP

## Slide 3: Designing ASICs for HEP Experiments: Key Challenges
🔑 Non-replicable systems
🔑 System-level complexity
🔑 Longevity and reliability
🔑 Limited resources
🔑 Long design and testing cycles

## Slide 4: Designing ASICs for HEP Experiments: Key Challenges
🔑 Non-replicable systems
🔑 System-level complexity
🔑 Longevity and reliability
🔑 Limited resources
🔑 Long design and testing cycles
Aspect | CERN HL-LHC ASICs | Big Semi (Qualcomm, Broadcom,…)
Engineers per ASIC | ~2–10 | 50–1000
Total ASIC designers | ~150–200 | 2000–10,000+
Timescale | 5–10 years | 1.5–2 years
Unique ASIC / cycle | ~50–60 across 4 experiments | 50+ across product families

## Slide 5: Designing ASICs for HEP Experiments: Key Challenges
🔑 Non-replicable systems
🔑 System-level complexity
🔑 Longevity and reliability
🔑 Limited resources
🔑 Long design and testing cycles
Each design cycle introduces new technologies, methodologies, and challenges.

## Slide 6: The Digital Impact: Mixed-Signal ASICs
Analog accuracy drives performance, while digital logic drives system behavior and integration.
Readout
Front
End
Serializer
Digitizer
ANALOG
DIGITAL
Sensor
Mixed-Signal Readout ASIC
Digitizers enable a fully digital readout:
Robust to Noise
High Bandwidth
On-chip data compression and selection
Multi-chip data aggregation

## Slide 7: The Digital Impact: Digital-on-Top (DoT) methodology
Bring the advantages of the digital domain to the chip-level!
Top-level RTL description for full-chip verification and system-level simulation
Automated flow, easy to modify and respin
Chip-level timing and power analysis
Readout
Front
End
Serializer
Digitizer
ANALOG
DIGITAL
Digital-on-Top Mixed-Signal Readout ASIC

## Slide 8: The Digital Impact: Analog vs Digital flow
Analysis
Implementation
Block description
Schematic design
Full-Custom Layout
RTL design
Synthesis + P&R
Analog block
Digital block
Signoff Analysis
Transistor model
Gate Library
Analog simulation
Digital simulation
Design
Verification
Transistor model
Analog Domain
Digital Domain

## Slide 9: The Digital Impact: Analog vs Digital flow
Analysis
Implementation
Block description
Schematic design
Full-Custom Layout
RTL design
Analog block
Signoff Analysis
Transistor model
Gate Library
Analog simulation
Digital simulation
Design
Verification
Transistor model
Analog Domain
Digital Domain
Code-based
Higher abstraction
level
Automated flow
Discrete
handle huge complexity
Analytical
Synthesis + P&R
Digital block

## Slide 10: The Digital Impact: Digital-on-Top flow
Schematic design
Full-Custom Layout
RTL design
Analog block
Chip Implementation
Signoff Analysis
Transistor model
Gate Library
Analog simulation
Digital simulation
Design
Verification
Transistor model
Analog Domain
Digital Domain
Model
Synthesis + P&R

## Slide 11: The Digital Impact: The digital designer’s point of view
RTL Design &
Implementation
Non-Digital block
Integration
Signoff Analysis
Path toward submission

## Slide 12: RTL Design and Implementation: Data Aggregation Problem
Verification Regression report
Event frame
Frame size depends on FE occupancy and mode of operation
HEADER
PKT #1
PKT #2
PKT #500
…
FIFO 0
FIFO N
Data Aggregation & Formatting
FE Data 0
FE Data N
…
…
DUT
Verification Environment
RTL design
STIMULI
MONITOR
SCOREBOARD

## Slide 13: RTL Design and Implementation: Data Aggregation Problem
> 10s failures appeared after fixing coverage
Verification MUST include Coverage
Coverage for a fully passing regression
Avoid Data-dependent Control logic

## Slide 14: RTL Design and Implementation: The Hidden Cost of Clever Logic
The digital flow offers designers enormous flexibility.
But the hidden cost of such flexibility often surfaces late, typically during functional coverage analysis, or worse, only after integration and system testing.
Spiderman #1, 1962
Digital flow
RTL design
P&R flow design
Digital block
Signoff Analysis
Gate Library
Transistor model
Code-based
Higher abstraction
level
Automated flow
Analytical

## Slide 15: Guidelines I: A Versatile, not overcomplicated design
1. Clear separation of data and control paths
2. Design with Hardware and Verification in Mind
3. Static configuration with controlled start-up sequence
4. Early and comprehensive coverage analysis
RTL Design &
Implementation
Non-Digital block
Integration
Signoff Analysis
Path toward submission

## Slide 16: Best Practice Examples: Data formatting
LA-Picopix : A 4-lane 100 Gbps Data-Driven Pixel Readout Chip
Use a single packet size aligned with the Physical Layer.
Support multiple packet types, minimizing impact on control/data transfer.
Avoid mixing packet formats; any mode change requires a soft reset.
>10 operation modes share the same packet size

## Slide 17: R&D Topic: Toward standardization & programmability?
https://indico.cern.ch/event/1556239/
Workshop: RadTol RISC-V SoC
RIBEX 28 nm
https://indico.cern.ch/event/1502285/contributions/6554384/
TriglaV 28 nm
STRV 28 nm
…other solutions needs to be explored: eFPGA, CGRA, … .

## Slide 18: The Digital Impact: The digital designer’s point of view
RTL Design &
Implementation
Non-Digital Block
Integration
Signoff Analysis
Path toward submission

## Slide 19: Non-Digital Block Integration: Characterization step
Schematic design
Full-Custom Layout
RTL design
P&R flow design
Analog block
Chip Implementation
Signoff Analysis
Transistor model
Gate Library
Analog simulation
Functional simulation
Formal simulation
Design
Verification
Transistor model
Analog Domain
Digital Domain
Model

## Slide 20: Non-Digital Block Integration: Characterization step
Schematic design
Full-Custom Layout
RTL design
P&R flow design
Analog block
Chip Implementation
Signoff Analysis
Transistor model
Gate Library
Analog simulation
Functional simulation
Formal simulation
Design
Verification
Transistor model
Timing, power, signal integrity data
Implementation models
Verilog, Verilog-AMS,…
Simulation models
Characterization
Analog Domain
Digital Domain

## Slide 21: Non-Digital Block Integration: Corrupted model
Example: Integration of an SRAM compiler-generated
Observed Issue
Failures detected during testing.
No failures predicted by analog simulations.
No violations during P&R and sign-off analysis.
Findings:
Large capacitance at SRAM clock input.
Simulations and characterization assumed an ideal clock buffer
Root Cause:
Hidden timing failure due to a mismatch between idealized simulation assumptions and actual integrated load conditions.
SRAM MACRO
CLK
Large internal
capacitance
Ideal buffer
Wrong Setup/Hold timing margin in implementation model

## Slide 22: Non-Digital Block Integration: Macro integration in a DoT design
Validation
Verification
Modeling
Integration
Schematic design
Full-Custom Layout
RTL design
P&R flow design
Analog block
Chip Implementation
Signoff Analysis
Analog simulation
Digital simulation
Analog Domain
Digital Domain
Model

## Slide 23: Non-Digital Block Integration: Characterization step
Analog Domain
Schematic design
Full-Custom Layout
Digital Domain
RTL design
P&R flow design
Analog block
Digital Block
Signoff Analysis
Transistor model
Gate Library
Analog simulation
Functional simulation
Design
Verification
Transistor model
Characterization & Validation
Mixed-Signal sim.
Close the loop!
Accurate,
transistor-level, continuous signal
Post-Layout
Included
in the tool

## Slide 24: Guidelines II: A Robust Mixed-Signal Implementation Flow
1. Identify analog–digital boundaries and critical blocks
2. Address timing-critical blocks with care
3. Extend verification beyond digital-only approaches
4. Validate macro quality and modeling accuracy
RTL Design &
Implementation
Non-Digital Block
Integration
Signoff Analysis
Path toward submission

## Slide 25: Best Practice Examples: Analog-Digital-Mixed Signal boundaries
LHCb FastRICH Example: A 16-channel TDC-based Fast Timing (25 ps) readout chip
Digital Domain
Analog Domain
⚠ Custom Flip-Flop
https://doi.org/10.1016/j.nima.2024.169664
Digital TDC
A/D Boundary

## Slide 26: Best Practice Examples: Integration and Verification flow
Example: Mixed-Signal flow for a Latch-based Time-to-Digital Converter block
Capture FF Analog design
Schematic & Layout
SPICE Simulation
Capture FF block
TDC Digital design
RTL design
P&R flow design
Chip-level Digital Verification
Functional
Post-Layout
TDC block
Analog simulation
Analog Verification
MS simulation
models
Characterization & Validation
Schematic
& Layout
Stimuli and
expected response
VCD simulation Post-Layout analog simulation with stimuli and expected response from Verification environment
CONFORT
ZONE

## Slide 27: The Digital Impact: The digital designer’s point of view
RTL Design &
Implementation
Non-Digital block
Integration
Signoff Analysis
Path toward submission

## Slide 28: Signoff Analysis: What is an Analysis!?
Example: Static Timing Analysis
Analytical calculation based on the gate library:
Setup/Hold/Propagation Delay/…/ for a certain corner
Checking compliance under static assumptions for Process-Voltage-Temperature

## Slide 29: Signoff Analysis: Dynamic vs Static current consumption
In ASICs with a large digital component, current consumption is highly dynamic.
Specifications typically define current consumption in terms of average values.
The Power Delivery Network (PDN) is designed based on these specifications, considering factors such as bonding approach (Wire vs Bump), package type, and module design
T1
T2
Time
Average current
Peak current
Current

## Slide 30: Signoff Analysis: Dynamic Power Analysis
Real-life example: Dynamic power Analysis based on post-layout netlist simulation
Post-Layout simulation
Current Extraction
Chip activity
Vector-based current profile in FF corner
Clock rising
edge
Clock falling
edge
Avg. Current
~ 500 mA

## Slide 31: Signoff Analysis: Dynamic Power Analysis
The clock is aligned for most of the logic in the chip
Skew < 200ps
Insertion delay [ns]
Causes a large current peak at clock switching
Triplicated clock distribution tree
Consequence of over-optimized design

## Slide 32: Signoff Analysis: Dynamic Power Analysis
Real-life Example: Dynamic power Analysis based on post-layout netlist simulation
Post-Layout simulation
Current Extraction
Voltage rail analysis with package parasitics
Chip activity
Current profile
Vector-based current profile in FF corner
Clock rising
edge
Clock falling
edge
Avg. Current
~ 500 mA

## Slide 33: Signoff Analysis: Dynamic Power Analysis
Voltage (VDD – VSS) drop
Real-life Example: Dynamic power Analysis based on post-layout netlist simulation
Post-Layout simulation
Current Extraction
Voltage rail analysis with package parasitics
Chip activity
Current profile
Vector-based current profile in FF corner
Clock rising
edge
Clock falling
edge
Wirebond in QFN package
Avg. Current
~ 500 mA

## Slide 34: Signoff Analysis: Dynamic Power Analysis
Post-Layout simulation
Current Extraction
Voltage rail analysis with package parasitics
Chip activity
Current profile
Vector-based current profile in FF corner
Clock rising
edge
Clock falling
edge
Wirebond in QFN package
Avg. Current
~ 500 mA
Voltage for different pkg. parasitic
Strong supply oscillation
Real-life Example: Dynamic power Analysis based on post-layout netlist simulation
Assumes stable supply

## Slide 35: Signoff Analysis: Dynamic Current & Parasitic
NO ACTIVITY
MID ACTIVITY
HIGH ACTIVITY
Voltage probing on-package
Data Corruption caused by large dynamic current in combination with significant parasitic inductance
Static assumption is not valid anymore

## Slide 36: Guidelines III: System-level integration flow
Perform early system-level power modelling
2. Co-design ASIC, PCB, and packaging with PDN awareness
3. Allocate sufficient on-chip decoupling capacitance during floorplanning
4. Validate with IR-drop and EM simulations including package parasitic
RTL Design &
Implementation
Non-Digital block
Integration
Signoff Analysis
Path toward submission

## Slide 37: Best Practice Example: A module-level power model
1 - Develop a Simplified Power Model
Include average and peak current sources.
Model on-chip parasitics and off-chip parasitics.
Signal and Power Integrity using Ansys Electronics Desktop: Practical Case Studies, F. Martina [ https://indico.cern.ch/event/1518027/ ]
2 - Evaluate Power Delivery Network (PDN)
Assess PDN quality under defined current and parasitic conditions.
3 - Set Implementation Constraints
Define package and assembly specifications.
Verify ASIC and package compliance with specs.

## Slide 38: R&D Topic: IR-drop induced Jitter Analysis
Post-Layout simulation
Current Extraction
Voltage rail analysis with package parasitics
Chip activity
Current profile
IR-drop induced
Jitter Analysis
TIE Jitter across cycles
- 40 ps
+ 40 ps
Presented at TWEPP ‘23
https://cds.cern.ch/record/2906018
Instances Voltage

## Slide 39: Guidelines: Summary
Design
Integration
Analysis
Path toward submission
Where to implement these guidelines
?
Design
1. Clear separation of data and control paths
2. Design with Hardware and Verification in Mind
3. Static configuration with controlled start-up sequence
4. Early and comprehensive coverage analysis
Integration
1. Identify analog–digital boundaries and critical blocks
2. Address timing-critical blocks with care
3. Extend verification beyond digital-only approaches
4. Validate macro quality and modeling accuracy
Analysis
1. Perform early system-level power modelling
2. Co-design ASIC, PCB, and packaging with PDN awareness
3. Allocate sufficient on-chip decoupling capacitance
4. Validate with IR-drop and EM simulations before tapeout

## Slide 40: Conclusion: Chip Skeleton
HEP projects evolve → specifications cannot be expected to remain fixed from the start.
Control this evolution with Infrastructural specifications, aka the “chip skeleton”:
Defined early in the project
Assessed through initial virtual prototyping studies
Discussed and/or reviewed with external experts
Block Diagram
Macro requirements
A/D Boundaries
Early Power model
Architecture Exploration
Packaging
System integration
Verification flow
…
Chip Skeleton
Requirements
Guidelines
Early Virtual Prototyping

## Slide 41
Thank You!