## Slide 1: Novel monochromatic and tunable γ-ray light sources through exposure of acoustically modulated monocrystals to ultra-relativistic charged particles beams
Nektarios A. Papadogiannis1,2*
M. Kaniolakis1,2, K. Kaleris1,2, E. Kaselouris1,2, Y. Orphanos1,2, M. Bakarezos1,2, V. Dimitriou1,2, Michael Tatarakis1,3
1Institute of Plasma Physics and Lasers, Hellenic Mediterranean University (HMU), Rethymnon, Greece
2Physical Acoustics and Optoacoustic Lab, MTA, HMU
2Department of Electronic Engineering, HMU, Chania, Greece
*email: npapadogiannis@hmu.gr

## Slide 2: TECHNO-CLS: The European try for Crystalline Undulators for γ-ray generation
European Innovation Council (EIC) Pathfinder Project TECHNO-CLS (2022-2027)
Horizon Europe EIC-Pathfinder Project TECHNO-CLS: "Emerging technologies for crystal-based gamma-ray light sources"
TECHNO-CLS project aims at the breakthrough in technologies needed for designing and practical realisation of novel gamma-ray Light Sources (LS) operating at photon energies from ~100 keV up to GeV range that can be constructed through exposure of oriented crystals (linear, acoustical bent and periodically bent) to the beams of ultra-relativistic charged particles.

## Slide 3: Crystalline vs Magnetic Undulator
Creator: Cyprian Lothringer
Copyright: European XFEL
K. Kaleris, E. Kaniolakis Kaloudis, Emmanouil E. Kaselouris, K. Kosma, E. Gagaoudakis, V. Binas, S. Petrakis, V. Dimitriou, M. Bakarezos, M. Tatarakis, & N. A. Papadogiannis, Applied Physics A. 129, 1007 (2023)
Magnetic Undulator
λu~ 1-10 cm, ℏω=1-10 KeV
Crystalline Undulator
λu~ 1-100 μm, ℏω=0.1-10 ΜeV

## Slide 4
First Idea:
Mechanically bend crystals

## Slide 5: CU parameters – conditions and suitable accelerators

## Slide 6: Experiments in various accelerators

## Slide 7
Mechanically bend crystals first experimental results in MAMI
CH-Channeling
DCH -Dechanneling arises due to incoherent scattering leading to inefficiency!
VR-Volume reflection or volume capture (VC)
Mechanisms of interaction between charged particle beams and bent crystals
(1) and (6) the crystal is not aligned to the beam. (2) Indicates channeling, (3) points to dechanneling, (4) identifies VR, and (5) identifies VC.

## Slide 8: Manufacturing Periodically bent crystals (static)

## Slide 9
Channeling in binary crystalline bending structures (static)
Bending can be achieved by variation of the dopant content in binary crystals [1]
Ge and Si have different lattice parameters which leads to a deformation in Si1−x Gex [2]
Scheme of Si1−x Gex crystal bending due to variation of Ge content [3].
[1] Mikkelsen& Uggerhøj, NIMB 160(2000) 435
[2] Krause, Korol,Solov’yov, &Greiner, NIMB, 483(2002) 455
[3] Korol, Solov’yov, Greiner, “Channeling and radiation in periodically bent crystals”, Springer (2014)
Model by
MBN Explorer ®
Using MD methods

## Slide 10
Acoustic Crystalline Undulators: principle of operation
Acoustic crystalline undulator: device structure
Novel Idea!

## Slide 11
Acoustic Crystalline Undulators: expected advantages!
AW CUs will allow for real-time experimental optimization and scanning of a broad parameter range!

## Slide 12
A-CU modeling: proof of principle
Step1
Simulate acoustic wave propagation inside crystal
Step2
Extract the displacement of the lattice planes due to the pressure distribution
Step3
Calculate particle trajectories and generated γ-ray radiation
Undulation peak
Photon Energy
Radiation intensity
Diagonal distance
Displacement
Finite element method
(LSDYNA)
Molecular dynamics
(MBN explorer)
K. Kaleris, E. Kaselouris, V. Dimitriou, E. Kaniolakis-Kaloudis, M. Bakarezos, M. Tatarakis & N. A Papadogiannis
G. B. Sushko, A. V. Korol & A. V. Solov’yov
Physical Review Accelerators and Beams 28 (3), 033502 (2025)

## Slide 13
Near single frequency sinusoidal profiles
f = 40MHz
f = 10MHz
Increasing the excitation frequency

## Slide 14
Calculation of 20GeV positrons exemplary trajectories
MBN Explorer
K. Kaleris, E. Kaselouris, E. Kaniolakis-Kaloudis, M. Bakarezos, M. Tatarakis, V. Dimitriou, N. A. Papadogiannis and G. B. Sushko, A. V. Korol, A. V. Solov’yov, Narrowband γ-ray radiation generation by acoustically driven crystalline undulators, Phys. Rev. Accel. Beams 28, 033502 (2025).

## Slide 15
A-CU γ-ray radiation tunability!!!
Number of periods: radiation intensity
Undulation period: γ-ray photon energy
Peak @ ~2 MeV
Peak @ ~10 MeV
Photon Energy (MeV)
10 MHz
Photon Energy (MeV)
40 MHz
Periods: 20
Periods: 5
K. Kaleris, E. Kaselouris, E. Kaniolakis-Kaloudis, M. Bakarezos, M. Tatarakis, V. Dimitriou, N. A. Papadogiannis and G. B. Sushko, A. V. Korol, A. V. Solov’yov, Narrowband γ-ray radiation generation by acoustically driven crystalline undulators, Phys. Rev. Accel. Beams 28, 033502 (2025).

## Slide 16
Experiments towards
the realization of AW CU

## Slide 17
Fast Laser Refractive Imaging (FLRI)
Imaging of dynamic acoustic fields
Δy=y-ys

## Slide 18
Computational model
Assuming there is no light lost due to refraction, all the initial optical intensity reaches the camera sensor:
The derivative can be calculated by ys:

## Slide 19
Emmanouil Kaniolakis Kaloudis, TECHNO-CLS, Bremerhaven 2025
So finally we get:
Equation links the light intensity captured by camera to the pressure amplitude of the high frequency ultrasounds and also yields the modulation of the initial intensity distribution!!!
Computational model

## Slide 20
FLRI experimental set up
Fast probing via 6 ns laser pulses allows for static imaging (snapshots) of the dynamic acoustic field inside thin crystals!!!

## Slide 21
FLRI results and signal processing
Characteristic images of TeO2 crystal obtained with phase imaging technique: without excitation (left), with excitation (right)
Analysed image, demonstrating the fringes generated by the deflection of light from the refractive index gradient
Quantification of the 2D spatial distribution of the acoustic pressure field
FLRI captures the images of the light intensity distribution
Division of the acoustically modulated image (signal) by the unmodulated image (reference)
The new image clearly reveals the intensity distribution of the laser beam due to the pressure gradients in the crystal sample, since any irregularities of the laser beam profile are suppressed
3) The 1D representation of the intensity distribution is taken via a lineout along the y direction of the divided image.

## Slide 22
Computational model validation
Results of parametric study
Validation of linear relation between:
Acoustic Pressure / Lattice Displacement and Driving Voltage
Validation of inverse proportionality between:
Acoustic wavelength and Driving Frequency
Calculation of lattice displacement from the experimentally estimated pressure amplitude
Cno= Δlc/V

## Slide 23
Computational model validation
Image captured via FLRI
Intensity modulation line-out
Signal Analysis (for 25 MHz, 10 Vpp)
Pressure: 80 ± 5 kPa
Displacement: 40 pm
Wavelength: 340±20 um

## Slide 24
A-CU Devices under characterization
10 MHz device
Si <100> crystal
20×20×1 mm3
100 um thickness PZT transducer
20 MHz device
The transducer is bonded on the Si crystal using a thin film of vacuum epoxy, ensuring low acoustic losses!!!
200 μm thickness PZT transducer

## Slide 25
Characterization of the dynamic acoustic field in Si based devices
10 MHz device
20 MHz device
Insets: images of the optical intensity pattern captured by FLRI, depicting a snapshot of the dynamic acoustic field in the 1 mm - thin crystal.
10.92 MHz
Pressure: 1530 ± 17 kPa
Displacement: 1.10 nm
Wavelength: 774±11 um
21.40 MHz
Pressure: 295 ± 4 kPa
Displacement: 0.12 nm
Wavelength: 390±9 μm
Kaniolakis et al. Precise control of high frequency ultrasounds in thin crystals for the development of tunable narrowband and directional γ-ray sources, under minor revision in JASA
Plots: line-out and model estimation of the optical intensity modulation due to the acoustic field at the time instance of probing.

## Slide 26
Frequency domain representations of the line-outs of the optical intensity modulation, obtained via FFT
Strong harmonic components indicate the suitability of the devices for the generation of narrowband γ radiation.
Characterization of the dynamic acoustic field in Si based device
Peak: 1295 m-1
Peak: 2538 m-1
10 MHz device
20 MHz device

## Slide 27
Towards higher frequencies !!!
Successful characterization of HFUS in Si <100> crystals with nominal resonance frequencies of 10 MHz and 20 MHz, using FLRI and supported by a specially developed computational model.
Kaniolakis et al. Precise control of high frequency ultrasounds in thin crystals for the development of tunable narrowband and directional γ-ray sources. Underreview in JASA

## Slide 28
The role of ultrafast lasers in generation of localized ultra high frequency acoustic waves in crystals

## Slide 29
Electron dynamics
J. Hohlfeld et al., Chem. Phys. 251, 237 (2000)
Non-thermal electron excitation
Electron thermalization (via e-e & e-ph)
Electron-lattice thermal equilibrium
Lattice Dynamics
Laser-induced localize strain
Strain propagation
Strain reflection from interface
Detection of strain at surface (echo)
Ultrafast phenomena in metallic optoacoustic transducers

## Slide 30: Degenerate pump-probe transient reflectivity typical set-up
Brillouin scattering observation through interference:
Reflected beam from material surface
+
Reflected beam from
fast moving strain pulse

## Slide 31
New results in Tantalum/Silicon
20 nm Tantalum on Si
Super fast electronic excitation
Fast electron-phonon
transferring
Brillouin oscillations in substrate (Si)
The oscillation period depends on the sound speed in any depth of the substrate
Visibility of oscillations depends on the intensity of nanoacoustic wave in any depth of the substrate

## Slide 32: Acoustically-driven Crystalline Undulators for γ-ray generation
From: A. V. Korol, A. V. Solov'yov, W. Greiner, Channeling and Radiation in Periodically Bent Crystals, Springer (2013)
Working principle
Design principle
Travelling acoustic waves
K. Kaleris, E. Kaniolakis-Kaloudis, E. Kaselouris, K. Kosma, E. Gagaoudakis, V. Binas, S. Petrakis, V. Dimitriou, M. Bakarezos, M. Tatarakis, N. A. Papadogiannis, Efficient ultrafast photoacoustic transduction on Tantalum thin films, Applied Physics A (2023) 129:527
Piezo-electric driving
Ultrafast Laser driving

## Slide 33: Studying the transducers’ nature - Experiments
E. Tzianaki, et al, Optics Express 23, 17191 (2015)
K. Kaleris, et al , Applied Physics A (2023) 129:527

## Slide 34: Computational model based on FEA in LS-DYNA software

## Slide 35: Results – Tantalum on Si induce train of nanoacoustic strains!
Solid blue and dot-dashed red lines correspond to Ti/Si and Ag/Si cases, respectively. Vertical dashed line corresponds to the metal/Si interface position
Calculated strain pulse distribution in 25 nm metal/Si systems as a function of depth, at different time instants.
Solid blue and orange lines correspond to Ta/Si and Ti/Si cases, respectively. Vertical dashed line corresponds to the metal/Si interface position

## Slide 36: Results II– Tantalum on Si induce train of nanoacoustic strains!
Calculated strain distribution in 25 nm metal/Si systems as a function of time, for a depth of 4 nm in the Si substrate
Solid blue and orange lines correspond to Ta/Si and Ti/Si cases, respectively.

## Slide 37
Possible Applications of monochromatic and brilliant
γ-rays
Generated by CU

## Slide 41
Relativistic
e- and e+ micro-accelerators
via Multi-TW and PW lasers
N.A. Papadogiannis1
Grigoriadis1, G. Andrianaki1, I. Tazes1, M. Bakarezos1, V. Dimitriou1, E. Benis2, M. Tatarakis1
IPPL, HMU Greece
Physics Dep, UoI, Greece

## Slide 42: Traditional Relativistic electron accelerators

## Slide 43
Classic light EM-Fields(a) vs Relativistic EM-Fields(b)
Lorentz
a) Classic Fields α0<1 (b) Relativistic Fields α0>1 ->
0<1
-> α0>> α02
α0<<α02
Acceleration in z-axes
Oscillation in x-axes
x
z
x
z

## Slide 44: Generation of Laser-Plasma waves
Physical 1D system example: EM pulse, λ=1μm, τpulse=100 fsec, Plasma, n0=1018 cm-3 (λp=30μm) (i.e. cτpulse ~ λp)
Non-relativistics case, a0=0.3
Relativistics case, a0=2.0

## Slide 45: Laser Plasma miniature electron accelerators
100 mm
The ponderomotive force (gradient of laser intensity) pushes electrons away from axis and generates a charge separation between ions and electrons

## Slide 46: The Dream electron beam by LWFA
46
First theoretical prediction of non-linear plasma waves as accelerators Tajima and Dawson, PRL, 43, 267 (1979)
First experimental demonstration of monoenergetic (~100 MeV) electron generation from relativistic laser-plasma interactions
Mangles, S.P.D. et al., Nature, 431, 535 (2004)
Geddes, C.G.R. et al., Nature, 431, 538 (2004)
Faure, J. et al., Nature, 431, 541 (2004)
First >GeV demonstration of monoenergetic electron generation
Leemans, W.P. et al., Nature Physics, 2, 696 (2006)
Long interaction length, i.e. 33 mm,
via guiding through a Hydrogen filled,
discharge capillary

## Slide 47
Plasma waves with Ε-field > 100 GV/m
Electron energy gain: Mev to GeV
Laser Wakefield Acceleration (LWFA)
V. Malka
Electron Injection in plasma bubbles
ion
cavity
ion
cavity
Ponderomotive forces of laser larger than space charge restoring force of the ions

## Slide 48
LWFA experimental station @ IPPL
Clark EL, Grigoriadis A, Petrakis S, et al. High-intensity laser-driven secondary radiation sources using the ZEUS 45 TW laser system at IPPL/HMU, High Power Laser Science and Engineering. 2021;9:e53. doi:10.1017/hpl.2021.38

## Slide 50: The role of laser nozzle geometry
0.8 mm Nozzle
He
850 mJ
Nozzle Density Profile
Electron Spectra
Interferometric Characterisation
He
950 mJ
3 mm Nozzle
Electron Spectra
Interferometric Characterisation
Nozzle Density Profile
A Grigoriadis et al 2022 Plasma Phys. Control. Fusion 64 044007
G Andrianaki et al 2023, Rev. Sci. Instrum. 94, 103309

## Slide 51: Generation of Betatron radiation I
X-ray CCD
Lanex
CCD
A. Grigoriadis et al
Applied Physics Letters 118, 13 (2021)

## Slide 52: Generation of Betatron radiation Varying the gas nature
Self Injection
Ionisation Injection
He
N2
Ne
Ar
570 mJ
A. Grigoriadis et al Applied Physics Letters 118, 13 (2021)

## Slide 53: Non-linear QED approach for betatron radiation in a laser wakefield accelerator
Non-linear QED (classical regime) accurately models LWFA betatron radiation
Reproduces experimental results across targets and laser powers with reduced computational cost
Simplifies experimental reproducibility by minimizing runs and parameter scans
Provides an efficient framework for advanced LWFA schemes (ionization injection, multi-stage, high-power lasers)
Ong, J.F., Berceanu, A.C., Grigoriadis, A. et al. Non-linear QED approach for betatron radiation in a laser wakefield accelerator. Sci Rep 14, 605 (2024)

## Slide 54
The role of the laser chirp on LWFA

## Slide 55: Light Synthesizer – Mode-locking for fs pulses
t
0
w1
w2
w3
w4
w5
w6
Graphs by R. Trebino Open Acess Presentations

## Slide 56: Chirp of an ultrashort Gaussian-like laser pulse
A chirped laser pulse has an E-Field:
where:
The instantaneous frequency is:
which is:
So the frequency increases linearly with time.
Positive chirp β>0
Negative chirp β<0

## Slide 58: The Experimental set-up for chirp experiments
Grigoriadis, A., Andrianaki, G., Tazes, I. et al. Efficient plasma electron accelerator driven by linearly chirped multi-10-TW laser pulses. Sci Rep 13, 2918 (2023).

## Slide 59: Method to varying the chirp (Dazzlers or AOPDF)
The AOPDF (for Acousto-Optic Programmable Dispersive Filter) relies on a longitudinal interaction between a polychromatic acoustic wave and a polychromatic optical wave in the bulk of a birefringent crystal.
Optical signals in the hundreds of Terahertz range are then controlled by RF signals in the tens of Megahertz range.
The spectral phase control is as accurate as the material properties of the crystal are known, without any assumption or hypothesis, thus allowing users to fully trust the shaping characteristics. The Dazzler phase control is obtained through the control of group delays versus wavelength.
The interaction between an optical wave and an acoustic wave also prevents the user from spectral phase discontinuities inherent to pulse shaper based on pixelated modulators.
Unlike other ultrafast pulse shapers relying on 4-f lines to spatially disperse the spectral components, the Dazzler does not require a complex optical set up. The Dazzler crystal is the only component inserted in your setup, and installation is performed in only few minutes.
Moreover, due to the physics of the acousto-optic interaction, the Dazzler system only requires a single point calibration to achieve accurate results.

## Slide 60: Typical Experimental Results on electron acceleration
FTL pulse
Grigoriadis, A., Andrianaki, G., Tazes, I. et al. Efficient plasma electron accelerator driven by linearly chirped multi-10-TW laser pulses. Sci Rep 13, 2918 (2023).

## Slide 61: Theoretical Modelling Method
Model utilizing PIC Simulations
2D PIC simulations performed in the EPOCH PIC code
The computational domain was set as 120×100 μm and was discretized by 2400×500 cells, with 5 particles per cell
The gas density geometry, determined in our earlier works, was used in the code, while the gas type was set to fully ionized He
The laser pulse parameters were set according to the ones experimentally used
The simulations ran for three cases of laser pulses: i) an FTL pulse, ii) a positively chirped pulse and a negatively chirped pulse. In the latter, the chirped value was set at +400 fs2, which corresponds to the positive chirp value with the highest electron energy measured
A moving window configuration was used for a total simulation time of 11.4 ps.

## Slide 62: Results of the theoretical Model
PIC Simulation clearly show that Positively chirped pulses generate finally the highest maximum electron kinetic energy compared to the negatively chirped and the FTL pulses
Positively chirped pulses show a large energy gain rate that is wider in time, compared to the negatively chirped and FTL pulses, thus resulting in the highest maximum electron kinetic energy.
Grigoriadis, A., Andrianaki, G., Tazes, I. et al. Efficient plasma electron accelerator driven by linearly chirped multi-10-TW laser pulses. Sci Rep 13, 2918 (2023)

## Slide 63: The role of laser chirp in relativistic electron acceleration using multi-electron gas targets
A Grigoriadis et al 2023 Plasma Phys. Control. Fusion 65 044001
He
Mechanism of direct ionization injection of inner-shell electrons in multi-electron targets, that proceeds at appropriate laser peak intensities and laser chirp values, also contributes to the efficient electron acceleration resulting in relatively high maximum electron energies
Larger plasma density requires higher positive chirp values for efficient electron acceleration.
K-shell electrons of nitrogen can be field-ionized by tunneling near 0 chirp

## Slide 64: LWFA electrons
160 TW Gemini Laser @ RAL UK (collaboration QUB, IC, UM Ann Arbor, CLF RAL)
Narrow energy spread Positrons
105 positrons per pulse in 5% energy bandwidths around 0.5 GeV
Breit–Wheeler processes

## Slide 65: Coherent Transition Radiation (CTR)
How CTR is Generated?
Electron Nanobunch Formation:
Ultra High-intensity laser pulses with a target, accelerating electrons into dense, sub-micron-sized relativistic electron "nanobunches“
2.Phase Coherence:
These nanobunches maintain a synchronized, "coherent" phase relationship, meaning their electromagnetic waves align, leading to constructive interference and enhanced radiation intensity.
3. Transition to Vacuum and CRT generation:
When these nanobunches are emitted through the rear surface of the material, they undergo a rapid change in the electromagnetic field. This change, or "transition," at the boundary between the material and vacuum, generates the coherent transition x-ray or γ-ray radiation!

## Slide 66: Coherent Transition Radiation to accelerate positrons
Electron acceleration driven by LWFA has made remarkable progress reached multi-GeV energies with a small energy spread
The acceleration of pre-generated positrons is not as straightforward as it was for electrons. A key issue is that the plasma wakefield valid for electron acceleration defocuses positively charged particles
Coherent Transition Radiation (CTR) proposed to accelerate positrons and obtained a quasi-monoenergetic positron beam:
  Stage I: generation and acceleration of high-charge high-energy electrons with LWFA
  Stage II: positron generation in high Z material (eg copper target) via Bethe-Heitler process
  Stage III: acceleration process of positrons. Dense electron bunch from LWFA induce strong CTR inside the copper target that propagating into a vacuum, capable of trapping and accelerating positrons for a long distance.
  Simulation results show that the CTR field is up to 10's GV m-1, which captures and accelerates the positrons to peak energies up to 500 MeV (energy spread ~20%). An external longitudinal magnetic field of 30 T is also applied to guide the electrons and positrons during the acceleration process.
Shanghai Institute of Optics and Fine Mechanics Chinese Academy of Sciences
Bethe-Heitler process: high-energy photons (light particles) create matter—specifically, an electron and a positron pair—when they pass near a heavy nucleus

## Slide 67
Kim, H.T.; P et. al. Multi-GeV LaserWakefield Electron Acceleration with PW Lasers. Appl. Sci. 2021, 11, 5831
Multi-GeV electrons using LWFA

## Slide 68
Field gradients of different accelerator technologies and their relation to wavelength and frequency of the accelerating field.
Laser Plasma accelerators: a promising research field for the future
Hidding, B., Hooker, S., Jamison, S., Muratori, B., Murphy, C., Najmudin, Z., Pattathil, R., Sarri, G., Streeter, M., Welsch, C., Wing, M., & Xia, G. Plasma Wakefield Accelerator Research 2019 - 2040: A community-driven UK roadmap compiled by the Plasma Wakefield Accelerator Steering Committee (PWASC), arxiv (2019)
IPPL-HMU
Non-exhaustive overview of laboratories working on laser-driven (black) and particle beam-driven (green) plasma wakefield acceleration.
This rapid scientific and technological progress is now posing the realistic question as to whether plasma-based acceleration could be a viable complementary technology for the next generation of particle colliders to break the TeV barrier

## Slide 69
European Strategy for Particle Physics 2022 report recognizes the potentiality of Laser Plasma acceleration

## Slide 70
Advanced and Novel Accelerators for Colliders (Towards TeV Collider)
Eric Esarey, Lawrence Berkeley National Laboratory
ANA: potential for multi-TeV collider
− 1-10 GV/m: compact linacs
− Ultrashort bunches: reduce power
− Gamma-gamma, polarized e+e-
• Vigorous research, rapid progress − >1000 pubs/yr
• Strong European endorsement
− EuPRAXIA
• Next Steps: Upgrade existing facilities
− Remain productive and competitive
− Ensure progress on R&D roadmap
• Need for integrated design study
− Include auxiliary systems
• Need design for intermediate energy facility
− Build physics case 20-100 GeV
• Intermediate applications
− Light sources, compact accelerators

## Slide 71
Acknowledgement
Part of the presented work was funded by the European Commission through Horizon Europe EIC-Pathfinder-2021 Project TECHNO-CLS (Project No. 101046458). The HMU team acknowledges the grant of computational time by the Greek Research and Innovation Network in the National HPC facilities ARIS under project ID pr016025-LaMPIOS III.